## Slide 1: Digital Manufacturing using STEP-NC
Martin Hardwick
Blair Downie
David Loffredo
info@steptools.com
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: Current NC programming using RS274D
%
N05 G54
N10 G00 Z10.000
N15 G91 G0 Z200
N20 T5 D1 WW
N30 G90 M5
N35 G00 X0.000 Y-150.000
N40 G00 Z5.000
N45 M08
N50 S3183.000
N55 M03
N60 F1477.000
N65 G00 X60.000 Y-150.000
N70 G00 Z5.000
N75 G00 X60.000 Y-150.000
N80 G01 Z-0.500
...
machine-specific part program with axis data generated by a postprocessor
vendor-specific extensions of the original standard
only primitive motion and switch commands
no standardized data format for spline processing and sophisticated NC technology
Courtesy WZL RWTH Aachen
STEP-NC replaces this with a
rich, integrated data format
Ideal for Paper Tape!
The standard for 40 years!

## Slide 3: STEP-NC is integrated
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 4: Key feature of STEP-NC
STEP-NC describes “what” not “how”
  Make this geometry from this stock
  By removing these features
  In this order
  With these tolerances
  And tools that meets these requirements
The old standard described “how”
  Move tool to this location
  Move tool to this location
  And so on for millions of commands

## Slide 5: GDLS Demonstration
B’port
Mill
Std B’port
Controller
MS Windows
STEP-NC enable a legacy Bridgeport Controller
  Press “Run” to make the part
  Press “Verify” to check tool paths for collisions
  Press “Document” to create a spreadsheet of operations
Totally Push Button!
Minimal user input
Run
Verify
Document
Micro Process Planning
G-Code
GibbsCAM
.vnc
Post
DTK
STEP-NC
Plug-in
STEP-NC Controller
Internet
XML
STEP-NC
file
optimize

## Slide 6: Getting Started
GibbsCAM
ST-MachineTM Plug-in
MASTERCAM
ST-MachineTM Plug-in
Explorer
ST-PlanTM Plug-in
ST-NCTM Server
http://www.stepnc.com
There are about 65,122 small manufacturing enterprises using about 500,000 CNC machines.
Send us STEP or STEP-NC files
Esprit Plug-in soon!
Manufacturing
Detailing
Manufacturing

## Slide 7: Enabling Tools
Detailing using the ST-Plan Explorer Plug-in
  Read STEP data into web site
  Recognize features
  Recognize tool requirements
  Enter critical tolerances
  Enter critical surface finishes
  Write STEP-NC data
Manufacturing using the ST-Machine CAM Plug-in’s
  Read STEP-NC data from web site
  Build CAM geometry automatically
  Match tools
  Build CAM operations automatically
  Optimize, verify and post
Detailing
On the WWW
Define the design requirements
STEP
ST-NC
Server
Customer
Manufacturing
Using a CAM
Optimize & execute the manufacturing process
CNC
Supplier

## Slide 8: Super Model Project (1999 –2005)
  GE Fanuc
  CNC Data (Mastercam)
  CADKEY
  Alibre
  Boeing
  General Electric
  General Motors
  Gibbs and Associates (GibbsCAM)
  Hurco Companies Inc.
  Lockheed Martin
  IBM
  NASA (GSFC)
  NASA (JPL)
  NCMS
  Northrop Grumman
  Unigraphics Solutions
  Parametric Technology Corp
  DP Technology (Esprit)
  NIST Intelligent Systems
  Caterpillar
  Lawrence Livermore Laboratories
  DaimlerChrysler
  Watervliet Arsenal (Benet)
  Pratt & Whitney
  General Dynamics Land Systems
  Cincinnati Machine
  US Army
  EMPT
  Cambridge Valley Machining
  Honeywell
  RPI
Industrial Review Board
Round 1 Pilot Project Participants

## Slide 9: Pilot Project Goals
Pilot Project participants show STEP-NC can be used to make production parts
  Round 1 2.5D feature milling 6/1/02 to 11/30/02
  Round 2 Surface milling 12/1/02 to 5/31/03
  Round 3 Casting 6/1/03 to 11/30/03
  Round 4 Probing 12/1/03 to 5/31/04
Round 1 goals
  Design related
    Optimize feature recognition
    Complete detailing
  Manufacturing related
    Optimize tool matching
    Optimize CAM operations
  AP-238 related
    Verify standard
    Verify benefits
Before next meeting (9/25 & 26)
Put 5 test files onto web site
Make at least one test part
Send crib sheet data to STEP Tools

## Slide 10: Press Interest
Combined circulation > 1 million