## Slide 1: History-based (macro) parametrics for PLIB
2002. 6. 12
Soonhung Han
KAIST, PartDB
shhan@kaist.ac.kr

## Slide 2: Idea
Crash recovery of a DBMS: Transaction log file of SQL commands
Exchange of (implicit) design intents included in commands sequence
STEP
AP203
Proposed Technology

## Slide 3: Translate command history
CAD 1
Command
history of shape modeling
CAD 2
Command
History (translated)
Re-generated
model

## Slide 4: Comparison – related works
LOD /
Granularity
Parametrics
type
User
command
API
B-rep
geometry

## Slide 5: Comparison
AP203: pure B-rep without parametric information
Part 108: explicit parametric approach at the geometry level (constraints)
OMG CAD Services: API level with some parametric feature information
EDM(ENGEN) and SMCH: hybrid approaches
Macro-parametric: pure procedural approach at the level of modeling commands

## Slide 6: Analysis of Modeling Commands of Commercial Systems
Pro/E
CATIA
IDEAS
SolidWorks
UG
Standard modeling commands set

## Slide 7: Documentation using EXPRESS
SOLID_Create_Protrusion_Extrude is defined as follows. It creates extruded solid with a profile_sketch through orthogonal linear path
  ENTITY SOLID_Create_Protrusion_Extrude;
  name : STRING;
  profile_sketch : STRING;
  flip : BOOLEAN;
  start_condition : end_type;
  start_depth : REAL;
  end_condition : end_type;
  end_depth : REAL;
  END_ENTITY;
Where name arguments is a extrusion instance name, profile_sketch is a sketch name, flip is TRUE to reverse the extrusion direction, start_condition is the condition of start face such as Blind, Through all and Up to face, start_depth is start depth of extrusion, end_condition is the condition of end face such as Blind, Through all and Up to face, and end_depth is end depth of extrusion.

## Slide 8: Structure of modeling commands (WD3R2)
Create
Protrusion
Extrude
Level 1
Level 2
Level 3
Level 4
ROOT
SOLID
Revolve
Sweep
Variational Sweep
Helical
Loft
Form Feature …
Operate
Cut …
Modify …
Delete
Copy
Boolean
Unit
Intersect
Difference
Filleting
Fillet
Chamfer
Simple
Advance
…
WD3R2
  Sketch 67
  Solid 44
  Surface 22
  Constraint 29
  Total 162
  Korean version

## Slide 9: Development through test
Stage | Test Model | Solid Commands to be tested (cumulative)
1 | L-Block | SOLID_Create_Protrusion_Extrude SOLID_Create_Cut_Extrude SOLID_Operate_Filleting_Fillet_ (Chamfer ,Blend )
2 | Y-Model | SOLID_Create_Protrusion_Revolve ( Sweep)
3 | Gas Spring (real part) | SOLID_Create_Cut_Revolve
4 | Linear Sensor | SOLID_Create_Cut_Sweep SOLID_Create_Protrusion_Variational_Sweep
5 | Engine Airfilter Housing | SOLID_Operate_Boolean_ (Union , Intersect,Difference) SOLID_Operate_Pattern_ (Rectangular,Circular)
6 | Pneumatics Cylinder | SOLID_Create_Feature_ (Hole_Counterbored, Hole_Countersunk, Groove, Pocket, Pad )
7 | Boat | SOLID_Operate_Transform_ (Move,Rotate, Mirror) SOLID_Create_ (Protrusion_Loft , Cut_Loft)

## Slide 10: Test Cases
3-1
Gas Spring
2
Y-model
1
L-block (SMCH)
4-2 Pneumatics Cylinder
4-3 Boat
3-2
Linear Sensor
4-1 Engine Airfilter Housing

## Slide 11: Translator implementations
Macro Parametrics
Pro/E
CATIA
SolidWorks
UG
김병철
문두환
양정삼
이한민
김준환
김흥기

## Slide 12: Verification of L-block
SolidWorks98
CATIA V5R3
Pre-processor
Standard macro file
Post-processor
Macro file (Script file)
Macro file (swb file)
Parametric
changes
Notes: It shows the translator between difference CAD systems using macro parametrics.

## Slide 13: SolidWorks  Catia
Tests with real parts

## Slide 14: Pro/E  Catia
Pro/Toolkit

## Slide 15: 2 possible applications
Translator based on
macro-parametric
Standard set of
modeling commands
CAD data
translation
(DEX) service
A module
of a
commercial
CAD
** Collaborative modeling

## Slide 16: Pilot translation service
Started in April 2002
On the Web: http://partdb.com
Start with relatively simple parts
NWI at Nov. Seoul meeting (Nov. 2002)

## Slide 17: NWI
Exchange of command history or procedure need a set of standard commands for reference (100s IR)
Parts manufacturers use heterogeneous CAD systems
Scope: They need a relatively simple but robust translator
Commands for assembly and complex operation are out of scope

## Slide 18: Relative position
Command = entity (thing, Part 42) + action (process, operation)
Implementers/Developers
Representation
User
requirements
Command
Entity
Mike
UK
Bill
PDES
Soonhung
Korea

## Slide 19: Command = entity + action
History, sequence, procedure involve time
Entity is static, no time involvement
Command should include action, operation, process
Command = entity + action
STEP entities: Part 42, Part 108
Macro, Script, Operation sequence, Commands sequence, Journal, Log

## Slide 20
Q & A

## Slide 21: Other work to be done
Persistent naming
Vendor support: Friendly Macro (script, command log) file
Beyond: Compound commands, Assembly

## Slide 22
Paper
Drawing
CAD 1
CAD 2
AP203
Designer 
Designer 
??

## Slide 23: Standard set of modeling commands for history-based parametrics
2002. 6. 11
Soonhung Han
KAIST, PartDB
shhan@kaist.ac.kr