## Slide 1
AP224-Enabled Implementations
STEPTrans, STEPValidator, and STEPPlan implementations in the DoD EMALL and the US Army’s Tank-Automotive and Armaments Command
Presented by:
Dr. Bill Freeman, Jr. Mr. Len Slovensky
ISO TC184/SC4 Meeting
Stockholm Sweden
June 2002

## Slide 2: Overview
  STEP Manufacturing Suite
  Product Introduction
  DoD EMALL Implementation
  TACOM’s National Automotive Center STEP Implementation … N-STEP
  Len Slovensky’s presentation on STEPTrans, STEPValidator, and STEPPlan

## Slide 3: A STEP Manufacturing Suite
AP224
AP2XX
AP238
STEP
Product Data
Generation
Macro
Process
Planning
Micro
Process
Planning
AP2XX
with
AP224
Features
AP224
AP238
STEP-NC
Shop
Floor
Part
Fabrication
(DESIGN)
(FACTORY)
(FACTORY)
(FACTORY)
STEP In, STEP Out,
STEP Throughout
Functions
Standards
Technology Example(s) STEPTrans STEPPlan CAM System CNC Controllers
STEPValidator LOCAM Turning and/or
Milling Centers
ISO 6983
M&G Codes

## Slide 4: AP224-Enabled Products
STEPTrans An AP224 translator and order manager
STEPValidator A tool to view AP224 files and validate them
STEPPlan A CAD-based macro process planner
QCAB/PARIS A quote management system (QCAB) integrated with a data repository and access system (PARIS)
Plan 2 Production A detailed process planner and shop floor control solution

## Slide 5
Vendor View: DoD EMALL ODM
Data
Validation
Site(s)
PARTS
DEMAND
QUALITY
PARTS
Data
Conversion
Sites
Reverse/
Re-Engineering
Sites
Product Data
Broker
Manufacturing
Broker
Customers:
Military Serv.
Vendors:
Non-STEP Mfg Sites
World
Wide
Web
QCAB
STEPTrans
PARIS
STEPValidator
QCAB
STEPValidator
PARIS
QCAB Server
PARIS
QCAB
PARIS
STEPPlan
Plan2Production
QCAB
PARIS Server
QCAB
QCAB
PARIS
QCAB
PARIS
Plan2Production
STATUS
Vendors:
STEP-Enabled
Manufacturing Sites
Raw
Material
Suppliers
Orders w/
STEP data
Orders w/
non-STEP
data
DoD EMALL
QCAB
PARIS
STEPPlan
www.partsalacarte.com

## Slide 6: TACOM’s N-STEP Project
Parts
Demand
Legacy
Data
World
Wide
Web
Technology Infusion
STEP-Enabled Manufacturing
CAMP’s Member Manufacturers
TBD
STEP-Enabled Manufacturing for Additional Commodities
Gears
Castings
Forgings
Electronics
Etc.
Mechanical STEP Data Mgt
Verification
Storage
Conf. Mgt
Mechanical STEP File Generation
(backup)
R&D
Develop New STEP APs
Develop New STEP Tools
Demo Projects
Plan For And Execute Pilot Demo Projects For New APs
Mechanical Part Orders
(Near-Term)
Add’l Commodity Part Orders
(Long-Term)
Brokering
Product Data
Manufacturing
R&D
PM IAV
PM FCS
Other PMs
PM Abrams
WindchillTM
Technology Infusion
STEP File Generation
Technology Infusion
STEP-Enabled Manufacturing
Technology Infusion
STEP-Enabled Manufacturing
STEP-NC
Focus:Hope
GDLS
Technology Infusion
STEP-Enabled Manufacturing
ANNISTON ARMY DEPOT
Production Activities
R&D Activities

## Slide 7: STEPTrans

## Slide 8
This figure shows a part being displayed in Pro/Engineer product design system. The STEPTrans translator is displayed in the menu bar.
To start a STEP translation, select the STEPTrans menu option.

## Slide 9
After selecting the STEPTrans option, select either AP203 or AP224.

## Slide 11: STEPValidator

## Slide 12
The STEP Validator is useful tool for a non-technical operator to open any AP224 file for viewing and validation purposes.
Upon opening a file, STEPValidator extracts geometry and feature information and immediately displays four shaded views.

## Slide 13
STEP Validator has several display settings that toggle the view among shaded, wire-frame and wire-frame with hidden lines removed using the [Display] menu or the toolbar
Using the [ClickDrag] menu or the toolbar, the operator can change the mouse behavior to rotate, pan or zoom the isometric view.

## Slide 14
The four-pane view can be switched to a single isometric pane from the [Window] menu.
These view modes and mouse behavior changes aid the operator in locating and identifying certain features.

## Slide 16
Using the [View] menu, the operator can see the part's feature list by selecting [Item List].
The "Feature Item List" organizes and lists the part features and their respective details to help locate each item and track validation findings.

## Slide 17
To view a features details, select an item and click on the [Apply] button.
STEP Validator will open a feature details window and highlight the selected feature on the geometric views.
This window enables the operator to validate the feature data against the source data and subsequently mark the feature as Pass or Fail.

## Slide 18
The feature details window can also record the operator's comments that should prove useful to the engineer in understanding the nature of a failure.

## Slide 19
The "Feature Item List" will track the validation status of each feature.
This data is recorded by STEP Validator as a Quality Assurance Report.
The QA Status Report can be accessed from the [View] menu.
The STEP Validator operator can send this report to the engineer for correction.

## Slide 20: STEPPlans

## Slide 21
STEPPlan is a knowledge based Process Planning tool, used by Manufacturing Engineers to develop Process Plans for parts and assemblies. STEPPlan is a tool that can be used by any level of experience ME. STEPPlan allows the more experienced ME the ability to modify and customize the process plan to whatever level of detail they want, STEPPlan acts as an intelligent assistant for the lesser experienced ME. STEPPlan is built upon KTI's knowledge-based engineering software tool ICAD. STEPPlan will work with any relational database. This demo uses Oracle. It is currently only available on UNIX based workstations.

## Slide 22
STEPPlan is driven by orders. An Order may be Created or, if one has already been created, Started from the Top Level. Orders consists of a set of electronic files that are either STEP (AP224 or AP203), IGES or a Graphic Image. The Order may contain any combination of these file types. When Starting an order, the ME is prompted to input an appropriate Order Number. Based on the input file types, the ME is presented with either a Part Model or Assembly to work with.
First step

## Slide 23
The Part Model is used by the ME to become familiar with the part. When the Part Model button is selected at the Top Level, STEPPlan reads in the input files contained within the order. IGES files are presented to the ME using ICAD's IGES translator. Graphic Image files are displayed using a graphics imager. STEP file types are interpreted using STEPPlan's STEP Interpreter.

## Slide 24
For AP224 files, Features,
Tolerances,
Datums,
Feature and General Notes, and
Material descriptions are extracted and presented to the ME. A Solid Model of the Part Model is constructed and presented in the Graphics View as well. The Material definition will be presented when available, as well as alternate materials if any.

## Slide 25
All General Notes are presented to give added insight into the parts definition. Within the various levels under the Part Model, the ME may highlight dimensions of the attributes of the part in the graphics view. Also, using the Display Options button, the ME may choose to view or remove the hidden lines of the Part Model or its subsequent features.

## Slide 26
This is a typical feature presentation. It shows the features solid model relative to the finished Part Model. The attributes that define the feature are presented and may be highlighted in the Graphics View. Associated Tolerances and Notes are also presented.
After the Part Model has been fully investigated by the ME, the next step is to select a material from the material database.

## Slide 27
The ME is prompted through several steps in the selection process. Due to the ambiguous nature of the material definition within the AP224 file, this process must be done manually.
The database of material is queried for the list of current materials.
The entire list may be viewed and selected from
or it may be reduced to a more manageable number by presenting only materials that fit certain criteria such as material shape, size or type.

## Slide 28
The material may be changed by the ME after initial selection. It may be repositioned or resized as well. The manufacturing quantity may also be altered. If an appropriate material is not found, the database may be modified to include a new material. Once the material has been selected, a line is added to the Bill Of Material with the material description. A graphic of the raw stock relative to the part model is presented in the graphics view.

## Slide 29
Once a Raw Stock has been selected, the ME proceeds to create a Process Plan for the Part. This is done by selecting the Process Plan button from the Top Level.

## Slide 30
STEPPlan Process Plans consists of Operations. The Operations are either Machining or Non-Machining. A database driven definition of all the Operations is accessed and pre-assigned selections are presented in the Process Plan view.
The ME may alter the Operation's as needed. Typically only Non-Machining Operations are pre-populated. The ME must select the Appropriate Machining Operations for the specific Part. Non-Machining Operations include Tool Preparation, Material Preparation, Fixturing etc.
Machining Operations are typically Turning, Milling or Hole Making. The Process Plan view gives the ME the ability to edit the Process Plan at all levels. This is accomplished using the Add, Delete, or Reorder buttons.

## Slide 31
All Operations are defined by Time Standards. These Time Standards are contained within the database as well. Time Standards may be defined to whatever level of granularity or detail the ME wants. For example, they may be a generic as
  "Take part and mount it in the machine, 5 minutes." or
  more detailed as "For parts over 50 lbs, use crane to lift part, 2 minutes".
In the Non-Machining Operations, the ME can change the Time Standards as necessary to fit the part. Non-Machining Operations contain only Time Standards while Machining Operations contain both Time Standards and Features to be realised in that Operation.

## Slide 32
After adding a Machining Operation and selecting it from the Process Plan top level, the ME is presented with the Machining Operation view.

## Slide 33
Selecting the Add Features button presents the ME with the view used to select the features for machining during this Operation. The ME may select the Features from the list provided or they may be graphically selected using the mouse. The method used is dependant on the remaining features, typically they are selected from the Unplanned Features List.
  If all the features have been selected prior, the ME may reselect one of the Features using the Select from List of All Features. This may be done when a Feature has been partially processed in a prior Operation.
  The ME may also define their own Features using the Create a Feature method. This will prompt the ME through a variety of menus to choose the type of Feature and its appropriate definition. This method does not modify the Solid Model.
  During the creation of Features, the ME may probe the Part Model for information or measure its geometry to help determine the attributes of the Feature.

## Slide 34
After selecting features, the ME is given the opportunity to edit what was selected using the Add, Delete or Reorder buttons. At this point, STEPPlan will select machining processes to use to realize the Features on this Machine. Machine type and Feature attributes will be used in this determination.
The ME may preview these selections using the Show Feature Processes button. Features are realized via Processes. Processes are made up of Machining Steps. These Steps are the actual cutting of material and may include roughing or finishing types for example. The Steps are defined by what Tool to use as well as the Feeds and Speeds to set the machine to and how much time it will take to make the cut.

## Slide 35
Choosing the Show Feature Processes shows a list of the Features along with the chosen machining Process with the Feature dimension used to fill in the Process dimensions.
After perusing this list the ME may decide that all Processes chosen are good and can then continue on to subsequent Operations or Generate Outputs. Otherwise the ME may change the selected Processes.

## Slide 36
Selecting the View Partial Process Plan will generate the process plan as it has been defined for this Operation to this point. The ME will peruse this as well and determine if the plan is what is desired. If not they may modify the Features or Time Standards accordingly.

## Slide 37
If the Plan is fine the ME will continue with selecting Features until all are realized and processed. From there they will proceed to generate the outputs. If there are changes required the ME may go into the individual Feature and modify the Process selected or change the Process to another more suitable for this feature. The processes may also be modified to change the Steps that define the Process.

## Slide 38
After the Part has been fully Processed, the ME can now generate Output Reports.

## Slide 39
The Outputs button on the Top Level gives the ME access to all the available Reports that can be generated. There are many predefined reports available, including Process Plan Description, Routing, Bill of Material etc. The Process Plan can also be stored in a database for report generation or manipulation from there.

## Slide 40
This is an example of a database driven report for the Process Plan Summary.