## Slide 1: ISO TC184/SC4/WG12 Parametrics Group: Status Report Mike Pratt LMR Systems/NIST Leader, ISO TC184/SC4/W12 Parametrics Group
ISO TC184/SC4 meeting
Stockholm, Sweden
9 – 15 June 2002

## Slide 2: Overview
Part 108 - ‘Parameterization and constraints for explicit geometric product modelling’
Construction history modelling
  Report on ‘basic mechanisms’ resource proposal, supplementing Bill Anderson’s report on AP203 ed. 2
Part 109 - Enhanced assembly modelling with parameterization and constraints
  Part 109 is being prepared for its CD ballot, and is not further discussed in this presentation.
Long-term (‘General Case’) project
  No progress

## Slide 3: Part 108: Pameterization & Constraints
CD ballot Result (Jan. 2002): Yes, with comments.
CD document was WG12 N940, dated September 2001. DIS version is now in preparation, due Oct. 2002.
Votes: YES (13), ABSTAIN (1), NO (2) - France, Germany
  The most major French and German comments were resolved in Myrtle Beach

## Slide 4: Procedural Modelling Project
PWI project on procedural modelling, i.e. capture and transfer of construction history.
Working Draft exists of a proposed new resource ‘Procedural and hybrid representation’; it will be submitted after this meeting for an NWI/CD ballot.
Allows generation of constructional procedures based on any ISO 10303 entities – in particular, the proposed resource will work with Parts 41 – 44, Part 108, the feature module in AP203 ed. 2, etc, etc.
Working with PDES Inc., CAD vendors and others on representations and on proof-of-concept tests.

## Slide 5: Procedural (history-based) modelling
Model defined as sequences of constructional operations
  New resource uses existing and newly written constructional entities to represent construction operations
  Need to write EXPRESS representations of many types of design features (being done for AP203 ed. 2).
  Other medium-level CAD operations also need to be modelled (KAIST work will provide these).
In the purest approach, no explicit faces, edges, vertices in procedural shape models – nothing but operations
Hybrid models (supported by most CAD systems) may also involve explicit entities
  e.g. (procedural) sweep operation on explicitly defined 2D profile

## Slide 6: Construction History Achievements
Documentation:
  WD of ‘basic mechanisms’ resource (WG12 N983)
  CH module for AP203 ed 2
  Implementors’ Guide
  Parametrization/constraints resource (Part 108) has already passed CD ballot (WG12 N940)
Test implementations:
  PDES Inc.
  NIST
  KAIST (a slightly different approach, but harmonization is in progress within WG12)

## Slide 7: New STEP ‘mechanisms’ resource ‘Procedural and hybrid modelling’
Structured history file with provision for inclusion of design rationale information
Makes provision for history-based representation of general models, with geometric models as a specialization.
A short document – only about 40 pages.

## Slide 8: Construction History Test Implementations
Test model – L-block with hole
  explicit 2D sketch
  extrusion to create L-block
  constant-radius fillet of concave edge
  Boolean subtraction of cylinder + cone to create hole.
In full model, sketch and its constraints are defined using Part 108 capabilities
KAIST is also working with more complex models

## Slide 9: Test Part in CATIA 5.3 (courtesy of KAIST)

## Slide 10: Construction History Test Implementations
PDES Inc implementation (by Theorem Solutions)
  2-way exchange between CATIA and Unigraphics
  Uses a ‘basic mechanisms schema’ similar to N983
  Model not parametric - Part 108 not used
NIST implementation (Hua Jiang/Fujun Wang)
  2-way exchange between ProEngineer and SolidWorks
  Parametric model - Part 108 is used.
KAIST implementation (Soonhung Han’s group)
  5 systems (CATIA, I-DEAS, ProE, SolidWorks, UG)
  Some 2-way exchanges (demo given in Fukuoka, Oct 2001)
  Now based on EXPRESS schema of 170 operations
  Schema will be harmonized with PDES Inc. and WG12 Parametrics Group work before the end of 2002.

## Slide 11: Conclusions
The WG12 Parametrics group is working in several areas, and is beginning to generate a significant number of new ISO 10303 documents.
The Group is collaborating with PDES Inc. and with KAIST on concept generation and testing.
The capture and transfer of procedural or construction history models will be a major advance on current STEP methodology – it is hoped that a solid foundation has been laid for rapid progress to be made in this area.