## Slide 1: Shipbuilding AP’s: An Overview for Implementors
NSRP ISE – ESTEP Project
Ted Briggs
Intergraph Marine and Life Cycle Solutions
Blair Downie
STEP Tools Inc.

## Slide 2: Overview
Shipbuilding AP’s
  Introduction
  ISE Implementation project
Ship Common Model
  Common, unified ARM is basis for all Shipbuilding AP’s
Interpretation of Shipbuilding AP’s
ISE STEP and XML implementation
Summary

## Slide 3: Ship Product Model Exchange Requirements
T 23 APs (Integrated through the Ship Common Model)
Other teams for joint working Groups supporting T 23 usage
To be addressed in the future
Ship Structural Envelope
Distribution Systems
Mission Subsystems/Equipment
Miscellaneous
Ship Arrangements
ISO AP 215
Ship Molded Forms
ISO AP 216
Ship Structures
ISO AP 218
Piping
ISO AP 227
HVAC
ISO AP 227
Electrical
ISO AP 212
Ship Mechanical Systems
ISO AP 226
Outfit and Furnishings
Electronics
Weapons
Oper Logs, Records, Messages ISO AP 234
Part Library Exchange
ISO 13584
ISO TC 184/SC 4/WG 2
Ship Common Model
ISO 10303, Part 102 (Withdrawn)
ISO TC 184/SC 4/WG 3/T 23
Ship Product Model Data Exchange
ISO TC 184/SC 4/WG 3
Engineering Analysis
ISO AP 209, 233
Ship Structural Envelope (hull form, arrangements, structure)
Distributed Systems (piping, electrical, HVAC)
Mission Subsystems/Equipment (mechanical, electronics, outfit and furnishings, weapons)

## Slide 4: AP 216 – Ship Moulded Forms
Status: DIS ballot closes May 2002

## Slide 5: AP 215 – Ship Arrangement
Status: submit for DIS March 2002

## Slide 6
Status: submit for DIS March 2002
AP 218 – Ship Structure

## Slide 7
Plates
Stiffeners
Opening
Deck
Bulkhead
- Structural elements: plates, stiffeners
- Features: interior, edge cutouts, seams
- Structural System breakdown: bulkheads, decks, shell
AP 218 – Ship Structure

## Slide 8
System Components
Air Supply to Engine Room
Exhaust Gas Removal
Fuel Oil Treatment and Supply
Engine Lubricating and Cooling
Propulsion - Main Shaft/Couplings
Maneuverability - Rudder/Thrusters
Electrical Generation
Mechanical Components
Main and Auxiliary Engines
Pumps - Fuel Oil/Lubricating Oil/Cooling Water
Air Compressors and Receivers
Heat Exchangers
Deck Machinery - Winches/Cranes/Derricks
Product Definition Information
Connectivity Between Components and Systems
Geometry, Materials, Topology and Tolerances
Noise, Vibration and Shock Characteristics
Component/System Life Cycle and Operational History
Other Data Supported
Functional Description of Components
Quality Assurance Information
  Availability
  Reliability
  Maintainability
In-Service Inspection and Maintenance
Status: CD ballot closes May 2002
AP 226 Mechanical
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: AP227 Ed. 2 - Plant Spatial Configuration
Ed.2
Ship Requirements
Piping Fabrication
HVAC
Cableways
Status: CD ballot complete Feb 2002

## Slide 10
CIMS / Japan
1991 - 1994
ShipSTEP / EU
1994 - 1996
ITIS / Germany
1992 - 1995
NEUTRABAS / EU
1989 - 1992
MARITIME / EU
1992 - 1995
1991
1999
2003
2001
1997
1995
1993
1987
1989
NIDDESC / US 1987 - 1993
IT in Ship Operation
1994 - 1997
ISIT/US
SEASPRITE/ EU
1996 - 1999
GPME / Japan
1995 - 1996
MariSTEP
1996 - 1999
NCALS - ShipCALS/
Japan 1997
ISE ESTEP
2000 - 2003
HARVEST
2002- 2003
Shipbuilding Projects
Notes: <number>
<footer>
<header>
<date/time>
16
16

## Slide 11: ISE – ESTEP Project
ISE (Integrated Shipbuilding Environment)
  Consortium formed to addressing a broad-based interoperable application environment
    Foundation: STEP/XML, Web services, STEP AP, ISE architecture
  Funded by NSRP (National Shipbuilding Research Program)
ESTEP
  ISE project
  Develop and implement a means for Product Model transfer between shipyards
    Develop translators for AP 216, AP 218, AP 227 ed 2
  Support development and approval of ISO Shipbuilding AP
  Develop usage guide, test data to aid future implementations

## Slide 12: ISE Participants
STEP/XML
Intergraph
(ISDP,GSCAD)
Atlentec-es
(TRIBON,
CATIA)
Electric Boat
ABS
SafeHull
Proteus
Simsmart
STEP Tools
Inc
Northrop Grumman
Ship Systems
Sener
FORAN
Kvaerner

## Slide 13
AP216 - Moulded Forms
AP218 - Structure
2001
2002
ISEC Demo
Demo
2003
AP227 Ed.2 - Piping
Demo
ISE – ESTEP Schedule

## Slide 14: ISE Test Data
Torpedo Weapons Retriever (TWR)
  Full set of drawings release by Navy
  Integrated test suite of a real ship

## Slide 15: ISE Test Data – Moulded Forms
Length (Molded) 117 ft. 4 1/2 in.
Beam, Max 24 ft. 7-5/8 in.
Draft (hull, max) 6 ft. 9 in.

## Slide 16: Ship Common Model

## Slide 17: Shipbuilding AP
STEP Common Resources
Ship Common Model (SCM)
AP 216
Molded Forms
AP 215
Arrangements
AP 218
Structure
AP 226
Mech Sys.
AP 234
Op. Logs
AP 227
Dist. Sys

## Slide 18: Ship Common Model
Common, unified ARM data model for Shipbuilding AP
EXPRESS model
  Building Block
    Set of EXPRESS entities for one concept
  ARM schema for each AP generated from Building Blkocks
Common Units of functionality
    Items and definitions
    Location concepts
    Units and measures
Common interpretation
  Same mapping tables for common entities

## Slide 19: Building Blocks
approvals
changes
definitions
events
features
generic_product_structures
global_axis_characteristics
local_co_ordinate_systems
maintenances
measures
parts
performances
product_structure_by_assembly
product_structure_by_connectivity
product_structure_by_space
product_structure_by_system
repairs
representation_resources
ships
spacing_grids
survey_inspection
survey_status
versions

## Slide 20: Ship Common Model Concepts
Item
Definition
Representation
concept
Geometry & topology,
Viewable
representation
properties,
life-cycle aspects
of the Item
Set
Set

## Slide 21: Ship Common Model Concepts
definable_object
Item_structure
system
item
definition
design_definition
(implicit representation)
representation
functional_definition
(implicit representation)
manufacturing_definition
(implicit representation)
versionable_object
(version)
defined_for
contains

## Slide 22: Ship Coordinate System
Global
Coordinate
System
x
(30,0,0)
(0,0,0)
Ship Coordinate system attributes:
Aft Perpendicular offset = +30
Orientation = forward_pointing
Length Between Perpendiculars = 230
Forward
Perpendicular
z
y
(260,0,0)
Aft
Perpendicular
Fr 0
Fr -2
Frames
Fr 4
Fr 8
Fr 12
Fr 16
Fr 20
Fr 24

## Slide 23: GUID
GUID (Globally Unambiguous Identifier)
  Immutable, persistent identifier
    Maintained by exporting system for life of the object
  Receiving system must return same identifier if object is not changed
  System creating or updating an object must generate a new identifier
Allow data to be exchanged incrementally while preserving relationships
  Within an AP
  Between AP
    Plate references moulded form
    Pipe support references structure
Exchange scenarios
  Single exchange- integrated data model
    Multiple AP’s
    Multiple exchange files per AP
  Multiple exchanges - iterative design
    Only import new objects
  Multiple exchanges - concurrent design
    Only import changes, new objects

## Slide 24: ISE GUID Example
Example
  '<Moulded_form_Key
  x-href=//joshua.ingr.com
  Id="guid:123-123-123" />'
  '<Moulded_form_functional_definition_Key
  x-href="//joshua.ingr.com"
  x-owner="guid:123-123-123"
  x-rev="A"/>'
  '<Moulded_form_design_definition_Key
  x-href="//joshua.ingr.com"
  x-owner="guid:123-123-123"
  x-rev="A"/>'

## Slide 25: Implicit Representation
Representation defined via implicit topological relationships
Moulded Form
    Underlying surface
    Boundaries
      Set of curves
      Set of intersecting surfaces
      Set of intersecting moulded forms
Stiffener
    Profile shape (cross section)
    Trace curve
    Start point

## Slide 26: Units
Global
  Set of units defined for ship
Local
  Set of units defined for specific definitions
Values do not have units

## Slide 27: Interpretation of Shipbuilding AP’s

## Slide 28: Translator issues
AP 215, 216, and 218 use a different approach to map their information requirements into the AIM
  There is only 1 product in the file
    Represents the Ship
  Production_definition_formation entities DO NOT represent versions
    Revisions are modeled by assigning a version id to a product_definition or property_definition
  Properties of the Ship (e.g. principal characteristics), moulded forms, and structural parts of the Ship are represented as product_definitions
    Definitions have GUIDs – global unique identifiers
    Definitions maybe referenced via their GUID
      Ship exchange can involve multiple STEP files
  Each structural part, moulded form, or property has a representation, which could be a descriptive text, an individual measure value, or a geometric construct
  Two sets of units – global “ship” units and local units
    Local units are modeled independently of the representation they apply to

## Slide 29: Translator issues
Shape specific issues
  Overlap with AP203/214: brep, edge-based wireframe, geometric wireframe
  New: non_manifold_surface_shape_representation
    Also defined in AP 214 but has not been tested by the CAX forum
  There is NOT one shape_representation that contains the shape of the entire ship
    Each moulded form (e.g. hull, bulkhead, deck) and structural part (e.g. plate, cutout) has its own shape_representation
    Each shape_representation is related back to the product via a unique reference path
      shape_definition_representation
      product_definition_shape
      product_definition
      product_definition_formation\
      Product
  A moulded form may have multiple shape representations
    Explicit – like AP 203/214
    Implicit – surface geometry plus boundary relationships
      Modeled with shape_aspects

## Slide 30: AP 216 Example
ESTEP test ship – 120’ Torpedo Weapon Retriever

## Slide 31: Contents of the AP 214 file
product
product_definition_formation
product_definition
product_definition_shape
shape_definition_representation
non_manifold_surface_shape_representation

## Slide 32: Contents of the AP 216 file
product
product_definition_formation
product_definition
product_definition_shape
shape_definition_representation
non_manifold_surface_shape_representation
product_definition_formation
product_definition
product_definition_shape
shape_definition_representation
non_manifold_surface_shape_representation
hull
bulkhead

## Slide 33: ISE STEP and XML

## Slide 34: ISE Information Interoperability
W
E
B
S
E
R
V
I
C
E
S
STEP / XML
Parts
ISO 13584
(PLIB)
Product Data
ISO 10303:
227 Piping
PDM
216 Hull Forms
218 Structures
209 Analysis
(STEP)
CAM-NC
ISO 14659
(STEP-NC)
ERP
ISO15531
(ebXML, OAGIS)
<Part>
---------------------------------
---------------------------------
</Part>
<Product Data>
---------------------------------
---------------------------------
</Product Data >
<CAM-NC>
---------------------------------
---------------------------------
</CAM-NC >
<ERP>
---------------------------------
---------------------------------
</ERP >
Customer
Analysis
Production
Planning
Manufacturing /
Outfit
Collaboration
Life-Cycle
Support
ISE Virtual Document
Electronic Deliverables
Interoperability (system-to-system)
Data Exchange
ISE

## Slide 35: ISE Infrastructure
STEP/XML
Web services
ISE Architecture
STEP shipbuilding standards (APs)

## Slide 36: Interoperability Use Cases
Information
Repository
<XML>
<Part …./>
<Part …./>
</XML>
XML File
Information
Repository
Network or
SneakerNet
<XML>
<Part …./>
<Part …./>
</XML>
<XSLT>
and
<XSL>
B2B Use Case
A2A Use Case

## Slide 37: Web Services Architecture
Network (HTTP, FTP, etc)
XML-messaging (SOAP)
XML-information (STEP/XML)
Service Description (WSDL)
Service Yellow Pages (UDDI)
Service flow (WSFL)

## Slide 38: ISE Architecture
01 Executive Summary
02 Requirements
03 XML Evaluation
04 Subject Area Model
05 Interoperability Architecture
  01 Standards
    OSEB recommendation
    STEP/SOAP recommendation
  02 Edo key (persistent identifier)
    EDO identifier recommendation
    STEP GUID proposal
  03 Edo associations
06 Information Models
07 Messaging Models
08 Reference Architecture (Workbook)

## Slide 39: Interoperability Approach
XML business object interface
    Encapsulate, localize mapping of XML business objects to native data format
Presentation, Business Logic, Messaging
    Manipulate data in a uniform, consistent XML format
Data sources loosely coupled to system
    Easy to add new data sources
      No changes to business logic
Adapter
XML Data
XML Request
Data
Source

## Slide 40
XML = Industry Standard
Container for Data
STEP = ISO Standard
Language for Data*
Data
Company
A
Standards
Virtual
Ship
part(s)
Company
B
Transactions of Data Packaged in Standards
XSLT - map data to another XML schema
XML and STEP

## Slide 41: STEP/XML
OSEB encoding adopted in ISO10303-28 (v1)
  Designed by ISE team, adopted by PDES Inc
  Being adopted by users and implementors
SOAP encoding
  ISE team has designed XML Schema approach based on SOAP standard
    Working with International Alliance for Interoperability
Department of Navy -- Interim policy on use of XML for data exchange (9/6/01)
  Adopts W3C Recommendations
  Establishes XML Repository (information models)

## Slide 42: STEP compliance strategy
OSEB
XML file
SOAP
XML file
XSLT
STEP
AIM file
EDO
XML file
ISE
tools

## Slide 43: STEP XML compliance strategy
CAD /
PDM
Shipbuilding
Applications
STEP
Trans.
XML
Trans.
EDO XML
STEP XML
XSLT
Trans.

## Slide 44: Shipbuilding AP
STEP Common Resources
Ship Common Model (SCM)
AP 216
Molded Forms
AP 215
Arrangements
AP 218
Structure
AP 226
Mech Sys.
AP 234
Op. Logs
AP 227
Dist. Sys
Animated Slide

## Slide 45: EDO XML Namespace Approach
Navy Legacy
Namespaces
Enterprise Sys
Namespaces
Future PDM Intop Schema
Current PDM Intop Schema
SCLSIS
Namespace
PDM
Namespace
ISE PDM Schema
Molded Form
Namespace
ISE Molded Form Schema
Dist. Sys
Namespace
ISE Dist Sys Schema
Enterprise Data Object (EDO) Namespace
STEP Namespace
Ship Common Model (SCM) Namespace
Animated Slide

## Slide 46: EDO XML Schema Approach
ISE XML Schemas
    EDO (Enterprise Data Object)
      Key concept: EDO key
    Based on ISO STEP application level schemas
    Use ISO STEP Part 28 XML format
    Will become a standard for shipbuilding industry
    Intent is to register tags with DII-COE XML registry
ISE EDO SCM Schema
    Embodies Ship Common Model product structure
      Not an ISO standard
      Backbone of all Shipbuilding STEP AP standards
    Includes IPDE product model
      Spatial: Units, Zones, Compartments
      Functional: systems
      Parts and occurrences

## Slide 47: EDO XML Schema Approach
Navy Legacy
Namespaces
Enterprise Sys
Namespaces
Future PDM Intop Schema
Current PDM Intop Schema
SCLSIS
Namespace
PDM
Namespace
ISE PDM Schema
Molded Form
Namespace
ISE Molded Form Schema
Dist. Sys
Namespace
ISE Dist Sys Schema
Enterprise Data Object (EDO) Namespace
STEP Namespace
Ship Common Model (SCM) Namespace
Animated Slide

## Slide 48: Summary
Shipbuilding AP
  Culmination of 15 years of work
    DIS / IS by end of 2002
    Several implementation projects
    Translators are being implemented
  Integrated suite of AP
      Ship Common Model
      Use GUID to build integrated ship model
  Basis for ISE XML approach