## Slide 1: Summary of STEP for Electronics Activities for Spring 2002 ISO Meeting - Myrtle Beach, SC
Contributors:
Lothar Klein – LKSoftware
Tom Thurman – Rockwell-Collins
Greg Smith/Mike Keenan – Boeing
Russell Peak – Georgia Tech

## Slide 2: Summary of Ongoing Activities Related to STEP for Electronics
STEP Electro-Mechanical Activities
Standards Development and Deployment
AP210, AP210, AP233
Advocacy
Producibility Analysis (DFM) (B)
AP210 Viewer (B)
IDF/AP210 Conversion (R/B/N)
PWA/PWB Stackup (GT/N)
STEP Repository (GT/N/B)
AP203/AP210 Conversion (N)
Company Activities
AP210 Book (L)
Zuken AP210 Translation (R/L/AT)
Mentor AP210 Translation (B/N/L/AT)
Eagle AP210 Translator (L)
AP210 Primer (A)
Marketing
Implementation
Education
Related Activities
Company Legend
B – Boeing
N – NASA
GT – Georgia Tech
A – U.S.Army
R – Rockwell-Collins
GM – General Motors
L – LK Software
AT - ATI
Manufacturing Simulation (R)
Analysis Templates (GT)

## Slide 3: PWA/PWB Producibility Analysis using AP210
Company PWA/PWB
Guidelines
Codification of
Guidelines
(Rules Definition)
PWA/PWB Captured in Mentor Design Tools
STEP AP210
Rules
Producibility
Analysis
Report
Manufacturing Capabilities
STEP AP220
Comparison of Rules
Against Product Data
(Rules Execution)

## Slide 4: PWA/PWB Producibility Analysis using AP210
Producibility Analysis Report
Boeing PWA Analysis Completed - Generating Summary, Please Stand By...
During this Analysis:
14 Administration Checks were Executed.
40 Data Collection Checks were Executed.
52 Analysis Checks were Executed.
-----------------------------------------------------------------------
106 Checks Total were Executed.
The Analysis on PWA: B169-78762-4,
resulted in the possible violation of 5 rule(s) and 5 guideline(s).
The following (5) rules may have been violated by this design:
IPG Sec 3.3.4 Check PWA support for Surface Mount Automation (Check175 Ver248.25)
IPG Sec 3.3.2 Check PWA Requirement for In-Circuit Test (Check176 Ver241.29)
IPG Sec 3.2.9 Check Minimum PWB Dimensions for Wave Solder equipment (length) (Check17 Ver16.3)
IPG Sec 3.5.5 Check Surface Mount Device Test Keep Out Zone - Minimum Edge (Components) (Check185 Ver296.12)
IPG Sec 3.5.3 Check Wave Solder & Vibration Test Keep Out Zone - Minimum Edge (Components) (Check184 Ver531.9)
The following (5) guidelines may have been violated by this design:
IPG Sec 3.10 Check PWA support for Mixed Technology (Check58 Ver310.28)
IPG Sec 3.6.2 Check Common Surface Mount Component Orientation (Modulo 180) (primary) (Check34 Ver35.2)
IPG Sec 3.10.5 Check Radial Component Lead Span (Check157 Ver914.57)
IPG Sec 3.2.1 Check Maximum PWB Thickness (Check14 Ver245.8)
IPG Sec 3.10 Check PWA support for Mixed Technology (2) (Check70 Ver255.26)
***** Analysis Completed on 02/27/2002 at 8:20:03AM

## Slide 5: PWA/PWB Assembly Simulation using AP210
Rules (From
Definition
Facility)
Generic Manufacturing Equipment Definitions
Specific
Manufacturing Equipment Used
User Alerted on Acceptions to Producibility
Guidelines

## Slide 6: AP210 Viewer

## Slide 7: AP210 Book

## Slide 8: Express/XML-based GUIs in STEP-Book App. AP203 Example - Tree View Widget
LKSoft AP203
StepBook Application
XML GUI widgets specifying
Express-based information sources

## Slide 9: PDES, Inc. Electrical Manufacturing Pilot
Participants
  Boeing, Rockwell-Collins, NASA (JPL and Goddard), Georgia Tech, ATI, LKSoft, U.S.Army
Support the implementation of STEP for Electronics within the US and the world.
Series of min-activities worked by individual companies and teams of companies.
Activities include:
  Translator development and marketing
  Standards publicity
  Tool development
  Standard development/refinement (AP210, AP220, AP233).