## Slide 1: ISO TC184/SC4 Parametrics Group: Status Report Mike Pratt NIST & RPI, USA
Implementers’ Forum
Funchal, Madeira, Portugal
21 February 2001

## Slide 2: Overview
Motivation for Parametrics activities
Specific current activities
  I. Parameterization and constraints – Part 108
  II. Construction history modelling – PDES Inc. project
  III. Enhanced assembly modelling – Part 109 etc.
  IV. General Case Parametrics (longer-term project)

## Slide 3: Motivation for Parametrics Activities
STEP models as currently transferred convey no `design intent’ information.
They omit all data from the sending system concerning several major aspects of shape models:
  parameterization (design freedom)
  geometric constraints (design restraint)
  design features (high-level design constructs with possible links to functionality)
Consequently, received STEP models are ‘dumb models’ that cannot be effectively edited following transfer.
The WG12 Parametrics Group is working to rectify this situation.

## Slide 4: Dynamic models with ‘behaviour’
Current STEP shape models are static snapshots of a design at some stage in its creation.
We need dynamic models whose behaviour in a receiving system is controlled by information sent with the shape model.
Such behavioural information consists of the parameterization, constraint and feature data incorporated in the model by its original designer, and currently lost on transfer.
If we can transfer this data with the model it changes from a ‘dumb model’ to an ‘intelligent model’.
An ‘intelligent model’ knows what are the valid editing operations that can be performed on it – and, equally importantly, the invalid operations that must not be performed.

## Slide 5: Two Types of Dynamic Models
Explicit (STEP-type) models, augmented by additional information:
  parameterization
  geometric constraints
  features
Procedural or construction history models
Most ‘native’ CAD models are hybrids of these two types

## Slide 6: Augmented Explicit Model
B-rep model supplemented by
  parameterized dimensions
    allows family-of-parts definition
    dimensions may be made to depend on other, non-geometric, parameters
  geometric constraints between constructional elements
    parallelism
    perpendicularity
    tangency,
    symmetry, etc.
  Features (with parametrization & constraints)
Sometimes called a variational model

## Slide 7: I. New STEP Resource: Part 108 (1)
Title: ‘Parameterization and constraints for explicit geometric product models’.
Provides mechanism for associating parameters with model dimensions and other quantities
  Allows for capture of mathematical relations between parameters
Provides representations of geometric constraints and mechanism for associating them with elements of an explicit model (not necessarily just shape models).
Provides representations for 2D sketches or profiles used in feature creation.

## Slide 8: I. New STEP Resource: Part 108 (2)
Constraints work in both 2D and 3D – they can therefore be used to constrain assemblies. Specialized assembly constraints are defined for this purpose.
Parameterization and constraint capabilities are sufficiently general that they can be used with other models beyond shape models (plans, processes, organizations,…).
Part 108 is upwardly compatible with existing APs – it sets pointers into an AP203-type shape model but does not demand modification of existing schemas to provide reverse pointers.
Part 108 is currently technically complete and being prepared for its CD ballot (scheduled for mid-2001).

## Slide 9: I. New STEP Resource: Part 108 (3)
Part 108 schemas:
  Parameterization_schema
    (includes methods for representing mathematical relationships)
  Explicit_constraint_schema
    (very general basic mechanisms)
  Explicit_geometric_constraint_schema
    (includes such things as parallelism, perpendicularity, tangency, etc.)
  Parametric_assembly_constraint_schema
    (specialization of last schema for modelling of assemblies)
  Sketch_constructs_schema
    (includes neutral and positioned sketch representations)

## Slide 10: II. Construction History Modelling (1)
Construction history (CH) modelling is currently being pursued under an SC4 PWI project – but it is also a PDES Inc. project.
Work is being led by Bill Anderson of the Advanced Technology Institute.
Initial intention is to provide a proof-of-concept demonstration of transfer of a simple CH model between commercial systems.
Test model – L-block with hole
  2D sketch
  extrusion to create L-block
  constant-radius fillet
  Boolean subtraction of cylinder to create hole.

## Slide 11: II. Construction History Modelling (2)
Methodology for test:
  Write simple (but extensible) schema for the features involved in the model.
  Use Part 108 for sketch representations, parameterization and geometric constraints.
  Generate ‘Implementors Guide’ to help vendors working on the project.
Vendors currently active in the CH project:
  Alibre, Dassault Systèmes, SDRC, Spatial, Theorem Solutions
  NIST is doing some parallel work with ProE and Solidworks
  KAIST in Korea is also working in this area, using a slightly different approach

## Slide 12: II. Construction History Modelling (3)
Current status of CH project:
  Several versions of the features schema and the history modelling mechanisms have been discussed in a series of CH workshops (Myrtle Beach, Mar 2000; Bordeaux, Jun 2000; Charleston, Oct 2000 – next is scheduled for Myrtle Beach, Mar 2001).
  A simple method for avoiding the ‘persistent naming’ problem has been agreed upon, though we may need to do more work on this later.
  A method for structuring the history file has been agreed, and provision is made for the inclusion of human-understandable ‘design rationale’ information.

## Slide 13: II. Construction History Modelling (4)
Current status of CH project (continued):
  No translator work has been done yet, except at NIST and KAIST.
  At NIST we can cycle a simple parameterized model into and out of ProE, using a Part 21 file based on a simple non-STEP schema.
  KAIST in Korea is working at present on direct translation between native modeller-generated history files (Soon-Hung Han and his PhD student).
When we have evidence that our proposed method works, at least for a simple model, we will submit an NWI proposal to SC4 for the development of one or more new STEP resources for CH modelling.

## Slide 14: II. Construction History Modelling (5)
Priority 1 feature types
  linear sweep of sketch
  rotational sweep of sketch
  Boolean operations
  blends/fillets/chamfers
  rigid body transformation of features
  pattern features
  library features
Priority 2 feature types
  more general sweep operations
  shelling and offsetting
  skinning (lofting) of sets of 2D curve sketches
  tapering/draft angles
  sectioning of solid by a surface
  bending of a solid
All feature definitions will be parameterized and have built-in
constraints

## Slide 15: II. Construction History Modelling (6)
Exchange of history-based model may help to overcome the ‘geometric accuracy problem’ still causing some problems in current STEP exchanges
  Model is regenerated in the receiving system from constructional history, which is less subject to inaccuracy than a current STEP file
It is thought that history-based representations may also provide a stable form of archival storage for CAD models

## Slide 16: Technical Challenges in Construction History Modelling
Interface style (function-based vs. entity-based approach)
Granularity of high-level vs. low-level operations
Persistent naming and indirect references

## Slide 17: Persistent Naming
This is probably the most difficult problem — it is believed that most CAD vendors only have partial solutions
Academic work, e.g. by Hoffmann, Kripac, Pierra et al., Rappoport, Shapiro etc.
The problem for model exchange seems to be slightly easier than it is for internal system regeneration — we intend always have an explicit model (an AP203-type model) to refer to for guidance. This ‘current result’ model will be transferred together with the CH description. It will provide an example of the designer’s intentions.

## Slide 18: Persistent Naming (2)
STEP currently transfers the display model. The basic history model provides no references to its constituents.
History model
Display model
Revised history
model
Revised display
model
Edit
Generate
Regenerate
MASTER
GUI

## Slide 19: Indirect References
A generalization of the persistent naming problem
We need to be able to reference, in a CH file
  elements of parts defined in a parts library
  elements of instanced parts or assemblies
  elements used as datums in part construction but which have possibly been deleted by subsequent modeling operations
The problem is that a CH file contains no explicit elements, so we have to define indirect methods of referring to them.

## Slide 20: III. Enhanced Assembly Modelling (1)
Currently, STEP assembly modelling is of the parts list / bill-of-materials variety: sets of positioned and oriented parts.
For the future, we would like to capture
  logical relationships between parts expressed as assembly feature relations
  different types of contact between parts (continuous, intermittent)
  kinematic degrees of freedom between parts
  parameterized assemblies, with inter-part constraints
This will allow the full modelling of kinematic assemblies with parameterization and constraints

## Slide 21: III. Enhanced Assembly Modelling (2)
Current proposal is based on work by the JNC; WD exists (WG12 527 + some later draft module proposals)
NWI proposal submitted in 2000 was accepted by SC4 and allocated Part # 109. It is likely that the Part 109 resource will contain only the fundamentally new constructs required, and new modules will define specializations of existing constructs.
There have been discussions with AP 214 and 224 teams on harmonization of feature representations, though the use of Part 108 for parameterization and constraints will demand alternatives to the shape_aspect approach

## Slide 22: IV. General Case “Long-term” Parametrics
An additional project in the ISO TC184/SC4/WG12 Parametrics Group, looking ahead towards future developments in CAD systems technology that will lead to standardization requirements.
  Design process representation, for capture of the logical process of design evolution from the concept stage
  Design knowledge representation
Parametrics’ Long-term subcommittee is currently led by Richard Wittenoom of AusSTEP, Australia, who is preparing a Technical Report to SC4.

## Slide 23: Primary Contributors to Parametrics Work
Bill Anderson, Advanced Technology Institute, USA
Noel Christensen, GE Honeywell, USA
Ray Goult, LMR Systems, UK
Tom Kramer, NIST, USA
Akihiko Ohtaka, Nihon Unisys, Japan
Vijay Srinivasan, IBM
Nobuhiro Sugimura, Osaka Prefectural University, Japan
Richard Wittenoom, AusSTEP Consultants, Australia
Past major contributors:
  Guy Pierra, Université de Poitiers, France
  Chia-Hui Shih, Pacific STEP, USA

## Slide 24: Other Collaborators
  Richard Baumann, Fraunhofer IPK, Berlin, Germany
  Abdelaziz Bouras, Université Claude Bernard, Lyon 1, France
  Jean-Marc Brun, Université Aix-Marseille II, France
  Julian Fowler, PDT Solutions, UK
  Soon-Hung Han, KAIST, Korea
  Kazuya Kobayashi, Toyama Prefectural University, Japan
  Philip Kraushar, Boeing Phantom Works, USA
  Greg Paul, Lockheed Martin Energy Systems, USA

## Slide 25: Conclusions
ISO TC184/SC4/WG12 Parametrics Group is extending STEP for the exchange of dynamic models:
  aiming to standardize parametrization and geometric constraints for explicit models in Part 108
  aiming to standardize feature-based history-based model representation in one or more new resources
  assembly representation is being enhanced through a combination of a new resource, extensions to existing resources , and development of new modules
The Long-term Parametrics subcommittee is looking ahead towards future standardization needs.