## Slide 1: The PDM Implementor Forum
Combined ProSTEP /
PDES, Inc. Activity
Goal:
Harmonize PDM implementations based on the STEP PDM Schema
PDM Schema Usage Guide, Recommended Practices
Test campaigns
Status:
High interest of both PDM users and vendors
PDM Schema 1.2 available
PDM Schema Usage Guide 4.2 in March 2001
Four joint test campaigns have been performed in 1999 and 2000
Round 5C is planned for March

## Slide 2: Organizations Most Active in Realizing and Implementing STEP in Product Data Management
LKSoft Opel
PDTec
ProSTEP SAP
Scania
Siemens
Steyr-Daimler-Puch Fahrzeugtechnik
Volvo
VW/Audi
Zahnradfabrik Friedrichshafen
Alenia
Bae
BMW
Bosch
CASA
Contact Software
Continental Teves
DaimlerChrysler
DASA M
debis Systemhaus
Delphi Automotive
Eigner+Partner
ENOVIA/Dassault Systemes/IBM
Boeing
ISS
Lockheed Martin
Metaphase/SDRC
NASA
Northrop Grumman
PDES
PTC
Raytheon
Spatial
Unigraphics Solutions
Notes: The major players in the area of STEP and PDM come from the automotive and aerospace industries with their PDM system partners.

## Slide 3
Harmonized Workgroups at ProSTEP and PDES, Inc.
CAx Implementor Forum
(B. Marler, /W. Kerschbaum, BMW; P. Rosche, PDES/O. Guntermann, ProSTEP)
PDM Implementor Forum
(N.N.;
Dr. M. Leber, ProSTEP/P. Rosche, PDES)
ProSTEP User Round Table, Project Group: “CAD/PDM Integration”
(T. Fischer, BMW;
A. Trautheim, O. Guntermann, ProSTEP)
Technical Advisory
Committee
(J. Harris, Rockwell;
N.N., PDES)
ProSTEP
PDES
Level of
managers/
project leaders
Level of
software
developers/
implementors
PDM-IF Web pages (L. McGeorge, PDES)
PDM Schema/Usage Guide (M. Fischer, ProSTEP/K. Buchanan, PDES)
CAx-IF Test Results/Web pages (L McGeorge, PDES; J. Boy, ProSTEP)

## Slide 4
Members of the Joint PDES/ProSTEP PDM Implementor Forum (Status: Dec., 7th 2000)
Commercial PDM Systems
* PDM STEP file viewer/editor

## Slide 5: PDM Implementor Forum Contacts

## Slide 6: STEP PDM Schema

Common PDM data schema generated and maintained by PDES, Inc., ProSTEP and JSTEP

Real subset of PDM relevant STEP APs (AP203, 212, 214, 232)

Fulfils nearly all requirements for
PDM data exchange
Main functionality for parts and documents: - Identification - Versioning - Structures incl. transformations - Approvals and authorization - Project, work order, work request (not included in AP232) - Effectivities and validity - Classification and properties
AP214
AP203
AP232
AP212
PDM
Schema
Notes: The PDM schema is a joint effort carried out by PDES, Inc. ProSTEP and JSTEP, the largest STEP organizations. The schema and its documentation are not an ISO standard, but represent a real subset of the relevant application protocols of ISO10303 (STEP).
The necessary documentation is provided by PDES, Inc. and ProSTEP. This documentation is available to the public. The main documentation is the “Usage Guide for STEP PDM Schema”.

## Slide 7: PDM Schema v1.2
...available!

## Slide 8: PDM Schema 1.2 – New Functionality 1/3
New Functionality (changes visible both in Shortform and Longform schema)
+ SELECT type action_item
configuration_effectivity added
+ SELECT type action_request_item
property_definition added
+ SELECT type characterized_action_definition added
+ SELECT type date_item
organizational_project, security_classification, contract added
+ SELECT type date_and_time_item
organizational_project, security_classification, contract added
+ SELECT type document_reference_item
action_method, versioned_action_request added
+- SELECT type identification_item
product, product_definition_formation added
application_context removed

## Slide 9: PDM Schema 1.2 – New Functionality 2/3
+ SELECT type organization_item
approval, contract, security_classification added
+ SELECT type organizational_project_item
executed_action added
+ SELECT type person_and_organization_item
security_classification, contract added
+- SELECT type security_classification_item
document removed
document_file added
+ TYPE celsius_teperature_measure added
+ ENTITY founded_item added
+ ENTITY action_property added
+ ENTITY action_property_representation added

## Slide 10: PDM Schema 1.2 – New Functionality 3/3
New Functionality (changes implied by changes documented above, only visible in the Longform schema)
+ SELECT type derived_property_select
action_property added
+ SELECT type founded_item_select
founded_item added
+ SELECT type id_attribute_select
action_method, versioned_action_request added
+ SELECT type measure_value
celsius_temperature_measure added

## Slide 11: PDM Schema 1.2 – Error Correction
Error Correction (changes visible both in Shortform and Longform schema)
- fixed rules in document_file
- fixed WR1 in global rule product_requires_version

## Slide 12: PDM Schema 1.2 – Latest IR 1/3
Use of the Latest Version of the IR (changes visible in Longform, only)
+ ENTITY address
DERIVE attributes name and url added
+ ENTITY coordinated_universal_time_offset
DERIVE attribute actual_minute_offset added
local rules changed
+ ENTITY document
INVERSE attribute name changed from representation_type into representation_types
+ ENTITY document_file
local rules changed
+ ENTITY document_product_equivalence
local rules changed
+ ENTITY product_category
DERIVE attribute id and local rule added
+ ENTITY product_definition_shape
local rule changed

## Slide 13: PDM Schema 1.2 – Latest IR 2/3
+ ENTITY property_definition
DERIVE attribute id and local rule added
+ ENTITY shape_aspect
DERIVE attribute id and local rule added
+ ENTITY shape_aspect_relationship
DERIVE attribute id and local rule added
+ ENTITY time_interval_with_bounds
primary_bound attribute changed into OPTIONAL
+ ENTITY time_interval_with_bounds
attribute derivation changed into duration
+ ENTITY time_interval_with_bounds
additional local rule
+ FUNCTION acyclic_product_category_relationship
type changed from LOGICAL to BOOLEAN
+ FUNCTION acyclic_product_definition_relationship
type changed from LOGICAL to BOOLEAN

## Slide 14: PDM Schema 1.2 – Latest IR 3/3
+ changed FUNCTIONs
base_axis, build_2axes, build_axes, cross_product,
dimension_of, normalise, orthogonal_complement,
scalar_times_vector, using_items, using_representations,
valid_calendar_date, valid_units, vector_difference

## Slide 15
Scope of the STEP PDM Schema and Test Campaigns (Status: December 2000)
Alias Identifi- cation
Contract
and
Project
Work and
Change Management
Part Identification
Part Structure
Part Properties
Document Identification
Document Structure
File Identification
Document/ File Properties
Part Management
Document Management
Person and Organization
Approval
Security Classification
Date and Time
Authorization
performed
Effec-
tivity
Confi-
guration
External
Geom. Model
Transformation
Geometry
Assignment
Part
Classification
ongoing
upcoming

## Slide 16
Implementation of STEP PDM Schema 1.1 (Status: April 2000)
Part Identification
Part Classification
Part Properties
Part Structure and Relationships
Shape Properties
Document Identification
Document Classification
Document Properties
Document Structure and Relationships
External Files
Document and File Association to Product Data
Alias Identification
Authorization
Configuration and Effectivity Information
Engineering Change and Work Management
Functional Sections

= most constructs
Sept. ‘99

Test Campaigns
Dec. ‘99
March ’00
July ‘00





s

s
Nov. ‘00

?


completing
S = initial

? = not decided


## Slide 17: Testing at PDM-IF in 2001
Repetition of tests with new or re-activated participants (PTC, Matrix One, SDRC/Metaphase UG Solutions, etc.)
Further and more sophisticated tests for integrated/ combined data exchange from CAx and PDM
    additional part properties (e.g. material)
    several item structure relationships (e.g. make_from, alternate, substitute)
    approval information
    robust testing of CAX/PDM product/geometry structure

## Slide 18: Assembly Digital Mock-Up Image

## Slide 19: Overview for Test Case “External References”
RA
LBA
LBA
NBA
NBA
NBA
RA = Rod Assembly
LBA = L-Bracket Assembly
NBA = Nut-Bolt Assembly
plate
nut
rod
nut
l-bracket
nut
nut
nut
bolt
bolt
bolt
(see below)
Notes: 1
1
1
1
STEP, and AP214 in particular, is able to handle the different product data structures. The areas that represent part, document and geometric structures are linked.
In practice there is very often no clear distinction between these different structures. In the case of communication between two partners, it is essential that both sides understand and harmonize the semantics of the structures correctly.

## Slide 20: Key Scenarios for the Exchange of Product Geometry and Structures
1. CAD -> CAD
3. PDM/CAD -> PDM/CAD
5. PDM/CAD -> CAD
2. PDM -> PDM
CAD
CAD
- main structure will be lost in CAD system
- geometry relevant structure visible in the CAD system
PDM
CAD
PDM
CAD
PDM
CAD
CAD
PDM
PDM
Geometry file(s)
CAD relevant structures
PDM relevant structures and document meta data
optional including CAD structure
4. CAD -> PDM/CAD
- main structure visible in the PDM system
- geometry relevant sub-structure visible in the CAD system
PDM
CAD
CAD
- interactive input of meta data of „document“ in PDM system
- structures only visible in CAD system (without splitting)
4.a Special case: no „PDM file“
- only a template including meta data for CAD
- usually no structures
5.a Special case: no „CAD file“

## Slide 21: Key Objects of the PDM Schema representing Parts, Geometry, Documents and their Structure Relationships
Document Identification / Structure
External
file
Document rep.
view definition
Document
Document version
External file
relationship
Document version
relationship
Document
representation rel.
Geometry Identification / Structure
Product Identification /
Part
Part
view definition
Part version
select
Document
association
select
Shape to file
relationship
External geometric
model
Geometric
model
Geometric model
version
elements
. . .
Structure
Usage occurrence
Part structure
definition
Part structure
component rel.
Part shape
Portions of
part shape
select
select
Shape
association
select
Geometric model
relationship
Geom. model rel.
with transformation
select
select
Notes: 1
1
1
1
STEP, and AP214 in particular, is able to handle the different product data structures. The areas that represent part, document and geometric structures are linked.
In practice there is very often no clear distinction between these different structures. In the case of communication between two partners, it is essential that both sides understand and harmonize the semantics of the structures correctly.

## Slide 22: PDM / TDM Integration The Conflict between a PDM and a TDM/CAD Data Model
Data Structure of a PDM System (according STEP AP214)
?
TDM / CAD Data Structure
TDM / CAD systems are often unable to distinguish between product, document and geometric model structures
Document Structure
Product Structure
Document Assignment
Notes: The representation of product data structures in different systems is often handled in different ways. Typical product data structures are:
- geometric structures, which are mainly CAD assemblies including the position and/or transformation of geometric elements
- part structures, which are the basis for bill of materials or part lists; there are static and rule-based/configured part structures
- document structures, which are mainly hierarchical structures for parts of a document like chapters
Most PDM systems are able to handle and distinguish between these three types of product structure. “Team Data Management” systems (TDM) are designed to handle data of CAD systems, typically from the same vendor. They handle a single structure, which is usually the geometric structure.

## Slide 23: Product Structure vs. Geometry Structure
Reasons for structuring CAD models :
Model splitting: - size is too large > 5 MB - different modelling methods (e.g. brep, wireframe, csg...)
A (specific) assembly structure
Necessity of specific checks (e.g. model space defined for installation investigation)
Differences between external and internal structure regarding the supplier e.g. starter from Bosch -> Request for documentation (overall model) as opposed to supplier documentation (a number of single models)
Differences between external and internal structure regarding the customer
Additional structuring of CAD partial models (one part, but several models)
Key result: The model structure may only be the same as the product structure in case 2
Source:
Notes: 1
1
1
The results of an internal analysis of the factors influencing the structure of CAD models by SFT illustrate the importance of making a distinction between different types of structures.