## Slide 1: STEP-NC AIM Issues Discussion
David Loffredo
loffredo@steptools.com
Funchal ISO Meeting
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: Overview of STEP-NC AIM Work
Draft based on balloted ISO 14649-10, 11, and 111.
Nine Units of Functionality (UOFs)
  Measures
  Project
  Workpiece
  Features
  Executable
  Operation
  Toolpath
  Milling Process Operations Based on Part 11
  Milling Cutting Tools Based on Part 11-1
Based on Part 10

## Slide 3: Overview of STEP-NC AIM Work
One STEP-NC AIM will cover all technologies
  First edition will cover milling.
  Second edition will extend with turning and EDM.
  Amendments can add others as needed.
Based on Part 10
Measures
Project
Workpiece
Features
Milling Process Operations Based on Part 11
Milling Cutting Tools Based on Part 11-1
Turning Process Operations Based on Part 12
EDM Process Operations Based on Part 13
Executable
Operation
Toolpath
First
Edition
Second
Edition

## Slide 4: Overview of STEP-NC AIM Work
Draft document available.
Major concepts in each UOF mapped.
Mappings checked for consistency against APs
  Extensive checks with AP-214, AP-224 & DIS 213
  Selective checks against AP-209, AP-227, AP- 210
Discuss several mapping issues in Funchal before finishing off the UOFs.

## Slide 5: Measures UOF
Toleranced length measures
  defines upper/lower range
  how to map limits and fits specifier?
What about unit constraints in mapping?
  The ARM assumes certain units to simplify the model.
    lengths in milimeters, angles in degrees
    speed in meters/second
    pressure must be pascals
    rotation in 1/s
  STEP IRs require explicit units in all contexts.
  Restricting to specific ones would break existing AP-203/214/224 models.
  Let AIM have full flexibility with units.

## Slide 6: Project UOF
Project is the “main” deliverable
  Mapped as a product.
  Will be able to track approvals, configuration control, etc. if needed.
  Workpieces are related to project using product definition relationships.
  Similar to the way assemblies are put together with NAUOs.

## Slide 7: Workpiece UOF
Workpiece is also a product.
  More conventional product, with a brep shape description
Material can be handled two ways
  As a product.
    Done by AP-224 and AP-209.
  As a material_designation.
    Done by AP-214 and AP-213.

## Slide 8: Material Mapping (AP-224/209)
material_designation
“material name”
product_definition
with_associated
documents
(the material)
make_from_usage_option
“material”
material_property
property_definition_representation
representation
document
“specification
name”
product_definition
(the workpiece)

## Slide 9: Material Mapping (AP-214/213)
material_designation
“material name”
applied_document_reference
material_property
property_definition_representation
representation
document
“specification
name”
product_definition
(the workpiece)
material_designation_characterization

## Slide 10: Features UOF
Harmonize features with AP-214, AP-224
  Existing features with extra things, like planar face with boss and boundary curve.
New generic region features
  Swept curve, Geom. bounded surfaces, or Open shell
  Mapped as a shape aspect
  Create subtype region_feature, like transition & replicate?
  Look at general removal volume in 224 (shell only?)
  Should it be complex instance with feature_definition?

## Slide 11: Executable UOF
Sequential workplans easy to map.
  Use sequential_method to order them.
Control flow and the expressions are new.
Map expressions using PLIB Part 20
  AP-214 did this to describe units with an arbitrary expression
  They created expression_conversion_based_unit
  STEP-NC AIM must describe the control flow with an expression property.
  We will create expression_representation_item

## Slide 12: Expressions in AP-214 Units
generic_variable
expression_conversion_based_unit
environment
context_dependant_unit
variable_semantics
associated
defining
expression
named_unit_variable
named_unit
derived_unit_variable
derived_unit
The L-Value
R-Values

## Slide 13: Using Expressions as Properties
expression_representation_item
generic_expression
May also need the AP-214
unit variable defs so that
variables have proper units.
Also need to review suggestions
from P. Huau and check new Part 108
parameter definition
control flow workingstep
(if/then, while, etc)
usual property to
representation relationship
“controlling expression”
representation_item
P108 defines parameter
against generic_variable

## Slide 14: Operation UOF
Use action_method mappings discussed at previous meetings.
  Relationship between machining operation & toolpath uses a unnecessary toolpath_list object in the middle.
  Map directly from operation to toolpath, but how to document that we are ignoring this extra type?

## Slide 15: Action Method Subtyping
action_method
action_method_relationship
sequential_method
other relation subtypes
machining_process_executable
machining _operation
machining _workplan
machining _workingstep
machining _strategy
machining _technology
machining _machine_function
machining _toolpath
subtypes for categories of
milling operations
plane milling, side milling,
drilling, boring, reaming, etc.

## Slide 16: Milling Process Operations UOF
Straightforward mapping.
  Just defining new property parameters within the established action_method framework.
  May group the parameters.

## Slide 17: Mapping Approach for Properties
Major Concepts
  Mapped to product, action_method, action_resource.
Relationship between major concepts
  Mapped to ***_relationship named link.
Property with complex description
  Only a property of a major concept, no other relationships
  Mapped to a representation with multiple rep items.
major concept
major concept
relationship
property
representation
property
representation
property
representation

## Slide 18: Property Representation
action_property
“cutspeed”
machining_technology
measure_
representation_item
value: 0.1123
unit: m/s
action_property_representation
representation
action_property
“spindle”
measure_
representation_item
value: 23.4
unit: rev/s
action_property_representation
representation
First draft used separate properties for each parameter.

## Slide 19: Property with complex representation
measure_
representation_item
name: “diameter”
value: 0.1123
unit: m/s
measure_
representation_item
name: “tool_top_angle”
value: 23.4
unit: rev/s
rep item for other
parameter
rep item for other
parameters
Representation with multiple parameters, distinguished by rep item name.
AP-224 & AP-213 use this approach for implicit feature
description.
resource_property
“tool dimension”
machining_tool_body
resource_property_representation
representation

## Slide 20: Toolpath UOF
Use action_method mappings discussed at previous meetings.
  No outstanding issues.

## Slide 21: Milling Cutting Tools UOF
Mapped as action resource subtype.
  Properties give all of the parameters.
Tool cutting point needs a material.
  Cutting point mapped as compound rep item.
  Can this be related to either mapping of material?
  Not directly, but perhaps complex instance with characterized object?

## Slide 22: Remaining Tasks
Update draft with issue resolutions.
Submit NWI/CD with updated draft.
  Target mid-March, early-April.
Draft and copy of this presentation available
  http://www.steptools.com/projects/stepnc_aim