## Slide 1: Propositions for future update of ISO 14649 based on DIS ballot version
February 20, 2001
Suk-Hwan Suh
National Research Lab for STEP-NC Technology (NRL-SNT)
School of Mechanical & Industrial Engineering
POSTECH, KOREA (http://stepnc.postech.ac.kr)
Notes: Hello every one.
My name is Suk-Hwan Suh of NRL-SNT or National Research Lab for STEP-NC Technology in POSTECH, KOREA
As you know, the ISO 14649 is the new data model between CAM and CNC, which is available as a DIS version.
The purpose of this presentation is not to advocate our findings, but to bring rather open issues for the future update of the current version.

## Slide 2: Contents
1. Incorporation of nonlinear process plan
2. Incorporation of other manufacturing processes for Part 10
3. Details for 3D freeform machining
4. Inclusion of tool monitoring
5. Details for adaptive control
6. For intelligent control
7. Establishment step
8. Harmonization of future Part 1x1 and ISO 13399
Notes: The propositions can be summarized by 8 items as shown below:
1. Incorporation of nonlinear process plan
2. Incorporation of other manufacturing processes for Part 10
3. Etc…

## Slide 3: 3 Types of STEP-compliant CNC
Conventional
control
CAD kernel
Post
processing
New
control
New
intelligent
control
Intelligent
functions
ISO14649 Interpreter/Referencing
CAPP kernel
CAM kernel
CAD DB
STEP IR
AP203
AP224
CAPP DB
STEP IR
AP213
CAM DB
Tool path
ISO14649 - Milling
Geometry
Technology
Tool
Main
program
EIU
G-code
interpreter
feedback
ISO 13399
Part 2
Part 3
Workplan
Type 1 : Conventional control
  “ISO 14649 to G-code” post processing
Type 2 : New control
  Interpreting ISO 14649 code and tool path
  Faithfully performs as specified in ISO 14649
Type 3 : New intelligent control
  Autonomously performs various intelligent functions based on ISO 14649
  Autonomous tool path generation and modification
  Automatic tool selection
  Automatic cutting condition selection
  Automatic tool approach and retract path generation
  Automatic machining feature detection
  Status monitoring and automatic recovery
  Machining status and result feedback
Notes: Before getting into the details, let me address that the purpose of ISO 14649 is to establish a new data model so that the new CNC or STEP-Compliant CNC can be developed for the intelligent control. I will use STEP-CNC for STEP-compliant CNC to distinguish from the data model of STEP-NC.
The new data model can be implemented in 3 types as shown here:
Postprocessing-based where the conventional controller can used via postprocessing, This is not the desired one.
The second type is Interpreter-based, where the ISO 14649 interpreter is installed in the CNC. The prototype STEP-CNC developed by EU and USA can be fall into this category.
The 3rd and promising type is A New Intelligent Control, capable of various intelligent functions listed here:
1)
2)

## Slide 4: 1-1. Nonlinear Process Plan (NLP)
Nonlinear Process Plan
  To represent alternatives for the machining sequence of the manufacturing feature
  To introduce flexibility in the process plan
  Choice is made by the CNC giving flexibility for the CNC
   Key to the autonomous and intelligent STEP-NC control
Relationship of Execution in the Nonlinear Process Plan
  7 types : sequential, conditional choice, iterative, concurrent, unordered serial, selective, parallel
    Sequential : execution by a sequence
    Conditional Choice : binary choice according to the given condition
    Iterative : repetitive execution
    Concurrent : all executables are started at the same time
    Unordered Serial : all executables have to be executed but the order of execution does not matter
    Selective : execute only one among several executables
    Parallel : all executables don’t need to be started at the same time
Notes: Keeping in mind that let me get into the first item; On the nonlinear process plan (NLP); which is
- To represent …
- To introduce …
Note that the choice is made by the CNC giving flexibility for the STEP-CNC, which is key for the intelligent CNC control
To represent NLP, we found that 7 entities are ncessary:
- Sequential (“linear” or “serial” process plan mostly assumed in the current version)
- Conditional Choice, …

## Slide 5: 1-2. Limitations of current schema for NLP
Current Data Model
  Current data model can represent only 4 types of relationship
    Sequential execution  “workplan” entity
    Conditional choice execution  “if_statement” entity
    Iterative execution  “while_statement” entity
    Concurrent execution  “parallel” entity
Restriction of Current Data Model
  In case of “if_statement”, all branch conditions are to be set one by one in advance, which would be a bothersome and hard work
  In case of “parallel”, it only represents the relationship of all branches are started at the same time
  Cannot represent the relationship of “parallel (cf. concurrent)”, “unordered serial”, “selective”
Notes: In the current Part 10, only 4 are included:
- Sequential by “workplan” entity
- Conditional Choice execution by “if_statement” entity
- Iterative execution by “while_statement” entity
- Concurrent execution by “parallel” entity
In other words, 3 entities; “concurent,” “unordered serial,” and “selective” are not included
Even if the current entities may be used for other purposes; for instance,
- In case of “if_statement”, all branche conditions should be set by the programmer in advance, which is bothersome and hard work
- I case of “parallel,” it only represents the relationship of all branches are started at the same time, which is not realistic

## Slide 6: 1-3. Inefficiency example with the current schema
Example
  3 executables (1, 2, 3) are machined in an “unordered serial” fashion
#1=MACHINING_WORKINGSTEP (…);
#2=MACHINING_WORKINGSTEP (…);
#3=MACHINING_WORKINGSTEP (…);
#10=WORKPLAN (…, (#1,#2,#3), …);
#11=WORKPLAN (…, (#1,#3,#2), …);
#12=WORKPLAN (…, (#2,#1,#3), …);
#13=WORKPLAN (…, (#2,#3,#1), …);
#14=WORKPLAN (…, (#3,#1,#2), …);
#15=WORKPLAN (…, (#3,#2,#1), …);
#100=IF_STATEMENT(condition, #10,#101);
#101=IF_STATEMENT(condition, #11,#102);
#102=IF_STATEMENT(condition, #12,#103);
#103=IF_STATEMENT(condition, #13,#104);
#104=IF_STATEMENT(condition, #14,#15);
100
10
101
11
102
12
103
13
104
14
15
T
T
T
T
T
F
F
F
F
F
#10 = NONSEQUENTIAL (#5,#6,#7);
By Proposed Schema
Notes: For instance, consider work plan problems for 3 executables, whose execution is not really matter.
With the current schema, you have to specify the workplan by “if_statement” for 6 cases as shown here.
If a certain condition is met, execute 10. Otherwise if another condition is met, then execute 11, etc.
This is the programming contents for the example.
It will be very difficult to specify all the conditions for the branch at the time of programming.
You need (n! – 1) “if_statement”s
In other words, the number of lines will be increased as the number of executables increases.
If “non_sequential” statement is used only one statement is necessary shown here

## Slide 7: 1-4. Proposed schema incorporating NLP plan
(ABS) Executable
(ABS) Workingstep
1
(ABS) NC_function
(ABS) Program_structure
Workplan
Parallel
If_statement
While_statement
Assignment
1
……
……
Selective
Nonsequential
Executable
BOOL
branches S[2:?]
concurrent
Proposition (EXPRESS-G)
Notes: This is a proposed schema to accommodate NLP plan.
The yellow ones are new entities to be included, and
The green one is new attribute for the “concurrent”

## Slide 8: 1-5. Proposed entities incorporating NLP
ENTITY nonsequential
SUBTYPE OF (program_structure) ;
its_executables : SET [1:?] OF executbale ;
END_ENTITY ;
ENTITY selective
SUBTYPE OF (program_structure) ;
its_executables : SET [1:?] OF executbale ;
END_ENTITY ;
ENTITY parallel
SUBTYPE OF (program_structure) ;
branches : SET [1:?] OF executbale ;
concurrent : BOOLEAN ;
END_ENTITY ;
Proposition (EXPRESS)
Notes: And these are the proposed entities in Express format including “non_sequential,” “selective,” “parallel,” where concurrence is specified by “boolean” attribute.

## Slide 9: 1-6. Example with proposed NLP schema
#10 = WORKPLAN (…, (#1,11), …);
#11 = NONSEQUENTIAL (#12,#3,#4);
#12 = SELECTIVE (#13,#14);
#13 = WORKPLAN (…, (#8,#2,#7), …);
#14 = WORKPLAN (…, (#2,#15), …);
#15 = NONSEQUENTIAL (#5,#6,#7);
SA, JA : “unordered serial”
SO, JO : “selective”
1
SA
SO
8
2
2
7
SA
5
6
7
3
4
JA
JO
JA
Start
End
Example
Notes: Using the proposed schema, NLP plan represented by “AND-OR” graph can be efficiently represented.
In this example, after working step 1, working step 3, 4, and this group of working steps are executed, in unordered fashion.
This group can be done by either 8-2-7 in sequential or 2 & this unordered group 5-6-7.
If the new schema is used, this NLP plan can be compactly represented by 6 statements.
I don’t think you can program this by using the current scheme

## Slide 10: 2-1. Part 10 : General Process Data Current schema (1)
  Part 10 has to specify the process data which generally is needed for NC-programming within all machining technologies
  But the current schema does not take into consideration the other machining technologies except the milling data model
  Schema of Part 10 should have the capability of covering the manufacturing features and operations used in turning and EDM technology
Notes: The next item is about Part 10, the General Process Data Model.
As you know Part 10 is supposed to …
But, …
In other words, Schema of Part 10 should be updated to cover ,,,.

## Slide 11: 2-2. Part 10 : Current schema (2)
(ABS) Manufacturing_feature
(ABS) Region
(ABS)Two5D_manufacturing_feature
(ABS) Transition_feature
1
(ABS)Machining_feature
(ABS)Replicate_feature
Planar_face
Step
(ABS) Pocket
Slot
Round_hole
Compound_feature
General_outside_profile
Generic_feature
1
1
Notes: Specifically, this is the current schema, where “Machining_feature” (including mostly for milling operation) is subtype of “Two5DMmanufacturing_feature,”
With this scheme, we cannot find appropriate place to put the features for other manufacturing processes, such as turning feature.
For instance, turning features, such as cylinder, cone, groove, cannot be be place under Two_5D_manufacturing_feature.

## Slide 12: 2-3. Proposed schema for Part 10
(ABS) Manufacturing_feature
(ABS) Region
(ABS)Machining_feature
(ABS) Transition_feature
1
(ABS) General_feature
Compound_feature
1
1
EDM_feature
(ABS) Revolved_feature
(ABS)Multi_axis_feature
region
Two5D_manufacturing_feature
knurl
Revolution_feature
Groove
thread
Turn_edgeround
Turn_chamfer
……
Notes: What we propose is that is to change the location of machining feature as subtype of manufacturing feature, and Two5D_manufacturing_feature as a subtype of Multi_axis feature as shown here.
In this way, turning feature is in the same level as the milling feature (renamed as Multi_axis_feature),
And EDM feature in the same fashion.
Of course, the turning feature shown here can be changed later in as Part 12 is established.

## Slide 13: 3-1. Current schema for freeform machining
Current schema for 3D freeform machining
  It is oriented to 2.5D machining
  Some supplements for 3D freeform machining are needed considering the complexity and difficulty of 3D freeform machining
Current Schema
(ABS) Freeform_operation
(ABS) Region
Region_projection
Region_surface_list
Topological_region
1
  Feature
  Operation
  Strategy
(ABS) Freeform_strategy
Uv_strategy
Plance_cc_strategy
Plane_cl_strategy
1
Leading_line_strategy
Cutmode_type
Pathmode_type
pathmode
cutmode
Notes: Next item is related with representation of free form machining.
The current schema for free form machining is oriented 2.5D machining, and
Details for 3D free form machining are not sufficiently included as summarized here:
- For operation: “Freeform_operation” without subtypes
- For feature: Region including 3 subtypes
- For strategy: Freeform_strategy with 6 subtypes

## Slide 14: 3-2. Limitations with the current schema
Operation type should be included as subtype of “freeform_operation”
  freeform_rough_milling
  freeform_finish_milling
  freeform_pencil_cutting
Current machining strategy cannot generate the APT-type tool-path and helical tool-path
“region” entity cannot cover the digitized data like a CMM data
Notes: We found that:
- Subtype of freeform operation should be given, for instance; freeform_rough_milling, freeform_finish_milling, freeform_pencil_cutting
- In regard to machining strategy, the current one does not include some crucial strategy; for instance, “APT-like tool path,” and “helical tool path.” as shown here.
- Also we found that the current Region entity does not cover the digitized data like a CMM data as a surface model

## Slide 15: 3-3. Proposed schema for freeform machining
(ABS) Freeform_operation
Freeform_rough_milling
Freeform_finish_milling
Freeform_pencil_cutting
1
(ABS) Region
Region_projection
Region_surface_list
Topological_region
1
Digitized_region
(ABS) Freeform_strategy
Uv_strategy
Plance_cc_strategy
Plane_cl_strategy
1
Leading_line_strategy
Helical_strategy
Cutmode_type
Pathmode_type
pathmode
cutmode
APT_like_strategy
Operation
Feature
Strategy
Notes: Based on the discussion so far, what we propose is the following schema where yellow marked new entities are inlcluded.

## Slide 16: 4-1. Current schema related with tool monitoring
Tool Monitoring
  Important for protection and efficient use of manufacturing resource (cutting tools)
  To be autonomous and intelligent, at least, the controller should have capability of monitoring the tool breakage
   Data model for monitoring of tool breakage and tool wear necessary
Current Schema
  Tool life, “expected_tool_life”, is reflected in “cutting_component” entity as an attribute
(ABS) Machining_tool
(ABS) Cutting_tool
Time_measure
(ABS) Cutting_component
its_cutting_edge L[0:?]
1
……
expected_tool_life
……
Notes: The next item is about toom monitoring.
As you know, tool monitoring is important for …
And to be autonomous and intelligent, at least, …
In other words, data model for monitoring of tool …
In the current schema, only Tool life, “expected_tool_life,” is reflected in …

## Slide 17: 4-2. Attributes for tool monitoring schema
Attributes based on the target of monitoring and sensors to be used
  Target of Monitoring : dimensional error, tool wear, tool breakage, safe spindle motor operation
  Sensor used : dimensional and proximity sensor, cutting force sensor, feed force sensor, spindle motor sensor, acoustic emission sensor
Incorporation on the current schema
  Defining Monitoring entity as subtype of “nc_function” (which describes operation without involving interpolation of axes)
  Attributes based on the target and sensors
Notes: Attributes for tool monitoring should be based on the target of monitoring and sensors to be used.
And the entity tool monitoring can be included as a subtype of “nc_function” which …
And the attributes as mentioned before.

## Slide 18: 4-3. Proposed schema for tool monitoring
ENTITY monitoring
SUBTYPE OF (nc_function) ;
END_ENTITY ;
TYPE monitoring_sensor_type = ENUMERATION OF (
dimensional_sensor, cutting_force_sensor, feed_force_sensor, spindle_motor_sensor, acoustic_emission_sensor) ;
END_TYPE ;
TYPE monitoring_target_type = ENUMERATION OF (
dimensional_check, tool_wear, tool_breakage) ;
END_TYPE ;
ENTITY tool_monitoring
SUBTYPE OF (monitoring) ;
its_sensor : monitoring_sensor_type ;
its_target : monitoring_target_type ;
END_ENTITY ;
(ABS) NC_function
(ABS) Monitoring
Tool_monitoring
Monitoring_sensor_type
Monitoring_target_type
its_target
its_sensor
EXPRESS
EXPRESS-G
Notes: This is the proposed scheme for tool monitoring in EXPRESS and EXPRESS-G form

## Slide 19: 5-1. Current schema for adaptive control
Importance
  Machining intricate details on parts often calls for slender cutters of low rigidity, and the cutting forces in contouring can easily exceed the limit of the cutter
  In order to increase productivity, proper feed rate should be assigned according to the NC tool path
Current Schema
  “adaptive_control” entity is defined
  But the description is rather short and the entity has no attributes at all
(ABS) Technology
feedrate
its_adaptive_control
Adaptive_control
Speed_measure
……
Notes: Next item is concerned with adaptive control.
As you know, AC is important for optimal machining and preventing excessive wear or breakage of the cutting tool.
And it is desired to include the data model for AC in ISO 14649.
Currently, AC entity is defined as a subtype of Technology without detailed attributes

## Slide 20: 5-2. Attributes for adaptive control schema
Attributes
  Adaptive control is closely related with the monitoring using a sensor
  Attributes to be added
    How to control the feed rate
    Using a certain type of a sensor
    By monitoring what
Sensors used in Gathering Signal for Adaptive Control
  Cutting force sensor
    Input : cutting force signal
    Mechanism : control feed rate by algorithm
  Spindle motor sensor
    Input : current, voltage and rotation speed of spindle drive motor
    Mechanism : control feed rate by letting the cutting torque be below the preset maximum cutting torque
Notes: Like tool monitoring, attributes of AC are composed of target and sensors to be used as shown here

## Slide 21: 5-3. Proposed schema for adaptive control
EXPRESS
ENTITY adaptive_control
its_sensor : monitoring_sensor_type ;
max_torque : OPTIONAL REAL ;
max_cutting_force : OPTIONAL REAL ;
its_control_algorithm : OPTIONAL adaptive_control_algorithm ;
END_ENTITY ;
FUNCTION adaptive_control_algorithm
……
END_FUNCTION ;
Notes: This is proposed schema for adaptive control, where sensors to be used, torque range, cutting force range, and control algorithm are included as attributes

## Slide 22: 6. For Intelligent Control
Workpiece Clamping Information
  Has only the attribute of a clamping position currently
  Geometry information of jig and fixture is required to avoid the collision of a cutting tool and jig and fixture
Automatic Setup of Workpiece
OMM (On-Machine Measurement)
Etc.
“New schemas specifying the intelligent functions are required”
Notes: We also found that some data models are necessary for intelligent STEP-CNC. 3 items are listed here.
First, workpiece clamping information should be given in detail.
Currently, only attribute of clamping position is given,
but for collision avoidnace, geometry information of jig and fixture is required.
Likewise, data model for Automatic setup of workpiece, and On-machine-measurement will be necessary

## Slide 23: 7. Inclusion of establishment step (less important)
General step for defining an Application Protocol of STEP
  Define AAM using IDEF0 diagram
  Constructing AO, AIC using UoF
  Define ARM using AO, AA
  Define AIM by mapping to STEP integrated resources
Inclusion of derivation procedure for ARM may be necessary
UoF, AO, AIC, AA are missing
Notes: Remaining items are relatively of less importance.
Like document for STEP-AP, we suggest inclusion of the derivation procedure of ARM data model may be useful for verification

## Slide 24: 8-1. Harmonization of Part 1x1 and ISO 13399
ISO 14649-111 and a portion of ISO 14649-10 on the cutting tool
  Overall structure of the tool description is the same as ISO/CD 13399
  Many definitions of tool body and geometry are referenced from the NIST tool model
ISO 13399 : Cutting Tool Data Representation and Exchange
  From the viewpoint of maker
  Currently, only data model for turning cutting tools are defined
  Has more attributes than ISO 14649
  Many attributes are useless for machining
Cutting Tool Data Representation in ISO 14649
  From the viewpoint of consumer
  Currently, only data model for milling cutting tools are defined
  Has less attributes than ISO 13399
  Sufficient information for machining
Notes: The final item is concerned with harmonization of Part 1*1 and ISO 13399.
As you know, ISO 13399 specifies tool data model currently mainly for small tools, such as turning tools and boring bites. This model is given in detail from the view point of tool maker.
In Part 111 of ISO 14649, the milling tool is modeled rather simply from the view point of consumer.

## Slide 25: 8-2. Harmonization of Part 1x1 and ISO 13399
Proposition
  2 approaches : one is just to reference ISO 13399 and the other is to simplify ISO 13399 and use it
  The latter seems to be reasonable for Part 121, 131, etc. to be established later
ENTITY tool_body
ABSTRACT SUPERTYPE OF (ONEOF (boring_tool, turning_tool));
manufacturer : OPTIONAL name ;
manufacturer_catalog_identifier : OPTIONAL designation ;
user_identifier : OPTIONAL designation ;
distributor : OPTIONAL name ;
… (some attributes are abbreviated)
tool_body_normal_rake : angle ;
tool_body_side_rake : angle;
tool_body_back_rake : angle ;
cutting_edge_angle : angle ;
lead_angle : angle ;
… (some attributes are abbreviated)
END_ENTITY ;
ENTITY turning_tool_body
SUBTYPE OF (tool_body) ;
tool_body_normal_rake : angle ;
tool_body_side_rake : angle;
tool_body_back_rake : angle ;
cutting_edge_angle : angle ;
lead_angle : angle
END_ENTITY ;
Notes: When defining tool model for turning, EDM, (which will be Part 121, and Part 131, respectively), we propose a simple model as taken in Part 111 as shown here.
Thank you for your attention. Again, what I presented is not to advocate our findings, but to bring issues for open discussion. I hope our propositions can be reflected in the future update of ISO 14649 in some manner.
Any questions, or comments, etc….???