## Slide 1: STEP-NC is Reality!
AMT
The Wire-EDM Technology
ARM ISO 14649 Part 13

## Slide 2: Resources
AMT
Agie SA Switzerland
Charmilles SA Switzerland
EPFL Lausanne
CADCamation Geneva
Wyss SA Geneva
Presentation by AMT Switzerland

## Slide 3: Introduction Wire-EDM
AMT
The EDM data model development has to be harmonised with ISO 14649. Part 11 of this standard describes the process data for milling. The EDM process data model is intended to be an independent new part of ISO 14649 standard. All similar or usable functionality and information can be taken from ISO 14649 Part 10 and 11. This way it is ensured that the new model remain consistent with the existing milling model. Since wire-EDM technology is considerably different form milling, therefore I will discuss some general aspects of this technology before the feature and technology definition. In milling operation the final tool path can be determined by the 1. Feature geometry 2. Machining tool geometry 3. Machining strategy
These information are basically machine independent for milling. In wire-EDM only the Feature geometry is machine independent all the two other information is machine and technology dependent.

## Slide 4: Introduction Wire-EDM
AMT
CAD
CAM
Geometry of the
workpiece
EXPERT
System
Toolpath of the final
piece workpiece
CNC
Final offset toolpath &
technology
Quality targets,
material, wire, etc.
.
.
The wire-EDM technology is a developing technology unlike to the milling, where the basic principles are already solidified. Especially this is true for the machining strategies of specific features e.g. sharp corners. Every machine builder has proprietary strategies for these specific features, which can not be standardised. The current CAD-CAM-CNC chain therefore always includes an expert system (which can be replaced by the expertise of the operator), which defines the final CNC code see in Figure.

## Slide 5: Basic Principle of Wire-EDM
AMT
The wire-EDM use defined tools similarly to the milling, therefore the geometric feature definition is possible. However the geometric dimension of the tool (this is the diameter of the wire) differs from the logical dimension of the tool. The logical dimension of the tool is defined by a diameter of the "range of action" (see on Figure 1). This logical dimension is depend on the technology is chosen, which is finally machine dependent.

## Slide 6: More Information on Technology
AMT
Since the logical diameter of the tool is technology- and machine- dependent, the offset paths of the final workpiece therefore can only be determined if the selected technology and machine is known. Furthermore there is no "analytical approach" to determine the logical radius, therefore it is determined based on experiments.
There are many factors that determine the offset calculation This has to be taken into consideration for the working step. There is basically three main type of working step:
Roughing, Finishing, Surface finishing
The number of working steps and the type of working steps required for one final geometry differs from machine to machine. The same workpiece might require 1 roughing 2 finishing and 3 type of surface finishing on one machine and 1 roughing 3 finishing 4 type of surface finishing working step on another machine. Also the definition of these working steps differs from machine to machine. This imply that it is rather difficult to define global working steps like in milling, because the definition of the technology of these working steps vary considerable.
In milling operation the final tool path can be determined by the
Feature geometry, Machining tool geometry, Machining strategy
These information are basically machine independent for milling. In wire-EDM only the Feature geometry is machine independent all the two other information is machine and technology dependent.

## Slide 7: Machine Independency
AMT
Expert system
Quality targets
Material
Wire
Workpiece
Machining- features
Working steps
Machine functions
Technology
STEP-NC file
One important goal of the STEP-NC project is to define a manufacturing data model, which can be used machine independently. This target is very difficult to accomplish in wire-EDM technology because the numerous reasons, discussed in the previous chapter.
Expert system Quality targets, Material, Wire, Workpiece, Machining features
Working steps Machine functions,Technology etc.

## Slide 8: Data Model and Expert System
AMT
STEP-NC file Since the expert systems are essential parts of the CAD-CAM-CNC chain in today’s practice we have to develop a data model, which supports this feature. The proposed solution is a data model that is capable to store information necessary for the input of the expert system and also the output of the expert system. This way the input information to the expert system are machine independent while the output are not.
With this approach Interchange ability is assured.

## Slide 9: Machining Features in Wire-EDM
AMT
We will define two types of geometrical object to describe the wire-EDM machining features. The base features and the high level features. The high level features are referencing the base features (replicate feature).
With the machining feature definition we try to be compatible a much a possible with ISO 14649 and ISO 10303-224.
Base features:
General profile
General path
General profile pocket
General path pocket
High level features:
Replicate feature

## Slide 10: Feature General Profile
AMT
This feature can be used to manufacture the workpiece on a 2- axis wire-EDM machine. This feature is similar to the ISO 14649 general outside features. That feature determines the workpiece by the parameterisation of the feature boundary. When travelling along the feature boundary curve as defined by its sense, the material is to the left of the curve.
Since in the wire-EDM operation there is always material on both side of the wire, therefore with the feature boundary parameterisation one can specify which side of the curve has the workpiece and which side of can the offset tool path curves defined.
ENTITY general_outside_profile
SUBTYPE OF (machining_feature);
feature_boundary: bounded_curve;
END_ENTITY;
Feature_boundary: The contour of the profile to be followed by the tool. Note that this attribute describes the profile itself, not the tool path. When travelling along the curve based as defined by its sense, the final workpiece lies to the left of the curve.

## Slide 11: Feature General Path
AMT
upper curve
ruled surfaces
lower curve
This feature can be used to describe the workpiece to manufacture on a 4-axis wire-EDM machine. Generally the 4-axis wire-EDM manufacturing can result a workpiece with boundary surface described by a ruled surface. There are no corresponding feature defined neither in ISO 14649 nor ISO 10303-224 standards. The General_removal_volume feature defined in ISO 10303-224 standard includes the general path feature, but this feature is a kind of "catch all" feature, therefore it is defined rather generally. The General_removal_volume feature is geometrically defined as Brep_model, which can described any kind of geometry.
We can foresee three different ways to define the general path feature:
Definition by two synchronised bounded curves that are the upper and lower boundary curves of the feature.
Definition by a list of bounded curves together with a direction vector function. The transition type between the segments can be the following types: Constant radius, Conical, Sharp Definition by the ruled surface.

## Slide 12: Feature Ruled Surface
AMT
This definition is the "catch all" mode, which can be used always if the previous two definition are not sufficient for some reasons. Usually ruled surface is not stored as geometrical object in CAD system. The ruled surfaces stored as Brep_model. The ruled surface is used as type of construction method on CAD system, but the resulted surface is stored as a general Brep_model. Taking into account the constraint of the CAD systems, this definition type should also use a Brep_model, which correspond to the General_removal_volume feature of ISO 10303-224.

## Slide 13: General Profile Pocket
AMT
This feature describes is used to remove material within a profile curve. This feature can be used for two axis wire-EDM manufacturing. If the feature has some hole within the boundary curve, they don't have to be cut. This peculiarity is similarly to the boss of pocketing in milling operation. One can define also open and closed pockets in EDM. The feature boundary of pockets and the holes inside the pocket, should be defined with General Profile feature.
Closed pockets
Feature_boundary: General outside profile (closed)
Its_holes: list of General outside profile (closed)
Open pockets
Feature_boundary: General outside profile (open)
Wall_boundary: Optional General outside profile (open)
Its_holes: list of General outside profile (closed)
If Wall_boundary is not presented the start and end point of the feature boundary curve is closed with a line.

## Slide 14: General Path Pocket
AMT
This feature is similar to General Profile pocket but this can be used in 4-axis wire-EDM manufacturing. The feature boundaries and the internal hole boundaries are defined using the General Path feature.
Closed pockets Feature_boundary: General outside path (closed) Its_holes: list of General outside path (closed)
Open pockets Feature_boundary: General outside path (open) Wall_boundary: Optional General outside path (open) Its_holes: list of General outside path (closed) If Wall_boundary is not presented the start and end point of the feature boundary path is closed with a line.
Replicate Feature The replicate feature is defined in exactly the same manner as the one in milling. The only difference is the base features, which are the bas wire-EDM features in this case.
Replicate_base_feature: The feature which forms the basis of the replicate feature. This can be General Profile, General Path, General Profile Pocket or General Path Pocket.

## Slide 15: Machining Operations Principles
AMT
Beside the machining features of milling, the EDM machining operations have to be revised considerable in order to fit the wire-EDM technology. The machining operation entity describes the technology and machine related function of this type of manufacturing. Based on expert group discussions the design of the overall functional model of machining operation entity, was done as shown in the following Figure.
Some general remark concerning this structure: Machining operation entity is strongly machine dependent. The machine type, however is not stored in the database, because this information can be stored together with the whole STEP-NC file.
It has to be further discussed, which parameters are optional and which are required. The general rule is that the required parameters should describe some features that is available for every wire-EDM machine.
This entity can be used also to provide input for an expert system and also store the output of it. It has to be evaluated which parameters can be output parameters of an expert system, because they must be optional parameters.
Machining Operation entity will be inherited from the general Operation entity of ISO 14649. Therefore there will be the possibility to define the tool path directly, if no machining feature is available. Also the whole object hierarchy of Executables entity will be reused.

## Slide 16: Machining Operations Diagram
AMT

## Slide 17: End
The End
Thank you for your attention
AMT