## Slide 1: STEP-NC is Reality!
AMT
The Turning Model
Overview and Information

## Slide 2: Resources Turning Model
AMT
ISO TC184/SC1/WG7
European STEP-NC IMS Project
ISW Stuttgart
Daimler Chrysler
Presentation by Amt Switzerland

## Slide 3: Context of Turning Model within ISO 14649
AMT
Due to the different machining technology there are significant differences between the requirements for turning and the already existing data model for drilling and milling. The major reasons for this are a result of the different description requirements for the two parts (milling/drilling and turning) and machining technology types. In contrast to the drilling and milling processes, machining features for turning parts are not defined before.

## Slide 4: Dependencies between feature, operation, and Workingstep
AMT
Manufacturing_feature
Machining_workingstep
Machining_operation
Each data model consists of three parts : the geometric model (feature), the process model (operation), and the execution sequence (workingstep). Feature and operation together yield the workingstep, or more exactly : The attributes of a workingstep are a (optional) feature and an operation

## Slide 5: Turning Features
AMT
The entity turning_feature is the abstract base class for all manufacturing features used for turning. Currently, the following features are defined: end_face, cylinder, shoulder, cone, thread, and groove. (Maybe generic feature and compound feature in future.) Turning is characterised by the fact that tool movements occur only in the xz plane (in the machine co-ordinate system)

## Slide 6: Turning Features, Face and Shoulder
AMT
radius1
radius2
Z
X
End Face
Shoulder
The end face is used to describe machining of a plane surface on the end wall of a workpiece (bar). The position of the feature is given through the feature placement of the major class two5D_manufacturing_feature. To reach this position material has to be removed.
A shoulder is a kind of plan face in radial direction (see Figure 6). In contrast to an end face a shoulder plane is not down to the center. Shoulders are used if the radial plane has special requirements on the quality of the surface. For example when turning a groove at both sides of the groove results a plane. If its surface has to be finished, a shoulder feature must be inserted.

## Slide 7: Turning Features, Cut in + Thread
AMT
Cut in with bottom transition.
Thread with groove at its left side
A cut in is a kind of slot or groove. Depending on the used turning tool it is possible to create a cut in only by moving the x axis. In this case the shape of the cut in is identical to the tool. If the cut in is wider than the tool the z axis has to be moved too. The shape of the cut in is not any longer identical to the shape of the tool. To describe the bottom of the feature especially the transition between the vertical and the horizontal parts a property bottom_condition is introduced.
A thread is a type of machining feature that is a ridge of uniform section on the form of a helix on the rotational surface.

## Slide 8: Turning Features Cylinder + Cone
AMT
A cylinder is used for turning a cylindrical surface along the z axis. It is characterised by its radius and width. The radius is along the width constant.
A cone describes a continual transition from one radius to another radius across a certain width. As shown in Figure 10 radius1 and radius2 is given. So it is possible to obtain cones which become narrow or wide seen from the left side. Further it is possible to set one of the both radii to zero to get a point. This option is dependent on the clamping position, because the point has to be in the opposite of the chuck.
Cylinder
Cone

## Slide 9: Turning Features Slope at Bottom
AMT
Slope at the bottom
This entity describes the linear transition from the vertical to the horizontal part at the bottom of a turning feature (especially groove). The shape of the slope is determined by its offset in the horizontal and its angle against the bottom of the feature.

## Slide 10: Turning Features Rounds
AMT
Round. Left picture concave, right picture convex.
This entity describes the curved transition from the vertical to the horizontal part at the bottom of a turning feature (especially groove). The shape of the curve is determined by two offsets and its radius.

## Slide 11: Turning Features Bottom Conditions
AMT
radius
center
Z
X
center
radius
Z
X
Radiuses bottom condition
Planar bottom condition with a slope at the left side
The entity cut_in_bottom_planar describes the plane bottom of a feature. Both bounds can have different transitions as shown in Figure 13. At the left side there is a slope and the right side has a sharp corner.
The entity cut_in_bottom_radiuses allows to define a spherical shape of the cut in bottom. As shown in Figure 14 the surface can be concave or convex. The parameter which describe the appearance of the surface are the radius and the centre. If the curve is concave or convex depends on the centre.

## Slide 12: Other Turning Features
AMT
General Contour A general contour is used if the contour can not be described with the other features. The movement of the tool tip is given through an explicit path. Generic feature As discussed in Part 10 of this specification a generic feature is used to enable the definition of tool movements not covered by the previously listed features. Toolpathes have to be assigned explicitly to the operations associated with this feature.This feature can be used as an expedient if none of the turning features is suitable to describe the respective contour of a workpiece or a part of this.
Compound feature The compound feature is described in Part 10 of this standard. This is a feature composed from two or more features. As opposed to the replicate feature, there is no regular spacing between the elements of the compound feature. In general, they will also not be of the same type. Further information can be found in Part 10. TYPE thread_rotary_direction This type allows the definition of the rotary orientation of a thread. For example a screw can be screwed in clockwise or counter-clockwise. In the first case the screw has a right-handed thread, in the second case it has a left-handed one.

## Slide 13: Mapping ISO 14649 P12 – AP224
AMT
features in ISO 14649 Part 12
features in ISO 10303 AP224
cylinder
outer_diameter
cone
outer_diameter
general_contour
general_revolution
end_face
outer_diameter
shoulder
outer_diameter_to_shoulder
thread
thread
cut in
groove

## Slide 14: Turning Strategies Overcut + Linear
AMT
Z
X
overcut
tool
overcut_length : The overcut on the open side(s) of the feature. It is not allowed for manufacturing of features which an optional flag only for roughing workingsteps. If true, this is the standard roughing operation with multiple passes, i. e. several layers of material are removed sequentially, taking into account the maximum cutting depth. If false, this is the special roughing operation for pre-cast features with one pass. Default is true. re bounded by material on all sides, i. e. grooves.
Turning in a linear fashion, i.e. going from one side to the other, then lifting the tool and going back to the starting point. The starting point has always to be outside of the contour, i. e. in the right picture of Figure above. As also shown in the figure the solid lines mean removal of material and the dashed lines are rapid movements.
Unidirectional turning (axial and radial).

## Slide 15: Turning Strategies Bi-directional
AMT
Bi-directional turning (axial and radial).
Turning in a zigzag fashion shown in Figure . Bi-directional turning means that cutting is started from one side (i.e. the left side). On reaching the other side the cutting tool moves downwards and then back to the first side, while also removing material. Note that special tools are needed for bi-directional turning. These tools must be able to cut their way in the second direction. For example a tool, used for grooving, which blade is along the front side is not able to cut sideways.

## Slide 16: Turning Strategies End Face + Groove
AMT
End face turning
(radial and axial tool movement).
Z
X
Z
X
Grooving in radial and axial direction
End face turning This entity describes the turning of a planar face at the end of a shaft (bar). It is the super type for roughing and finishing operations for turning an end face. End face turning can be done axial or radial. An end face can also be yield by cutting off the end of the workpiece, Grooving in This is a strategy for cutting into the material. This operation is used for grooving at a certain position without moving sideways. In this case the shape of the groove is dependent on the used tool. The groove is at most as wide as the tool. Figure 23 shows the grooving in radial and axial direction.

## Slide 17: Plunging Strategies
AMT
Retract plane
Z
X
Plunge in the direction of the tool axis.
Plunge with ramp.
Retract plane
Z
X
angle
Retract plane
Z
X
This is the base class for all approach movements which include cutting of material. This is typically the case for grooving operations where the approach to the depth of the first cutting layer or between cutting layers requires the removal of material in order to create the approach path.
All plunge movements are guaranteed to occur within the boundaries of the underlying feature. All plunge movements will start at the retract plane valid for the current operation. They will end in the start point of the cutting operation, with the tangent of its approach path coinciding with the tangent of the ensuing cutting motion.

## Slide 18: Approach and Retract
AMT
Z
X
angle
Approach and retract movement with angle
Z
X
Approach or retract movement with tangential transition
This is the base class for all approach or retract movements through the air.
Unlike the plunge_strategy types these movements are not limited to the inside of the feature. All of these movements shall take place in a plane which is defined by the normal of the machined feature and the tangent of the cutting path in the start or end point, respectively, of the related cutting movement. If the start or end point lies at the intersection of two planes, as may be the case for turning a step operations, the surface normal is deemed to be the intermediate direction between the two normals.

## Slide 19: Name Angle Form ISO code Circle - R Triangle 60° T Square 90° S Rectangle 90° L Pentagon 108° Hexagon 120° H Special_hexagon 80° W Octagon 135° O Rhombus 35°, 55°, 75°, 80°, 86° V, D, E, C, M Rhomboid 55°, 82°, 86° K, B, A
AMT
Base forms of indexable inserts

## Slide 20: Turning Tools
AMT
Entity to describe a turning tool as such. It is a subtype of the entity machining_tool (not cutting_tool) defined in Part 10 of this standard. A turning tool consists of the tool holder and the index able insert. The optional its_technology attribute connects the tool with a machining technology.
Its_indexable;_ Index able insert: This attribute allows to define the properties of the indexable insert of the turning tool. The index able insert is one part of the turning tool. It is the really tool tip which removes material from the workpiece. The main characteristics of an indexable insert are defined in ISO 1832. Based upon this standard the entity indexable_insert was created.
Its_tool_holder : Tool Holder; This attribute describes the tool holder part of the turning tool.
Its_technology : Technology: With the attribute its_technology it is possible to assign machining technologies, e.g. rotation speed of the spindle or feed rate. Note that normally the used technology for a workingstep will be given through its respective operation (attribute its_technology defined in the entity machining_operation). If the technology in turning_tool is not omitted it will override the one from the operation.

## Slide 21: Turning Tools
AMT
feed
indexable
insert
workpiece
feed
indexable
insert
workpiece
right
left
workpiece
indexable
insert
feed
neutral
Cutting side of the indexable insert
t
t
t
t
Thickness of an indexable insert
The cutting side Defines the side – viewed in the direction of feed – of the indexable insert which is able to remove material from the workpiece (see Figure 2). Using a left oriented indexable insert for removing material at its right side causes damage of the insert. Indexable inserts which are characterised as neutral can be used on both, left and right side.
This attribute Describes the thickness (t) of the indexable insert (see Figure 1). The thickness is explicitly given in millimetre and not through symbols of ISO 1832.

## Slide 22: Cutting Edges and Cutting Geometry
AMT
Cutting Geometry of an Indexable insert with plane corner.
Possible shapes of the cutting edge.
This type describes the shape of the cutting edge of the indexable insert. As shown in Figure 5 the edge can be sharp, rounded, or chamfered. A special case is a combination of a chamfered and rounded cutting edge.

## Slide 23: Insert Position in Tool holders
AMT
clamping from top
clamping through hole
clamping from top and through hole
screwed through counter bore hole
Fixings for the indexable insert.

## Slide 24: End
The End
Thank you for your attention
AMT