## Slide 1: STEP-NC is Reality!
AMT
The SINK EDM Technology
State of the Art and
Conclusions for STEP-NC

## Slide 2: Resources
AMT
Agie SA Switzerland
Charmilles SA Switzerland
Mitsubishi Japan
Wyss SA Switzerland
CADCAMation Switzerland
Presentation by AMT Switzerland

## Slide 3: Introduction Sink EDM
AMT
The EDM die sinking process is generally a simple operation in which an electrode is sunk down into a workpiece, and nearly automatically driven by the CNC. However there are some applications in which the process is much more complex, for example when using a simple electrode for doing contouring or pocketing, or when using multiple electrodes.
The benefits expected from a new STEP-NC data interface is a standardization of proprietary cycles and a portability of complex programs.

## Slide 4: Programming methods
AMT
There are mainly three programming methods for the die-sinking EDM machining:
1. Z-sinking: A simple or a complex electrode is sunk down along the Z-axis. When available orbiting and planetary cycles are highly used.
2. Programming with machine specific cycles: The final geometry of the cavity will depend on the movement and of the shape of the electrode.
3. Moving an electrode (simple shape, cylindrical, rotating tubular)

## Slide 5: The Principle
AMT
Workpiece
Side Gap
Frontal Gap
Electrode
Dielectric liquid
Principle of EDM die-sinking

## Slide 6: The Manufacturing Process
AMT
This figure shows the manufacturing process for EDM die sinking. The several sequential steps are: designing the final workpiece on a CAD system, designing the electrode(s), programming the machining of the electrode(s) with a CAM system, manufacturing of the electrode(s) by conventional milling, turning or wire EDM, programming the die sinking on the CNC and at last processing the die sinking.

## Slide 7: Type of applications using EDM die-sinking
AMT
Source: Charmilles Technologies
The EDM die-sinking technology is mainly used in industries and workshops making moulds for plastic injection. It is also used to produce very small accurate parts for the industry of watches or micro-machines

## Slide 8: Z-sinking with multiple electrodes
AMT

## Slide 9: No connection between CAM system and CNC for conventional die-sinking
AMT
CAM system
CNC
The users of the Z-sinking method do generally not use a CAM system. Most of the CNC of the EDM die-sinking machine have proprietary programming functions to easily drive the sinking process.

## Slide 10: Orbiting or planetary based machining
AMT
Polishing
Sharp edges can be achieved using the star mode.
Application of the EQUIMODE
Machining of recesses
Orbiting or planetary based machining is highly rational: It assists the flushing, permits better distribution of the wear and yields savings in electrode manufacture

## Slide 11: Principle of planetary based machining
AMT
During orbiting or planetary based erosion the electrode moves relative to the workpiece about its main axis, according to the selected strategy until the programmed nominal dimension is attained. When planning the electrode it must be taken into account that the shape produced by the movement differs from that of the electrodes.

## Slide 12: Machine specific cycles
AMT
Most EDM machines have specific cycles for machining various shapes with simple electrodes. These cycles are programmed to produce a vector, helical, conical, square or other movement of the electrode.

## Slide 13: Principle of EDM milling
AMT
On three or four axis EDM machines an electrode can be used for contouring. A cylindrical and rotating electrode is moved along the contour of the workpiece. It will produce vertical ruled surfaces and works like a EDM wire process with no taper. The trajectory of the electrode is driven by a specific tool path, similar to milling, The wear of the cylindrical electrode must be compensated in the computed trajectory.

## Slide 14: Principles of EDM contouring
AMT

## Slide 15: Principle of EDM Scanning
AMT
The principle is to drive a tubular rotating electrode which bottom removes horizontal slices of material (10~100m for roughing, 1~10m for finishing) by a pocketing method until the desired shape is formed (figure 9).
This process eliminates the problem of electrode wear which has to be considered in conventional Die-sinking. EDM milling uses high-wear machining conditions, which speeds production and maintains the tool's sharp edge, while the Z-axis feed automatically advances the electrode to compensate the wear

## Slide 16: Assignment of different Electrodes Toolpathes and Technologies
AMT
Workpiece
Electrode1
Electrode2
Electrode3
..
Toolpath1
Toolpath2
Toolpath3
Technology1
Technology2
Technology3
The workpiece geometry has to be considered as one feature and leave to the specific implementation (CAM systems), how to design the electrode and the corresponding tool paths.

## Slide 17: Process planning: Differences between Die sinking and EDM Milling
AMT
CAD design of Workpiece
CAD design of Electrode
Programming of electrode machining
Electrodes manufacturing
Die sinking
Programming of Die sinking
CAD design of Workpiece
Programming of
EDM Milling
Die sinking
Die Sinking
EDM Milling
The EDM Milling has the potential to simplify the process planning by eliminating several traditional steps of the Die sinking (electrode design and fabrication). The figure 10 shows the differences between Die sinking and EDM milling process chain.
To obtain the same final shape the erosion time is longer for EDM milling than for Die sinking. But for complex cavities the whole process would be shorter, more automated and would be a more economical solution.

## Slide 18: Requirements toward STEP-NC interface
AMT
STEP-NC interface
Complexity of the electrode
Process type
Complex electrode
Primitive shape electrode
Z-sinking (with orbiting)
Simple
electrode
Pocketing, contouring
Special cycles
Electrode shape
Planning and Programming problems
CAD/CAM STEP-NC CNC
Sectioning of a complex electrode into several simple electrodes
Computation of electrode trajectory and definition of workingsteps
% of use
CNC programming to obtain the final cavity shape
Complexity of programming

## Slide 19: Conclusion Sink EDM
AMT
EDM sinking machines are mainly used to produce moulds and dies for the plastic and composite injection industry. They are also used for the fabrication of metallic parts for micro-machines. Different processes are used for these applications: mainly Z-sinking, but also machine dependant cycles. On multi-axis machines contouring trajectories and pocketing of cavities can be programmed. Some specific machines have been developed for EDM milling, an emerging technology that allows the machining of very hard materiel.
The main requirements of EDM die-sinking process concern the standardization of the data and the portability of the programs on different machines and CNC. For STEP-NC at a later time!

## Slide 20: End
The End
Thank you for your attention
AMT