## Slide 1: Make Anywhere using STEP-NC
Martin Hardwick, President
hardwick@steptools.com
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: STEP-NC
Direct control of machine tools from 3D data
  STEP-NC under development in Europe and Far East for 4 years
  Milling, Turning, Wire EDM, CMM others anticipated
Benefits
  35% reduction in CAM planning time
  75% reduction in time to send data from CAD to CAM
  50% reduction in machining time for small to mid sized job lots
  Elimination of post processors
  Safer, more adaptable machine tools
http://www.steptools.com/library/stepnc
CAD
CAM
CNC
35% faster
75%
faster
50%
faster
STEP
(AP-203)
STEP-NC
(AP-238)
Same geometry
e-Design
e-Manufacturing

## Slide 3: Current NC programming using ISO 6983
%
N05 G54
N10 G00 Z10.000
N15 G91 G0 Z200
N20 T5 D1 WW
N30 G90 M5
N35 G00 X0.000 Y-150.000
N40 G00 Z5.000
N45 M08
N50 S3183.000
N55 M03
N60 F1477.000
N65 G00 X60.000 Y-150.000
N70 G00 Z5.000
N75 G00 X60.000 Y-150.000
N80 G01 Z-0.500
...
machine-specific part program with axis data generated by a postprocessor
vendor-specific extensions of the original standard
only primitive motion and switch commands
no standardized data format for spline processing and sophisticated NC technology
Courtesy WZL RWTH Aachen
STEP-NC replaces this with a
rich, integrated data format
Ideal for Paper Tape!
The standard for 50 years!

## Slide 4: STEP-NC is integrated
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 5: What is STEP
An International Standard for technical data about products including
  Geometry and topology
  Assembly and configuration information
  Manufacturing attributes
Move to STEP initiated by CAD users in 1984
  More interoperability in design and manufacturing
  Reduce costs for supply chain
Two hundred product data specialists meeting three times per year.
  Experts from Europe, Far East and USA
  Most of the worlds major engineering companies represented
  $180M investment by aerospace, shipbuilding and automotive industries
More then one million CAD stations use STEP
  All major CAD systems have STEP interfaces
  Grown in IBM supply chain from 0% in 1998 to 17% in 1999 to 30% in 2000
STEP-NC extends STEP for CAM and CNC control

## Slide 6: PDM Benefit
A 3D model is sent to the supplier instead
of paper drawings
Estimated by Raytheon
CAD
CAM
CNC
35% faster
75%
faster
50%
faster
STEP
(AP-203)
STEP-NC
(AP-238)
Same geometry
e-Design
e-Manufacturing
For each 1 file made by design 100 are made by manufacturing – Ford Motor

## Slide 7: PDM Benefit Assumptions
AS-IS Process
  Make drawings for each stage of manufacturing from 3D models
  Annotate drawings with product specifications as text
  Send drawings to manufacturing
TO-BE Process
  Send STEP-NC data containing AS-IS and TO-BE model for each manufacturing stage
Accelerants
  No need to make so many drawings
  Manufacturing gets an electronic product specification
Risks/Unknowns
  How to define manufacturing tolerances?
    By translating design tolerances?

## Slide 8: CAM Benefit
The supplier creates the CAM plan from a
3D product model instead of paper drawings
Estimated by Lockheed Martin
CAD
CAM
CNC
35% faster
75%
faster
50%
faster
STEP
(AP-203)
STEP-NC
(AP-238)
Same geometry
e-Design
e-Manufacturing
Of 13M engineering hours on Boeing 777 project an estimated 8M spent on data correction and administration

## Slide 9: CAM Benefit assumptions
AS-IS process
  CAM user receives drawing
  CAM user converts drawing into CAM model
  CAM user generates RS274D from CAM model
TO-BE process
  CAM user receives 3D model with product specifications
  Feature recognition used to initialize CAM model
  CAM user generates AP-238 from CAM model
Accelerants
  Feature recognition
  Features sent to CNC instead of M and G codes
Risks/Unknowns
  Reliability of feature recognition

## Slide 10: CNC Benefit
The machine computes optimum speeds and
feeds from full fidelity geometry information
Estimated by Cincinnati Machine
By value, 75% of manufacturing
is for lots of 50 or less – Manufacturing Roadmap
CAD
CAM
CNC
35% faster
75%
faster
50%
faster
STEP
(AP-203)
STEP-NC
(AP-238)
Same geometry
e-Design
e-Manufacturing

## Slide 11: CNC Benefit assumptions
AS-IS process
  Machine executes RS274D codes
TO-BE process
  Machine gets complete manufacturing specification
    Geometry, tolerances, tool requirements, fixtures, material
  Machine computes optimal speeds and feeds
    Algorithms + tool database + geometry/tolerances
Accelerants
  5 axis machining becomes easier to use so it is used more often for small and medium lot manufacturing
Risks/Unknowns
  How long until the new algorithms are available in the controller?

## Slide 12: AS-IS Process
CAD
CAM Macro Planning
CAM Micro Planning
CAD
CAM Macro Planning
CAM Micro Planning
IGES
NC Controller
RS274D
NC Controller
RS274D
E.g MASTERCAM or GIBBSCAM
E.g Unigraphics or Pro/E
Post Processor
Post Processor
Integrated CAD/CAM for OEM’s
IGES Data Exchange for supply chain
Must be coordinated by user
Must be coordinated by user
Macro planning is stock definition, feature selection, process ordering and tool requirements.
Micro planning is tool path generation with tools that meet the requirements

## Slide 13: TO-BE Process
CAD
CAM Macro Planning
CAD
CAM Macro Planning
AP-203
NC Controller
e.g. FB Mach
E.g Unigraphics or Pro/E
Integrated CAD/CAM for OEM’s
Supply chain
CAM Micro Planning
AP-238
NC Controller
CAM Micro Planning
AP-238
Post Processor is invisible to the user.
Micro planning (tool path generation) is automatic using MASTERCAM or GIBBSCAM embedded into the NC Controller.

## Slide 14: Pilot Project Framework
Super Model Server
Milling Machine
at local or remote supplier
Any CAD
PC Controller
STEP-NC
Adapter
Software chosen
by enterprise
Software supplied
by STEP Tools
Custom code for a specific Shop Floor Programming (SFP) system
Shop Floor
Programming
Conversion from
STEP-NC to
controller codes
without manual
input
MasterCAM
GibbsCAM
EZ-MILL etc.
FBMach
AP-203
XML
AP-238
CAD
CAM

## Slide 15: Super Model Project
  GE Fanuc
  CNC Data (MASTERCAM)
  CADKEY
  Alibre
  Boeing
  General Electric
  General Motors
  Gibbs and Associates
  Hurco Companies Inc.
  Lockheed Martin
  IBM
  Monarch Machine Tools
  NASA (GSFC)
  NASA (JPL)
  NCMS
  Northrop Grumman
  Unigraphics Solutions
  NIST Intelligent Systems
  Caterpillar
  Lawrence Livermore Laboratories
  Chrysler
  Watervliet Arsenal (Benet)
  General Dynamics Land Systems
  Cincinnati Machine
  The Design Edge
  RMC Associates
  Fala Technologies
  Cambridge Valley Machining
  Honeywell
  Electro Mechanical Integrators
  Liberty Consulting
  RPI
Industrial Review Board