## Slide 1: STEP-NC Proposed Methods for Implementation Testing
Fred Proctor
Control Systems
Group Leader
NIST
Simon Frechette
Manufacturing Standards
Metrology Group Leader
NIST

## Slide 2: Types of Testing
Conformance Testing
Interoperability Testing
RESULTS
System A
System A
System B
System B
Test Spec
Test Spec
Test Spec
RESULTS
RESULTS
Conformance Test
Conformance Test
Notes: 1
1
1
1
1
OPEN STANDARDS Are NEEDED to ENABLE EC
Business to business communications of Industrial Data
Replacing drawings/supporting info with electronic forms
  Reduce scrap/rework parts by ~25% (3-5% of cost)
  Shorten time for engineering changes (30 - 45 days)
  Reduced time to market - New product Autos - 5 yrs < 24 mos
  Reduced # engineering changes, Higher quality
Why different
- Reuse - enhance a proven design
- coordination among functions within company
- coordination among suppliers
37% of value of car is out sourced and growing
Because systems can’t communicate there are big losses in productivity
Boeing -- a 500 Million a year problem
Single worldwide agreements on the content and format
information created once -- used again and again for downstream functions

## Slide 3: Testing Scope and Organization
Structured according to conformance class
  based on usage scenarios
Further structured in some logical way
  functionality groupings
  minimum/basic tests
  typical/critical tests
  extremes/limits tests

## Slide 4: Testing Nomenclature
Test Assertion (TA)
  A testable assertion which is extracted from a standard specification. Form can be schema data structure (ent-attr) or rule.
  Also called Semantic Requirement or Test Requirement
  Example: “Non-positive radius is an error condition”
Test Purpose (TP)
  Discrete, finite set of explicit testing objectives. Specific - from specific domain knowledge; Derived - from the AP
  A reformulation of Test Assertion(s) as a testing directive
  Example: “Verify that radius is positive” would be a Test Purpose for validating file instances, and “Verify that interpreter treats non-positive radius as an error condition” would be a Test Purpose for interpreter or viewer testing

## Slide 5: Testing Nomenclature
Test Case (TC)
  an component of the Test Suite that implements one or more Test Purposes, and hence verifies one or more Test Assertions
  Example: A test file which contains a hole with a negative radius
  In practice (and abstractly), the relationship of TAs to TCs is many-to-many
Traceability
  The ability, in a Test Suite, to trace a Test Case back to the applicable rest requirement(s) in the standard specification

## Slide 6: Testing Nomenclature
Verdict Criteria: expected outcomes from Test Purposes
  basis for determining if test purpose is satisfied
  specific - corresponding to specific test purposes
  derived - from AP
Coverage: what’s included, what’s left out
  coverage requirements should be based on experience/discretion/industry priority
Test Suite: organized set of Test Cases

## Slide 7
AP203 Conformance Test Case
Test Case: AB_Revolved_Object_With_Void
Test Summary:
Test the processing of information elements as defined in the UoF advanced_boundary_representation. Specifically, the postprocessor input contains instances of adv_brep_shape_rep, brep_with_voids and elements used in their consruction (CC6).
Input Specification:
(Model design, application elements and values)
Verdict Criteria:
General verdict criteria apply: gvc1, gvc2, and gvc3
VC1:The model realized in the IUT must generally correspond in shape to the model represented
VC2::This model can be created by revolving a composite curve 360 degrees about an axis. The length of the axis is 0.49 m.
VC3 :This model contains a void. The volume of this model, excluding the void, is 0.4330 cu.m.

## Slide 8: Syntax, Structure, Semantics
Syntax conformance is essentially a grammar check of the exchange file
  #<name>=(<data>, <data>, … );
Structure conformance checks that the schema is properly implemented
  are the entities and relationships in the model those permitted in the AP schema - elements, attributes, rules, functions, procedures, and constraints?
Semantics conformance determines if the information realizes the test case specification

## Slide 9: STEP NC Conformance Testing
STEP NC covers the data interface between CAM systems and CNC machine tools
  CAM systems generally output (add to) STEP NC data
  CNC systems generally input (use) STEP NC data
  at this point, “data transfer” is usually accomplished using a physical file with a specific format (part 21, XML CEB, etc.); data sharing scenarios (i.e., a common database) may be utilized in future
Input and output activities need to be tested separately

## Slide 10: The Overall Process
STEP NC
CAM
CNC
Art
CAD
Part

## Slide 11: CAM Conformance
Geometry
Material Specs
Tooling
STEP NC
Is the STEP NC output correct for the given data and specifications?
Validation is difficult - cannot simply provide reference data sets for comparison, since there is no unique output for a given input, e.g., independent feature ordering (at least) is arbitrary
CAM System

## Slide 12: CAM Conformance
Conformance of a STEP NC implementation to STEP file format, and STEP NC schemas is relatively straightforward with software (e.g., STEP Tools)
Verification that a STEP NC implementation produces a valid process plan for the given design is more difficult
  solid model NC verification of STEP NC implementation output against the part design is a possible solution, some sort of rule-based tool is another possible solution
  this compares the resulting solid model properties with the design model properties, e.g., dimensions, mass properties, etc.
  first action may be to translate STEP NC  ISO 6983 (G code) and then use some existing NC verification software, such as, Virtual Gibbs - better would be native STEP NC verification tool (reference implementation)

## Slide 13: CAM Conformance Test
NC verification
Solid model comparison
CAM
CAD
STEP NC
G codes
Solid
Model
CAD
Originating data
Test Case
STEP NC Checker
Procedures that describe what is being done, what the results should be, how to interpretet the results, how to report the results, and other natural-language instructions to help the testers through the process
Comparison procedures

## Slide 14: CAM Test Case Data
Geometry from CAD
  AP 203, AP 214
Manufacturing data
  Tolerances (annotations in CAD? drawings?)
  Stock description (geometry, material: format?)
  Setup and tooling information
    is tooling determined beforehand?
    can new tools be added?
Outputs:
  STEP NC data

## Slide 15: CAM Testing Procedures
1. Interactive CAM is accomplished and STEP NC control data produced
2. STEP NC data (file) is checked for syntax, structure, and rule-based checking (e.g., center drill before twist drill)
3. NC verification software is used to produce solid model
  translation from STEP NC to ISO 6983 (G codes) is done first, if necessary
  solid model NC verification is run and solid model is created
4. Target features in NC-derived solid model are compared with those in the original or reference CAD solid model
  easy: mass properties
  harder: 3-D fitting (however, software is available to do this)

## Slide 16: Testing Caveats
What’s not tested:
  process selection (e.g., drilling v. boring v. reaming)
  optimal process parameters (e.g., feed, speed, connect moves)
What’s inadvertently tested:
  operator capability

## Slide 17: CNC Conformance Testing
STEP NC
Is the part machined correctly for the given input?
Standard artifact can be provided; CAD files and drawings may suffice
Additionally, a suite of STEP NC files can be provided that test exceptions that should be caught by the CNC
  ISO 10303/21 syntax errors
  STEP NC data structure errors

## Slide 18: CNC Conformance
CNC
Part
Part inspection
Validated STEP NC test data
Results
Test
Case
Part measurement comparison
Expected results
Procedures that describe what is being done, what the results should be, how to interpretet the results, how to report the results, and other natural-language instructions to help the testers through the process
Procedures that describe what is being done, what the results should be, how to interpretet the results, how to report the results, and other natural-language instructions to help the testers through the process

## Slide 19: CNC Test Case Data
Validated STEP-NC files
  some with explicit tool paths, some without
  some with strict tool requirements, some with general
  the suite should exercise generative NC, smart tool selection, and other expected STEP-NC benefits
Expected results of part measurement
  feature location, tolerances
  surface quality
Outputs:
  Machined part

## Slide 20: CNC Testing Procedures
1. Preliminary checks
  can the controller process the file (data), etc.?
2. CNC machining is accomplished
3. Part inspection follows with comparison of results to test requirements (CAD design or prints)
  are the features machined as intended?
  are the geometry and surface finish within the specified tolerances? Other metrics? (time, ancillary processes?)
4. Additionally, proper exception handling can be tested with suite of files with known errors

## Slide 21: Testing Caveats
What’s not tested:
  optimizations (e.g., cutter paths, tool selection)
  optimal process parameters (e.g., feed, speed, connect moves)
What’s inadvertently tested:
  tool setup
  part fixturing
  CNC accuracy
  machine operator tending

## Slide 22: Issues
ISO 14649 defines 6 conformance classes
  should we have 6 suites of tests?
  industry priority?