## Slide 1: SC4 Preliminary Work Item Proposal
AP224 - extension for gear manufacturing data
Tony Fry - UK MoD
ISO TC184 / SC4 Meeting
10th - 15th June 2001 - San Francisco

## Slide 2: AP224 - Extension for Gear Manufacturing Data
Economic case for inclusion of gears
Suggested scope
Gear representation overview
Other potential AP224 enhancements

## Slide 3: Economic Case for Inclusion of Gears
Review of UK naval spares inventory
  Identification of gears and geared components
  Breakdown into gear types
    Analysis of numbers of spares
    Analysis of value of spares
  Justification of suggested scope

## Slide 4: Review of UK Naval Spares Inventory
Identification of gears & geared items
  Review scoped over entire naval inventory
    Technical data in ISIS
    Commercial data in CRISP
  Supply classifications indicated good starting point
    NSC 3010 - “torque converters & speed changers”

## Slide 5: Review of UK Naval Spares Inventory
Identification of gears & geared items
  Focused on single piece parts
    Assemblies not considered
    Hence, numbers and values are conservative
  Wide range of sizes
    Food mixer to main drive transmission

## Slide 6: Review of UK Naval Spares Inventory
Total number of units in store around
6,000
Total value of stored units around
£4,000,000

## Slide 7: Review of UK Naval Spares Inventory
Breakdown of gear types
  Spur gears / gearshafts
  Helical gears / gearshafts
  Bevel gears / gearshafts
  Worm gears / gearshafts
  Gear quadrants
  Racks & pinions

## Slide 8: Stores Held vs Type

## Slide 9: Stores Held vs Type
Notes: Pie chart showing the same as the previous slide by proportion.

## Slide 10: Stored Unit Costs vs Type

## Slide 11: Stored Unit Costs vs Type
Notes: Pie chart showing the same as the previous slide by proportion.

## Slide 12: Review of UK Naval Spares Inventory
Ranking of types according to Naval requirements
  Spur gears
  Helical gears
  Bevel gears
  Worm gears
  Racks / pinions
  Gear quadrants (various forms)

## Slide 13: Suggested Scope
Based upon analysis & technical ease of representation within AP224
  Spur gears / gearshafts
    > 50% store cost
  Helical gears / gearshafts
    20% store cost
  Others represent < 10% store cost each

## Slide 14: Suggested Scope
Tooth Form
Involute
  Most common form
    Fully defined by reference to rack
    Cutters can be cheaply produced
    Easy to obtain correct intermeshing
    Tolerant of centre distance variations

## Slide 15
Notes: ANIMATED SLIDE!
Shows formation of involute profile.

## Slide 16
Gear Types
Spur and helical gears
  Broadest application domain
    Parallel shafting gear trains
    Wide range of velocity ratios
    High speed and load capacities
Consideration in representation to be given to future extension to include other gear types

## Slide 17: Overview of representation of spur & helical gears
Specification of basic geometry
  Number of teeth z
  Normal module mn
  Reference pressure angle α
  Rack shift factor x
  Nominal tooth depth h/mn
  Face width b
  Tip diameter da
Not dissimilar to (but more complex than) data required to specify screw threads, knurls

## Slide 18: Reference cylinder, etc.
Reference cylinder = reference surface of a cylindrical gear
Reference diameter = diameter of the reference circle
Reference surface = imaginary conventional surface relative to which the dimensions of the teeth of a gear are defined
Notes: Reference slide… normally hidden.

## Slide 19: Normal module
Normal module = quotient of the pitch at the reference surface,
expressed in millimetres, divided by 
Normal module = reference diameter/number of teeth = d/z
OR
Notes: Reference slide… normally hidden.

## Slide 20: Reference pressure angle
As gears rotate, the point of contact moves along a straight line (contact line). This line at angle  (pressure angle) is always normal to the two mating tooth surfaces at the point of contact and is tangential to the base circles
Notes: Reference slide… normally hidden.
As gears rotate, the point of contact moves along a straight line (contact line). This line at angle alpha (pressure angle) is always normal to the 2 mating tooth surfaces at the point of contact and is tangential to the base circles

## Slide 21: Tooth depth
Tooth depth = radial distance between the tip and root circles
Nominal tooth depth = h/mn
ha
hf
root circle
tip circle
Notes: Reference slide… normally hidden.

## Slide 22
Representation of basic geometric information for gears - ARM EXPRESS-G

## Slide 23: Other considerations
Inspection requirements
Surface treatment
Accuracy / tolerance
Meshing information?
Profile & / or helix modifications
*Form of explicit geometry*

## Slide 24: Other Potential AP224 ed3 Enhancements
References to standard parts
  Include bought-out items in assemblies?
Harmonisation with AP223
  Cast base shape datum harmonisation?
Composite materials
  Facilitate the use of composite base shape?