## Slide 1: Introduction to STEP-NC
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
In-Process Features

## Slide 2: The Problem
The removal volume for a workingstep may not be the same as a feature on the final workpiece.
  An open slot on the final part may be machined as a closed one, then a later profile may open it up.
  The feature on the final part does not have the correct extent or slot end type for the actual milling operation.
First Cut
Second Cut

## Slide 3: Another Example
Consider a series of steps on a part
  The final part features just describe the final step dimensions.
  Workingsteps could machine the deep first or the shallow first.
  Choice changes the dimensions of the features that we want to machine
WS
#1
WS
#2
WS
#3
WS #1
WS #2
WS #3

## Slide 4: The Approach
Define “in-process” features to represent the features needed by the manufacturing process
  Final part features describe the end-result of manufacturing.
    They never change unless the part geometry changes
  In-process features describe the part as it exists during the manufacturing process.
    You may delete and replace them if the process plan changes
A workingstep can refer to two features.
  Always refers to the final part feature, relates the workingstep to the end product of the workplan.
  May also refer to an in-process feature. If present, it is used to determine what the workingstep should remove.

## Slide 5: Example
Not all workingsteps will require in-process features.
In-Process Feature
(closed slot)
Final Part Feature
(open slot)
Final Part
Feature
(step)
Workstep #1
Bottom & Side Mill
Workstep #2
Bottom & Side Mill

## Slide 6: In-Process Features
How do we distinguish between in-process features and final part features in the AIM?
  Use a classification assignment.
All Features are shape aspects
  All are related to the product shape.
  Final part features with an explicit representation may reference geometry from the product shape.
  In-process features with an explicit representation may reference geometry from an in-process shape.
  Features with an implicit representation don’t care.

## Slide 7: How Features are Attached
Workpiece
product /
product definition
formation /
product definition
shape definition
representation
shape representation
(usually an advanced
brep shape rep)
product definition
shape
shape definition
representation
shape representation
product definition
shape
explicit
description
The Feature
complex instance
of instanced_feature
and feature_definition
subtype
through
shape_aspect
of_shape
shape definition
representation
shape representation
with parameters
product definition
shape
other shape
aspects describing
aspects of the
feature
implicit
description

## Slide 8: How In-Process Features are Called Out
product definition
shape
The Feature
complex instance
of instanced_feature
and round_hole
shape definition
representation
shape representation
with parameters
axis_placement_3D
name = “orientation”
applied_classification_assignment
group
name = “in-process”
classification_role
name = “feature category”
other features
Features on the final part do not need a classification, but if desired, they can have one of “final”

## Slide 9: Relating Workingsteps
How to relate a workingstep to an in-process feature?
  Use same method as for any other feature.
  Workingstep must be related to a final feature
  May also be related to an in-process feature.
Goals are to manufacture features
  action (property_process) related to feature.

## Slide 10: EXPRESS-G for Workingstep AIM
subtypes for operation type, tool,
strategies, technology, etc.
action_method
action_method_relationship
action
action_relationship
property_process
product_definition_process
manufacture a feature
(shape aspect)
manufacture entire project
(product definition)

## Slide 11: Workplan AIM Representation
action_method
machining_process_executable
machining _operation
machining _workplan
machining _workingstep
subtypes for categories of
milling operations
subtypes for other
ARM definitions
Executables and operations are represented using action methods
  Special subtypes for operations, workplan, and workingstep
  Related to each other using action_method_relationships
  Use MFP to relate workingsteps to features
machining_feature_process

## Slide 12: Associating Workingsteps with a Feature
property_process
“machining”
machining_feature_process
process_property_association
property_or_shape, as a shape_aspect
through property_or_shape_select
process
action subtype
action_method
subtype
chosen_method
working steps to manufacture the feature
to product_definition_shape
and product_definition
The Feature
instanced_feature
workingsteps collected
together using action
method relationship

## Slide 13: In-Process and Final Feature
The Feature
complex instance
of instanced_feature
and round_hole
classification assignment
“in-process”
machining_feature_process
The Workingstep
machining_workingstep
property_process
process_property_association
action method
relationship
“in-process feature”
The Feature
complex instance
of instanced_feature
and round_hole
machining_feature_process
property_process
process_property_association
action method
relationship
“final feature”
Optional
Required