## Slide 1
Ted Vorburger and Simon Frechette
MEL/NIST
Bill Danner
Seneca-IT.com
SC4 Meeting
Fukuoka, Japan
October 1, 2001
Report on AP219

## Slide 2
Contents
Scope
Activities since June SC4 Meeting
Status - Documents Developed Thus Far
Harmonization Efforts
Future Work

## Slide 3
Scope and Functional Requirements
This Application Protocol (AP) will specify information
requirements to manage dimensional inspection of solid
parts or assemblies, which includes administering,
planning, and executing dimensional inspection as well as
analyzing and archiving the results. Dimensional inspection
can occur at any stage of the life cycle of a product where
checking for conformance with a design specification
is required.

## Slide 4
Project Activities since June SC4 Meeting
Conference calls 23 August and 21 September
Began draft of Object Definitions
Refined Harmonization Tables
Contract in place to develop harmonization modules with AP203

## Slide 5: Participants include:
Steve Scigliano & Joe Schafer - Tecnomatix
Clay Tornquist - B& S Agilent
John Wootton & Keith Morton - LK
Bill Danner - Seneca-IT.com
Alan Jones & Tom Hendrix - Boeing
Curtis Brown - Honeywell
Joe Fallert & Bob Waite - DaimlerChrysler
Mark Cluff - Wilcox
Osborne Martin - UNC Charlotte
Glen Allen - Ford
Ted Vorburger, Simon Frechette, Larry Welsch, Howard Harary - NIST

## Slide 6
Contents
Scope
Activities since June SC4 Meeting
Status - Documents Developed Thus Far
Harmonization Efforts
Future Work

## Slide 7
Status,
Draft Documents developed thus far:
Application Activity Model (AAM)
Glossary for the AAM
Application Reference Model (ARM) - Four draft versions
AP219/DMIS/AP214/AP224 Harmonization Tables for
- Features,
- Geometric Tolerances,
- Dimension Tolerances

## Slide 8: AP219 Usage Scenario Activity Model
dim meas prog
modified dim meas prog
dim
meas
data
Analyze
Execute
/ Modify
Plan
dim meas prog archive
dim
meas
program
identification
dim meas
parameter
results
design and
manufacturing
information
part
information
dim
meas
features
& tols
dim
meas
data
dim
meas
program
identification
dim
meas
features
& tols
Scenario 1
dim meas
parameter
results

## Slide 9: AP219 Dimensional Inspection
Information requirements, modules for ARM Version 0.5
  Parts Identification
  Dimensional Measurement Features
  Dimensional Measurement Tolerances
  Dimensional Measurement Program ID
  Dimensional Measurement Results

## Slide 10: AP219 Dimensional Inspection
Harmonization
  STEP Modules (Part identification) / PDM Schema
  AP224 (Mech prod def using machining features)
  AP214 (Automotive mechanical design)
  AIC519 (Geometric tolerances)
  DMIS (Dimensional Measuring Interface Standard)
  Web Dimensional Measurement Analysis Project
  STEP NC (future activity)

## Slide 11: DMF (Dim meas feature): Tolerance harmonization AP214 & AP224
plus_minus_
bounds
limits_&_fits
limitation_
definition_
select
lim_def
(ABS)
dimensional_
measurement_
feature
identifier
label
dmf_circle
dmf_
dimensional_
parameter
diameter
measured_
parameter_
with_limits
measured
_values
S[1:?]
REAL
INTEGER
value_
determination_
enumeration
value_determination
sig_digits
upper_bound
lower_bound
REAL
(ABS)
measure_
with_unit
STRING
unit
nominal_
value
limited_value
value_comp
AP219_entity
AP224_entity
specified_tolerances S[1:?]
dmfdp_tolerance_select
numeric_parameter_
with_tolerance
value_
limitation
value_limit
limit_qualifier_
enumeration
limit
limit_qualifier
AP214_entity
calculated_limits S[1:2]
lim_method
measured_
parameter
text
calc_method
calculated
_value

## Slide 12: DMF (Dim meas feature): Features harmonization AP224 & AP214
AP219_entity
AP224_entity
circular_
closed_profile
diameter
numeric_
parameter
REAL
STRING
diameter
parameter_unit
parameter_value
AP214_entity
multi_axis_
feature
hole
round_hole
machining_
feature
manufacturing_
feature
shape_
instance
shape_
aspect
shape
elements S[0:?]
num_param
with_tol
assoc_
param
shape_
element
elements S[0:?]
dmf_
dimensional_
parameter_
association
dmf_
dimensional_
parameter
included_
feature
dmf_dp_
assoc_feature
_param_select
assoc_
feature
_param
dmf_dim
_param
feature_
parameter
design_
feature_
parameter
shape_
instance
assoc_
param
machining_
feature_
parameter

## Slide 13: Geometric tolerance Tolerance harmonization AIC519
toleranced_shape_element
shape_
aspect
geometric_
tolerance_
with_datum_
reference
angularity_
tolerance
circular_
runout_
tolerance
concentricity_
tolerance
parallelism_
tolerance
perpendicularity_
tolerance
position_
tolerance
symmetry_
tolerance
total_runout_
tolerance
precedence
datum_
reference
datum
INTEGER
identifier
datum_system S[0:?]
referenced_datum
identification
circularity_
tolerance
cylindricity_
tolerance
flatness_
tolerance
straightness_
tolerance
geometric_
tolerance_with_
defined_unit
modified_
geometric_
tolerance
limit_
condition
linear_
profile_
tolerance
surface_
profile_
tolerance
unit_size
modifier
AIC519_entity
Geo tol
module ?
(ABS)
geometric_
tolerance
text
identifier
measure_
with_unit
descrip
mag
name

## Slide 14
"Dimensional Measuring Interface Standard, Version 4.0”,
Submitted to ISO as ISO 22093.

## Slide 15
Portion of Harmonization Table for Geometric Tolerances

## Slide 16
The WebAnalysis Project,
led by Joe Fallert, DaimlerChrysler,
aims to consolidate the current dimensional measurement
analysis and reporting processes and products at
DaimlerChrysler (and elsewhere) into one robust common
product and process using industry standards and commercially available, Web-based software.

## Slide 17
Analysis & Reporting Corp Landscape
Supplier Base
Stamping
Plant
Database
CMDANA
D b
Assembly
Plant
Database
Powertrain
Component
Plant
Database
Powertrain
Assembly
Plant
Database
Intranet
Intranet
Supplier Support AutoWeb
WebAnalysis@DCX.com
Exterior Build
Objectives
Root Cause Tree
Hood Asm Checks
BSA Audit
DCAH
DCS
1250 Users at CTC
400 Internet Users
200 Suppliers
J. Fallert

## Slide 18: Web Analysis: Information requirements (circle_feature)
reverse eng
(ABS)
circle_
feature
nominal_
circle_
feature
measured_
circle_
feature
STRING
diameter_max
diameter_min
diameter
diameter
Web Analysis
Logical Model
(not AP219)
<!ELEMENT nominal_circle_feature
(center_point,normal,diameter,(start_vector,angle)?)> <!ATTLIST nominal_circle_feature %reporting_transform; > <!ELEMENT measured_circle_feature
(center_point,normal,diameter, diameter_min,diameter_max,(start_vector,angle)?)> <!ATTLIST measured_circle_feature %reporting_transform; > <!ELEMENT circle_feature ((nominal_circle_feature) | (measured_circle_feature)| (nominal_circle_feature, measured_circle_feature))> <!ATTLIST circle_feature type (INNER | OUTER | UNKNOWN) #REQUIRED >
XML DTD
Web Analysis
Implementation Model

## Slide 19
Contents
Scope
Activities since June SC4 Meeting
Status - Documents Developed Thus Far
Harmonization Efforts
Future Work

## Slide 20
AP219 Object Definitions
Currently contains ~102 entities gathered from AP214

## Slide 21
Dimensional Inspection Information Exchange
Technical Report (draft by 1/31/02)
Outline
Introduction, Motivation, Outline of Following Sections
Application Activity Model for Dimensional Inspection
Application Reference Model (ARM) in EXPRESS-G of
Dimensional Inspection Information Requirements
- Consisting of five modules: Parts Identification, Features,
Tolerances, Program ID, Results
- Harmonized with information requirements in
AP214, AP224, DMIS, and the Web Analysis Project
Object Definitions for Entities and Attributes in the ARM
Harmonization Tables for Features and Tolerances
Outline of Future Activities

## Slide 22
Future Work
To facilitate implementation:
A contract is in place
to develop harmonization modules with AP 203.
Completion of contract planned for 9/02.

## Slide 23
Summary
Project need and constituents/collaborators well established
Dimensional inspection information requirements model
(ARM) Version 0.5, consisting of 5 modules
- planned for 1/02
Draft NISTIR/STEP Technical Report on the ARM
- planned for 1/02
Will develop harmonized modules with AP203
- completion planned for 9/02
Facilitate Metrology Interoperability Consortium as needed
New Work Item under STEP - submit early FY03