## Slide 1: AP-238 Walkthrough
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Myrtle Beach SC4 Meeting
David Loffredo
loffredo@steptools.com

## Slide 2: Walkthrough Agenda
What is AP-238?
The Backbone: Workpiece and Features
The Backbone: Executables and Operations
Milling Operations and Strategies
Milling Tool Types
Projects and Setups
Advanced Control Flow for Programs
Explicit Toolpaths

## Slide 3: What is AP-238?
AP-238 describes machining process.
  AP-238 maps the ISO 14649 information requirements to the integrated definitions used by all other AP.
  So you can use existing CAD systems, viewers, etc.
Units of Functionality
  Project, Workpiece
    Brep geometry harmonized with AP-203/AP-214.
    PDM details harmonized with PDM schema.
    Uses AIC 519 tolerance definitions.
  Features
    Harmonized with AP-224 representation.
  Executable, General Operation, Milling Operations, and Milling Tool requirements.
    Process and process resource description using Part 49, Part 41, and PLIB expressions for conditional control.

## Slide 4: Overview of AP-238
Based on Part 10
Measures
Project
Workpiece
Features
Milling Process Operations Based on Part 11
Milling Cutting Tools Based on Part 11-1
Turning Process Operations Based on Part 12
EDM Process Operations Based on Part 13
Executable
Operation
Toolpath
First
Edition
Second
Edition
AP-238 will cover all technologies
  First edition covers milling.
  Second edition will extend with turning and EDM.
  Amendments can add others as needed.

## Slide 5: Workpiece and Stock
Workpiece describes the final output of a manufacturing process
Also defines stock, with geometry and material.
These are STEP products, so the standard PDM schema information can be applied.
  Owner, Approval, Release Date, etc.

## Slide 6: Setup
A setup describes the orientation and locations of workpieces on the machine
  Referenced by a workplan
  Conceptually similar to an assembly
  A setup may have many copies of the same workpiece
  Also describes “keep out” regions where fixtures may be.

## Slide 7: STEP-NC Features
round hole
counterbore hole
compound feature
pocket with
through bottom
condition
pocket with
flat bottom
condition
slot with
radius
ends
2.5D milling features
  Hole, pocket, slot, step, etc
Transition features
  Edge round and chamfer
Replicate feature
  Patterns of repeated features
Region features
  Surfaces for freeform milling
Notes: This slide represents the highlights of AP224.
The list of items in each box represents a sample of what AP224 contains.
To summarize - AP224 contains everything found on a drawing of a part

## Slide 8: STEP-NC Machining Features
manufacturing
feature
transition
region
2.5D manufacturing
machining feature
replicate
feature
profile
hole
planar face
toolpath
feature
step
slot
pocket
compound
feature
STEP-NC Features
Explicit geometry, points out a surface for freeform milling
(5 axis and such)
Implicitly described using profile and path parameters, not explicit geometry

## Slide 9: Feature Description
Features are described parametrically using a combination of Profiles and Paths
  A Profile is swept over the entire length of a Path
  Profiles described by key parameters, like length, radius.
For example, a round_hole is defined by a Complete_circular_profile and a Linear_path

## Slide 10: Features AIM Representation
Features describe material removal areas
Features are represented as shape aspects on the workpiece shape
  Implicitly defined features are described by a profile moving along a path.
  Explicitly defined features are described by surfaces from the workpiece shape.
  Profiles, paths and other conditions are defined as shape aspects associated with the feature.

## Slide 11: Project
Project is the “root” of a STEP-NC file
  Points to the main workplan
  Points to one or more workpiece
Project is represented as a product
  We can use all of the PDM information to track the project as well as the workpieces
Project has a workplan and set of workpieces
  Workplan related as previously described

## Slide 12: Machining Programs
Heart of the STEP-NC model
Executables
  Describes control flow and sequencing.
  Workingstep associates an operation and a feature.
  Technology independent
Operations
  Describes what to do within the feature context given by a workingstep — plane mill, center drill, etc.
  The basis for all technology-specific extensions.
  Specifies details like
    spindle, feedrate and other technology parameters
    coolant & other machine functions
    plunge strategies, tool paths, etc.

## Slide 13: ARM for Machining Programs
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Program steps that do not move any machine axes
(display message, etc.)
Control flow for the machining program
workplan
parallel
if_statement
while_statement
Program steps that move
the machine axes

## Slide 14: ARM for Machining Programs
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Focus on a simple machining program
A Workplan
containing a sequence of Workingsteps
workplan
parallel
if_statement
while_statement

## Slide 15: Simple Machining Program
A Workplan
  Has a list of workingsteps to be executed
A Workingstep
  Refers to an operation that describes what to do.
  Refers to a feature that describes a location and material removal volume.
  Has a security plane for moving to/from other steps.
All executables (workplans and workingsteps)
  Have an id so you can refer to them.

## Slide 16: Overview
STEP-NC supports a rich set of control flow for machining workplans
  More types of programs than simple linear sequences of machining workingsteps
  Branches, parallel segments, feedback from probing
  Room for future intelligent controllers to optimize
Questions
  What other types of workingstep and functions are available?
  What control flow options are available?
  How are controlling expressions represented?

## Slide 17: ARM for Machining Programs
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Program steps that do not move any machine axes
(display message, etc.)
Control flow for the machining program
workplan
parallel
if_statement
while_statement
Program steps that move
the machine axes

## Slide 18: Other Types of Workingsteps
Rapid Movement
  return_home
Touch Probing
  workpiece_probing (offset in one direction
  workpiece_complete_probing (x, y, z offsets)
  tool_probing
    tool_length_probing
    tool_radius_probing
NC Functions
  display_message
  exchange_pallet
  index_pallet
  index_table
  optional_stop
  program_stop
  set_mark
  unload_tool
  wait_for_mark

## Slide 19: Nonlinear Control Flow
STEP-NC supports seven kinds of control flow
  Workplan (Sequential) : execution by a sequence
  Unordered Serial : all executables have to be executed but the order of execution does not matter
  Concurrent : all executables are started at the same time
  Parallel : all executables don’t need to be started at the same time
  If Statement : binary choice according to the given condition
  Selective : execute only one among several executables
  While Statement : repetitive execution
Notes: Keeping in mind that let me get into the first item; On the nonlinear process plan (NLP); which is
- To represent …
- To introduce …
Note that the choice is made by the CNC giving flexibility for the STEP-CNC, which is key for the intelligent CNC control
To represent NLP, we found that 7 entities are ncessary:
- Sequential (“linear” or “serial” process plan mostly assumed in the current version)
- Conditional Choice, …

## Slide 20: Controlling Expressions
STEP-NC ARM defines machining control flow (if/then, while, etc) controlled by expressions.
  Expressions use literal values and variables that are associated with the result of a measurement operation.
Map expressions using PLIB Part 20
Property with expression representation.
  The PLIB definitions only references PLIB things.
  Need some way to relate this to a STEP representation.

## Slide 21: Summary
Machining Workingsteps
  Describe a sequence of material removals, location, and associated parameters
Workingsteps are organized into a workplan
  Using sequential_method, a type of action method relationship, to describe the ordering
Have related properties
  Which are described by a representation
Are related to an operation
  Using an action method relationship
Are related to features and project
  Using action, of which the workplan is the chosen method

## Slide 22: ARM for Milling Operations
2.5D Machining Operations
  Plane and side milling.
  Tool can move in the X-Y plane or along the Z axis, but not at the same time.
  Set of strategies
Freeform Machining Operations
  For sculpted surfaces
  3, 4, and 5axis motion
  Set of strategies
Drilling Operations
  Drilling, boring, back boring, tapping/threading
  Tool moves in the Z axis only
  Many strategy parameters

## Slide 23: ARM For All Machining Operations
All Machining Operations can have:
  A cutting tool requirement
  A start point and retract plane
  Technology parameters, which are grouped and shared between operations
    Spindle speed, feedrate, feedrate per tooth, etc.
  Machine settings, which are grouped and can be shared between operations
    Coolant, misting, chip removal, etc.
Operations can also have strategies
  All operations can have an associated machining strategy
  All milling operations can also have an associated plunge strategy and a retract strategy

## Slide 24: 2.5D Milling Operations
2.5D Machining Operations
  Plane and side milling.
  Tool can move in the X-Y plane or along the Z axis, but not at the same time.
    bottom_and_side_milling
    side_milling
    plane_milling
All operations have rough and finish versions
  Rough milling leaves an allowance of material
  Finish milling goes right to the feature boundaries

## Slide 25: 2.5D Milling Strategies
Bidirectional Contour &
vice versa
Contour Parallel & Spiral
Center Milling
Unidirectional
Bidirectional

## Slide 26: Freeform Milling Operations
Freeform Machining Operations
  For sculpted surfaces
  3, 4, and 5axis motion
  No special subtypes
Usually for use with region feature or other explicit surface geometry
  Has a scallop height and chord parameters to help controllers decide how to generate toolpaths.
Freeform Strategies
  Cutter contact, cutter location, UV, leading line

## Slide 27: Drilling Operations
Drilling Operations
  Drilling, boring, back boring, tapping/threading
  Tool moves in the Z axis only
    drilling_operation
      drilling, center_drilling, counter_sinking, multistep_drilling
    boring_operation
      boring, reaming
    back_boring
    tapping
    thread_drilling
Only one drilling strategy, but with many parameters
  Feed rates for starting, ending, and retract, dwell, depths, etc.

## Slide 28: Summary
Operations
  Describe what is to be done.
  Currently supports 2.5D milling, freeform milling, drilling
  With many strategies and parameters
Future editions will add operations for other machining technologies
  Turning
  Grinding
  EDM

## Slide 29: Cutting Tools
Every operation can have a tool associated.
  Represents tool requirements, not a physical tool on a machine.
  Potential for some best-fit optimization by the controller.
  Only important parameters should be set.
    The more constrained the tool is, the less flexibility the controller will have
Previously, G&M codes just reference tool #1, #2, etc.
  Human must make sure that #1 corresponds to the right thing.
  Controller not able to add any value to the process.

## Slide 30: Overview
Toolpaths allow us to capture exact machine axis movements.
  Workplan still has “macro” plan with features and operations.
  Captures a “micro” plan for particular operations.
  More flexible to give a controller a macro plan and let it generate the micro plan itself.
Question
  What types of tool paths can we specify?
  How are they represented in the AIM?
  How are they attached to an operation?

## Slide 31: ARM for Toolpath UOF
toolpath
feedstop
parameterised
path
trajectory
cutter location
cutter contact
axis
STEP-NC Toolpaths
Dwell at a particular
location
Movements generated by the controller using certain parameters
approach lift path
connector
connect secplane
connect direct
Movements following explicit curves with respect to certain reference points
A/L angle
A/L tangent