## Slide 1: 3D Data for Pipe Bending and Cutting Machines
Blair Downie
downie@steptools.com
Martin Hardwick
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: Introduction
3D Data for Pipe Bending and Cutting Machines
  SBIR Phase I award
  Office of Naval Research
  Topic N02-049: Technology for Shipbuilding Affordability
Objective:
  To develop a new high level control language for pipe bending and cutting machines based on the STEP and STEP-NC standards

## Slide 3: STEP-NC
Direct control of machine tools from 3D data
  STEP-NC under development in Europe and Far East for 5 years
  Milling, Turning, Wire EDM, inspection, others anticipated
Benefits
  35% reduction in CAM planning time
  75% reduction in number of drawings sent from CAD to CAM
  50% reduction in machining time for small to mid sized job lots
  Elimination of 4,500+ post processors
  Safer, more adaptable machine tools
  Easier repair
http://www.stepnc.com
Design
Planning
Manufacturing
35% faster
75%
faster
50%
faster
STEP
(AP-224*)
STEP-NC
(AP-238)
Same geometry

## Slide 4
Contouring
Milling and Drilling
Wire EDM

## Slide 5: Current methods
RS274D (ISO 6983) defines the data input interface for Pipe Bending controllers
  CNC Vendors compete by adding codes to RS274D
  OEM uses Post to manage RS274D flavors
  Supplier uses conversational programming
Conversational
Programming
Bending
machine
CNC Control
RS274D
Bending
machine
CNC Control
Pipe design and detailing
RS274D
CAD/CAM
Post
CAD
Specific API
Integrated Enterprise Method
Job Shop Method
Drawing
data

## Slide 6: Current NC programming using RS274D
%
N05 G54
N10 G00 Z10.000
N15 G91 G0 Z200
N20 T5 D1 WW
N30 G90 M5
N35 G00 X0.000 Y-150.000
N40 G00 Z5.000
N45 M08
N50 S3183.000
N55 M03
N60 F1477.000
N65 G00 X60.000 Y-150.000
N70 G00 Z5.000
N75 G00 X60.000 Y-150.000
N80 G01 Z-0.500
...
machine-specific part program with axis data generated by a postprocessor
vendor-specific extensions of the original standard
only primitive motion and switch commands
no standardized data format for spline processing and sophisticated NC technology
Courtesy WZL RWTH Aachen
STEP-NC replaces this with a
rich, integrated data format
Ideal for Paper Tape!
The standard for 40 years!

## Slide 7: STEP-NC is integrated
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 8: STEP-NC method
Put a CAM onto the control to compile STEP-NC
  Post processor is eliminated or hidden from the end user
  Tool path generation is done using the CAM
  CNC vendors compete by writing STEP-NC compilers to take maximum advantage of their machine features
New Controller
Detailing
Legacy Controller
STEP-NC Compiler (CAM)
Same data for internal and external suppliers
Optimize
STEP-NC Controller
STEP-NC Controller
Piping CAD
STEP AP-227
STEP-NC AP-238
STEP-NC Compiler (CAM)
Same or
different PC’s

## Slide 9: Key feature of STEP-NC
STEP-NC describes “what” not “how”
  Make this geometry from this stock
  By removing these features
  In this order
  With this tolerance
  And tools that meets these requirements
The old standard described “how”
  Move tool to this location
  Move tool to this location
  And so on for millions of commands

## Slide 10: Research Goals
Define how to use the STEP-NC standard to control pipe bending and cutting machines
Prototype CAD, CAM, and CNC systems with the new interfaces for pipe bending and cutting
Quantify the productivity benefits and ROI for using STEP-NC for pipe bending and cutting in US Shipbuilding

## Slide 11: NC Bending Parameters
Bending machines need three key parameters
  Length
  Roll angle
  Bend angle
Typical workplan
  Move pipe forward "z" inches
  Make 45 degree bend
  Move pipe forward "y" inches
  Rotate pipe by 180 degrees
  Make 45 degree bend
  Move pipe forward "x" inches
Bending radius for this setup
Machine Limits
x
y
z

## Slide 12: Prototype Interfaces
NC INSTRUCTIONS
NC INSTRUCTIONS
MATERIAL LISTS
FABRICATION
INSTRUCTIONS
PIPE ASSEMBLIES
Pipe
Interference
Checks
Design
Rule
Checks
PIPE DETAILS
MMAP
CATIA
VIVID
(NNS)
AP
-
227
3D PIPING
AP
Input Interfaces
Re
-
DESIGN
AP
-
238
Plan
EB
SHIPYARD
PIPE ASSEMBLIES
PIPE DETAILS
NNS
SHIPYARD
OTHER
SHIPYARDS
DESIGN APPROVED
-
INPUT OPTIONS
-
EXECUTABLE
-
OUTPUT OPTIONS
Process
Plan
Migrate
functions
onto
machines
AP
-
238 enhanced
for pipe bending