## Slide 1: The Integrated Steel Processing Environment Background, Requirements Summary, and Future Plans
13 March 2003

## Slide 2: Briefing Topics
ISPE Objectives, Team Members, & Tech Strategy
Phase 0 Activities & Requirements Approach
Phase 0 Results & Conclusions
Phase 1 and 2 Preview

## Slide 3: ISPE Objectives
The Integrated Steel Processing Environment (ISPE) Team proposed to develop technologies and integrate a pilot system that will enable CAD-independent interchange of steel fabrication work packages among associate shipyards.
The ISPE system that we will pilot in will demonstrate:
  Decoupling CAD from CAM
  Efficient Partnering Among Yards
  CAM front end (CAD Neutral)
  Use of STEP as the primary interchange mechanism

## Slide 4: Technical Strategy (Phase 0 and Beyond)
Approach
  Pilot System design/development
  Focus on COTS component integration via data standards
  Build on ISE products and methods
Innovations
  Comprehensive information/data model for steel processing
  Prescription for controlled, consistent application of STEP protocols
  Middleware for CAD interoperability with ISPE CAM
  Methods and tools for accuracy management
Demonstrate using a real ship section

## Slide 5: ISPE Team Members
Team
Member
Phase 0 Role
NGSS
Prime contractor, Lead Shipyard, Shipyard Integrator for pilot project,
Shipyard implementation requirements, ISDP, SPADES
, CATIA v5
NGNN
Shipyard implementation requirements, CATIA v4, SAP
Electric
Boat
System Design, Shipyard Requirements
and Interoperability,
architecture support, standards support (STEP), CATIA v4
NGIT
System Integrator, legacy code analysis, data warehouse
development, new code creation
Sigmatek
NC system interface, Commercial
-
off
-
the
-
shelf (COTS) Nesting
solutions provider
AeroHydro
Geometry exchange, including transformation of Legacy data to ISPE
STEP representation, accuracy management
STEP
Tools
Support applicability and extension of current AP218, STEP-NC
standards, CATIA v5
Atlantec Enterprise Solutions will be joining the project for Phase 1 and 2

## Slide 6: ISPE Responds to the NSRP Strategic Investment Plan
Development of the Integrated Shipbuilding Environment has attacked the problem of exchanging design-centric information among various CAD systems. However, another important aspect of shipyard integration (which has been largely ignored) involves the problem of exchanging a designed ship between different computer-aided manufacturing (CAM) systems. [SIP, page 47]
The emphasis on cross-shipyard teaming has shown that there are significant challenges not only in migrating design information from one shipyard’s CAD system into another’s manufacturing stream, or within the same shipyard, but also from new 3D CAD systems into legacy manufacturing systems. [page 47]
The CAM Interfaces sub-initiative under Systems Technologies will enable CAD information to be efficiently transferred to various CAM systems to support the initiatives in Shipyard Production Processes. [page 48]
CAM Interfaces should focus on developing an environment where the evolution of CAD systems is decoupled from the CAM systems, enabling yards to add new CAD SYSTEMS TECHNOLOGIES systems by adding only one pathway to a neutral format CAM database. [page 47]
To date, STEP has not been widely deployed in production-worthy systems in the shipbuilding industry”…”Due to this limited deployment, STEP has had little real impact on the industry. [page 49]
The highest priority of the Systems Technologies initiative must be to provide an implementation method, based on currently available Internet and object technology, for the STEP shipbuilding product models. [page 49]
Develop data exchange for CAM
Decouple CAM interfaces from personalities, customer varieties, and evolution of CAD
Evolve and leverage the STEP standard in Ship Production

## Slide 7: ISPE Builds on Existing ISE Products and Research
ISE
Parts Libraries
Design & Engineering
  - Piping
  - Structures
Product Data
Management(PDM)
ISPE
STEP AP218* Development
Interoperability Infrastructure
- Web Technologies
- STEP/ XML
TWR Test Data
Mfg Rule Base
Work Packages
CAM Interfaces
Manufacturability
Analysis
Preliminary Design
Production
*AP218 – Ship Structures

## Slide 8: Briefing Topics
ISPE Objectives, Team Members, & Tech Strategy
Phase 0 Activities & Requirements Approach
Phase 0 Results & Conclusions
Phase 1 and 2 Preview

## Slide 9: ISPE Phase 0 Activities
July 02
Aug 02
Sept 02
Oct 02
Nov 02
Dec 02
Jan 03
Project Kick-off
Yard-specific Requirements
Collection
Newport News
Requirements Review
Common Requirements
Consolidation
Plan follow-on
Rqmnts Complete
Ingalls
Avondale
Electric Boat
Requirements Kick-off
Go/No Go

## Slide 10: ISPE Project Funding
The National Shipbuilding Research Program (NSRP) funded approximately 40% of the ISPE Phase 0
Dollar cost sharing was provided by the Shipyard team members. Other team members provided software license and support cost sharing
Notes: The total estimated cost for ISPE, Phase 0 completion is $1,241,250. Of this $500,000 is the estimated reimbursable and $741,250 is the estimated cost share.

## Slide 11: Requirements Collection Approach
Included a broad based industry representation (Avondale, Ingalls, Newport News and EB)
Used the Zachman Frameworks as a guide
Information gathering focused on steel processing: Groups, Functions, Applications, Data, Interfaces, and Manufacturing Rules
Each yard was provided with training, a requirements collection manual, and in-process feedback
Consolidated requirements were developed from the yard specific requirements

## Slide 12: Information Collection Tasks
Task Description
Products
Steel Processing/Organizational Model
Definition
Steel Processing Flow Diagram
Group and Function Description
Systems Technology Definition
Information Resource Catalog
- Current applications business function mapping
Data Architecture Definition
Steel Processing Entity List
Description of Data Entities Relationships
Entity Relationship Diagrams
Entity Attributes
Parametric Part Data
Capture Manufacturing Rules
Manufacturing Rules database
Survey the Data Dependency of Applications and Functions
Function/Application Create-Update-Reference Tables
Elicit Data Sharing Practices
Documentation of Data Sharing Practices

## Slide 13: Briefing Topics
ISPE Objectives, Team Members, & Tech Strategy
Phase 0 Activities & Requirements Approach
Phase 0 Consolidated Results & Conclusions
Phase 1 and 2 Preview

## Slide 14: Common Steel Processing Functions
html_functions

## Slide 15: Manufacturing Product Model Definition
Shell Plate Design
CAD
Develop Flat Plate
Specialized Macro
Add Excess Stock for Rolling
Manufacturing Rule
Adjust Size for Weld Shrinkage
Manufacturing Rule
Yard Processes and Assembly Plan
Add Edge Prep & Punch-marking
Source
Process

## Slide 16: The Common Data Model
Common data dictionary
  Entities with common names and business descriptions
  Entity attributes with names, business descriptions, and mapping to each entity which uses the attribute
Common entity relationship diagram showing:
  Entities common names
  Inter yard entity nomenclature and content similarities/differences
These provide a consistent terminology for names and definitions used in Steel Processing.
They also provide a logical data architecture foundation upon which physical data structures
and standard interfaces (e.g. STEP, XML Schema) can be developed.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Common Data Architecture Categories
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Build Tree Entities
Build Tree entities define manufacturing assembly stages. Each assembly stage, called a build tree level by ISPE, includes parts, sub assemblies, construction drawing references, and other attributes.
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Build Tree Attributes
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Design and Manufacturable Components
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Component Types
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Design vs. Manufacturable Component
Yard Neutral
Yard Specific
+ yard & shop
specific attributes
=
3D
Design
Component
3D
Manufacturable
Component
Added material
Removed material
Chamfers
Welding access
Reference lines
Beveling
Intercostal Clearance
**Manufacturable Components have Yard-Specific, Rule-Based Attributes**
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Part Entity
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Part Attributes
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Part - Manufacturing Aids
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Part - Labels and Marking Lines
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Part - Penetrations
A penetration is an interior cut-out that typically allows for the passage of a distributive system element
Various types of penetrations can be applied to components and parts
Penetration can be identified as distinct objects by NC part files
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)

## Slide 28: NC File Attributes (for nest tape)
BUILD TREE LEVELS
MANUFACTURING
COMPONENTS
EDGE PREPARATIONS
PROCESS & ROUTE
NC FILES
PART SPECIFICATION
(Marking & Annotation, Mfg. Aids, Penetrations & Cutouts)
DESIGN
COMPONENTS
PARTS
(Plate, Profile, Shell)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Using STEP to Represent ISPE Data
AP218 (Ship Structures) accommodates most of the ISPE data requirements
STEP-NC will be developed and utilized to provide additional data for specific interfaces
Notes: <number>
<footer>
<header>
<date/time>
AP218 weak in the area of text labels
Support for yard-specific labels, marking lines, symbology requires ‘placeholders’ for data with logical information
Relationships among parts, along with yard-specific routing, would provide a basis for mfg rule application

## Slide 30: Using STEP to Represent ISPE Data (cont.)
Areas within AP218 that will need enhancement:
  At the Component level
    Need to be able to specify manufacturing data (material characteristics, strength requirements, adjacency information, added material, etc.)
  At the Part level
    Need to add features for each edge, not just the entire part
    Need to add min & max extents, area, center of gravity, quantity nested, etc.
  Labels/Symbology
    To allow for the definition/placement of yard-specific annotations, symbols, marking lines, etc.
  Design/Manufacturing definition extensions
    To provide support for logical instructions that will aid in the application of yard-specific mfg rules
    Need additional manufacturing aid specifications
  Additional scheduling & routing information

## Slide 31: ISPE Concept of Operations
Shipyard Mfg
Model
Create
Detailed
Design
Neutral Mfg
Model
Neutral Design
Model
Generate
Shipyard
Products
ISE Export of Design Data
<AP 218>
Reports
NC
Aids
To/From other yards
ISPE Interface/API
Enterprise
Systems
Nesting
Robotic
Welding
…
01010100101001010010010
ISPE
Interfaces to other systems and yards
CAD
Status &
Configuration
<AP 218>
<AP 218/STEP NC>
Validate
Structural Design/
STEP Import
Annotate
Mfg Rqts.
Apply/Validate
Shipyard Mfg
Processes
Mfg Req
Mfg Rules
Problems and Issues
Yard Proc

## Slide 32: Possible ISPE Usage Scenarios
Enable CAD system independence while maintaining current lofting functions
Transition to rule-based manufacturing model development
Provide a front-end to shipyard CAM processes
Subcontractor builds units or entire hull to a lead yard’s specifications
Lead yard out-sources Lofting Functions
Legacy Design is ingested into ISPE
Late breaking planning requires use of alternate yard processes or external yard processes

## Slide 33: Recent Prototypes by ISPE Team Members
ISE STEP and XML CAD interoperability
Programmatic viewing and editing of CAD STEP data using the STEP Tools viewing capability
Use of an implicit representation of CAD data consisting primarily of parametrically-specified structural components (Component STEP)
STEP nesting interface
XML interface for the Ingalls Structural CAD Application (ISCA) … from a co-lateral project

## Slide 34: Summary of Phase 0 Conclusions
Steel processing at the four participating shipyards can be mapped to a common process and data model
STEP AP’s include most of the product model data requirements. Some refinements are needed to accommodate manufacturing model definition and CAM consumption requirements
AP 218 CAD design export demonstration by the ISE project will provide the initial capability interface for ISPE
Work-share can be enabled by separating yard-specific manufacturing rules from the shared work digital specification
COTS software applications already exist for most of the ISPE pilot components

## Slide 35: Briefing Topics
ISPE Objectives, Team Members, & Tech Strategy
Phase 0 Activities & Requirements Approach
Phase 0 Consolidated Results & Conclusions
Phase 1 and 2 Preview

## Slide 36: ISPE Functional Architecture (Phase 1 & 2)
ISPE Repository
CATIA v4
export
CATIA v5
export
Tribon
export
AP218 Validation
Manufactur-ability Analysis
MRP Interface
Reports and Drawings
Manufactur-ing Data
Nesting
Adjust for Weld Shrinkage
Define Edge Preparation
Part
Generation
AP218
(Ship
Structures)
AP216
(Ship Molded Forms)
AP218
STEP-NC
Simulation
Robotic Welding
Phase 1
Phase 2
Config Mgt
Shipyard Proc
Mfg Rules
Shop Planning
Create Manufac-turing Aids
~2Q2003 to 1Q2004
~2Q2004 to 1Q2005

## Slide 37: ISPE Phase 1 and 2 Tasks and (Team Lead )
Project Leadership (NGNN)
Technology Transfer (NGIT)
Studies (NGNN)
ISPE Pilot Development
  Integration (NGIT)
  Model Yard Processes (NGNN)
  218 Export (EB)
  218 Validation/Preprocessor (STEP Tools)
  ISPE Repository (NGIT)
  Shop Process/Rule Mgmt System (Atlantec)
  Mfg Product Model & Reports (NGIT)
  Nesting & MRP Interface (SigmaTEK)
  Manufacturability Analysis (AeroHydro)
  Robotic Welding (NGSS)
  Simulation (NGNN)
  Manufacturing Data (NGNN)
Phase 2 only
Notes: Phase 1 Study task involves research, to be conducted concurrently with the phase 1 tasks, for components that will be implemented in phase 2. Doing so will allow the design and development work, that is completed in phase 1, to satisfy phase 2 additions and modifications. Specifically, the areas to be included in this research are the integration of robotic welding, manufacturability analysis tools, and manufacturing simulation.
Phase 2 Study task includes a study on how to deploy the ISPE and/or selected components to existing yards and research into how the ISPE and/or selected components might be commercialized. Both phases will conclude with a Return on Investment (ROI) analysis to be included as part of the project’s deliverables. Time is also allocated for various trade studies to be performed within both phases.