## Slide 1: AP-238 Direct Interface
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2
Contouring
Milling, Drilling,Turning
EDM

## Slide 3: Problems in current method
Current process is inefficient
  Design sends incomplete data
  Manufacturing makes fixes but does not document them
  End result is a control file that can only run on one machine at one supplier
  RS274D is more than 40 years old
Extensive CMM to check the geometry of as-built parts
Incomplete
Information
Partial
geometry
with “issues”
Undocumented
fixes added
Machine specific control
file that works only if
all conditions correct
Machine specific
translator
Processing information is lost
Design
Manufacturing
Detailing and Path Planning
Post
IGES
CAD
CNC Control
RS274D
CAM
CL File

## Slide 4: STEP-NC at NASA JPL
Rapidly manufacture AP-238 models
  Focus on making ordinary parts on multi-axis machines
  Default tolerances and finishes set using Crib sheets
  Allow ordinary machinists with little CAM training to be competitive with experienced machinists with extensive CAM training
ST-Plan
Planning
Fadal CNC with
GibbsCAM and
ST-Machine
STEP-NC Control
Modeling
AP-203
AP-238
Pro/E
Detailing
Complete
Model
Required
Wizard to define
Tolerances
Features
Processes &
Tool Requirements
Machine
Independent CNC Control File
What are
the
benefits?

## Slide 5: Verification
Old Method
105 minutes
90 minutes
16.5 minutes
New Method
15 minutes
90 minutes
23 minutes
Programming
Set up
Machining
Measured at 6th IRB meeting at NASA JPL on January 30, 2003
  This is the first saving
  Second saving occurs when easier programming leads to better machines being used for smaller jobs
  Third saving when drawings no longer needed

## Slide 6: AP-238 Direct Interface
We are building a library of STEP-NC access and calculation code to simplify programming directly against AP-238.
  Can use from detailed C++ applications or from lightweight COM/VB applications.
  Called STIX, for STEP Index
  Copy-left licensing for testing and evaluation
Advantages
  Start writing applications against AP-238 quickly and from different environments
  Take care of most common access paths and calculations.
  Allows for update path to modify AP-238 data.

## Slide 7: AP-238 Direct Interface
AP-238
Part 21
Tool Kit layer
Index Layer
Application
AP-238
Part 21
Tool Kit layer
Mapping
Layer
Tool Kit layer
Application
XML
Tool Kit layer
Application
EXPRESS-X
CEB Part 28
DOM
NEW
OLD
Good for Prototyping
New Method
  Enables Updates
  Smaller footprint
  Easier to maintain
  More sophisticated functions.

## Slide 8: STIX – STEP Index
AP-238
Data
STIX
C++ API
Index
COM
Shell
Geometry
Kernel
Validation
Application
Provide a direct interface to the AP-238 data.
  Read and build in-memory indices and backpointers on the AP-238 data for speed of processing.
  Simplify use of AP-238 data by providing API to common access paths and calculations.

## Slide 9: Properties and Relationships
setup info
Feature
Feature
Components
Path, Profile,
Taper, Bottom
placement,
orientation,
face geometry,
and other
parameters
component
parameters
Project
Workpiece
Workplan
Functions to access major concepts, relations, and parameters
  No longer need to be an AIM expert to do something useful.
  Even AIM experts will find this saves time. Already traverses through the property definitions, reps, rep items, etc.
Workstep
machining params
stock, shape,
material, other
parameters
Tools
tool characteristics
setup

## Slide 10: You Avoid Having to Learn This:
The Feature
complex instance
of instanced_feature
and round_hole
shape definition
representation
shape representation
with parameters
product definition
shape
axis_placement_3D
name = “orientation”
The Depth
path_feature_component
description = “linear”
shape definition
representation
shape representation
with parameters
property definition
length_measure_with_unit
name = “distance”
value = 100 mm
feature
component
definition
product
definition
shape
shape defining
relationship
shape
aspect
property definition
representation
direction shape
representation
direction
axis_placement_3D
Round Hole Depth

## Slide 11: STIX Example
Print a simple report
  Test harness during development
STEP-NC Index Contents Report ------—
------------------------------
Projects: 1 present
[0] name = 1 (id #184)
workplan = machining operations (id #75)
------------------------------
Setups: none
------------------------------
Workpieces: 2 present
[0] name = 1 A A (id #171)
shape = advanced_brep_shape_representation (id #633)
shape length unit = millimetre
stock = <no-name> A A (id #173)
stock length unit = millimetre
stock min/max X = 0 / 125 (125)
stock min/max Y = 0 / 75 (75)
stock min/max Z = 0 / 50 (50)
[1] [ . . . the stock . . . ]
#include "stix.h”
main() {
StixNC stepnc;
stepnc.load (argv[1]);
stepnc.dump_report();
}

## Slide 12: STIX Example (continued)
Report writer
------------------------------
Root Workplan: workplan machining operations (id #75)
1 elements
setup = none
[0 - 1] workplan Drill-2 (id #76)
1 elements
setup = none
[0 - 1] workingstep drilling (#46)
parent = Drill-2 (#76)
description = Drill-1-Micro-1-Hole-01
operation type = Drilling (drilling_operation)
property = security plane
property = retract plane
property = cutting depth
tool: type: 12.7000 mm TWIST_DRILL (id #32)
name: TL DRILL-2
diameter: 12.7
edge (flute) length: 21.1845
edge radius: 0
circumference angle: 0
technology (#19)
property = spindle
property = cutspeed
functions (#11)
property = coolant
in-process feature = round hole (#145)
final feature = round hole (#145)

## Slide 13: STIX Example (continued)
Report writer
------------------------------
Features: 2 present
[0] round hole (id #145)
feature faces: #423 #422
sar 0 name=[hole depth] desc=[path feature component usage]
linear path desc=[linear] ed_desc=[hole depth occurrence]
sar 1 name=[diameter] desc=[profile usage]
closed circular profile desc=[boundary] ed_desc=[diameter occurrence]
sar 2 desc=[hole bottom usage]
unrecongized aspect desc=[conical] ed_desc=[bottom condition occurrence]
feature depth: 25
feature orientation:
x-axis: 1 0 0
y-axis: 0 1 0
z-axis: 0 0 1
origin: 100 40 25
------------------------------
Tools: 1 present
[0] type: 12.7000 mm TWIST_DRILL (id #32)
name: TL DRILL-2
diameter: 12.7
edge (flute) length: 21.1845
edge radius: 0
circumference angle: 0

## Slide 14: Moving Forward
STIX
COM
Application
Indexing
Interface
Concept Library
data
STEP for the breadth of Manufacturing
  Next level of optimization using information compilation
  Machine independent CNC control data
    Milling, Turning
    Inspection, Robotics
Manufacturing Control