## Slide 1: Evaluator-enabled AP-238
Chen-Han Lee

## Slide 2: Problem Statements
STEP and STEP-NC are data standards and don’t provide the “methods” to evaluate geometry and machine the part.
Actual processing must be done in the native modes of commercial systems that provide the “methods”.
Invocation of any commercial system involves a round trip translation and translation causes data loss and distortion.

## Slide 3: An Example
Modeling
Data in
ABC
AP-203
Modeling
Data in
DEF
Process
Data in
XYZ
Process
Data in
PQR
AP-238
Modeling
Data in
GHI
The following illustrates the stages of data translation using the Super Model project as example.
ST-Plan
ST-Machine

## Slide 4: Modeling Data Loss
In the previous page, the same modeling data is translated 4 times (ABC AP203 DEF AP203 GHI), even though the 3 modeling engines ABC, DEF, and GHI may be the same.
Translation jeopardizes the high precision of models, especially when the underline geometrical representations are different.

## Slide 5: A Key Observation
In manufacturing applications (such as Super Model), we only need to access (evaluate) the modeling data and rarely modify it.
All we need is a set of functions/methods (API) to evaluate the geometrical data and don’t care about how the modeling data is constructed.

## Slide 6: Evaluator Approach
Define a standard set of (portable) Evaluator API for modeling data.
The CAD data comes with the “methods” (API) from the black-box engines.
It guarantees that all CAD data are evaluated (through the standard API) in the native mode.

## Slide 7: AP-238 with Evaluator
AP-238 allows the attachment of Evaluator API for the CAD data.
AP-238
AP-203
Evaluator
API
Native (black-box)
CAD Engines
STIX
Applications

## Slide 8: Similar Problem with CAM
Again, STEP-NC doesn’t provide the “methods” to machine the part.
Problems with the compatibility/interoperability between on-line/off-line CAM systems.
Data loss from the translation between AP-238 and commercial CAM systems.

## Slide 9: Generator Approach
For an application like ST-Machine, all we need is a set of methods to compute the toolpaths (from the given operations).
How about define a standard set of API for toolpath “Generator”?
The CAM data comes with the Generator API for the black-box engines.

## Slide 10: AP-238 with Generator
AP-238 allows the attachment of Generator API for the CAM data.
AP-238
AP-203
Evaluator
API
Native (black-box)
CAD Engines
STIX
Applications
Generator
API
Native (black-box)
CAM Engines

## Slide 11: How about CNC?
Follow the same thinking, we can define a set of “Control” API to drive the machine tools (from the given toolpaths).
Hopefully the efforts of OMAC may lead to this eventually.
It’s a little easier to push for a standard API than a standard data format.

## Slide 12: Summary of Benefits
Minimize or eliminate the data loss from translation.
Empower STEP/STEP-NC with methods.
Turn STEP/STEP-NC competitors into allies.
Get out of the business of defining every detail of the data.
  Manufacturing data is too semantic and diverging.