## Slide 1: AP-238 Status
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Resolving the
Remaining Feature
Harmonization Issues

## Slide 2: Remaining Issues
During Seoul meeting, all CD ballot comments were examined and resolutions agreed upon.
  Still need technical fix for transition feature.
  Some additional, subtle issues revealed during DIS prep and by implementation tests.
Structural Issues
  Structure of features are different.
  Transition features relating two sets of geometry faces vs. relating two other features
Subtle Issues
  Structures are the same, but values differ.
  Placements and description of the volume to be removed by feature.

## Slide 3: Structural Issue — Transition Feature
KR2,4
  Accept. Resolution still open.
  Current AIM mapping relates the transition feature to a face shape representation.
  Desired target is a shape aspect, but we need to do this in a way that doesn’t conflict with the existing ap224 style relationship.
  Len, Dave and SC1 will continue to discuss specific technical approaches.
14649 Transition
feature
feature
224-style Transition
set of faces
set of faces

## Slide 4: Subtle Issues
During comment resolution and implementation tests, several subtle issues became clear.
  Issues where structures are the same, but values differ.
    Placements
  Issues where some extra information may be needed.
    Not enough information to determine the volume of material to be removed for a feature.
All of the subtle issues are related to the volume to be removed by a feature.

## Slide 5: Feature Volume
To manufacture, need to know the boundaries of the as-is material, if you don’t know, you must be conservative.
  Assume material extends to the edge of the original stock.
  Wastes time milling air.
  Feature data in AP-224 concerned with the to-be shape remaining on the part. Volume to be removed unclear in several cases.
  ISO 14649 uses some extra attributes and conventions to clarify that volume. May not be sufficient in some cases.
Discuss how to communicate that volume.
  Some features may require more information?
  Proper place in AIM?

## Slide 6: In-Process and Final Features
An AP-238 model has the notion of final feature and in-process feature
  Final feature is on final part, from upstream, possibly from an AP-224 or AP-240 application. As such, some features might only define a volume when combined with the stock.
  In-process features are the features pointed to by ISO 14649 workingstep. Specific to a workplan, needs full volume limits.
  AP-238 workingstep points to in-process feature and final feature that it contributes to. Many workingsteps and in-process features may contribute to one final feature.
Final feature in red (POCKET)
In-process features to:
- Drill the corners (HOLE)
- Mill out center with large tool (POCKET)
- Mill remaining material
with smaller tool (???)
(what is the feature for the last?)

## Slide 7: ISO 14649 Conventions
ISO 14649 tried to address volume by adding a depth attribute to all features.
  Information already well defined in AIM for some (hole, pocket) but doesn’t address material to the sides (outside profile, step)
Also plays with placement to indicate material
  AP-224-style features usually give location on to-be shape.
  ISO 14649 features usually give location on as-is shape.
We will look at each feature in detail.
planar face removal volume
AIM
placement
ARM
placement
ARM
depth

## Slide 8: Round Hole
ARM attributes
  placement (at top pointing up)
  diameter
  depth
AIM entities
  placement (at bot. point up)
  circular closed profile, has diameter property
  linear path, has distance property for depth.
  compute by sweeping circular profile along path distance.
  bottom condition is extra removal added at the end of the path.
Volume
path
bottom condition
ARM origin
AIM origin

## Slide 9: Closed Pocket
ARM attributes
  placement (at top pointing up)
  closed profile
  depth
AIM entities
  placement (at top pointing down or bottom pointing up)
  closed profile
  linear path, has distance property for depth.
  closed pockets use more types of profile than holes, but otherwise compute the volume in the same way.
  pocket bottom condition is added at the end of the path. (See discussion on next slide)
Volume
path
bottom condition
ARM origin
AIM origin

## Slide 10: Pocket Bottom Condition
AIM approach adds the pocket bottom condition to end of path.
  Same as holes.
ARM assumes bottom condition already added into the depth (maximum feature depth)
  Not consistent with handling of holes.
  Not practical for general pocket bottom, since you need to compute lower boundary of surface and “backup” to find out the placement.
  ARM makes general pocket bottom into separate region feature, probably to get around this. Not harmonized with the AP-224 feature set.
Handle AIM-style and compute ARM depth value if needed.
  May need to add a property to the new ISO 14649 radiused pocket bottom condition.

## Slide 11: Pocket Placement
AIM / AP-224 lets orientation go out or in.
  At bottom with Z axis out (OR)
  At top with Z axis in.
  Neither is satisfactory. Want the placement at the top with the Z axis away from the material.
  Bottom is flat, general, or through. 224 doesn’t say how depth contributes to it, but guess intent is end of depth path as with hole.
ARM has origin at top pointing out
AIM recommendation
  Place at bottom with Z axis pointing up.
  Apply transform in code if ARM version is desired.

## Slide 12: Slot
ARM attributes
  placement (not well defined)
  course of travel
  open profile
  depth
AIM entities
  placement (Z along path)
  course of travel
  open profile
  Calculate the depth by using the placement and the profile limit property on the open profile.
  slot end conditions?
Volume
path
end condition
AIM origin
ARM
origin
profile limit

## Slide 13: Slot Placement
AIM origin at one side of slot
  Z axis points along slot
  Y axis points up and out
  This is so that the origin of feature and profile can be the same. (Profile is XY, with Y pointing up and out.)
  Placement is at bottom of slot, where the profile origins are.
ARM
  Course of travel says that it is placed at the top of the material, but does not say how the cross section is related. Presumably the profile is translated down by “depth”
  Says that travel path lies in the XY plane, which can be interpreted to mean that Z points up out of the slot.
AIM recommendation
  Place at bottom with Z axis pointing along travel path.
  Set open profile “profile limit” attribute to the top of material.
  Apply transform in code if ARM version is desired.

## Slide 14: Open Pocket
ARM attributes
  placement (at top pointing up)
  open profile (sweep)
  open profile (wall, optional)
  depth
AIM entities
  placement (at top pointing in or bottom pointing up)
  open profile
  linear path, has distance property for depth.
  pocket with open profile handled the same as closed. Use profile limit on the open profile to find the edge of material removal.
  Operations have parameters for overcut allowance.
  Note that in both ARM and AIM styles the open edge is only ever a plane.
  Wall profile gives no new information. Do not use.
Volume
path
bottom
condition
wall
profile
profile
limit
on open
profile
open
profile
ARM origin
AIM origin

## Slide 15: Planar Face
ARM attributes
  placement (at top of material)
  course of travel
  linear profile
  face boundary
  depth
AIM entities
  placement (at final surface)
  course of travel
  linear profile
  face boundary
  removal direction
  How do we get the depth?
  Removal direction element?
    Already seems to be implied by constraint on Z axis in 224.
  Face boundary provides outer limit of material removal.
Volume
path
AIM origin
ARM
origin
face boundary
profile
depth??

## Slide 16: Planar Face
Need some way of encoding the depth of removal the AIM.
  A new “maximum material limit” element
    that is a plane?
    A linear path component just like pocket and hole?
    A linear profile placed appropriately?
  AP-224 has “maximum feature limit” plane, is this the intent?
path
plane?
linear path?
linear profile?

## Slide 17: Outside Profile
ARM attributes
  placement (at top of material)
  feature boundary (profile)
  linear path
  depth
AIM entities
  placement (at final surface)
  boundary profile
  linear path, has distance property for depth.
  How do we get the surrounding material limits?
  Add material extent profile?
  ARM depth attribute redundant?
Volume
profile
ARM
origin
AIM origin
path
surrounding material?

## Slide 18: Outside Profile
AIM
  Z axis toward direction of travel of profile. (bottom pointing up, or top pointing down)
  Y axis points away from the part (confirmed by profile_feature)
  Placement is on the boundary
ARM
  Talks about material being to left of part as you go around the profile, but that is not really well defined since we don’t know the directions for profiles.
  Placement is not clear, from diagram appears to be opposite side of linear path.

## Slide 19: Shape Profile
ARM attributes
  placement (at top of material)
  boundary profile
  linear path
  floor condition
  removal direction vector
  depth
AIM entities
  placement (at final surface)
  boundary profile
  linear path
  floor condition
  removal direction vector
  Same issues with placement and surrounding material limits.
Volume
floor condition
profile
ARM origin
AIM origin
path
surrounding
material?

## Slide 20: Shape Profile
What is the difference between an outside profile and a shape profile with a through bottom condition?
AIM
  Placement is as with outside profile, with Y pointing out.
ARM
  Shows placement on boundary with Y pointing into material

## Slide 21: Step
ARM attributes
  placement (at top of material)
  vee profile
  open boundary (linear path)
  depth
AIM entities
  placement (at vee vertex)
  vee profile
  linear path
  How do we get the surrounding material limits?
Volume
profile
ARM origin
AIM origin
AIM path
ARM path
ARM depth

## Slide 22: Step
AIM defines placement as placement of profile
  Origin is vertex of the profile
ARM defines placement at top of material
  Displacement of profile origin is given by depth.
    Presumably you need to factor in angle of profile if not 90deg to offset the profile horizontally
a
a- 90
offset
Tan(a-90) * offset

## Slide 23: Depth and Width
Use profile limit?
  can only describe a plane.
  can angle plane so that it clips both axes of vee in appropriate places, but this seems pretty indirect.
Other mechanisms
  Use profile limit plane to trim one arm and maximum feature limit plane to trim the other?
offset
depth

## Slide 24: Spherical Cap
ARM attributes
  placement (center of sphere)
  radius
  internal angle
  depth
AIM entities
  placement (center of sphere)
  radius
  internal angle
  How do we get the surrounding material limits?
  Angle measured from X axis, but in what plane? XY or XZ? Neither spec very clear.
  Material limits to top and sides?
    Similar to a boss on a planar face, so use profile and plane limits like with that?
Volume
angle?
origin
radius

## Slide 25: Rounded End
ARM attributes
  placement (not clear)
  course of travel
  partial circular profile
  depth
AIM entities
  placement (center of arc)
  course of travel
  partial circular profile
  What is the ARM depth?
    radius of profile?
    length of path?
  How do we get the surrounding material limits?
  Material limits to top and sides?
Volume
profile
origin
travel path

## Slide 26: Rounded end
AIM
  Placement at center of arc. Z points into the material. It is almost like a “positive slot”.
ARM
  Same as AIM, which is inconsistent with the other ARM features, which have Z pointing out of the material.
Material limits all around?

## Slide 27: Transition feature
No placement
  Determine placement from related faces/features
Material extent?
  Extend underlying faces/features to define volume?

## Slide 28: Other Features
Compound Feature
Replicate Feature
Region / General Removal Features?
  May need to know material extent in any direction.

## Slide 29
Review of Profile Placements
and Parameters

## Slide 30: Locations and orientations
All features, paths, and profiles have a placement
  Feature placement is required
  Path placement is optional, gives location relative to the feature placement. Defaults to feature placement.
  Profile placement is optional, gives location relative to the path placement. Defaults to (path or feature?) placement.
  Some mappings mandate a particular placement
feature placement
path placement
direction
distance
profile placement

## Slide 31: Travel Paths
Linear path
  distance from origin
General Path
  Origin for curve
  Normally a bounded curve, although AIM also allows an edge curve or a path containing a list of oriented edges.
path placement
direction
distance

## Slide 32: Circular Paths
Partial and complete circular paths
  origin is from center
  Radius and swept angle (for partial)
  Where the swept angle starts/ends is not clear in either ap224 or 14649. From partial circular profile, we can infer that one end must be on X axis.
    Assume start on X axis, sweep towards positive Y as per right-hand rule.
placement
radius
radius
x
Y
sweep

## Slide 33: Profiles
AP-224 defines all profiles to lie in the XY plane of its placement
ISO 14649 either:
  Does not define where the origin of the profile lies (most)
  Or defines them to be in the YZ plane! (general profile, tee profile diagram)
Directive: Use the XY plane.
  Submit comment against the 14649 docs to clean this up

## Slide 34: Open Profiles
Rounded U Profile
  According to 224, origin is in the center on the arc, with the X axis tangent and the Y axis pointing up out of the profile.
  14649 does not state.
Square U Profile
  According to 224, origin is center of base. Profile is in the XY plane, with the base aligned with the X axis and the Y axis pointing up out of the profile.
  14649 diagram shows Z instead of Y! Text does not state.
Vee Profile
  According to 224, origin at intersection of two sides. Opening is in Positive Y direction. Tilt angle measured from X axis to nearest side, profile angle measured between two sides.
  Note that if a radius is given for the bottom, the profile will not reach all the way down to the origin.
  14649 does not state

## Slide 35: Open Profiles
Tee Profile
  According to 224, origin is center of base. Profile is in the XY plane, with the base aligned with the X axis and the Y axis pointing up out of the profile.
  14649 does not state
General open boundary
  orientation defined by curve
  14649 says YZ plane, but 224 says XY!
“Tee” Profile

## Slide 36: Open and Closed Circular Profiles
Circular profiles
  Handle as with circular paths. Origin at center, sweep angle from the X axis as per right-hand rule.
  Partial circular open profile has radius.
  Circular closed profile has diameter.
Partial
Circular
Circular
Closed

## Slide 37: Closed profiles
Rectangular profile
  origin in center of rectangle
  X axis parallel to length, Y axis parallel to width.
Ngon profile
  origin in center of ngon.
  X axis parallel to one side crossing -Y axis.
General closed profile.
  orientation defined by curve
  14649 says YZ plane, but 224 says XY!