## Slide 1: Update on the Standard for the Exchange of Product Model Data – STEP ISO 10303-224
Dr. Bill Freeman Mr. Len Slovensky
(843)760-3791 (513)383-8311
freeman@scra.org slovensky@scra.org
www.nist.gov/sc5/soap/
www.isg-scra.org
Presented to:
TC184/SC4/WG3/T24
manufacturing

## Slide 2: Explicit base shape representation
Explicit_base_shape_representation
    Information to indicate type of explicit shape, for example:
      Machined from Forgings and Castings
      Machined from Aluminum Plate or Block (Hog Out)
      Machined from Aluminum Extrusions
Notes: The explicit base shape has additional information to indicate if the base shape is a casting, forging, etc.
This will assist the down stream process planning determine with addition information about the initial shape of the stock.

## Slide 3: Standard Part fasteners (AP224 3rd edition)
Assembly of parts for manufacturing process
  Add standard part fasteners to the mating definition
  AP224 will reference a parts library (PLIB) that contains fasteners definitions
Notes: A reference to a Parts Library (PLIB) will allow the use of standard fasteners for assemblies. Examples of Fasteners would be bolds, screws, washers, etc.
AP224 defines the mating condition where two parts interact with one another. This mating condition could be a nut and bolt fastener, with a definition of the nut and bolt found in PLIB.

## Slide 4: Gear feature (AP224 3rd edition)
Bevel gear
Spur gear
Helical gear
Notes: The gear feature has been added as a new AP224 feature.
Breakdown of gear types
– Spur gears / gearshafts
– Helical gears / gearshafts
– Bevel gears / gearshafts
– Worm gears / gearshafts
– Gear quadrants
– Racks & pinions
Focused on Spur, Helical, and Bevel. They are the most common and represent a high percentage of
Gears being manufactured.

## Slide 5: AP224 3rd edition schedule
AP224 3rd edition and AIC522 2nd edition documents complete
  Internal review – underway (UK)
  Project review – underway (US)
DIS ballot start before October ISO meeting