## Slide 1
AP224 edition 3
Alan Crawford
Tuesday 24th June 2003
Stuttgart
Notes: 2

## Slide 2: Review of UK Naval Spares Inventory
Total number of units in store around
6,000
Total value of stored units around
£4,000,000

## Slide 3: Review of UK Naval Spares Inventory
Breakdown of gear types
  Spur gears / gearshafts
  Helical gears / gearshafts
  Bevel gears / gearshafts
  Worm gears / gearshafts
  Gear quadrants
  Racks & pinions

## Slide 4: Stores Held vs Type

## Slide 5: Stores Held vs Type

## Slide 6: Stored Unit Costs vs Type

## Slide 7: Stored Unit Costs vs Type

## Slide 8: Review of UK Naval Spares Inventory
Ranking of types according to Naval requirements
  Spur gears
  Helical gears
  Bevel gears
  Worm gears
  Racks / pinions
  Gear quadrants (various forms)

## Slide 9: Suggested Scope
Based upon analysis & technical ease of representation within AP224
  Spur gears / gearshafts
    > 50% store cost
  Helical gears / gearshafts
    20% store cost
  Others represent < 10% store cost each

## Slide 10: Suggested Scope
Tooth Form
Involute
  Most common form
    Fully defined by reference to rack
    Cutters can be cheaply produced
    Easy to obtain correct intermeshing
    Tolerant of centre distance variations

## Slide 11
Gear Types
Spur and helical gears
  Broadest application domain
    Parallel shafting gear trains
    Wide range of velocity ratios
    High speed and load capacities
Consideration in representation to be given to future extension to include other gear types

## Slide 12: Overview of representation of spur & helical gears
Specification of basic geometry
  Number of teeth z
  Normal module mn
  Reference pressure angle α
  Rack shift factor x
  Nominal tooth depth h/mn
  Face width b
  Tip diameter da
Not dissimilar to (but more complex than) data required to specify screw threads, knurls

## Slide 13: AP224 Gear Feature
Scope...
  Cylindrical gears
  Involute teeth
  Spur & helical form
Source information...
  ISO 1122-1: Definitions related to geometry
  Symbols consistent with AGMA & ANSI

## Slide 14: Requirements
Master parameter set
Spur gear parameters
Helical gear parameters
Derived parameters
Gear modifications
Feature application requirements

## Slide 15: Master Parameters (1 of 5)
pitch_diameter (D)
  The diameter of the pitch circle
  Use pitch diameter to derive diametral or circular pitch values

## Slide 16: Master Parameters (2 of 5)
root_diameter (DR)
  The diameter formed by the “bottom land” between teeth
outside_diameter (Do)
  The diameter formed by the tips of the teeth
Notes: d

## Slide 17: Master Parameters (3 of 5)
pressure_angle ( )
  The angle subtended by a tangent to the tooth profile and a radial line, at its pitch point

## Slide 18: Master Parameters (4 of 5)
root_fillet_radius ( )
  The radius of the fillet between the flank and the root circle

## Slide 19: Master Parameters (5 of 5)
number_of_teeth (N)
  Clearly a fundamental parameter
internal_or_external_gear
  Special property of spur and helical gears that they may be internal or external

## Slide 20: Spur Gear Parameters
Spur gears require no additional parameters to those defined by the supertype

## Slide 21: Helical Gear Parameters (1 of 2)
left_or_right_twist
  The helical twist is defined as begin either left or right according to the right hand rule

## Slide 22: Helical Gear Parameters (2 of 2)
helix_angle (Ψ)
  The angle between the tangent to the to a helix and the straight line generator of the cylinder on which it lies

## Slide 23: Derived Parameters (1 of 3)
diametral_pitch
  The number of teeth per unit length along the pitch circle (spur gear)
circular_pitch
  The distance along the pitch circle between corresponding flanks of adjacent teeth (spur gear)
Notes: d

## Slide 24: Derived Parameters (2 of 3)
axial_pitch
  The distance between corresponding points of adjacent teeth measured parallel to the gear axis (helical gear)
  Normal diametral and circular pitches can also be derived for helical gears

## Slide 25: Derived Parameters (3 of 3)
base_diameter
  Diameter of the imaginary base circle from which the involute geometry of a tooth profile is defined

## Slide 26: Gear Modifications (1 of 6)
Tip relief...
  Removal of material at the tip of the tooth
  Parameterise?

## Slide 27: Gear Modifications (2 of 6)
Root relief...
  Removal of material at the root of the tooth
  Parameterise?

## Slide 28: Gear Modifications (3 of 6)
End relief...
  Linear or progressive reduction of tooth thickness towards each end face of a gear
  Parameterise?

## Slide 29: Gear Modifications (4 of 6)
Undercutting...
  Facilitates subsequent machining operations
  Parameterise?

## Slide 30: Gear Modifications (5 of 6)
Crowning...
  Progressive reduction of tooth thickness towards each end face of a gear
  Parameterise?

## Slide 31: Gear Modifications (6 of 6)
Corrected pinions...
  Improves meshing of pinions with a small number of teeth
  Parameterise?

## Slide 32: Feature Application Parameters
applied_shape
  Specifies the physical shape of the part that defines where the gear feature will be applied
partial_profile
  Specifies the limitations to be applied on the gear feature.

## Slide 33: Feature Application Parameters