## Slide 1: AP-238 DIS Walkthrough
STEP Tools, Inc.
216 River Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Poitiers SC4 Meeting
October 2003

## Slide 2: Document Status
Integrating comment resolutions and preparing DIS document for ballot.
  In response to comments, added UoFs for requirements beyond ISO 14649, and also to support turning model.
  Completed mappings for toolpath subtypes.
  Updated transition feature mappings to support both styles of relation: two features (Part 10), two face sets (AP 224/214)
  Updated adaptive_control based on Seoul discussions.
  Turning model mostly complete.
  Many editorial fixes, mapping table fixes.

## Slide 3: Document Status
GD&T
  Add AOs and mappings for harmonized Dimensional Tolerances once consensus has been reached between Module, AP-214 and AP-224 teams.
PDM information
  As per comments, added “management” UoF with AOs and associated mappings to clarify the handling of approvals and other PDM data.
  approvals (details use of approval IR element in 14649-10, harmonized with module 1012)
  security classification (harmonized with module 1015)
  timestamp for certain process elements (as per OMAC comments)

## Slide 4: AP-238 Units of Functionality
Current UoFs (red are new)
  measure
  project
  workpiece
  manufacturing feature
  executable
  toolpath
  process data for milling
  cutting tools for milling
  manufacturing feature for turning >> Part 12
  process data for turning >> Part 12
  cutting tools for turning >> Part 121
  measurement limits >> GD&T
  management >> PDM

## Slide 5: Toolpath ARM
toolpath
feedstop
parameterised
path
trajectory
cutter location
cutter contact
axis
STEP-NC Toolpaths
Toolpath has an enum attribute called its_type with values:
approach, lift, connect, non_contact, contact, trajectory_path
What does this mean?
approach lift path
connector
connect secplane
connect direct
Class structure also seems to imply some of these “types”
A/L angle
A/L tangent

## Slide 6: What is the meaning?
The attribute seems to be giving some indication of how the movement is used
Class structure does some of this too, but also indicates mathematical representation of path.
No constraints on usage of attribute
  connector entity with attribute = “approach”
  approach_lift entity with attribute = “connect”
  etc.
Suggestions
  At the very least, change name of attribute to something more descriptive than “its_type” and indicate the relative roles of the class structure vs this attribute.

## Slide 7: Toolpath AIM Representation
machining_toolpath
action_method
ARM Toolpath and subtypes are mapped to AIM machining_toolpath.
  Toolpath base class was already completely mapped.
  Added mapping table entries and corresponding AIM EXPRESS local rules for the subtypes.

## Slide 8: Turning Process Data
Adding support for the turning parts
  Part 12 (version 12)
  Part 121 (version 9)
Updates almost complete
  Mappings are straightforward and follow conventions established by the mill/drill mappings.
  Added UoFs, mapping tables, and updated AIM where rules for the turning model, updated in long/short forms, and clause 5.2 AIM entity descriptions.
  The EXPRESS rules for some of the representation subtypes began to get a bit lengthy, so I abstracted the common idioms into new EXPRESS functions:
    verify_[optional/required]_rep_item
    verify_[length/angle]_measure_rep_item.

## Slide 9: Turning Operation AIM
machining_operation
milling_type_operation
drilling_type_operation
action_method
turning_type_operation
Several Subtypes
Turning operations represented using several new AIM subtypes
  As with milling/drilling, attributes represented using a collection of action properties.

## Slide 10: Turning Strategies AIM
machining_strategy
milling_type_strategy
freeform_milling_strategy
drilling_type_strategy
machining_approach_retract_strategy
action_method
machining_technology
machining_functions
turning_type_strategy
Turning strategy represented using a new AIM subtype.
  Same techniques as with milling/drilling strategies
  Part 12 references existing approach/retract strategies

## Slide 11: Turning Tech and Functions AIM
action_method
machining_technology
machining_functions
Turning technology and machining functions did not require any new AIM types.
  Milling technology/functions already distinguished by an action_method.description of “milling”.
  Use action_method.description of “turning” to distinguish the turning technology/functions.
  Many properties are common between milling/turning versions. AIM EXPRESS rules simplified.

## Slide 12: Cutting Tools for Turning ARM
tool_body
turning_tool_dimension
machining tool
cutting tool
turning machine tool
turning machine tool body
Referenced From Operation
Part 10
Part 121
Very similar to Part 111 organization
Not as many tool body types
Several Subtypes
Grooving, Knurling, Threading, General
and User Defined

## Slide 13: Turning Tool AIM Representation
action_resource
action_resource_type
Required equipment
Turning tools did not require any new AIM types
  Use action resource subtype machining_tool for the ARM turning_machine_tool concept.
  Has a “kind” attribute that categorizes the resource
    We use value “milling cutting tool” for Part 111 data
    Now add value “turning cutting tool” for Part 121.
machining_tool
kind

## Slide 14: Turning Tool Body and Dimension AIM
S[1:?]
representation_items
representation
representation_relationship
No new AIM types needed for body or dimension
  Use existing representation subtypes developed for Part 111
  As with all of our complex types, properties handled as various representation items within.
  Distinguish tool bodies using the representation.name
  Distinguish milling/turning/other tool dimensions using representation.name “milling”, “turning”, etc.
machining_tool_dimension_representation
machining_tool_body_representation
items

## Slide 15: Turning Features
manufacturing
feature
machining
features
2.5D manufacturing
turning feature
replicate
feature
cut_in
STEP-NC Features
outer diameter
revolved feature
outer round
groove
general revolution
revolved round
revolved flat
knurl
outer diameter
to shoulder
Turning features now appear to be harmonized between Part 12 and AP-224/AP-214
Will verify this as I incorporate the harmonized mappings for turning features from AP-224
diagonal knurl helix hand?
tool knurl == catalog knurl?

## Slide 16: Knurl Subtypes
Part 12
diagonal_knurl
  helix_angle
diamond_knurl
  helix1_angle
  helix2_angle (if missing, same as ap224 representation
straight_knurl
tool_knurl
  no atts
AP-224
diagonal_knurl
  helix_angle
  helix_hand
diamond_knurl
  helix_angle
  (Is Part 12 richer with the helix2 att?)
straight_knurl
catalog knurl
  documentation

## Slide 17: Yet To Do
GD&T
  Add UoF and AOs for harmonized Dimensional Tolerances once consensus has been reached between Module, AP-214 and AP-224 teams.
Turning
  Turning features — Need to incorporate harmonized mappings for turning features from AP-224.
  Turning process — No technical issues, finish mapping table text and associated AIM EXPRESS where rules.
Other
  EXPRESS-G updates for adaptive control change, new turning operation & several new turning representation AIM subtypes.
  Trim AIM SELECT type values not referenced by any of the mappings (as per ballot comments)
  Document CC 1-3