## Slide 1
Overview of ASAM ODS
Introduction
The ASAM Standards
The ODS Base Model
The Measurement Data Model
The ASAM ODS specification
ISO TC184/SC4 Meeting June 2003, Stuttgart
Gerald.Sammer@avl.com
AVL List GmbH
ASAM e.V.

## Slide 2
Data acquisition systems, collecting data from a vehicle, an engine, etc.
Test control systems, used for running test procedures
Optimization tools, looking for an optimum set of calibration parameters
Analysis and reporting tools, presenting data to engineers and decision makers
Evaluation tools, supporting research and development tasks
ASAM ODS describes service interfaces. They can be used by any component of the testing environment to store its data and/or retrieve data required for proper operation.

## Slide 4
ASAM ODS
Open Data Services
defines interfaces for storage, interpretation and exchange of test and measurment data
Not restricted to automotive industries

## Slide 5
Test Bench
Road Test
Crash Test
ISO TR 13499
Engine Test
Where does ASAM ODS help ?

## Slide 6
Application A
Application B
Technical data
Meta information
The basic idea

## Slide 7
RDBMS
Access Layer (phys. Storage)
Application Model
Application Programming Interface
ASAM ODS BASE MODEL (STEP EXPRESS)
Application
Physical Data Storage
Flat
Files
ASAM
Transport
Format
Mixed Mode
Meta
Information
Flat
Files
ASAM ODS Architecture

## Slide 8
ODS Base Model
ODS Application Model
The application model is derived from the base model
Each application entity must be derived from one of the entities defined in the base model
The application entities can be extended with additional application attributes not defined in the base model
The application entities can be extended with additional application relations not defined in the base model
ASAM ODS Application Model

## Slide 9
ODS Base Model
Engine Test
Model
Crash Test
Model
NVH
Model
ASAM ODS Application Model - Examples

## Slide 10
Derive your specialised ODS-Application-Model from the ODS-Basemodel
AoMeasurement
AoUnitUnderTest
AoUnitUnderTestPart
Acquisition
Vehicle
Crankshaft
Cylinder
Engine
Tire
Gearbox
Base Model
Application Model

## Slide 11
Application Entity
Base Entity
Database Table
Persists as
Is derived from
ASAM ODS Programming Interface (API)
Application Entity
ASAM ODS Server Application
Transfer to Client
ASAM ODS Client Application
Implementation View
ASAM ODS Base Model
Base Entity
Refers to

## Slide 12
A data model that covers the aspects that the data used in measurement and testing technology have in common
Management Data
Descriptive Data
Security
Quantities and Units
Measured Values
Others

## Slide 13
AoUnit
AoQuantity
AoQuantity
Group
AoUnit
Group
AoPhysical
Dimension
AoMeasurement
AoMeasurement Quantity
AoSub
matrix
AoLocal
Column
AoTest
Abstract
AoTest
AoSubTest
AoUnitUnderTest
Abstract
AoUnit
UnderTest
AoUnit
UnderTest
Part
AoTestSequence
Abstract
AoTest
Sequence
AoTest
Sequence Part
AoTestEquipment
Abstract
AoTest
Equipment
AoTest
Equipment
Part
AoAny
Quantities and Units
Descriptive Data
Others
Management Data
Measured Values
AoTest
Device
Security
AoUser
AoUser Group

## Slide 14
AoEnvironment
AoTest
AoTestSequence
AoTestEquipment
AoUnitUnderTest
AoMeasurement
AoMeasurementQuantity
AoSubmatrix
AoLocalColumn
AoTestDevice
AoUnit
AoPhysicalDimension
AoTestEquipmentPart
AoUnitUnderTestPart
AoTestSequencePart
AoSubTest
AoQuantity
AoExternalComponent
Note: Not all entities and references shown

## Slide 15
Base Attributes
asam_base_entity
Each base entity is derived from the super type asam_base_entity
There are a set of attributes which are included in each entity, like:
  Id (a serial integer)
  Name (a unique name)
  Description (optional)
  ...
id
INTEGER
STRING
name
version
description
AoMeasurement
t_date
Measurement_begin
Measurement_end
t_id

## Slide 16
Measurement Data Model
A measurement consists of a set of one or more submatrices
Submatrices are homogenous matrices consisting of a set of columns (channels)
Channels measured with different frequencies are kept within seperate submatrices
The actual measurement values are kept in the list of Values of type value_sequence which is a super type for all valid ODS data types.
AoMeasurement
AoMeasurementQuantity
AoSubmatrix
AoLocalColumn
value_sequence
Values L[1:?]

## Slide 17
Measurement Data Model - Example
Model View
Independent channel of submatrix 1
Independent channel of submatrix 2
Logical View
Logical measurement matrix constucted by merging matrix1 and 2 according to the independent channel

## Slide 18
Measurement Data Model - Advantages
AoMeasurement
AoMeasurementQuantity
AoSubmatrix
AoLocalColumn
Because submatrices are homogenous they need less database space and network bandwith
Submatrices are transfered faster over networks
No redundancy in measurement data instances
The application can decide whether to merge the matrices or process them independently
value_sequence
Values L[1:?]

## Slide 19
ODS
ODS-Clients, each coming from different Vendors
ODS Server: publishes the ODS Applicationmodel containing the data of the testruns on the testbeds, parameters, etc.
ODS datasources: e.g. engine testbed-systems (also ODS clients) coming from different vendors
ODS Server
ODS Clients
ODS
ODS
Example implementation
ODS Clients

## Slide 20
Product Demonstration
PUMA
Model
VDM
Model
Engine testing
Component testing
ASAM ODS Server
API
ASAM ODS Server
API
Base
Model
Client 2
Client 1
Base
Model
Base
Model

## Slide 21
The Specification
Chapter 1, Introduction to ASAM ODS
Chapter 2, ASAM ODS Architecture
Chapter 3, Physical Storage
Chapter 4, The Base Model (27)
Chapter 5, ATF 1.4.1
Chapter 6, ATF in XML
Chapter 7, Security
Chapter 8, Mime Types
Chapter 9, The ODS-API (RPC-Interface)
Chapter 10, The ODS-API (CORBA-Interface)