## Slide 1: XSTEP: STEP-NC Programming
Martin Hardwick
David Loffredo
Joe Fritz
info@steptools.com
STEP Tools, Inc.
14 First Street
Troy, NY 12180
http://www.steptools.com

## Slide 2: XDM-STEP demonstration
Tool to make it easy for users to get started with STEP-NC programming in AP-238.
Converts manufacturing command data.
Use with a simple GUI.
Optional
GUI
STEP-NC
Script
XDM STEP
AP-238
STEP-NC
data
AP2-38
Mapping
Tables

## Slide 3: The XDM STEP Process
The input can be
  ISO 14649 P21 file
  An AP-238 ARM XML File
The output can be
  AP-238 AIM P21 File (this is the standard)
  AP-238 XML Modules (this is the new standard)
ISO 14649
P21
XDM STEP
Pre-processor
AP-238
ARM XML
AP-238
ARM XML
XDM STEP
AIM Mapping
AP-238
AIM P21
Directory
XML
Modules
XML
Modules
XML
Modules
Basic condition for a single common standard.
AP-238 ARM XML is a 1 to 1 presentation of the current 14649 P21 ARM in XML format. It can only use implicit features.
Only the AIM data allows explicit features! It is possible to extract the ARM data from the XML modules in a fairly simple manner.
The common standard are the XML Modules.
A pre-processing (on the controller) step will allow to strip down all not needed data.
What data will be used depends on the implementation.
The XML Modules offers a wider range of data handling, incl. feedback data.
Modules can be used for repeating operations and be adapted by just changing the attributes.
Feedback will use the data management facilities of XML. Implementation dependent. No violation of the standard.
There is one XML Modele per ARM entity e.g. 1 workplan or 1 workingstep.
This can be in 1 or different files.
Each module contains the ARM and the AIM data.

## Slide 4: The Best News
XSTEP is free
XSTEP can be used to create data for ST-Machine
  STEP-NC Input for Mastercam
  STEP-NC Input for GibbsCAM
Simple
GUI
XDM STEP
ST-Machine for
Mastercam
ST-Machine for
GibbsCAM

## Slide 5: What’s Next
ST-Developer v11 will contain new C++ classes
  Big objects to represent ARM data
  Little objects to represent AIM data
  Code generated from the mapping table links the two
  STIX will be folded into Developer
ST-Machine will use XSTEP
  Current version reads STEP-NC data into a CAD system
  New version will add ability to edit the STEP-NC data