## Slide 1
Using EXPRESS-X Mapping language
Development of Feature Recognition
Contact:inouye@fqs.fujitsu.com Fujitsu STEP R&D Center Aug,20.2001
Fujitsu STEP R&D Center has MOU with EPM Technology A.S for technical cooperation and sales.
Feature recognition by Mapping technology using STEP/Express-X is quite useful, and it decreases a lots of coding works because the input is described by STEP.
Features are recognized by two step procedures in the points of schema and geometry. - Schema investigation(First point) - Geometry investigation(Second point)
To bush up the recognition level, more improvements testing a many sorts of practical data are necessary.
It seems that ARM like output may be useful than AP224 AIM considering today’s shop environment.
Summery
Most of the commercial CAD system have STEP geometry translators such as AP 203/214.
In these days, the seamless data transfer from geometry to manufacturing becomes hot focus, inspired by such as STEP/NC project. As the key technology, feature recognition from geometry data has an important role in these purpose.
This development is to make STEP/AP224 format data from an input of AP203 recognizing manufacturing features; - Input : STEP AP203 File - Output : STEP AP224 File - Using STEP/Mapping(EXPRESS-X)
Though as feature recognition, GSS in India is famous, the target in this project aims same and/or higher recognition level.
The development is also supported by ECOM/JSTEP activity.
EXPRESS-X(mapping) makes relationship between a target and a source schema using extended Express language. Using this technology, data translator can be realized.
Things to develop are as follows; - STEP schema - AP203->AP224 mapping schema including Feature Recognition - STEP Engine (From EPM)
A commercial EXPRESS-X engines are supplied from STEPtools, Inc(US), PDTech (Germany), EPM(Norway), etc. And EPM is the leading company in this area.
Outline
Configuration

## Slide 2
Using STEP AP224/AP240
STEP based Computer Aided Process Planning
Contact:inouye@fqs.fujitsu.com Fujitsu STEP R&D Center Jul,02.2004
This project is held under the assistance of MER supported by the ECOM and MSTC.
SCAPP Step based Computer Aided Process Planning system is developped how the STEP AP will contribute in manufacturing through design.
The system receives a Step file containing feature definitions,i.e AP224 file, and create process planning definition according to the AP240 specification. The system makes guidance for interactive macro process planning, and generates micro process planning, automatically,referencing the Manufacturing Technology Database.
The feature defined int AP224 step file is created by automatic feature recognition from geometry data in Step AP203/214 file.
Feature based Manufacturing Technology Database contains the data of cutting tools, workingsteps and realationships between feature and workingstep.
Outline
The system, for the first time, creates "feature dependency" for the basic plane to support feature assignment at the every process.
The system shows every candidate feature depending on the target plane for interactive macro process planning.
The system, as micro process planning, automatically decides a workingstep for each feature assigned according to the definition of Feature based Manufacturing Technology Database.
The system maps AP240 schema and create Step file using STEP/Express-X mapping language.
Features
SCAPP
Step based Computer Aided Process Planning has proved that the Step data can contribute seamless migration between design and manufacturing throughout the all stages.
Summery