## Slide 1: GD&T Harmonization Results Bath SC4 Meeting
David Loffredo
loffredo@steptools.com
2004-07-08
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax

## Slide 2: Progress During Week
Discussed and Resolved Incompatibilities
  Handling of value qualifications (range, plus/minus, etc)
    reviewing proposed change for value range, all other qualifications RESOLVED
  Types of dimensions identified: RESOLVED
  Mapping of envelope principle: RESOLVED
  Directed angular location, determination of angle orientation
    All models already harmonized. Continue to study ways to improve the ARM. Leave alone for now.
Discussed Big Picture Strategies for GD&T
  Linking of dimensions with the draughting presentation elements of the dimensions. Presentation Given
  Relationships with TC 10 and TC 213
  Developed response to TC-213 “expression of concern”

## Slide 3: Position Statement For TC-213
In response to TC-213 “expression of concern”:
We are happy to use TC 213 terminology, and note that we are already referring to 5459:1981 for the definition of Datum.
We ask TC-213 to point out areas where we differ and we will be happy to adopt their terminology.
  Already using the “Common_Datum” term as AIM entity defined in AIC 519
  Will change uses of “Compound Datum” term to “Common Datum.”
  Welcome the chance to meet for a harmonization workshop on an as-needed basis.

## Slide 4: Summary of Resolutions (1/2)
Value qualifications
  Limitation, agreement to clarify mappings in AP-224
  Plus/minus, agreement on separate representations for use inside and outside of dimensions. AP-214 to correct mappings inside dimension to make proper use of dimensional_size, add new mapping for use outside of dimensions
  Limits and fits, as with plus/minus
  Value range, still in discussion. Willingness from AP-224 to use value_range outside of dimensions, and extend ARM to support ranges for normal properties. AP-214 unsure about using two rep item approach inside of dimensions.
  Continue discussion on value range via email/conf call, once Max has had time to get additional input from his team.

## Slide 5: Summary of Resolutions (2/2)
Types of Size Dimensions
  Update AP-214, AP-224, and Module 1050 as follows:
  Expand list of specific size dimensions to the union of types in 224, 214 and those “hiding” under general_size.
  Rename general_size to externally_defined_size and add a document reference that calls out where it is defined.
    Upward compatible change to AP-214, 1050
Envelope Principle
  Update AP-214/Module 1050 AIM mappings to current AP-224 approach and will relax ARM to allow envelope on any size dimension.
  Update AP-224 ARM to restrict usage of envelope to size only by moving attribute in the ARM to size_dimension

## Slide 6: General Approach During Week
Reviewed ARM and AIM issues.
Surveyed the room for technical and business priorities and constraints.
Considered each issue to find options consistent with above priorities.

## Slide 7: Goals
Rank the following technical priorities so that we can evaluate our options
  Absolute minimal changes to existing standards
    May make standards more complex with alternate mappings. Benefits current implementations.
  Absolute minimal changes to existing implementations
    Standard may become more complex than above, even more benefits to current implementations. Minimize or eliminate change visible to implementers.
    Customers which would be disillusioned by any changes to the standard.
  Simplicity of resulting specification
    Consistent pattern so implementers know what to expect. Benefits adoption and future implementation.
    Also may encourage use in other contexts
    Minimize adoption time
  Accurate use of Integrated Resource semantics

## Slide 8: Positions
Person (Perspective) -- Prioritization of values
A - Min Change to STD, B- Min Change to Impl., C- Simplicity, D - IR accuracy
Bill Freeman (customer rep), Len Slovensky (224, 240, 223) - B, A, D, C
Sean Barker - D + Speed
Vanessa Lees (CTC) - D
Alan Crawford (224, customer rep)- Customer Impact (B), Credibility of STEP, Reuse of Existing Base
Martin Gibson - Customer Impact (B), Credibility of STEP
Max Ungerer (214, customer rep) - B (tolerances not implemented, but value ranges are implemented in other areas of the standard), A, speed, C, D
Tom Hendrix (203e2/modules) - D + Speed
King Yee (203e2/parametrics) - D + Speed, B
Chiakai Sakamoto (240) - B, A, D, C
Hiroyuki Hiraoka - C, Expandability
Vijay Srinivasan (TC213) - none of the above (IBM/Dassault) D + Speed
Friedrich Glantschnig (14649) - As with Alan Crawford above, push back any changes to IRs
Suk-Hwan Suh (14649) - C + Speed
Martin Hardwick (tool vendor) - Maximum new implementation => D, C, Speed
Ted Vorburger (219) - B, A, and to lesser extent D, C

## Slide 9: Analysis
B very important, D very important, Speed important
  A - Min Change to STD, B- Min Change to Impl., C- Simplicity, D - IR accuracy
AP-214 tolerances not implemented, but value ranges and limits are implemented in other areas of the standard
AP-224 tolerances implemented with all qualifications
  Plus/Minus most common
  range, limitation, limits and fits - how common?
AP-224 feature plus/minus widely used
  use of limitation outside of dimension - how common?
  does not support use of value range, limits and fits outside of dimensional tolerance

## Slide 10: Discussion Results
Value Limitation
Value Range
Plus/Minus
Limits and Fits
Set of Possible Size Dimensions
Envelope Principle
Angular Location Dimension

## Slide 11: Value Limitation Mapping
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
Dimension or property definition
on something
Adds qualified representation item to the
complex instance
type_qualifier
name = “maximum”
precision_qualifier
precision_value = 4
This approach is defined in both AP-214 and AP-224
Name of Limit
AP-214 specifies “maximum” or “minimum”
AP-224 does not specify string, but uses “MAX” and “MIN” in an example
Separate qualifier significant digits
Numeric value
for limit

## Slide 12: Value Limitation Resolution
AP-224 will clarify ARM by creating subtype of Tolerance_limit for:
  Maximum limit -- mapping will call out name=“maximum”
  Minimum limit -- mapping will call out name=“minimum”
  Other limit - mapping will leave name unconstrained.

## Slide 13: Value Range
AP-224 has no mapping for use of value range outside of dimension.
  Willing to adopt AP-214 usage in those cases.
AP-214 has mappings for value range but no vendor implementation within dimension.
  There are vendor implementations of value range outside of dimension

## Slide 14: Value Range AP-214 Mapping
representation
complex instance of
value_range
qualified_representation_item
name = “length”
For significant digits, a complex instance with qualified rep item is used, which points to a precision qualifier
complex instance of
measure_representation_item
length_measure_with_unit
name = “upper limit”
value = 100 mm
complex instance of
measure_representation_item
length_measure_with_unit
name = “lower limit”
value = 75 mm
Property definition
on product, feature, feature component, action, resource, or anything using a representation
precision_qualifier
precision_value = 4

## Slide 15: Value Range AP-224 Mapping
shape dimension
representation
Significant digits are related to each value separately using a measure qualification
complex instance of
measure_representation_item
length_measure_with_unit
name = “upper range”
value = 100 mm
complex instance of
measure_representation_item
length_measure_with_unit
name = “lower range”
value = 75 mm
dimensional_size
dimensional characteristic
representation
shape_aspect
geometry and placement
instances
measure_qualification
measure_qualification
precision_qualifier
precision_value = 4

## Slide 16: Value Range - Still In Discussion
Proposed solution is to use
  AP-214 value_range AIM mapping outside of dimensions
  AP-224 two rep item mapping inside of dimensions
Willingness from AP-224 to use value_range outside of dimensions, and extend ARM to support ranges for normal properties.
AP-214 unsure about using two rep item approach inside of dimensions.
  Max Ungerer wants to discuss this with his team.
  Continue discussion on value range via email/conf call, once Max has had time to get additional input from his team.

## Slide 17: Plus/Minus
AP-224 has implementation of both plus/minus mappings (in dimensions, in feature properties)
AP-214 has mappings for plus minus but no vendor implementation within dimension.
  No implementations outside of dimensions
  Mappings currently have an error that always requires the use of dimensional_size, even in a location dimension.
Module 1106 and 1050 mappings
  1106 has Plus/Minus for use outside of dimensions
    Adopt the qualified rep item mappings
  1050 has Plus/Minus for use inside dimensions
    Should have correct mappings, but derived from AP-214, so check to make sure that they do not have the same problem.

## Slide 18: Plus/Minus Resolution
Agreement on separate representations for use inside and outside of dimensions.
  See following slides for diagrams
AP-214 to correct mappings inside dimension to make proper use of dimensional_size, add new mapping for use outside of dimensions

## Slide 19: Plus/Minus Outside of a Dimension (1/2)
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
All other property definitions
on product, feature, feature component, action, resource, or anything using a representation
Adds qualified representation item to the
complex instance
standard_uncertainty
measure_name = “upper limit”
uncertainty_value = 0.001
standard_uncertainty
measure_name = “lower limit”
uncertainty_value = - 0.001
precision_qualifier
precision_value = 4
Points to separate qualifiers for upper,
lower limits and significant digits
NOT FOR USE WITH A SIZE DIMENSION OR LOCATION DIMENSION
(which are mapped to Part 47 dimensional_size or
dimensional_location)
This is an example with length, could be used for angles, times, velocities, etc. as supported by the range of things representable by measure_with_unit

## Slide 20: Plus/Minus Outside of a Dimension (2/2)
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
All other property definitions
on product, feature, feature component, action, resource, or anything using a representation
standard_uncertainty
measure_name = “upper limit”
uncertainty_value = 0.001
standard_uncertainty
measure_name = “lower limit”
uncertainty_value = - 0.001
precision_qualifier
precision_value = 4
This is current AP-224 representation.
AP-214 to add alternate mapping for use outside of dimensions when correcting mapping of plus/minus tolerance to dimensional_* entities
NOT FOR USE WITH A SIZE DIMENSION OR LOCATION DIMENSION
(which are mapped to Part 47 dimensional_size or
dimensional_location)

## Slide 21: Plus/Minus Using Dimension
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
value = 100 mm
precision_qualifier
precision_value = 4
dimensional_size
dimensional characteristic
representation
shape dimension
representation
shape_aspect
plus_minus_tolerance
tolerance_value
length_measure_with_unit
value = 0.001
length_measure_with_unit
value = - 0.001
lower_
bound
upper_bound
of_shape
Geometry and location
measure_qualification
measure_qualification
AP-214 current mapping always requires a dimensional_size, even if a location dimension
(need to fix mapping)

## Slide 22: Limits and Fits
AP-224 need information about implementation.
AP-214 has mappings for limits and fits but no vendor implementation within dimension.
  No implementations outside of dimensions
  Mappings currently have an error that always requires the use of dimensional_size, even in a location dimension.
AP-238 has requirement for use outside of dimension (as a property)
  Has developed mappings based on qualified rep item that follow the AP-224 plus / minus pattern.
Agreed to follow resolution adopted for plus minus
  Dave will email mapping paths for this to exploder.

## Slide 23: Limits and Fits Outside of a Dimension
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “diameter”
value = 100 mm
All other property definitions
on product, feature, feature component, action, resource, or anything using a representation
Adds qualified representation item to the complex instance
Uses qualitative_uncertainty for descriptors
qualitative_uncertainty
measure_name = “form variance”
uncertainty_value = “A”
qualitative_uncertainty
measure_name = “zone variance”
uncertainty_value = “H”
Follows the pattern established by the Plus/Minus mapping with qualifiers for each fit descriptor
qualitative_uncertainty
measure_name = “grade”
uncertainty_value = “IT01”
precision_qualifier
precision_value = 4
NOT FOR USE WITH A SIZE DIMENSION OR LOCATION DIMENSION
(which are mapped to Part 47 dimensional_size or
dimensional_location)

## Slide 24: Limits and Fits Using Dimension
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
value = 100 mm
precision_qualifier
precision_value = 4
dimensional_size
dimensional characteristic
representation
shape dimension
representation
shape_aspect
plus_minus_tolerance
limits_and_fits
form_variance = “A”
zone_variance = “H”
grade = “IT01”
of_shape
Geometry and location
AP-214 requires mapping fix already noted in plus/minus slide

## Slide 25: Current Dimension Types
Available Dimensions in AP-214 and AP-224
  location dimension
    distance_along_curve/curved_distance (224,214,202)
    angular_dimension/angular_location (224,214,202)
    location_dimension/linear_distance (224,214,202)
  size dimension
    radial_dimension (224)
    diameter_dimension (224)
    curved_dimension (224)
    angular_size_dimension (224,214)
    thickness (214)
    general_size (214)
  Module 1050 currently has only the AP-214 ones.
202

## Slide 26: Discussion
size dimension
  Comment to add size dimensions for each drawing symbol not attractive to cax-if vendors
  radial, diameter, curved currently under general_size in 214
  width, height may also be general_size in 214
  thickness (214)
    Requirements coming from tube/piping thickness, coatings
  AP-224 agrees to harmonize with any explicit tolerance types, but will not adopt a “generic” size tolerance.
  general_size (214) (NOT radius, diameter, dimension)
    Change to “externally_defined_size” with document reference

## Slide 27: Suggestion
ENTITY externally_defined_size_dimension SUBTYPE OF (Size_dimension); external_source_id : STRING; external_source : assigned_document_select; used_path : OPTIONAL Measurement_path; END_ENTITY;
Aside from renaming in the ARM, upward compatible with existing general_size definition
In ARM, AP-214 and modules may do as a separate document_assignment + rule to require it.
In ARM, AP-224 may do as above.
In AIMs, will be mapped as document assignment

## Slide 28: Dimension Type Resolutions
Change general_size to externally defined size as in previous slide.
  Upward compatible change to AP-214, Module 1050
  New addition to AP-224
Move specific types out from general_size
  radius, diameter, curved path become separate ARM objects in AP-214 and module 1050
  May be several others (width? height? length?)
Add missing size dimensions to AP-224
  thickness
  Others coming from general_size as above.
Agree on len/width/height via email/conf call
  length/width/height may just be the same type of thing with different measurement paths

## Slide 29: Envelope Principle
AP-224
  Mapped as the name of the dimensional characteristic representation
AP-214
  Mapped as classification assignment on plus_minus_tolerance
Module 1050
  Mapped as classification assignment on dimensional_size
See diagram on next slide

## Slide 30: Envelope Principle
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
dimensional_size
dimensional characteristic
representation
shape dimension
representation
name = “envelope tolerance”
shape_aspect
plus_minus_tolerance
tolerance_value
length_measure_with_unit
value = 0.001
length_measure_with_unit
value = - 0.001
lower_
bound
upper_bound
of_shape
Geometry and location
AP-224
applied_classification_assignment
classification_role
name=“further tolerance requirement”
group
name=“E”
description = “dimensioning principle”
AP-214
1050

## Slide 31: Envelope Resolution
AP-214/Module 1050
  Change to dimensional_characteristic_representation.name approach in the AIM.
  AP-214 must relax ARM to allow envelope on any size dimension. Move attribute envelope from value_limitation to size_dimension
AP-224
  Restrict usage of envelope to size only by moving attribute in the ARM to size_dimension

## Slide 32: Directed Angular Location
Notion of directed dimension currently supported by linear distance
  directed attribute on linear distance dimension
Not by angular location dimension in either AP
  No attribute for directed, but examples exist in other standards
Defer until we discuss other issues with angular location

## Slide 33: Angular Location Mirroring
There are cases where it is difficult to determine the angle
  Need some sort of path or location/orientation to be able to determine the enclosed angle
    If orientation is used, one line lies on X axis, other line lies counterclocwise towards Y axis. (right hand rule)
Leave this alone for now
  Not a harmonization problem, AP-224/AP-214
  Continue to study, if improvements become clear, handle as SEDS