## Slide 1: Machining Programs and Tooling
David Loffredo
loffredo@steptools.com
2004-10-06
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: Overview
STEP-NC is a new language for CNC control
  Complete, unambiguous model of the part and process
  Brings together machining process, tool requirements, geometry, tolerances, and PDM.
  Makes CNC systems
    More interoperable
    Faster to program
    Safer to operate
STEP-NC can enable million of dollars of savings using lean manufacturing

## Slide 3: Problem is Tool Motions
%
N05 G54
N10 G00 Z10.000
N15 G91 G0 Z200
N20 T5 D1 WW
N30 G90 M5
N35 G00 X0.000 Y-150.000
N40 G00 Z5.000
N45 M08
N50 S3183.000
N55 M03
N60 F1477.000
N65 G00 X60.000 Y-150.000
N70 G00 Z5.000
N75 G00 X60.000 Y-150.000
N80 G01 Z-0.500
...
machine-specific part program with axis data generated by a postprocessor
vendor-specific extensions of the original standard
only primitive motion and switch commands
no standardized data format for spline processing and sophisticated NC technology
Courtesy WZL RWTH Aachen
STEP-NC replaces this with a
rich, integrated 3D data format
Ideal for Paper Tape!
The standard for 40 years!

## Slide 4: Task-oriented Programming using AP-238
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterized_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 5: Task-oriented Programming
AP-238 describes “what” as well as “how”
  Make this geometry from this stock
  By removing these features
  In this order
  With these tolerances
  And tools that meets these requirements
  May even let the controller choose tool motion
The old standard only described “how”
  Move tool to this location
  Move tool to this location
  And so on for millions of commands

## Slide 6: Overview of STEP-NC
Based on Part 10
Measures
Project
Workpiece
Features
Milling Process Operations Based on Part 11
Milling Cutting Tools Based on Part 111
Turning Process Operations Based on Part 12
Turning Cutting Tools Based on Part 121
EDM Process Operations Based on Part 13
Other Technology Parts as they reach DIS
Executable
Operation
Toolpath
First
Edition
Second
Edition
AP-238 pulls together machining process, tool requirement, geometry, tolerances, and PDM.
  Start with process and tools described by ISO 14649 parts
  Add STEP PDM, Geometry, and Tolerances, and integrate so that features and all other data can be shared across APs
Dimensions and Tolerances STEP GD&T
PDM and Product Geometry Common to all APs

## Slide 7: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 8: Workpiece, Shape, and PDM
The workpiece is a STEP product description
With all of the owner information, approvals, dates and times.
Material and material properties
Shape for workpiece uses advanced B-REP, just like all of the other STEP APs.
Produced by any CAD system that supports STEP.

## Slide 9: Machining Features
round hole
counterbore hole
compound feature
pocket with
through bottom
condition
pocket with
flat bottom
condition
slot with
radius
ends
2.5D milling features
  Hole, pocket, slot, step, etc
Transition features
  Edge round and chamfer
Replicate feature
  Patterns of repeated features
Region features
  Surfaces for freeform milling
Turning features
  Outer round, knurl, groove
Notes: This slide represents the highlights of AP224.
The list of items in each box represents a sample of what AP224 contains.
To summarize - AP224 contains everything found on a drawing of a part

## Slide 10: Dimensions and Geometric Tolerances
Dimensions defining location
  Location defined by a linear distance
  Location defined by a distance along a curve
  Location defined by an angle
Dimensions defining size
  Curves, angle, diameter, radius, thickness, length, width, height
Geometric characteristics with datums as needed.
  angularity, circular runout, coaxiality, concentricity, cylindricity, flatness, line profile, parallelism, perpendicularity, position, roundness, straightness, surface profile, symmetry, total runout
0.01
0.01
A
0.01
A

## Slide 11: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 12: Machining Programs
The heart of the STEP-NC model
  Workplans containing a sequence of workingsteps.
  Each workingstep associates an operation with a feature somewhere on the workpiece.
  Each operation describes what to do and what strategies and parameter settings to use.
More information than M and G codes. Linked with geometric and technological information.
Parameters can be grouped and shared, e. g. tools, feeds, etc.
Intelligent NC controllers can calculate tool movements for standard features.

## Slide 13: Machining Programs
Project
  Starting place, defines setup and main workplan
Executables
  Describes control flow and sequencing.
  Workingstep associates an operation and a feature.
  Technology independent
Operations
  Describes what a workingstep does to a feature — plane mill, center drill, etc.
  The basis for all technology-specific extensions.
  Specifies details like
    spindle, feedrate and other technology parameters
    coolant & other machine functions
    plunge strategies, tool paths, etc.

## Slide 14: Control Flow and Sequencing
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Program steps that do not move any machine axes
(display message, etc.)
Control flow for the machining program
workplan
parallel
if_statement
while_statement
Program steps that move
the machine axes

## Slide 15: Toolpaths
Diagram WZL RWTH Aachen
Used for explicit control of the tool motion for an operation.
  Can use splines or other curves to describe motion and feedrates.
  Can describe path as machine independent motion of tool center point or tool contact point.
  Can also describe path using old-style machine dependent motion of individual axis.

## Slide 16: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 17: Milling Process Operations
Drilling Operations
  Drilling, boring, back boring, tapping/threading
  Tool moves in the Z axis only
  Many strategy parameters
2.5D Machining Operations
  Plane and side milling, roughing and finishing
  Tool can move XY or along Z, but not at the same time.
  Set of strategies
Freeform Machining Operations
  For sculpted surfaces
  3, 4, and 5axis motion
  Set of strategies

## Slide 18: Turning Process Operations
Turning Operations
  Contouring, facing, grooving, threading and knurling.
  Roughing and finishing for each
  Set of strategies
Possible Future Operations
  Work underway to describe operations for wire and sink EDM, contour cutting of wood and glass, grinding.
  Efforts in various stages of maturity.
  Will be added to AP-238 once the information requirements are mature.

## Slide 19: Milling Cutting Tools UOF
Every operation can have a tool associated.
  Represents tool requirements, not a physical tool on a machine.
  Potential for some best-fit optimization by the controller.
G&M codes just referenced tool #1, #2, etc.
  Human must make sure that #1 corresponds to the right thing.
  Controller not able to add any value to the process.

## Slide 20: Milling Cutting Tools
Basic definitions plus specific milling and turning tools
  backside_counterbore
  backside_countersink
  ball_endmill
  boring_tool
  bullnose_endmill
  centerdrill
  combined_drill_and_reamer
  combined_drill_and_tap
  counterbore
  countersink
  dovetail_mill
  drill
  endmill
  facemill
  grooving_tool
  knurling_tool
  milling_tool_body
  reamer
  side_mill
  spade_drill
  t_slot_mill
  tap
  tapered_drill
  tapered_endmill
  tapered_reamer
  tapered_tap
  thread_mill
  threading_tool
  twist_drill
  user_defined_tool
  woodruff_keyseat_mill

## Slide 21: Summary
AP-238 is a new language for CNC control
  Complete, unambiguous model of the part and process
  Integrates machining process, tool requirement, geometry, tolerances, and PDM.
Can enable million of dollars of savings using lean manufacturing by making CNC systems
  More interoperable: portable TCP and no more posts
  Faster to program: task-oriented programming
  Safer to operate: full checking information