## Slide 1: Geometric Dimensioning and Tolerancing Technology
ISO TC184SC4
Oct 6, 2004, Seattle Tom Hendrix
Boeing

## Slide 2: Agenda
GDT concepts
Requirements/Use Cases
Dimensioning standards
GDT and STEP

## Slide 3: GDT concepts.

## Slide 4: Direct Tolerancing of Dimensions “Plus-minus”
1  .2
vertex
must lie in
tolerance zone
50
40
“plus and minus” tolerancing
limit dimensioning
implied right angle

## Slide 5: Geometric Tolerances are not tied to a singe dimension
1.5 +.03
1.5
A
B
.76
.74
.76
.74
By dimensional
tolerancing
by geometric
tolerancing
value enclosed in box to designate dimension as “basic”
Geometric Tolerance callout
hole located from left side and top
datum feature callout
2.25 +.05
2.25
.75
Locating the center of a hole
0.75 + .01
hole located from bottom and right side
2.25+ .05
2.25 + .05
| 0.06 M |A|B

## Slide 6: Geometric Tolerance Zone Shape results in fewer parts rejected.
1.5 +.03
.75
1.5
.75
A
B
.76
.74
.76
.74
Dimensional
Tolerancing
Geometric
Tolerancing
center of hole must lie in rectangular tolerance zone
center of hole can be anywhere in round zone; thus more area,
fewer parts are rejected
Zone is round
2.25 +.05
2.25 +.05
1.5+ .03
1.5+ .03
0.06 M |A|B
Notes: Why GT? 1. convenient to not worry about tolerancing when you dimension
2. Make
You just about construct part 47 from this picture.

## Slide 7: Requirements/Use Case

## Slide 8: Detailed GDT requirement is: Support the dimensioning standards
ISO 1101, 5459, (GDT) and related standards
  Supported in many CAD systems
ASME Y14.5 (GDT) (and related standards)
  ANSI standard - US national.
  Supported in many CAD systems.
  90%-95% commonality with ISO 1101
  Some differences in
    the details of annotation
    Defaults
Other national standards.
  Many have high degree of commonality with one or the other of above.
Industry standards
  Constrained versions of ISO and national standards
  Some additional features – e.g. flexible parts for automotive.
Notes: When we ask our users about what the requirements are – they say – everything in the standards.
OF course these standards are thick

## Slide 9: Product Specification Scenarios All of these are supported by STEP APs
Drawings (and parts list) = views of part with annotations.
  with 3D CAD shape geometry model.
  with Associative dimensions and tolerances.
“Reduced dimension” drawing:
  Explicit, directly toleranced dimensions for size of features of size.
  All other tolerances defined Geometric tolerances.
  query the CAD geometry model for all other dimensions
3D “model based definition”
  no drawing sheets
  GDT annotations in 3D space with shape geometry, on 2D Annotation planes.
    This is really still a drawing. Just cut up and stuck in 3D.
Full GDT semantic model underlying the annotations.
  Machine readable
  query the model for GDT
  do we still need traditional annotations?
Notes: Per Ronald Dale:
Boeing 7E7 has LCPT (life cycle product teams). There are ASIT teams that integrate across LCPTs
James Day is ASIT for GDT
Phil Farcy is responsible for FTA in CATIA V5
Frank Tomich is working with MDB
Rick Zuray
CATIA and UGS both use integrated 3DCS. Boeing management strongly wants one consolidated vendor offering.
CATIA wants to be the Microsoft of CADCAM, and are delivering pretty well
For GDT folks, the move to V5 and integrated products was a step back, because valisys was more mature
Delmia and Metrologue provide a lot of dimensional inspection support – CCM and so forth. Ronald is responsible for implementing Delmia
Steve Walls is GDT lead on 7E7
CYW-
There is a
product
assembly
details geometry
Technology package
FTA
NOA (Non object attributes)

## Slide 10: Design Usage Requirements
Complete product definition
  for long term data retention.
  For supply chain.
Identify critical dimensions and tolerances for components
  Produceability.
Provide Dimensions/Tolerance data independent of orthographic drawings
  “Machine readable” for NC QC planning
  - e.g., for Coordinate Measuring Machine programming
  Get drawing creation off the engineering schedule
    “Just In Time” drafting (perhaps never).
Notes: Per Ronald Dale:
Boeing 7E7 has LCPT (life cycle product teams). There are ASIT teams that integrate across LCPTs
James Day is ASIT for GDT
Phil Farcy is responsible for FTA in CATIA V5
Frank Tomich is working with MDB
Rick Zuray
CATIA and UGS both use integrated 3DCS. Boeing management strongly wants one consolidated vendor offering.
CATIA wants to be the Microsoft of CADCAM, and are delivering pretty well
For GDT folks, the move to V5 and integrated products was a step back, because valisys was more mature
Delmia and Metrologue provide a lot of dimensional inspection support – CCM and so forth. Ronald is responsible for implementing Delmia
Steve Walls is GDT lead on 7E7
CYW-
There is a
product
assembly
details geometry
Technology package
FTA
NOA (Non object attributes)

## Slide 11: CATIA FTA http://plm.3ds.com/10+M54203c2ee8c.0.html#new

## Slide 12: UG/Geometric Tolerancing (from 2001)

## Slide 13: More Engineering product standards

## Slide 14: More Engineering standards
ASME Y14.41-2003 Digital Product Definition Data Practices
ISO/CD 16792 (TC10)
  Rebadging of ASME Y14.41 as ISO standard.

## Slide 15: Situation
Today we transmit product specs downstream.
  Full annotated model with underlying GDT via proprietary format.
    Machine readible GDT for partners of CAD vendors
    Human readible annotations, queries, with viewer from CAD vendor.
  Geometry in STEP or IGES, still need viewer or drawing for GDT. Drawing can be in IGES
  Can vectorize annotation, text, symbols and convert along with geometry to STEP or
Notes: Is this still true? Must use FTA.

## Slide 16: GDT and STEP

## Slide 17: GDT and STEP
GDT concepts and structures are modeled in several STEP standards as
Drafting and Annotation
  The alphabet: curve, text, symbol, ..., in 2D or 3D
  The words: dimension callout, geometric tolerance callout, datum feature callout, ....
GDT - the meanings
  directly presented by annotation (not always 1-1)
    geometric dimension, geometric tolerance, datum, ...
  Implied by annotation
    conical tolerances, virtual condition boundaries, ...
    datum system, datum reference frame, ...
A big question - Is there a market for adding 3D annotation to STEP
  Or should we use machine readable GDT as product definition..

## Slide 18: STEP GDT Annotations vs Machine readable GDT
THIS ON THE DRAWING
MEANS THIS
Typical figure from ASME Y14.5
12 +/- 0.4
12.4
11.6
Tolerance zone
Indicated origin plane

## Slide 19: Callout and data model
1.5
.75
A
B
.76
.74
2.25 +.05
1.5+ .03
0.06 M |A|B
Notes: Why GT? 1. convenient to not worry about tolerancing when you dimension
2. Make
You just about construct part 47 from this picture.

## Slide 20: Geometric Tolerance Feature Control Frame
1 2 3 4
1 - tolerance applies to position, e.g. hole.
2 - Tolerance zone description:
    (zone is cylinder). Diameter is) 0.06
    M ( or more, depending on size of as-made feature).
3,4 - Datum reference frame
  to locate this tolerance zone on actual product.
  A is primary “datum feature”
  B is primary (secondary) “datum feature” , M which can move around if it happens to be (say) a bigger hole than required.
| 0.06 M |A|B M

## Slide 21: Summary of Harmonized GDT in STEP Standards
Part 203e2 214 219/223/224 238/240
GDT
Defaults TBD Yes No No
Geom Dims Yes Yes Yes Yes
Dim Tol Yes Yes Yes Yes
Geom Tol Yes Yes Yes Yes
Drafting 2D&3D
Dimensions Yes Yes No No
Other annotation Yes Yes No No
Associative Yes Yes No No

## Slide 22: Data Exchange Standards

## Slide 23: Questions?

## Slide 24: Direction
Use measurement devices and sensors to adjust/correct automated manufacturing in process
Direct interaction with digital product definition for measurement processes
Common logical computing architecture for measurement
  object oriented, software measurement tools and standards , compliant with emergent industry standards
Notes: FCA website seems like not much is happening. Is Delmia the new factory computing architecture?
Are the still the direction, are they realized yet.
In-process inspection – we do very little, some in wichita (IDS does more). Goal of E7 is do more. Also create the design to capture- verification and acceptance. Includes that design and process capability (producability).
Mechanic doing build will be accountable. If there is a problem, remove and investigate. There is a non-conformance team. Not stopping the process.
Functional gages are done today. But would like to have work instructions. Operate gets a kit, system knows certifications, what job they have. Work instructions will be clear, will have verifications that work was.
There will still be auditing by QC. But the quality role will .
Not sure how much of ST function in GDT is being used. Will apply key characteristics. Will identify key characteristics and critical features will be done with FTA. Any implicit tolerances will be on general notes. We are saying in the measurement plan to . Can state it in general note section, or with FTA can put a flag note.
Two schools of thought: Intercim velocity for mfg plan – manufacturing executing. Also Demila DPM shop and process.
No distinct inspections. Delmia

## Slide 25: ASME Y14.41
First edition published 2003
Support use of either model plus drawing, or 3D model alone as a complete product specification.
Master model - 3D model based definition
  Capture GDT (annotations) and other specifications in a master dataset along with the geometric model.
  GDT annotation/presentation in same 3D space as the product’s shape representation.
    Call-outs confined to Annotation planes
    Support dimensions by queries and call-outs.
    Associativity between tolerances, datums, etc,
    Support highlighting when selecting with mouse.
  Geometric model represents mim, max, or mean of geometry, as specified in a note.

## Slide 26: Processes
Design the part
  Tolerance advisor to tell user what tolerances are legal or recommended on a feature.
Design an assembly
  Variational analysis – buildup of allocated component tolerances.
Fabricate the parts.
In-line inspection.
Inspect the part.
CMM and functional gaging.
Assemble the parts.
Notes: How do we send . A lot of suppliers use V4. They get access through low end viewer.
We can send via VRML. But not associative. Most go to low end viewer. A lot of V4 stuu the still get drawings.
7E7 will use FTA on all parts and assys. Partners are synchronized with CATIA. Tool set will match ours. CATIA ENOVIA, partial Delmia. They will do
SUPARS is alive. But does not support V5. Long beach , ST louis, Philadelphia use with UG. It is sent as part of geometry polylines and arc. It is good for human readible. Could store as representation. Ideally would like to preserve attribute data.
7E7 will do parametric design. Main reason is for design reuse. If you want to change a design. Especially for derivative.