## Slide 1
Lean Manufacturing Workshop
“New Technology for Faster Planning and Faster Machining”
How our CNC supports…….
GE Fanuc
Jim Spearman

## Slide 2
Case Study at Boeing

## Slide 3
Prototype Model to support CATIA V5 – GE Fanuc View
Supports Boeing’s concept on CATIA V5
G code program
converter
Part Verification Records
(1)
(2)

## Slide 4
CATIA V5 Enovia 3D Model
STEP
AP238 Format Converter
CNC G code Converter
F300i
Another STEP Data
Tooling etc….
(1) Create Part Program Generator (Demonstrated at IMTS 2004)
Collaboration with Boeing, MR&D
MR&D develops G code Converter (Part Program Generator)
GE provided systems to test proper part program execution
(2) Relationship with CAM vendor’s
Gibbs visited Fanuc, Japan to discuss to support requirements and future direction (July)
Master CAM has established relationship and participated at Fanuc in-house show (April)
Prototype Model to support CATIA V5 – GE Fanuc View

## Slide 5
STEP-NC Implementation with Tool Center Point (TCP) Programming
at IMTS 2004
GE Fanuc F30i series supports
Full Compensations at 5 axes machining
Supports Machining in all ranges
  Part Compensation for Reduced Setup Time
  Manual Feed for Reduced Setup & Minor Stoppages.
  Eliminate Stoppages & Program Re-Writes
  Enhanced Speed with 5-Sided Machining
Maximize full compensation features for users
  Supports STEP programmed TCP
  Coordinate with CAM to support GE Fanuc TCP

## Slide 6
CATIA V5 CAD/CAM
STEP-NC Implementation with Tool Center Point (TCP) Programming
at IMTS 2004
TCP
file
GE-Fanuc 30i
simulator
Part
design
workbench
Part
file
CL
File
Machining
workbench
Assembly
design
workbench
Product
file
CL TO AP238
converter
Process
file
AP238 TO TCP
converter
AP238
file

## Slide 7
%
N1(CONVERTED FROM STEP AP238 XML FILE)
N2(A0024007)
N3G1
N4T1
N5M6
N6(***************************************************************)
N7(OPERATION 10)
N8(ROUGH PART COMPLETE)
N9(2 X 0.01 X 4)
N10(***************************************************************)
N11(TRUE CUTTER/2.00 0.01 0 0 0 0 4)
N12(PPTOL / 0.0010, 0.0100)
N13F150
N14G43.5X-1.0Y8.2Z1.0H2
N15F60
N16Z-0.9875
N17F25
:
N28X-3.7Y-4.6185R7.03
N29G43.5Y-6.0
N34X-13.6185
N35G02X-16.03Y0.0R7.03
N36X-14.3Y4.6185R7.03
:
N1548F60
N1549Z1.0I0J0K100
N1550M30
STEP-NC Implementation with Tool Center Point (TCP) Programming
at IMTS 2004
Actual Output Examples
Advantages of GE Fanuc solution to support STEP
- Available for legacy GE Fanuc Control Systems
- Can apply GE Fanuc latest CNC Technology High Speed Machining Technology Special Compensations / interpolations
- CNC / CAM ( or converter ) Seamless connection

## Slide 8
Q
?
A