## Slide 1: Integrated Manufacturing Architecture using Machining features
By
Len Slovensky
SCRA / NGIT
slovensky@scra.org

## Slide 2: Integrated Manufacturing Architecture using Machining features
Dimensional Inspection Information Exchange
Machining
Features
Exchange of Design and Manufacturing Product Information for Cast Parts
AP219
AP224
Mechanical product definition for process planning using machining features
Process plans for
machined parts
AP240
CMM
Application interpreted model for computerized numerical controllers
CNC
AP238
AP223
CAD
Notes: At the ISO/TC184/SC4 meeting held October 1992 in Berlin, Germany, ISO 10303-224 was approved as a New Work Item (NWI). The scope of AP224 was to define Mechanical product definition for process planning using machining features. This STEP application protocol (AP) was published in 1999. Since that time four additional APs have been developed to define industry data for manufacturing:
AP219 - Dimensional Inspection Information Exchange
AP223 - Exchange of Design and Manufacturing Product Information for Cast Parts
AP238 - Application interpreted model for computerized numerical controllers
AP240 - Process plans for machined parts
An integral part of the development of these APs is to harmonize elements of requirements that are common across there different domains. One of the key elements that is harmonized is machining features. These features were first developed in AP224 but are now being used by all of the manufacturing application protocols. The purpose of this paper is to examine machining features and how they are used by the different APs.

## Slide 3: What is a Machining Feature ?
Definition of an aspect of shape on a part.
Terminology in terms of Manufacturing users
Defines explicit definition of shape:
  Geometry
Defines implicit definition of shape:
  Parametric attributes
Notes: One of the first APs to be published as an IS standard was AP203 “Configuration Controlled 3D Designs of Mechanical Parts and Assemblies”. This AP defined several types of geometry that could be exchanged, including Boundary Representation Geometry (B-Rep) that defined a combination of geometric elements and topology. Though B-Rep geometry was a useful representation for defining topological shape, applications still had a task, interpreting the B-Rep and determining what action to take based on the B-Rep shapes. More useful information was being asked for to help determine what the geometric shapes represented. Along came the development of AP224.

## Slide 4: Explicit feature information
Example: Slot
  Boundary Representation Geometry defines Slot Feature
  Face Topology defines Slot floor and side walls
Faces
Notes: Manufacturing process planning software that used STEP data was asking for additional information added to the STEP file to give additional meaning to the geometry. AP224 defined a layer of information on top of the B-Rep geometry to aide applications in determining what the geometry represented, called machining features. These machining features were a way of defining an aspect of this shape geometry with user defined terminology. For example an aspect of shape that is defined with topological geometry like loops, edges, and faces, can now be identified in user terminology as a Pocket, Slot, Groove, or Hole. Now downstream applications have a means of identifying the shape geometry and can make intelligent decisions on actions to take based on these definitions.

## Slide 5: Implicit feature information
Example: Slot
  Parameters defines Slot
    Slot depth
    Slot width
    Slot height
    Corner radius
Notes: AP224 was developed to contain even more user information about machining features. Besides the ability to represent geometric shapes as a machining feature, there is the ability to represent machining features implicitly with parameters. For example a Slot feature could be implicitly defined with numeric parameters that define the Slot width, depth, height, and corner radius. Applications are able to speed up processing time, because values no longer need to be derived from the underlying geometry, the actual numeric values are a part of the feature definition.
Creating implicit and explicit feature information adds several other useful benefits. For example a geometric tolerance like Flatness could be applied to topological face geometry that is use to define a Planar face feature. This helps bring together connectivity of machining features and the geometric tolerances to machine them. Also ‘limits and fits’, or a ‘plus minus’ tolerances can be applied to individual numeric parameters for a machining feature. A variety of things like properties, tolerances, and materials can be associated with the machining feature to aid applications using STEP data.

## Slide 6: Feature relationships
Feature
Geometric
Tolerance
Geometric
Shape
Position tolerance references Countersunk hole
Countersunk hole references cylindrical face
Explicit feature information

## Slide 7: Feature relationships
Implicit feature information
Feature
Dimensional
Tolerance
Feature
Attribute
For hole
depth
Plus minus
tolerance

## Slide 8: Feature relationships
Material_property
Process_property
Specifications
Surface_property
Part_property
1. MATERIAL:
STEEL ALLOY 4140 OR 8640,
ASTM-A322 OR ASTM-A331
2. HEAT TREAT TO ROCKWELL
C 34-40 PER MIL-H-6875
3. IDENTIFY PER MIL-STD-130:
MARKING METHOD PER ANSI/SAE
- AS478-2A 97403-13227E7185
MFR-CAGE
4. FINAL PROTECTIVE FINISH: TREAT
TYPE Z, CLASS 3, DOD-P-16232, (WAVE
PREPRODUCTION INSPECTION PARA.
3.1) PAINT PER REQUIREMENTS ON
DRAWING NO. 19207-12344344 COLOR
383 GREEN. INDICATED AREAS TO BE
FREE OF PAINT AND COATED WITH
PRESERVATIVE OIL MIL-L-3150.
5. FOR INTERPRETATION OF SCREW
THREAD FED-STD-H28 APPLIES.
6. ALL DIMENSIONS ARE IN INCHES
Example note block from a part
Property information may be linked to
feature information
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Machining Feature Example
Planar_face
Planar_face
(Rough)
Planar_face
(Rough)
Clamping Direction
Planar_face
Planar_face
Planar_face
Compound_feature
[Round_hole + Counterbore_hole]
General_outside_profile
Step
Slot
Countersunk_hole
Countersunk_hole
Thread
Countersunk_hole
Slot
Compound_feature
[Round_hole + Counterbore_hole]
Countersunk_hole
Slot
General_cutout
Rectangular_open_pocket
Rectangular_boss
Planar_face
Countersunk_hole
General_outside_profile
Planar_face
Countersunk_hole
Countersunk_hole
Groove
Clamping Direction
[Slot_D1]
Slot
[Hole_D1] 2 times
Countersunk_hole
[Thread_D1]
2 times Thread
[Head_D1]
Planar_face
（Finish)
[Head_E1]
Planar_face
（Finish)
[Slot_E1] Slot
[Hole_E1]2 times
Countersunk_hole
[Thread_E1] 2 times
Thread
Clamping Direction
Notes: The AP224 IS standard has defined some 18 different machining features, however these features are further defined into many different variations. For example the Hole feature can be defined as a round hole, counterbore countersunk through hole, a blined hole with several different bottom conditions, and all of these hole feature types can be defined with tapers. Therefore the 18 different machining features are used to define a large number machining feature variations.
After AP224 was published as an IS standard in1999, it was determined that these machining features could be used in many other STEP standards. Therefore the machining feature portion was removed from AP224 and a new ISO standard was created called Application Integrated Construct (AIC) 522. This AIC is a standalone construct that can be used by any AP to include the AP224 machining features in directly into the AP definition.

## Slide 10: AP224
Exchange from CAD to CAM
Result of feature recognition software
CAD
PRO/E
CATIA
UG
Feature
Recognition
CAPP
AP203
AP224 (With tolerances,
Properties, etc.)
AP224
(features
Only)
Notes: AP224 resolves these problems by providing machine part information that ensures the design information is 100-percent complete, accurate, computer-interpretable and reusable. Many computer-aided process planning (CAPP) systems on the market enable automated process planning from product data in a digital format. The AP224 standard provides the mechanism to define this digital data.

## Slide 11: AP224
Dimensions
Tolerances
Geometry with Topology
Features
Major component for AP
Drawing notes
Material property
Surface finish
Process property
Hardness
Part information
Security
Approvals
Materials
Notes: AP224 contains the following information, which is necessary to manufacture the required part.
• Necessary CAD geometry and topology in a neutral format.
• Machining feature information such as hole, boss, slot, groove, pocket, chamfer and fillet.
• Dimensional and geometric tolerance information.
• Material properties, process properties and material hardness.
• Administrative information such as approval, part name and ID, delivery date and quantity.

## Slide 12: AP240-Process plans for machined parts
work instructions for the tasks required to manufacture a part,
using which include:
  references to the resources required to perform the work
  the sequences of the work instructions
  relationships of the work to the part geometry
technical data for and/or out of the process planning
for machined pats which includes:
  machining features for defining shapes necessary for manufacturing
  machining feature classification structure
  geometric and dimensional tolerances of the parts being manufactured
  materials, and properties of the parts being manufactured
information contained in the process plans
for machined parts which includes:
  numerical controlled machines
  manual operations
Notes: AP240 defines the macro process planning for machining parts. This AP captures part shape, tolerances properties from AP224 and adds additional information contained in the process plans for machined parts which includes: numerical controlled machines, and manual operations. AP240 adds information on work instructions for the tasks required to manufacture a part, using which include: references to the resources required to perform the work the sequences of the work instructions relationships of the work to the part geometry. And AP240 has information on technical data for and/or out of the process planning for machined pats which includes: machining features for defining shapes necessary for manufacturing, machining feature classification structure, geometric and dimensional tolerances of the parts being manufactured and materials, and properties of the parts being manufactured.

## Slide 13: AP240 Feature dependency suggestions
A recommended order to process features on the part
An aid for the creation of manufacturing processes and operations per process.
Planar face
Slot
Compound
feature
Countersunk
hole
Thread
Pocket
Recess
Cutout
Notes: AP240 contains feature dependency information to aid in the creation of manufacturing processes and operations per process. The feature dependency information is a recommended order for processing machining features by the process plan.

## Slide 14: AP240 Machining operations
[Slot_D1]
Slot
[Hole_D1] 2 times
Countersunk_hole
[Thread_D1]
2 times Thread
[Head_D1]
Planar_face
（Finish)
[Head_E1]
Planar_face
（Finish)
[Slot_E1] Slot
[Hole_E1]2 times
Countersunk_hole
[Thread_E1] 2 times
Thread
Clamping Direction
Machining operations defines:
  Sequence of features for Manufacturing activity
Notes: AP240 also used machining features in defining in planning manufacturing activities and operations. A part will require multiple machine setups in order to machine each and every side of the part. Each setup activity definition contains a list of machining features that can are eligible for material removal. Also any other manufacturing activity that removes material from the part will have a list of machining features that pertain to that specific activity. Manufacturing activities are further subdivided into separate operations per that activity. For example there may be a manufacturing activity defined to drill all holes and thread some of the holes on the part. This activity would contain a list of hole and thread features. This activity would be subdivided into operations for drilling counter sinking, and tapping. Each of these operations would contain a subset of the manufacturing activity features. Adding the AP224 machining features has greatly enhanced the AP240 macro process planning information.

## Slide 15: AP240 Manufacturing activity
Manufacturing activity are defined to process the feature
Operations are defined for the manufacturing activity

## Slide 16: AP238 Application interpreted model for computerized numerical controllers
Manufacturing Features
Slot
Hole
Planar face
Thread
Outer Round
Chamfer
Workpiece
Workpiece
Material
Parameters
  Property
  Numeric
  Descriptive
Project
Project
Person and address
Tool path
Tool path
Feed stop
Parameterized path
Cutter contact and location trajectory
Measure
Limits and fits
Plus minus value
Tolerance length measure
Operation
Machine functions
Machining operation
Tool direction
Tool path list
Executable
Working step
Working plan
Setup
Cutting tool
If and While statement
Program structure
Process data for milling
Boring
Drilling
Reaming
Tapping
Cutting tools
Drill
Tap
Reamer
Boring tool
Notes: <number>
<footer>
<header>
<date/time>
AP238 is the next step in manufacturing after AP240; this AP defines the micro process planning. Where AP240 defined the high level details for manufacturing a part, this AP defines the specific information for a specific machine. This AP defines specific process information like boring, drilling, reaming or tapping. AP238 defines the setup, sequential working steps, cutting tool specifications for tools like drills, taps, boring tools, and reamers. AP238 describes how to make geometry from a piece of stock by removing AP224 machining features in a sequential order with specific tolerances with tools that meet all of these requirements.

## Slide 17: AP238
AP238 describes “what” not “how”
  Make this geometry from this stock
  By removing these features
  In this order
  With this tolerance
  And tools that meets these requirements
The old standard (ISO 6983) described “how”
  Move tool to this location
  Move tool to this location
  And so on for millions of commands
Notes: AP238 defines a machine work plan that contains a sequence of working steps these working steps specify what machining feature is being machined. Each working step consists of a set of machining operations. These machining operations specify the specific operation like plane milling, drilling, etc., cutting tool, machining strategy, machining technology and the specific machining feature. Tool path geometry is created based on this machining feature.

## Slide 18: AP238 – Machining operation
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
L[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterised_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Machining features

## Slide 19: AP223 - Exchange of Design and Manufacturing Product Information for Cast Parts
Casting process simulation
Shape representation
Process design parameters
Simulation results
Quality Control Records
Processes of building a sand mold, of building a die assembly, and of building an investment pattern assembly.
Processes of melting, pouring, cooling, shaking out, extracting, and knocking out a casting
Melting processing and resulting metal composition
Inspection and testing results of the cast part.
Process Plan
Process_plan harmonized with AP240
Melting, pouring, cooling, shakeout, extracting, and knocking out a casting
Process used to produce a casting
Metal alloys used to product a casting.
Equipment used to produce a casting.
Mold Design
Shapes of sand mold, die assembly, and investment pattern assembly
Materials used in the casting processes
Building a sand mold, a die assembly, and an investment pattern assembly
Data Supported
Shapes of cast parts
Materials of cast parts
Tolerances and surface finish
Physical and mechanical properties
Harmonized with AP224 features, tolerances, properties
Notes: AP223 brings together all of the information contained in AP224 and AP240. This AP defines the “as designed” AP224 type of data and the process planning information for cast part. However AP223 has unique requirements specific for castings. For example the AP224 machining features need draft angles to define cast features. The AP240 process plan needs activities and operations defined to support the casting foundry. Besides this overlap with existing APs,

## Slide 20: AP223
Product
Design
Customer
Pattern/Die
Manufacturing
Pattern/Die Shop
Foundry
Process
Design
Process
Modeling
5
Quality Control
Process Data
1
Casting Part Description
2
3
Mold Design
4
Simulation Data
Shop
Floor
AP224 features
Notes: AP223 also has additional requirements for simulation data, to simulate pouring molten medal into a mold and analyzing metal flow, cool spots, and poor mold design. This AP also support design information for the mold used to make the cast part. Casting molds contain a varied of features unique to the casting process like cope, drag, sprue basin, runners. Parting lines, etc. The machining features become an integral part of castings in defining the cast shape and in developing the mold information.

## Slide 21: AP223
Cast Part description using AP224 features
Pocket
Cutout
Mold Design

## Slide 22: AP219 - Dimensional Inspection Information Exchange
Analysis
Feature analysis mode
Feature tolerance mode
Parameter analysis mode
Dimensional Measurement features
Circle, arc, sphere
Geometric surface
Lines, planes
Pattern
Measurement execution
Execution result
Execution result measurement
Data acquisition software
Result parameter
Program run
Program identification
Run administrator
Measurement location
Program Run
Tolerances
Geometric tolerances
Dimension tolerances
Material condition modifier
Tolerance range
Part Properties
Calculated value
Parametric calculated value
Parameters
  Property
  Numeric
  Descriptive
Part
Part
Manufacturing features
Shape representation
  Brep model
  Explicit base shape
  Implicit base shape
Measurement parameters
Dimensional parameter
Point parameter
Vector parameter
Parameter value limits
Administration data
Person and Organization
Date and time
Time offset
Notes: <number>
<footer>
<header>
<date/time>
This Application Protocol will specifies the information requirements to manage dimensional inspection of solid parts or assemblies, which includes administering, planning, and executing dimensional inspection as well as analyzing and archiving the results. Dimensional inspection can occur at any stage of the life cycle of a product where checking for conformance with a design specification is required. AP219 uses AP224 features to define the “as designed” machining feature, and uses this information to create an inspection feature to define data “as inspected” AP219 then defines the calculated values from the inspection and links this data to the “as designed feature” and the “as inspected feature” for analysis.

## Slide 23: AP219 - Dimensional Inspection Information Exchange
Manufacturing
view
Dimensional
measurement
view
15mm + .25
25mm + .5
Hole 2
Hole 1
-
-
Circle 2
Circle 1
Circle 4
Circle 3
AP219 defines two different feature views:
Manufactured feature
Inspection feature

## Slide 24: Manufacturing and dimensional measurement views
DM view
Manufacturing view
Manufacturing
feature
Parameter
nominal
Parameter
tolerance
Manufacturing info
Part
Dimensional
measurement
feature
Dimensional
measurements
Measurement data
Dimensional
measurement
parameter
Parameter
calculated
value
Calculated
value
Measurement results
AP219 - Dimensional Inspection Information Exchange

## Slide 25: A STEP Manufacturing Suite using Machining features
STEP
Product Data
Generation
Macro
Process
Planning
Micro
Process
Planning
AP240
AP240
and
AP238
Shop
Floor
Finished Part
STEP In, STEP Out,
STEP Throughout
ISO 6983
M&G Codes
CMM
Inspection
Input from
Micro PP
NC programming
AP240
AP219
AP238
AP223
AP224
ISO-13399
Cutting tools
ISO-13584
fasteners
Conclusion
Notes: The architecture of all of the ISO manufacturing application protocols are tightly integrated around machining features. This paper has defined machining features and the use of these features across all of these APs. STEP driven manufacturing is based on machining feature driven manufacturing.