## Slide 1: The Barriers To General Acceptance of STEP-NC – A Provider’s Perspective
Chen-Han Lee
UGS

## Slide 2: Executive Summary
The focus is the barriers to the widespread acceptance of STEP-NC.
Brief review of STEP-NC and related efforts.
Analysis of the barriers from technology prospective.
Analysis of the barriers from market prospective.
Suggestions on how to overcome the barriers.
The key to overcome the barriers is tight technology and market integration.

## Slide 3: The Goals of STEP-NC
To enable new generation of smart controllers that:
  Machine the features on the parts, following the given process plans.
  Provide bi-directional communication with CAD/CAM systems.
  Don’t require post-processors.
  Support global collaborative manufacturing environments.
To move toward Closed-Loop Machining – the enabling technology for Lean Manufacturing.

## Slide 4: STEP-NC Paradigm
The new paradigm with STEP-NC controllers:
The old paradigm with conventional controllers:
CAD/CAM
STEP-NC
CNC
M&G
code
CAD/CAM
CNC
STEP-NC
data

## Slide 5: STEP-NC Data Model
STEP-NC data model (ISO14649/AP238) defines the data that the smart controllers need. It covers:
  Features and geometry.
  Process plans.
  Machining parameters.
  Resource data.
  Optional tool paths.
The signature is the richness of the data model.

## Slide 6: STEP-NC Implementation
STEP-NC itself is a passive data model and can’t accomplish the above goals alone.
Need to implement new technologies that utilize STEP-NC data model and demonstrate the benefits of the new paradigm.
Two key pilot projects:
  MDICM (Model Driven Intelligent Control of Manufacturing).
  Euro STEP-NC (European ESPRIT STEP-NC).

## Slide 7: MDICM Overview
The following is reproduced from the ATP Final Report of MDICM.
ST-Plan
ST-Machine
GibbsCAM/
Mastercam
Fadal CNC
AP238
FBMach

## Slide 8: Euro STEP-NC Overview
The following is copied from an AMT slide.
NC User
Interface
VAMOS
STEP-NC
CATIA V5
Open Mind
Siemens 840D
Open Mind
CATIA
Control
Siemens
STEP-NC Interpreter
NC Machine
  Application:
  Milling, Drilling,
  2.5D

## Slide 9: Summary of STEP-NC Projects
Both projects embedded a CAM processor in the controller to interpret and process the STEP-NC data.
Both projects used an off-line CAD/CAM system to perform feature-based process authoring and generate STEP-NC data.
CAD/CAM
Process Planner
STEP-NC CNC
with embedded
CAM Processor
STEP-NC
data

## Slide 10: Analysis of STEP-NC Projects
Both projects successfully demonstrated the controllers that interface with the rich STEP-NC data model. They proved the STEP-NC based data communication between the off-line CAD/CAM planner and the on-line CAM interpreter.
However, two critical issues remain to be proven/resolved:
  Data accuracy.
  Data utilization.

## Slide 11: Data Accuracy Issue
The actual processing is done in the native mode of the embedded systems, hence internal translation to/from STEP-NC is necessary.
Translation causes data loss and distortion and needs to be eliminated.
CAD/CAM
Processor Planner
STEP-NC CNC
STEP-NC
data
Translators

## Slide 12: Why Data Accuracy Is Critical?
High precision parts demand the evaluation of the geometry to produce the same results as how it was originally created.
Specialized machining processes demand the special process/machining parameters (some are semantic in nature) to be interpreted exactly the same way by different CAM processors.
The bottom line is to ensure the parts produced by different STEP-NC compliant controllers pass the same rigorous quality requirements.

## Slide 13: Data Utilization Issue
Although the embedded CAM interpreter reads STEP-NC data, the whole system doesn’t fully utilize it:
  The data fed to the motion processor is still at M&G code level – the loop of CAM and CNC is not closed.
  Some resource data (e.g., machine tool data) is not fully utilized by the path processor.
STEP-NC Controller
CAM
CNC
STEP-NC
data
M&G

## Slide 14: Why Data Utilization Is Critical?
It requires path processor, motion processor, and other components to work together to deliver Closed-Loop Machining:
  Accurate CNC-driven simulation/verification.
  True 3D cutter compensation.
  Optimized feed/speed and acceleration/deceleration control.
  Reliable, planned collision and pole avoidance.
  Precision driven motion interpolation (using actual geometry).
  Automated adaptive re-machining.
  Real-time in-process control.

## Slide 15: Summary of Technical Barriers
Need to resolve the data accuracy issue to ensure high quality production – to clear customer’s doubt.
Need to resolve the data utilization issue to deliver the values of Closed-Loop Machining – to attract customer’s interests.
It’s not enough to implement a sequential “water fall” paradigm.
We need a truly integrated “STEP-NC machining system” that demonstrates the complete closed-loop work flow.

## Slide 16: Key Market Barriers
Lack of customer demands, because:
  Customers are confused.
  Customers hate risks.
  Customers don’t see incentives.
Lack of vendor strategy, because:
  Vendors are confused.
  Vendors lack R&D funds.
  Vendors don’t see the market.

## Slide 17: Customers Are Confused
Customers are confused because they don’t understand the technologies that surround STEP-NC data standard.
10
Somewhat familiar (have understanding of basic concept of STEP-NC)
8
Aware that the STEP-NC specification exists
8
Not familiar (little understanding of basic concepts)
7
Have no idea what STEP-NC is
2
Very familiar (have understanding of Application Protocols)
28.6 %
22.9 %
22.9 %
20.0 %
5.7 %
From a recent OMAC survey of the question: “How familiar are you with STEP-NC?”

## Slide 18: Risks and Incentives
Many customers see the change of paradigm risky and costly.
The proof that there is a more flexible way to make the parts is not enough to justify a paradigm change.
We need to prove that the new paradigm produces better quality parts (accuracy issue) with less cost.
We need to prove that the new paradigm enables new machining technologies that can’t be done before (utilization issue).

## Slide 19: Vendor’s Issues with R&D
Many vendors share the same confusion of STEP-NC standard and the new technologies that implement STEP-NC.
Vendors see higher value in technologies than standards because the former generate new revenue.
It’s difficult for the vendors to estimate the scope and cost of the R&D to implement the new technologies using STEP-NC, when they are not certain what kinds of new technologies they should invest in.

## Slide 20: Vendor’s Issues with Market
CNC vendors see the CNC market, while CAD/CAM vendors see the CAD/CAM market. They see two separate markets.
The problem is that the new STEP-NC paradigm doesn’t fit CNC nor CAD/CAM market.
It corresponds to a new “hybrid” market that doesn’t exist today.

## Slide 21: Summary of Market Barriers
Need a clear direction (or directions) on the implementation of new technologies to realize STEP-NC paradigm.
Need to prove better quality parts and provide new enabling technologies.
Need to explore the new hybrid market.

## Slide 22: The Key Is Integration
To overcome the above technology/market barriers, we need a very tight integration and cooperation between CNC and CAD/CAM vendors. We need to work closely together to:
  Define the new integrated strategy.
  Develop the new integrated technologies.
  Create the new integrated market.

## Slide 23: Integrated Strategy
CNC and CAD/CAM vendors need to jointly:
  Define the new paradigm and the strategy on implementing STEP-NC.
  Promote the new paradigm.
  Educate the customers about the new paradigm.
  Seek and combine the limited R&D funding.

## Slide 24: Integrated Technology
It takes close collaboration between CNC, CAD/CAM, and Machine Tool R&D teams to develop the next generation of machining technologies.
Working sequentially, CAM and CNC can never accomplish Closed-Loop Machining.
We must erase the data, algorithm, and “water fall” barriers between CNC and CAM processors, and combine the technologies to build a system to fully close the manufacturing loop.

## Slide 25: Integrated Market
The new paradigm has no place in either the conventional CNC or CAD/CAM markets.
However, there will be plenty of opportunities for everyone if we see the new hybrid market beyond the horizon.
It will take the combined efforts from CNC, CAD/CAM, and Machine Tool vendors, plus the recognition from the customers and a little creativity, to build this new market.

## Slide 26: Final Words
STEP-NC is more than a data standard because it promises the new paradigm of Closed-Loop Machining.
STEP-NC alone cannot deliver the promise. It takes new technologies that utilize STEP-NC to realize the new paradigm.
The new technologies to realize Closed-Loop Machining require tight collaboration between providers of different technologies.
We also need to join forces on resource sharing and business development.

## Slide 27: Acknowledgement
Some of the thoughts presented here share similar views with:
  The framework paper from OMAC STEP-NC working group.
  The Direct Control research project in BYU.
  The white paper of “Intelligent and Precise Machine Control” project.

## Slide 28: www.ugs.com
The Barriers To General Acceptance of STEP-NC – A Provider’s Perspective