## Slide 1
Overview of
Feature based Process Planning system using AP240
2004-10-06
C.Sakamoto*1, T.Inouye*2
*1 Manufacturing Engineering Research Inc.
*2 Fujitsu Kyushu System Eng. Ltd.

## Slide 2: Overview of CAPP

## Slide 3
Features [ISO 10303-224,ISO 14649]
Geometric Feature Recognition
Feature based Workingstep
Feature based Process Plan
Software Program
Database
(Company based)
IT Solution

## Slide 4
Feature Data
（STEP AP224）
Create Macro Process Plan
1. Select Machine Tool for each Process
2. Decide Clamping Positions and Method.
3. Assign Manufacturing Features to each Process
Database for
Machining Technology,
Cutting Tools and
Machine tools
Process Plan Data
（STEP AP240）
Edit
Process Plan
3D Geometry Data of a Part
（STEP AP203/214）
NC Program
Recognize
Manufacturing Features
Add Tolerances and
Properties
[Function-1]
Create and Edit
Database
Functions of CAPP
Generate Micro Process Plan
1. Create Workingsteps for Features
2. Create Operation data for Workingsteps
(Cutting tool, Technology, Machining_strategy,
Finishing_allowance, Depth_of_cut, etc)
3. Sequence Workingsteps of the Process
Pocket with Hole
Hole
T_slot
[Function-2]
[Function-3]
[Function-4]
[Function-5]
[Function-6]
Generate
NC Program

## Slide 5
Feature Data
（STEP AP224）
Create Macro Process Plan
1. Select Machine Tool for each Process
2. Decide Clamping Positions and Method.
3. Assign Manufacturing Features to each Process
Database for
Machining Technology,
Cutting Tools and
Machine tools
Process Plan Data
（STEP AP240）
Edit
Process Plan
3D Geometry Data of a Part
（STEP AP203/214）
NC Program
Recognize
Manufacturing Features
Add Tolerances and
Properties
[Function-1]
Create and Edit
Database
Tools for Process Planning
Generate Micro Process Plan
1. Create Workingsteps for Features
2. Create Operation data for Workingsteps
(Cutting tool, Technology, Machining_strategy,
Finishing_allowance, Depth_of_cut, etc)
3. Sequence Workingsteps of the Process
Pocket with Hole
Hole
T_slot
[Function-2]
[Function-3]
[Function-4]
[Function-5]
[Function-6]
Generate
NC Program

## Slide 6: Recognize Manufacturing Features

## Slide 8
EXPRESS-X(mapping) makes relationship between a target and a source schema using extended Express language. Using this technology, data translator can be realized.
Things to develop are as follows; - STEP schema - AP203->AP224 mapping schema including Feature Recognition - STEP Engine (From EPM)
Configuration
Most of the commercial CAD system have STEP geometry translators such as AP 203/214.
In these days, the seamless data transfer from geometry to manufacturing becomes hot focus, inspired by such as STEP/NC project. As the key technology, feature recognition from geometry data has an important role in these purpose.
This development is to make STEP/AP224 format data from an input of AP203/214 recognizing manufacturing features; - Input : STEP AP203/214 File - Output : STEP AP224 File - Using STEP/Mapping(EXPRESS-X)
Though as feature recognition, GSS in India is famous, the target in this project aims same and/or higher recognition level.
The development is also supported by ECOM/JSTEP and MSTC activity.
Outline

## Slide 10: Create Macro Process Plan

## Slide 11
[Hole_1]
Compound_feature
[Hole_A31(Countersunk_hole) +
Hole_A32(Round_hole)]
[Step]
Step
[Slot_2]
Slot
[Hole_10, 11]
Countersunk_hole
[Hole_6]
Countersunk_hole
[Slot_1]
Slot
[Hole_4]
Compound_feature
[Hole_A21(Countersunk_hole) +
Hole_A22(Round_hole)]
[Hole_5, 7]
Countersunk_hole
[Slot_5]
Slot
[Pocket_1]
General_cutout
[Pocket_with_Boss_1]
Compound_feature
[Pocket_A11(Rectangular_open_pocket)
+ Boss_A11 (Rectangular_Boss)]
[Plane_7]
Planar_face
[Hole_8, 9]
Round_hole
[Outside_1]
General_outside_profile
[Plane_2]
Planar_face
[Hole_18, 19]
Countersunk_hole
[Hole_2, 3]
Counterbore_hole
[Slot_3]
Slot
[Slot_4]
Slot
[Hole_14, 15]
Compound_feature
[Hole_E11(Countersunk_hole) +
Thread_E11(Thread)]
A(0,0,+1)
D(0,+1,0)
E(0,-1,0)
C(-1,+1,0)
B(0,0,-1)
[Outside_2]
General_outside_profile
[Plane_3]
Planar_face
[Plane_8]
Planar_face
[Hole_16, 17]
Compound_feature
[Hole_D11(Countersunk_hole) +
Thread_D11(Thread)]
[Hole_12, 13]
Compound_feature
[Hole_A61(Countersunk_hole) +
Thread_A61(Thread)]
[Plane_3]
Planar_face
[Plane_8]
Planar_face
[Plane_6]
Planar_face
[Plane_5]
Planar_face
[Plane_4]
Planar_face
[Plane_3]
Planar_face

## Slide 12
[Boss_5]
Boss
[Plane_1]
Planar_face
[Plane_4]
Planar_face
[Plane_5]
Planar_face
[Plane_6]
Planar_face
[Boss_4]
Boss
[Boss_3]
Boss
[Boss_2]
Boss

## Slide 13
Manufacturing feature categorizes into Base Feature and Volumetric Feature. Base Feature --- Planar_face, Step, General_outside_profile Volumetric Feature --- Hole, Pocket, Slot, Boss Every Volumetric Feature has the relationship to Base Feature(s). At first, Base Features are assigned to the Process and then Volumetric Features are assigned to the Process.

## Slide 14
1. Select a Machine Tool for the Machining process
Macro Process Plan is composed of the following operations for each Machining process
2. Input the Axis relationship
between the machine tool Spindle and the Part
3. Input Clamping positions
4. Assign Features to the Machining process

## Slide 15
B(0,0,-1)
D(0,+1,0)
E(0,-1,0)
Clamping Direction
1st Process
[Plane_3]
Planar_face
[Plane_4]
Planar_face
[Plane_5]
Planar_face
[Plane_6]
Planar_face
[Plane_3]
Planar_face
(Rough)
[Plane_8]
Planar_face
(Rough)
[Plane_3]
Planar_face
(Rough)
[Plane_8]
Planar_face
(Rough)

## Slide 16
A(0,0,+1)
C(-1,+1,0)
2nd Process
[Hole_1]
Compound_feature
[Hole_A31(Countersunk_hole) +
Hole_A32(Round_hole)]
[Step]
Step
[Slot_2]
Slot
[Hole_10, 11]
Countersunk_hole
[Hole_6]
Countersunk_hole
[Slot_1]
Slot
[Hole_4]
Compound_feature
[Hole_A21(Countersunk_hole) +
Hole_A22(Round_hole)]
[Hole_5, 7]
Countersunk_hole
[Slot_5]
Slot
[Pocket_1]
General_cutout
[Pocket_with_Boss_1]
Compound_feature
[Pocket_A11(Rectangular_open_pocket)
+ Boss_A11 (Rectangular_Boss)]
[Plane_7]
Planar_face
[Hole_8, 9]
Round_hole
[Outside_1]
General_outside_profile
[Plane_2]
Planar_face
[Hole_18, 19]
Countersunk_hole
[Hole_2, 3]
Counterbore_hole
[Outside_2]
General_outside_profile
[Hole_12, 13]
Compound_feature
[Hole_A61(Countersunk_hole) +
Thread_A61(Thread)]

## Slide 17
Clamping Direction
3rd Process
[Plane_8]
Planar_face
(Finish)
[Plane_8]
Planar_face
(Finish)
[Plane_3]
Planar_face
(Finish)
[Plane_3]
Planar_face
(Finish)
[Slot_4]
Slot
[Hole_14, 15]
Compound_feature
[Hole_E11(Countersunk_hole) +
Thread_E11(Thread)]
[Slot_3]
Slot
[Hole_16, 17]
Compound_feature
[Hole_D11(Countersunk_hole) +
Thread_D11(Thread)]

## Slide 19
Indicate the Clamping Position(s) [ ] and Input the position type for each Clamping Position, Clamp, Locator or Jack
Jack (Adjustable locator)
Locator
Clamp
Locator
Locator

## Slide 21
Drill 8.5

## Slide 22: Create Manufacturing Technology Database

## Slide 23
An Example of Data Description in the Database

## Slide 24
Overview of ISO 14649 (Part-10 and Part-11)

## Slide 25
Tool Body（ISO 14649)

## Slide 26
Two5D Milling Strategy（ISO 14649)

## Slide 27
Micro Process Plan is composed of the following operations for each Machining process
1. Generate Workingsteps for Features
3. Sequence Workingsteps
2. Generate Operation data for Workingsteps

## Slide 28
Clamping Direction
[Plane_C1]
Flat_face
(Plane_
Finish_
Milling)
[Plane_D1]
Flat_face
(Plane_
Finish_
Milling)
[Plane_D2]
Flat_face
(Plane_Finish_Milling)
[Plane_C1]
Flat_face
(Plane_
Finish_
Milling)
[Slot_C1]
Slot
[Slot_D1]
Slot
[Hole_with_Thread_D1, D2]
Compound_feature
(Hole_D11(Composite_hole(d11+d12)) +
Thread_D11(Thread))
[Hole_with_Thread_C1, C2]
Compound_feature
(Hole_C11(Composite_hole(c111+c112)) +
Thread_C11(Thread))
Assigned Features to the 3rd Process

## Slide 29
An Example for the 3rd Process
1. Generate Process Activities for Features

## Slide 30
An Example for the 3rd Process
2. Sequence Process Activities