## Slide 1: Class Libraries for CNC and GD&T
Martin Hardwick
David Loffredo
info@steptools.com
STEP-NC Manufacturing Center
Watervliet Arsenal, Building 20
Metal Processing Manufacturing Division
Watervliet, New York 12189
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com

## Slide 2: Overview
STEP-NC AP-238 is a new language for CNC control
  Upward compatible extension of AP-203 (geometry) and AP-224 (features)
  Defines machine independent tool paths
  Makes CNC systems
    More interoperable
    Faster to program
    Safer to operate
Benefits are significant
Implementation effort can be significant
  Depending on the conformance class
We have new libraries to make implementation easier
  Our libraries for design data are in more than one million CAD stations

## Slide 3: Near term benefits
Reduce overhead
  More frequent direct load of customer data into CNC
  Faster set-up, less programming
Less waste
  Detect wrong program and workpiece
  Detect collisions
Increase throughput
  Optimal use of the machine
  Faster reprogramming
Replace RS274D axis data with AP-238 tool path and design data

## Slide 4: Example cost savings (1)
Description
Quantity
Annual Savings
Machined parts in the UK Navy inventory
90,000 (approx)
$640M
Parts in one depot (submarine)
25,539
Parts with available design data.
13,748
Savings using AP-224 for rapid manufacture
1,500
$4M
STEP-NC
Opportunity

## Slide 5: Example cost savings (2)

## Slide 6: Implementation Tools
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
APT-CL
Open CNC
HMI
CNC Motion
System
Geometry
Tool Motion
Customer
Shop
Machine Independent
CNC Control file
Write Libraries
Mapping driven
Customizable for each CAM
Writing AP-238 is difficult.
There are hundreds of integrated definitions
The CAM needs to create and link all of these definitions
“Save millions of dollars”

## Slide 7: Implementation Tools
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
APT-CL
Open CNC
HMI
CNC Motion
System
Geometry
Tool Motion
Customer
Shop
Machine Independent
CNC Control file
Read Libraries
Incremental validation
Units and origins
“New standard for Nano-Machining”
Reading AP-238 is difficult.
Application must find and validate the data it needs
Each instance can have its own units and origin

## Slide 8: Conclusion
AP-238 has many benefits for planning and machining
Implementing AP-238 has been a problem because of complexity
New class libraries make implementation much easier
  Write libraries can be customized to a CAM
  Read libraries validate and provide consistent interface for a CNC

## Slide 9: Backup

## Slide 10: AP-238 integrates tool path and design data
workpiece
machining_feature
S[0:?]
pocket
plane
region
hole
1
S[0:?]
machining_operation
workplan
machining_workingstep
L[0:?]
plane_milling
side_milling
drilling
1
tool
technology
strategy
L[0:?]
cutter_contact_trajectory
parameterized_path
cutter_location_trajectory
1
toolpath
geometry
geometry
geometry
Courtesy WZL RWTH Aachen

## Slide 11: Architecture for faster machining
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
APT-CL
Open CNC
HMI
CNC Motion
System
Geometry
Tool Motion
Customer
Shop
Define part
Export tool paths
Export part geometry
Machine part
Optimize tool motions
Detect set-up areas
Machine Independent
CNC Control file
CATIA, Unigraphics, Pro/Engineer, other APT-CL data sources
“Faster milling, drilling and turning”
GE Fanuc 16i, Siemens 840D, MDSI, other Open controls