## Slide 1
Case Study Reducing Inventory
in the Ship Support Industry
Lean Manufacturing Workshop
Seattle
Alan Crawford
alc@lsc.co.uk
Thursday, July 30, 2026
US$ values approximated at $2=£1
Notes: 2

## Slide 2: Agenda
Overview of RAMP
UK Evaluations of RAMP
  UK Navy RAMP Project
  Evaluation of UK Navy Store for AP224
  DML RAMP Evaluation Project
UK Deployment of RAMP
  Submarine Legacy Spares – business case
  Submarine Legacy Spares – status
  RAMP at DML

## Slide 3: Agenda
Overview of RAMP
UK Evaluations of RAMP
  UK Navy RAMP Project
  Evaluation of UK Navy Store for AP224
  DML RAMP Evaluation Project
UK Deployment of RAMP
  Submarine Legacy Spares – business case
  Submarine Legacy Spares – status
  RAMP at DML

## Slide 4: Rapid Acquisition of Manufactured Parts
Reduce capital expenditure on stock
Reduce storage requirements
  Store component in lowest cost form
    Ideally design information only
Supply item at lower cost
  Pre-manufacture savings
  Competitive tender
Reduce scrap of components
  Scrap during manufacture
  Design change and obsolescence
  “Lifetime buy” but never used
  “Lifetime buy” item out of stock – can it be made
The benefits
Rapid Acquisition of Manufactured Parts

## Slide 7
Ensure the quality of design information
  Legacy items
  Old standards
  Incomplete data
  Inconsistent drawing methods
Specialist material supply
Obtaining data
  Feasibility of identifying component sources
Speed of supply
  Expense of equipment downtime due to delays
  Competitive tender
Efficiencies to enforce
Rapid Acquisition of Manufactured Parts
Rapid Acquisition of Manufactured Parts
Notes: Enforce best practice
Example of first level fasteners where the Navy order by item of supply, yet DML have varieties of drawing for the same product.
Example of ordering a M12 bolt should reference BS2493 and not a design authority drawing number. This would slicken the drawing process.
RAMP is central to acquisition, but need efficient manufacture

## Slide 8
Design separation from manufacture
  Time
  Project
  Location
  Experience and expertise
  Physical equipment, material stock
Notes: MoD previous work on RAMP has shown

## Slide 9: STEP AP224 Representation
Manufacturing features
Hole Thread Spherical End
Product
Name ID Revision Security Classification
Surface Properties
Finish Coating/Process
Material/Alternate Material
Specification Hardness
Dimensions & Tolerances
Size Dimensions Location Dimensions Dimensional Tolerances Geometric Tolerances

## Slide 10: Agenda
Overview of RAMP
UK Evaluations of RAMP
  UK Navy RAMP Project
  Evaluation of UK Navy Store for AP224
  DML RAMP Evaluation Project
UK Deployment of RAMP
  Submarine Legacy Spares – business case
  Submarine Legacy Spares – status
  RAMP at DML

## Slide 11: UK Navy RAMP Project
Project partnership
  WSA, Babcock, Arnold Wragg, LSC, PAFEC, CIMTEL, Keyworth
Representation of a sample of UK Navy Store items in AP224
  394 fasteners
  191 axi-symmetric and prismatic items in AP224
Manufacture by two defence suppliers
  Evaluation trials of manufacture
  Technical & time based comparison
Demonstrated that RAMP is applicable to UK defence environment
Notes: Representations of fasteners were to standard not drawing – not realistic

## Slide 12: Naval Spares Inventory Analysis
Commissioned by WSA in 2000
Evaluation of applicability of AP224
  Test the extent of RAMP business
  Used NATO Item Name Code (INC)
  Sample examination of items in each INC
  Small number of INCs represent a large number of items in the inventory.
    100 INCs ~ 175,000 items in scope of AP224
Results
  191,000 items suitable for RAMP
Notes: Defined in the Item Identification Guide (IIG)
~ 31% of the inventory

## Slide 13
Warship Support Agency
  Initiated, funded and ran the project
  Involvement of Corporate Technical Services
  Feedback to IPTs
LSC Group Ltd
  Managed the project on behalf of WSA
  Generated the AP224 files
  Provided and configured RAMP manufacturing environment using LOCAM
DML
  Provided manufacturing resource and knowledge
  Manufactured components
  Feedback on times for comparative trials
DML RAMP Evaluation Project
Notes: Project to date
The project started in April 2001 with the selection of components for RAMP manufacture using STEP AP224.
The purchase and training in the use of EdgeCAM and the commissioning of Index turn/mill lathes delayed the start of the manufacture element of the project until November 2001 when the software and a post processor became available.
The first products were test manufactured in January and the project is on schedule to be completed early in March 2002.

## Slide 14
$600 million turnover
4000 employees
Owner/operator of Devonport Royal Dockyard
25 years experience refitting/refuelling nuclear submarines
Experience of refitting/design of surface ships
Design/build/refit of premium yachts
Rail support/overhaul facilities

## Slide 15: MoD RAMP project objectives
Enhance supplier understanding
  Technology introduction
  Improved supply of components
  Reduce costs by direct supply of spares
  Competitive tender
Spend to save
Test the applicability of RAMP
  Extend the comparative production matrix
    Across companies
    For a wider range of product
Notes: MoD previous work on RAMP has shown

## Slide 16
Replace component drawings
  distributed to DML as supplier
  product model using STEP AP224 definition
RAMP enabled DML manufacture
  first hand experience
  reference example for DML suppliers
Collation and analysis of project matrix
Project tasks
Notes: The AP224 representation, facilitates the automation of process planning: automated process planning systems use manufacturing logic to interpret the AP224 features and parameters in the generation of process plans.
These not only contain the necessary machining data (potentially including numerical control (NC) programs), but also complete manufacturing process and inspection schedules.

## Slide 17: Project components
First level fasteners - 25
  Comparative data from original UK Navy RAMP project
  Match to a large proportion of Naval spare items
  Economical to generate STEP data
Miscellaneous items - 15
  Complex components
  Not family groups – lower level of automation
Cast/forged items - 5
  Test new functionality of STEPTrans and trial manufacture
  High value stock items – store in lowest value stage
  Parts ordered for manufacture by DML during 2002
Notes: Components selected for manufacture during the project
The 45 parts selected for design/manufacture using RAMP can be broken down as follows.
First level fasteners (25)
These are components, which can be easily classified as family groups for manufacture.
The design, manufacturing rules (in LOCAM) and EdgeCAM work is complete. These products can be progressed from the AP224 design through process planning to the production of documentation and a CNC code for manufacture, with a minimum of human interaction. All of these family group products can be manufactured by DML.
Miscellaneous items (15)
The main selection criterion for this group of components was that they should not be suitable for family group approach to the manufacturing rules; consequently a lower level of automation of the production process is to be expected.
The two products that were capable of physically being manufactured on the Index machines achieved the same high level of automation as for first level fasteners. The many of the other components can be manufactured by DML using the AP224 design information and the LOCAM system on an interactive basis, producing planning documentation only. A post-processor has now been ordered for an alternative machine but it is too late in the project to incorporate the manufacturing experience.
Cast/forged items (5)
The cast/forged components were selected by DML in December 2001 & January 2002.
AP224 files have been produced for the cast and forged parts but a limitation in STEPTrans reduces the quality of the AP224 representation of the cast and forged blanks. It has also proved to be more difficult than expected to interpret information from features associated with an AP224 explicit base shape (of the type used for cast and forgings).

## Slide 18: Results (cost/times) data collection method
Set of parts provided a comparative matrix
Current and RAMP manufacture times
  Elapse time
  Cost time (actual hours worked)
  ‘New parts’ for manufacture
  ‘Repeat parts’ already planned / programmed
Evaluation environment and Integrated Production environment
Notes: Elapse time assumes that jobs land on desk and are treated as urgent – no lag whereas the cost time is hours that would have been booked to production (both direct and indirect costs).

## Slide 19
Evaluation environments results
elapse 333:1
cost time 3.5:1

## Slide 20
Integrated Production environment
elapse 1,380:1
cost time 33:1

## Slide 21: Results

## Slide 22: Agenda
Overview of RAMP
UK Evaluations of RAMP
  UK Navy RAMP Project
  Evaluation of UK Navy Store for AP224
  DML RAMP Evaluation Project
UK Deployment of RAMP
  Submarine Legacy Spares – business case
  Submarine Legacy Spares – status
  RAMP at DML

## Slide 23: RAMP - MXS Perspective
MXS inherits ownership of 90,000 line items
  It was valued at $640 million in October 03.
  It ranges from consumables to complete equipments.
  Usage varies from hundreds per year down to zero.
Significant task to rationalise
  Stock levels often determined by historical data only
  Working with industry can share the burden
  Industry have expertise to bring
  Transferring responsibility to industry can also shorten supply chain
Dan Smith Team Leader, Marine Auxiliary Systems IPT

## Slide 24: RAMP - Legacy Spares Contract
Submarine Legacy spares
  combined contract for 4 IPTs
  worth ~$10 million/year
  30,000 items
Awarded through competition to DML by MDMS IPT early 2002
“SMART” contract, heavily incentivised on both delivery performance and delivering reduced costs
Dan Smith Team Leader, Marine Auxiliary Systems IPT

## Slide 25: RAMP - Contract Initiatives
A number of potential initiatives were investigated and reported by DML early in the contract, eg Vendor Management, Spares Rationalisation
RAMP was one of the initiatives proposed for further work.
Initiatives were agreed on the assumption that DML were entitled to a share of the net savings accruing
RAMP therefore had to be self-funding and profitable!
Dan Smith Team Leader, Marine Auxiliary Systems IPT

## Slide 26: RAMP - Concept
RAMP - stock reduction by assured rapid supply
RAMP was a concept that had circulated for many years in the forerunners of the DLO but never converted into reality.
Simple in concept, holding the manufacturing information rather than parts, linked to machining centre.
DML had the advantage of already using similar facility on small scale in support of urgent refit requirements.
This contract formed the ideal vehicle to utilise RAMP, explore the boundaries of what was economically feasible.
With very little risk to the MoD!
Dan Smith Team Leader, Marine Auxiliary Systems IPT

## Slide 27: SLSC Project Definition Study
Identify range of items suitable
Review impact of RAMP
  Costs of preparing STEP files
  Relative costs of manufacture
  Relative stock-holding costs
Prepare a cost benefit analysis
Prepare operating procedures

## Slide 28: Item selection process
Identify items with known costs and savings
  – for DML investment
  Examination of sample items
  Determine design and manufacturing complexity
  Items capable of maximum automation
  Select based upon Item Name Code
Verify that stocks can be effectively used during the SLSC
  Forecast Demand Rate and stock levels
Ensure design information for item is available
  Identified from part number or previous supplier
  Remove proprietary items

## Slide 29: Technical Item Selection process
21,641 valid INC in ISIS
2,725 complex
8,920 simple
17,681 not graded

## Slide 30: Demand Rate Item Selection
RAMP requires an up-front investment in representing the design
Investment required for STEP file generation
  Obtaining & verifying design information from source
  Verification of designers intent
  Validation of the STEP representation
Restricted the selection to items where the DML investment could be recovered during the SLSC lifetime
  CRISP Forecast Demand Rate
  Current stock level

## Slide 31: Manufacture Rights
1,248 items proprietary
1,448 items difficult to obtain drawings
13,748 drawings already available
25,539 maximum figure

## Slide 32: Item Selection (continued)
Combine all three selections of items which satisfy criteria
  Technical, rights to manufacture, stock depletion
Manual review to remove unusual items
  Unexpectedly high/low price or unusual part-number

## Slide 33: Technical, Commercial, RTM
SLSC total
Technical
Stock depletion
Right to manufacture
RAMP items

## Slide 34: Costs and Benefits
Cost calculated
  Cost of current stock level
  Cost of stock replenishment without RAMP
  Cost of RAMP stock level
  Cost of raw material stock-holding
Comparison of the sustainable stock level with current and RAMP procurement
The study identified that RAMP for the 1,500 items will release in excess of $4million of inventory cost
Other business process and item quality benefits

## Slide 35: Agenda
Overview of RAMP
UK Evaluations of RAMP
  UK Navy RAMP Project
  Evaluation of UK Navy Store for AP224
  DML RAMP Evaluation Project
UK Deployment of RAMP
  Submarine Legacy Spares – business case
  Submarine Legacy Spares – status
  RAMP at DML

## Slide 36: DML RAMP Technical Centre
A new facility set-up an operated within DML
Technology transfer project
  Joint team from DML and LSC with input from MXS
  Moving to be DML operated
Two parallel implementations Design and Manufacture
The 1,500 items, effort divided into phases
  Phases scheduled by common product types
Contributions from Design and Manufacture teams
  Phase initiated when items identified on CRISP as RAMP supply
  We are currently at phase 1, 286 screw and bolt items

## Slide 37: RAMP Technical Centre Operation
Review of the commercial requirement of the SLSC items
Classification of designs
  Identification of product groups a
  Acquisition of drawings
Prepare Technical data pack and data cleansing
Identification of manufacturing engineering requirements
  Establish best feature represented for manufacture
Generation of STEP AP224 data verification
Identification of manufacturing processes
  Building knowledge base around item group
  Building NC command library

## Slide 38: DML RAMP Order Sequence

## Slide 39: DML RAMP Environment

## Slide 40: Design Product Team
Design product grouping allows for efficiency in the generation of item design representations as STEP files
  Model the family complexity once and re-use
  Application of standards to a range of products
  Reduced design verification time
Ensuring that the STEP file represents the designers intent
  Group similar enquiries to the design authority perhaps allowing precedence examples
  Increase familiarity with design requirements

## Slide 41: Manufacturing Product Team
Organisation of Manufacturing Engineering best practice
Optimum Material, equipment selection
  Supply of cut sequences for NC generation as appropriate
  Inspection criteria, generation of quality assurance requirements
Validation experience can be applied to the product group
  Formal testing of items within a range

## Slide 42: Agenda
Overview of RAMP
UK Evaluations of RAMP
  UK Navy RAMP Project
  Evaluation of UK Navy Store for AP224
  DML RAMP Evaluation Project
UK Deployment of RAMP
  Submarine Legacy Spares – business case
  Submarine Legacy Spares – status
  RAMP at DML

## Slide 43: RAMP in Operation
Reduction in order size and the time between item orders
RAMP helps with reduction in costs of processing orders
Order quantities adapted/minimised by SLSC manager
  to support immediate demand
  to meet the predicted demand supply within the lead time plus contingency
With continued refinement in use
  Manufacturing lead time will reduce
  Contingency will reduce
By partnership,
  Solution for MXS & DML is low stock, assured supply

## Slide 44: RAMP Operations
Notes: RAMP manufacture is conducted with the same material allocation, processing, machines. The main change is in the time between receipt of an order and being able to start manufacture. All of the design information is available, it needs to be prepared as current manufacturing procedures. This is the RAMP bit.

## Slide 45: RAMP Implementation
A prudent approach to implementation
  Not initially adopting a zero stock policy
  Preparing design and manufacture capability prior to reduced order sizes
Phased introduction of RAMP
  In four phases by design/manufacture product group
  Within each phase, deplete largest stock items first
Observed that the actual demand has been higher than CRISP FDR
  More items can be covered within the SLSC
  The cost benefits will be available earlier than predicted

## Slide 46: RAMP Progress Review
Project review
  Scheduled for 6 months from project start
Success, how do you measure?
  Implementation progress
    Item representation
    Ability to manufacture
  Financial review
    Order denials to avoid manufacture for stock
    Stock reduction

## Slide 47: RAMP Implementation progress
Financial review
Not all 286 items have been identified on the MoD procurement system as RAMP
Provides a controlled opportunity to compare procurement policy
Where procurement is by RAMP
  Achieved 1/3 of the projected total (8 year) savings
Where procurement have not been set RAMP
  Stock cost has increased significantly
Conclusion – need to get working for all items

## Slide 48: Looking ahead
We can expand the RAMP concept to other spares contracts, even to OEMs.
We should consider requiring the supply of manufacturing data rather than spare parts for new equipments.
We need to expand the range of RAMP capable items to include more technically complex parts
Manufacture locally if required.
RAMP can be used to hold items in lowest value form (eg casting), with different variants machined when demanded.
We could aggregate the production of parts from STEP files to gain competitive leverage in the market.
Dan Smith Team Leader, Marine Auxiliary Systems IPT

## Slide 49
Case Study Reducing Inventory
in the Ship Support Industry
Lean Manufacturing Workshop
Seattle
Alan Crawford
alc@lsc.co.uk
Thursday, July 30, 2026
US$ values approximated at $2=£1
Notes: 2