## Slide 1: Boeing’s AP238 Early Implementation Study

## Slide 2
David Odendahl
Al Glasscock – project manager
Ted Schultz – project architect
Mauro Costa
Steve Dostert
Sid Venkatesh
Keith Mackay
TEAM Members
BCA Tulsa Division
7E7 Factory Controls
Material & Process Tech.
BCA Fabrication Division

## Slide 3
Boeing is presently examining AP238 to see if the standard’s toolpath description capabilities can be used to streamline the data flow between existing CAD/CAM systems and CNC machine tools.
Why???

## Slide 4
Present Situation - “Dumb CNC”
Presently, CNC machines receive data defining the axis movement required in order to manufacture a part for a specific machine configuration. This is referred to as MCD or machine control data.
MCD is a very low level of instruction. Traditional NC manufacturing processes do not allow access to higher-level information about the tasks they are executing or the part they are trying to manufacture.
High-level intelligence is only utilized at the CAD and CAM stages of the manufacturing process.

## Slide 5: “Dumb CNC” Problems
Not Portable
  Unique data must be generated for each machine control combination on which the part is to be run
Not Adaptable
  No information is provided to the machine to help it adapt to real-time changes in machining dynamics and machine tool conditions.

## Slide 6: Target - “Smart CNC”
Cutter movement data, instead of axis movement data is sent to the CNC. Sophisticated CNCs have the capability of converting cutter movement data to axis movement data.
High level information about the part features, materials, cutters, and dimensional tolerances can also be sent to the CNC.
This information should be sent using a data standard such as: ISO 10303, AP238 (STEP-NC).

## Slide 7: Benefits
Portable
  Cutter motion data is “machine neutral” and may be used directly by machines with different geometries or kinematics.
Adaptable
  High level data can be used by the CNC to adapt to changing production environments and machining conditions.
Expandable
  A route is established to transfer other data/ information to and from the CNC, such as As-built measurement data, machine health, etc.

## Slide 8: Tool Motion Vs. Axis Motion
On machines with different geometries/kinematics, different axis motions are required to achieve the same cutter motion relative to the part

## Slide 9: Demonstration A: Portability
Plan – demonstrate portability
Result – identical parts from one file
AP238 file
5 Axis
Gantry
5 Axis
Horizontal
Profiler
5 Axis
Horizontal
Table/on Table
5 Axis
Vertical
Trunion
CNC Vendor A
Format
converter
NIST
5 Axis
5 Axis
Horizontal
Trunion
CNC Vendor B
Format
converter
5 Axis
Trunion
Head

## Slide 10: Test Part for Demonstration A
NAS 979 Circle-Diamond-Square combined with a NAS 979 cone test.
(This part, if complete in time would be shown at the OMAC and ISO meetings)

## Slide 11: Demonstration B: “Real World” Practicality
The practicality of using AP238 to define and produce a complex, 5-axis, “real-world” part is unproven
  Are file sizes reasonable?
  Is processing time unreasonable?
  Can the required software be produced?
  What other problems will be encountered?

## Slide 12
Test Part for Demonstration C
A Five-Axis Aerospace Part
(The part would be shown if completed in time for OMAC/ISO meetings)

## Slide 13: Progress to Date
Prototype converters for transferring CATIA V5 files to AP238 Part 21 format using Boeing-developed software and third-party software tools from STEP Tools written.
Prototype converters for transferring AP238 Part 21 files to CNC written.
NAS 979 CDS/Cone test part processed and dry run
5-Axis aerospace part processed and dry run

## Slide 14: NAS 979 CDS/Cone Test Part
CATIA CL file size: 201 KB
AP238 Part 21 file size: 114 KB
NC file size: 45 KB to 104KB
Total processing time: 5 seconds
( 1 GHZ Pentium )

## Slide 15
5-Axis Aerospace part
CATIA CL file size: 2077 KB
AP238 Part 21 file size: 2305 KB
NC file size: 560 KB to 1304 KB
Total processing time: 20 seconds
( 1 GHZ Pentium )

## Slide 16: Requested Enhancements to AP238
Add bounded_curve representation for machining_toolpath_speed_profile_representation
Allow selection of one of multiple possible tool position and vector (angle) solutions.
Add CNC pass-through capability
Define shape of tool holder for collision avoidance
Add toolpath_tolerance entity

## Slide 17: Add bounded_curve representation for machining_toolpath_speed_profile_representation
This enhancement will allow simpler, cleaner conversions of CL files to AP238.The existing standard only allows constant or b-spline representation of feedrate profiles. This would require that new toolpaths be generated for each feedrate change, or, for the existing feedrate, parametric curves be converted to and from b-spline format.

## Slide 18: Allow selection of one of multiple possible tool position and vector (angle) solutions
In some machine configurations, a given tool vector can be achieved in multiple axis positions. The addition of range limits to any axis allows the NC programmer to direct the CNC to select the correct tool vector solution(s).

## Slide 19: Add CNC pass-through capability
The addition of CNC pass-through capability allows the NC programmer to command machine functions that are presently unsupported by AP238. It is expected that over time, AP238 would be expanded to support this functionality

## Slide 20: Define shape of tool holder for collision avoidance
AP238 does not presently support the transfer of the geometry for the tool holders. This information is important in order to support collision detection at the machine.

## Slide 21: Add toolpath_tolerance entity
Modern CNCs are capable of making trade- offs between toolpath accuracy and speed. The addition of a toolpath_tolerance entity allows the CNC to optimize this trade-off with the guidance of the NC programmer

## Slide 22: Questions?