## Slide 1: The promise of AP-238 A Stand-Alone CAM Vendor’s Perspective
John Callen
VP, Marketing
Gibbs and Associates
Moorpark, CA
© 2004, Gibbs and Associates

## Slide 2: Presentation Outline
Current State of Technology & Industry
Primary Benefit of AP-238
Secondary Benefits of AP-238
Challenges
Outstanding Concerns

## Slide 3: Current State
CAM Market highly fragmented, with different proprietary solutions for market segments and regions
Users often have multiple CAM systems
Capital equipment investment in machine tools is high and length of service is long
Engineering drawings are still crucial to communicate product specification

## Slide 4: Primary Benefit of AP-238
Next generation data format for CNC machine tools, replacing RS274-D
  Supports higher representational level than stroke data
  Encodes part specification
  Provides comprehensive data to facilitate manufacturing

## Slide 5: Post Processing
Post processing is a considerable cost in manufacturing systems
  Whether vendor-supplied or user-developed post processors are required
Unique posts are needed to handle subtle machine differences
  For example, Gibbs’ post library contains over 6000 posts
AP-238 will provide a consistent post processing format for machine types

## Slide 6: Secondary Benefits
Though it is clear that AP-238’s purpose is to address the data requirements of CNC devices, there are a number of secondary benefits that can also be realized through the development of AP-238.

## Slide 7: Secondary Benefit #1
CAD-to-CAM data exchange does not provide enough information to support manufacturing automation
AP-238’s data requirements have raised the awareness of manufacturing data requirements

## Slide 8: Secondary Benefit #2
Vast majority of CAM systems are nominally based with limited automation
AP-238 requires the non-nominal data needed for CAM system automation

## Slide 9: Secondary Benefit #3
Proprietary nature of CAM systems prevents the exchange of manufacturing data between them
AP-238 provides a neutral format to represent process data

## Slide 10: Challenges
Even though AP-238 offers numerous benefits, there are a number of challenges that need to be addressed before it can be leveraged out in industry

## Slide 11: Challenge #1 “Chicken and Egg” Dilemma
Generating AP-238 Data
Without a strong demand for AP-238 by customers, vendors will not support it; users will not demand it if they don’t see clear value
- Use real-world prototype projects to validate AP-238 concepts and value

## Slide 12: Challenge #2 ”All Dressed Up, Nowhere to Go” Dilemma
Legacy Machine Tools
If the vast majority of machine tools do not “speak” AP-238, how can they use it?
- Using AP-238 CAM adaptors as a front-end to legacy machine tools

## Slide 13: AP-238 CAM Adaptor

## Slide 14: Challenge #2b ”All Dressed Up, Nowhere to Go” Dilemma
Controller Support
Without a strong demand for AP-238 by customers, vendors will not support it; users will not demand it if they don’t see clear value
- Next generation machine tool initiatives (SMPI, OMAC) require AP-238’s data

## Slide 15: SMPI (Smart Machine Platform Initiative)
  Next Gen machine tools
  Ensures “first part correct”
  Self-aware
    Self-adjusting
    Self-maintaining
    Self-optimizing
Figure courtesy of Clayton Teague,
Mfg Eng Lab, NIST

## Slide 16: Challenge #3 “Big Hose Connected to a Little Spigot” Dilemma
Product Data
Even though AP-238 supports non-nominal data, CAD systems currently only support exporting geometry
- AP-203 2nd Edition use by CAD will allow non-nominal data exchange

## Slide 17: Challenge #4 “Wouldn’t Know What to Do With A Surface Finish If It Saw One” Dilemma
Nominal CAM
CAM systems rely on users to blend imported CAD geometry and interpreted product specifications
- With the availability of product data, CAM technology and systems will evolve

## Slide 18: Outstanding Issues
With all the progress on AP-238 that has been made, that doesn’t mean that there aren’t some outstanding (technical) issues to be resolved for it to be successful

## Slide 19: Issue #1
Generic Process Plans
- Can process plans be defined so that they are portable across various types of “similar” machine tools?
- Can machine requirements be accurately deduced by parsing an AP-238 file?

## Slide 20: Issue #2
Non-nominal Manufacturing
- Do we really understand the full manufacturing implications of GDT?
- If we could build a non-nominal CAM system, where do we get the knowledge base it uses?

## Slide 21: Issue #3
Product Data Modeling
What will it take for CAD systems to move from geometric modeling to product data modeling?
Can computer-interpretable digital models replace engineering drawings?

## Slide 22: Issue #x
The Unknown
- What will we discover that we didn’t address when we get further down the road?

## Slide 23: Summary
The development of AP-238 has the potential to introduce a huge evolutionary step forward for manufacturing technologies realized not only through the standard itself, but by the ancillary technologies it will enable.

## Slide 24
Thank You!

## Slide 25: Follow-up
Gibbs and Associates
323 Science Drive
Moorpark, CA 93021
Phone (805) 523-0004
Fax (805) 523-0006
John.Callen@GibbsCAM.com
www.GibbsCAM.com