## Slide 1: AP-238 DIS Walkthrough
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Seattle SC4 Meeting
October 2004

## Slide 2: Walkthrough of AP-238 DIS
Based on Part 10
Measures
Project
Workpiece
Features
Milling Process Operations Based on Part 11
Milling Cutting Tools Based on Part 111
Turning Process Operations Based on Part 12
Turning Cutting Tools Based on Part 121
Executable
Operation
Toolpath
AP-238 pulls together machining process, tool requirement, geometry, tolerances, and PDM.
  Start with process and tools described by ISO 14649 parts
  Add STEP PDM, Geometry, and Tolerances, and integrate so that features and all other data can be shared across APs
Dimensions and Tolerances STEP GD&T
PDM and Product Geometry Common to all APs

## Slide 3: Updates Since CD Ballot
Updates include
  Clarified features in new “fundamental concepts” section, and extended 14649 definitions with necessary
  Added mappings for the turning model (P12, P121)
  Finished toolpath mappings and added enhancements.
  Added ARM description for PDM Information
  Added harmonized GD&T definitions
  Changes to accommodate SC1 concerns about clarity
  Many other smaller fixes.

## Slide 4: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 5: Updates Since CD Ballot
Features
  New “Fundamental Concepts and Assumptions” section addresses remaining feature harmonization issues.
  Worked with Len and Alan in January 2004 to add AIM rule changes to AIC522e2 and ARM changes to AP-224e3.
PDM Information
  Added new management UOF and mappings to clarify the handling of approvals and other PDM data. Harmonized with the appropriate modules (ISO 10303-1012, 1015).
GD&T
  Resolved all harmonization issues.
  Added ARM and mappings for harmonized definitions
  Extended ARM definitions in “Measure” UOF to explicitly describe units, tolerances on parameters beyond length.

## Slide 6: Workpiece, Shape, and PDM
The workpiece is a STEP product description
With all of the owner information, approvals, dates and times.
Material and material properties
Shape for workpiece uses advanced B-REP, just like all of the other STEP APs.
Produced by any CAD system that supports STEP.

## Slide 7: Updates: PDM
Added new management UOF and mappings to clarify the handling of approvals and other PDM data.
  Harmonized with module 1012 for approvals and module 1015 for security classifications
  New application objects for Approval, Approval_relationship, Approval_status, Approving_person_organization, Security_classification, Security_classification_assignment.
  Person and organization ARM concepts already present in the Project UOF.
Added last modified timestamps as per ballot comments
  can associate with projects, workpieces, executables, operations, or toolpaths

## Slide 8: Machining Features
round hole
counterbore hole
compound feature
pocket with
through bottom
condition
pocket with
flat bottom
condition
slot with
radius
ends
2.5D milling features
  Hole, pocket, slot, step, etc
Transition features
  Edge round and chamfer
Replicate feature
  Patterns of repeated features
Region features
  Surfaces for freeform milling
Turning features
  Outer round, knurl, groove
Notes: This slide represents the highlights of AP224.
The list of items in each box represents a sample of what AP224 contains.
To summarize - AP224 contains everything found on a drawing of a part

## Slide 9: Updates: Fundamental Concepts
Added the new “Fundamental Concepts and Assumptions” section to clarify features
  Structural Issues had been harmonized long ago, but some subtle issues remained.
  Clarify assumptions on how to interpret origin for positioning, calculate feature volume and other things.
  Explain additional capabilities beyond ISO 14649, such as explicit representation and process vs. final features

## Slide 10: Updates: Feature
Additional attributes to bound the volume
  Previously, open profiles infinite in extent
  Added to ARM, mappings to describe how far profile extends
  Square “U”, Rounded “U”, and “Vee” profiles for slots, steps, and open pockets
  Removal depth on planar face
  Pushed back changes to other APs through AIC522e2 and ARM changes to AP-224e3.
extent #1
extent #2

## Slide 11: Updates: Feature
Additional attribute to link to explicit shape
  ISO 14649 has no way to link feature with part geometry
  ISO 10303 can provide an explicit description linking geometry
  Both ISO 14649 and ISO 10303 provide implicit feature description (profiles and paths)
Implicit description
A round_hole is defined by a complete circular profile and a linear path
Explicit description
Refers to the B-REP faces on the geometry that describe the hole

## Slide 12: Updates: Explicit Shape
Workpiece
product /
product definition
formation /
product definition
shape definition
representation
shape representation
(usually an advanced
brep shape rep)
product definition
shape
shape definition
representation
shape representation
explicit
description
The Feature
complex instance
of instanced_feature
and feature_definition
subtype
through
shape_aspect
of_shape
product definition
shape
other shape
aspects describing
aspects of the
feature
shape definition
representation
shape representation
with parameters
implicit
description

## Slide 13: Update: Process and Final Features
An AP-238 model has the notion of both final feature and process feature
  Final feature is on final part, from upstream, possibly from an AP-224 or AP-240 application. As such, some features might only define a volume when combined with the stock.
  Process features are the features pointed to by ISO 14649 workingstep. Specific to a workplan, needs full volume limits.
  In AP-238 workingstep can also point to one or more final features that it contributes to. (and many workingsteps and process features may contribute to one final feature)
Final feature in red (POCKET)
Process features to:
- Drill the corners (HOLE)
- Mill out center with large tool (POCKET)
- Mill remaining material
with smaller tool (FINAL POCKET)

## Slide 14: Updates: Added Turning Features
manufacturing
feature
machining
features
2.5D manufacturing
turning feature
replicate
feature
cut_in
STEP-NC Features
outer diameter
revolved feature
outer round
groove
general revolution
revolved round
revolved flat
knurl
outer diameter
to shoulder
Turning features are now harmonized between Part 12 and AP-224/AP-214
No problems encountered adding the mappings for all turning features.

## Slide 15: Dimensions and Geometric Tolerances
Dimensions defining location
  Location defined by a linear distance
  Location defined by a distance along a curve
  Location defined by an angle
Dimensions defining size
  Curves, angle, diameter, radius, thickness, length, width, height
Geometric characteristics with datums as needed.
  angularity, circular runout, coaxiality, concentricity, cylindricity, flatness, line profile, parallelism, perpendicularity, position, roundness, straightness, surface profile, symmetry, total runout
0.01
0.01
A
0.01
A

## Slide 16: Updates: GD&T
Added GD&T ARM definitions and mappings
  49 new ARM objects, plus things in the measure UOF
Before adding to AP, needed to resolve some harmonization issues between APs.
  Harmonized across AP-214, AP-224, AP-240, and AP-203e2, which uses Modules 1050 and 1051. Will also be going into AP-219 and other APs.

## Slide 17: Updates: GD&T Harmonization
Discussed and Resolved Incompatibilities
  Resolved AIM mapping differences on handling of all four value qualifications (range, plus/minus, etc)
  Agreed on common set of size dimensions
    New externally defined size, length, width, height
  Harmonized mapping of envelope principle
  Harmonized mapping of angular size full/half angle
  Extended directed flag to all location dimensions
  Adopted simplified angular location using axis placement.
  Added centered/adjoining flag to radial size dimension
Issues arising from AP-214 SEDS
  Added qualifying notes, including “auxiliary” and “theoretically exact” for dimensions (SEDS 888-891)
  Added way to specify dimensioning standard for a workpiece (SEDS 892)

## Slide 18: Updates: GD&T Harmonization
Discussed Big Picture Strategies for GD&T
  Linking of dimensions with the draughting presentation elements of the dimensions.
  Relationships with TC 10 and TC 213
  Developed response to TC-213 “expression of concern” about some terminology usages.
In Seattle, resolved some issues discovered on Geometric Tolerances
  Mapping path for affected_plane attribute (harmonization)
  Mapping for Common_datum in AP-224 vs AP-214/1051 (harmonization)
  Distinction between Datum reference and Datum (usage)
  Link between datums and manufacturing features (usage)

## Slide 19: Updates: Enhancing the Measure UOF
The original ISO 14649 measures
  Do not allow choice of units. Fixed to mm, deg, m/s
  Defines plus/minus, limits & fits for length parameters only
Enhanced the ARM definitions in AP-238 so that:
  All measures can specify their units, as in all other APs.
  Parameter tolerances can be used for any quantity, not just lengths. Now available for angles, speeds, etc.
  Allows Max/Min limitation for toleranced parameters.
The mappings are harmonized with GD&T

## Slide 20: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 21: Progress Since CD Ballot
Toolpaths
  Completed mappings for toolpath subtypes, added all of the matching EXPRESS constraints to the relevant AIM types.
  Added ARM and mappings for toolpath enhancements determined by 5-axis implementation tests.
Relationship with SC1
  New relationship subtypes from WG12 meeting.

## Slide 22: Machining Programs
The heart of the STEP-NC model
  Workplans containing a sequence of workingsteps.
  Each workingstep associates an operation with a feature somewhere on the workpiece.
  Each operation describes what to do and what strategies and parameter settings to use.
More information than M and G codes. Linked with geometric and technological information.
  Parameters can be grouped and shared, e. g. tools, feeds, etc.
  Intelligent NC controllers can calculate tool movements for standard features.

## Slide 23: Machining Programs
Project
  Starting place, defines setup and main workplan
Executables
  Describes control flow and sequencing.
  Workingstep associates an operation and a feature.
  Technology independent
Operations
  Describes what a workingstep does to a feature — plane mill, center drill, etc.
  The basis for all technology-specific extensions.
  Specifies details like
    spindle, feedrate and other technology parameters
    coolant & other machine functions
    plunge strategies, tool paths, etc.

## Slide 24: Control Flow and Sequencing
executable
nc function
program
structure
workingstep
machining workingstep
rapid movement
touch probing
STEP-NC Executables
Program steps that do not move any machine axes
(display message, etc.)
Control flow for the machining program
workplan
parallel
if_statement
while_statement
Program steps that move
the machine axes

## Slide 25: Updates: Relationship Subtypes
In discussions with SC1, agreed to help clarify data by adding AIM subtypes for relationships
  Analyzed AP and found 18 distinct relationships
  Create AMR subtypes and name them based on thing that is being referenced
    machining_adaptive_control_relationship
    machining_functions_relationship
    machining_operation_relationship
    machining_operator_instruction_relationship
    machining_process_model_relationship
    machining_strategy_relationship
    machining_technology_relationship
    machining_toolpath_sequence_relationship (actually a subtype of sequential_method)

## Slide 26: Updates: Relationship Subtypes
Further subtyping helpful for some relationships.
  multiple inheritance used when a different subtype is also needed for sequencing.
  machining_feature_relationship
    machining_feature_sequence_relationship (also inherits from sequential_method)
  machining_final_feature_relationship
  machining_process_body_relationship
    machining_process_sequence_relationship (also inherits from sequential_method)
    machining_process_concurrent_relationship (also inherits from concurrent_action_method)
    machining_process_branch_relationship

## Slide 27: Old Way: Milling Operation
The Operation
bottom_and_side_
milling_operation
desc = “rough”
To Workingstep
action_method_relationship
name = “machining strategy”
action_method_relationship
name = “approach strategy”
action_method_relationship
name = “machine functions”
action_method_relationship
name = “technology”
action_method_relationship
name = “operation”

## Slide 28: New Way: Milling Operation
The Operation
bottom_and_side_
milling_operation
desc = “rough”
To Workingstep
machining_strategy_relationship
name = “machining”
machining_strategy_relationship
name = “approach”
machining_functions_relationship
machining_operation_relationship
machining_technology_relationship

## Slide 29: Project and Setup Subtypes
Also added subtypes to clarify project and setup
  Added product subtypes to identify the project/setup
  Replaces the use of a product category classification.
    machining_project
    machining_setup
  Added product definition relationship subtypes to clarify the linkage between workpieces and the project or setup.
  Replaces the use of a plain PDR with a name string.
    machining_setup_workpiece_relationship
    machining_project_workpiece_relationship

## Slide 30: Old Way Project Example
product definition
product
name = “MAKE PARTS FAST”
product definition
formation
The Project
product_related_product_category
name = “machining project”
product definition
product
“widget”
product definition
formation
The Workpieces
product definition
product
“doohickey”
product definition
formation
product_related_product_category
name = “detail”
product definition relationship
name = “workpiece”
product definition relationship
name = “workpiece”

## Slide 31: New Way Project Example
product definition
machining_project
name = “MAKE PARTS FAST”
product definition
formation
The Project
product definition
product
“widget”
product definition
formation
The Workpieces
product definition
product
“doohickey”
product definition
formation
machining_project_
workpiece_relationship
machining_project_
workpiece_relationship

## Slide 32: Toolpaths
Diagram WZL RWTH Aachen
Used for explicit control of the tool motion for an operation.
  Can use splines or other curves to describe motion and feedrates.
  Can describe path as machine independent motion of tool center point or tool contact point.
  Can also describe path using old-style machine dependent motion of individual axis.

## Slide 33: Updates: Toolpaths
Added toolpath enhancements for 5-axis work
  Maximum deviation for path or tool direction
  Milling tool holder profile to enable collision checking
  Relaxed curve constraints on speed profile to allow polylines
  Machine Axis constraint to limit the range an axis may traverse
  NC pass through capability to allow legacy codes to be passed through to the underlying controller

## Slide 34: Toolpath AIM Representation
machining_toolpath
action_method
ARM Toolpath and subtypes are mapped to AIM machining_toolpath.
  Toolpath base class was already completely mapped.
  Added mapping table entries and corresponding AIM EXPRESS local rules for the subtypes.

## Slide 35: AP-238 Units of Functionality
Product Description
  Workpiece, PDM and Product Geometry
  Features
  Dimensions and Tolerances
  Measures
General Process Description
  Project
  Executable
  Operation
  Toolpath
Technology Description
  Milling Process Operations
  Milling Cutting Tools
  Turning Process Operations
  Turning Cutting Tools

## Slide 36: Progress Since CD Ballot
Turning Model
  Added mappings for turning features, operations and tools.
  Reworked mappings for feedrate, spindle speed, and dwell time to unify usage across milling and turning models.

## Slide 37: Milling Process Operations
Drilling Operations
  Drilling, boring, back boring, tapping/threading
  Tool moves in the Z axis only
  Many strategy parameters
2.5D Machining Operations
  Plane and side milling, roughing and finishing
  Tool can move XY or along Z, but not at the same time.
  Set of strategies
Freeform Machining Operations
  For sculpted surfaces
  3, 4, and 5axis motion
  Set of strategies

## Slide 38: Turning Process Operations
Turning Operations
  Contouring, facing, grooving, threading and knurling.
  Roughing and finishing for each
  Set of strategies
Possible Future Operations
  Work underway to describe operations for wire and sink EDM, contour cutting of wood and glass, grinding.
  Efforts in various stages of maturity.
  Will be added to AP-238 once the information requirements are mature.

## Slide 39: Milling and Turning Cutting Tools
Every operation can have a tool associated.
  Represents tool requirements, not a physical tool on a machine.
  Potential for some best-fit optimization by the controller.
G&M codes just referenced tool #1, #2, etc.
  Human must make sure that #1 corresponds to the right thing.
  Controller not able to add any value to the process.

## Slide 40: Milling and Turning Cutting Tools
Can call out characteristic tool parameters
  Endmills, facemill, ball endmill, bullnose endmill, side mill, tslot, tapered, dovetail, threading and woodruff keyseat mills
  Drills, centerdrill, twist, tapered, or spade drills, combined drill and reamer or tap
  Boring and reaming tools, tapered reamer, counterbore, countersink, backside counterbore and countersink
  Turning, grooving and knurling tools, taps and threading tools

## Slide 41: Updates: Turning Process Data
Added support for the turning parts
  Part 12
  Part 121
Required no major changes
  Mappings are straightforward and follow conventions established by the mill/drill mappings.
  Added UOFs, mappings, and updated AIM constraints.
  The EXPRESS rules for some of the representation subtypes began to get a bit lengthy, so I abstracted the common idioms into new EXPRESS functions:
    verify_[optional/required]_rep_item
    verify_[length/angle]_measure_rep_item.
Very encouraging experience for adding other technology parts

## Slide 42: Turning Operation AIM
machining_operation
milling_type_operation
drilling_type_operation
action_method
turning_type_operation
Several Subtypes
Turning operations represented using several new AIM subtypes
  As with milling/drilling, attributes represented using a collection of action properties.

## Slide 43: Turning Strategies AIM
machining_strategy
milling_type_strategy
freeform_milling_strategy
drilling_type_strategy
machining_approach_retract_strategy
action_method
machining_technology
machining_functions
turning_type_strategy
Turning strategy represented using a new AIM subtype.
  Same techniques as with milling/drilling strategies
  Part 12 references existing approach/retract strategies

## Slide 44: Turning Tech and Functions AIM
action_method
machining_technology
machining_functions
Turning technology and machining functions did not require any new AIM types.
  Milling technology/functions already distinguished by an action_method.description of “milling”.
  Use action_method.description of “turning” to distinguish the turning technology/functions.
  Many properties are common between milling/turning versions. AIM EXPRESS rules simplified.

## Slide 45: Cutting Tools for Turning ARM
tool_body
turning_tool_dimension
machining tool
cutting tool
turning machine tool
turning machine tool body
Referenced From Operation
Part 10
Part 121
Very similar to Part 111 organization
Not as many tool body types
Several Subtypes
Grooving, Knurling, Threading, General
and User Defined

## Slide 46: Turning Tool AIM Representation
action_resource
action_resource_type
Required equipment
Turning tools did not require any new AIM types
  Use action resource subtype machining_tool for the ARM turning_machine_tool concept.
  Has a “kind” attribute that categorizes the resource
    We use value “milling cutting tool” for Part 111 data
    Now add value “turning cutting tool” for Part 121.
machining_tool
kind

## Slide 47: Turning Tool Body and Dimension AIM
S[1:?]
representation_items
representation
representation_relationship
No new AIM types needed for body or dimension
  Use existing representation subtypes developed for Part 111
  As with all of our complex types, properties handled as various representation items within.
  Distinguish tool bodies using the representation.name
  Distinguish milling/turning/other tool dimensions using representation.name “milling”, “turning”, etc.
machining_tool_dimension_representation
machining_tool_body_representation
items

## Slide 48: Progress Since CD Ballot
Other Improvements
  Other CD comment resolutions and fixes.
  Many mapping table bugs fixed, discovered during XML work.
Yet to do:
  Update ARM & AIM EXPRESS-G diagrams.
  Document conformance classes as discussed.
  Add informative annex with XML schema.
  Run through checklists and signoffs
Must submit for DIS ballot by end of October 2004 to satisfy ISO time constraints