## Slide 1: AP-238 Toolpath Extensions
Seattle SC4 Meeting
October 2004

## Slide 2: Toolpath Enhancements
Boeing implementation tests running 5-axis toolpath tests revealed several weak spots.
  Presented briefly at Bath meeting
  Participants met mid-August for three days to work through issues and develop resolutions
Added several enhancements
  Maximum deviation for path or tool direction
  Milling tool holder profile to enable collision checking
  Relaxed curve constraints on speed profile to allow polylines
  Machine Axis constraint to limit the range an axis may traverse
  NC pass through capability to allow legacy codes to be passed through to the underlying controller

## Slide 3: Maximum Deviation
Maximum deviation for path or tool direction
  So that controller can adjust linearization tolerances as well as feed and acceleration rates to remain within the allowed deviations.
  Added as a pair of optional ARM attributes on Cutter contact trajectory and Cutter location trajectory
  Mapped as length (path) or angle (tool direction) action property on the toolpath action_method.

## Slide 4: Milling Tool Holder Profile
Define shape of holder to enable collision checks.
  Added as optional ARM attribute on Milling_cutting_tool (Turning cutting tool had sufficient info for checks)
  Describes what the tool and holder looks like between the end of the flutes (max depth of cut) and the gage line.
  Mapped as surface of revolution resource property on the machining_tool action_resource

## Slide 5: Bounded Curve for Speed
Relaxed curve constraints on Toolpath_speed profile to allow polylines
  Without this, you could only use Bsplines speed curves, and even then only with Bspline path description.
  But polylines are common path description!
  Simply allows you to use the same range of curves in the speed description as you can in the path description.
  Relaxing ARM, no change to the integrated representation.

## Slide 6: Machine Axis Constraint
In some machine geometries, may be more than one axis solution for a given tool motion curve
  If you don’t care, the controller will just pick one.
  If you do care, how to provide guidance?
  Added Machine Axis Constraint identifies an axis and the range of values it is allowed to traverse.
  Extends Milling_machine_functions so that it has a new optional attribute refering to a set of machine axis constraints
  Machine dependant and should be avoided.

## Slide 7: NC Pass-through
During production use, may occasionally need access to capabilities that:
  May be supported by a the underlying controller
  Are currently not addressed by the standard
Add new NC_legacy_function application object
  Clear warnings in normative text to prohibit pathological use
  “shall not be used if equivalent machine behavior can be achieved using other capabilities of this part of ISO 10303.”
  “should not be used because the resulting workplan will no longer be machine independent”
  Added as a new type of nc_function with a string containing the legacy codes.