## Slide 1: GD&T Harmonization Final Results
wg3n1514
David Loffredo
loffredo@steptools.com
2004-10-08
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax

## Slide 2: Harmonization Status
Harmonization now complete!
  Resolved all harmonization issues with dimensions
  Discovered and resolved issues with geometric tolerances
  Resolved SEDS against dimensions
Document owners now finalizing updates
  Len produced updated text and adding into documents
    AP-224 for Edition 3
    AP-240 when submit IS (end of year)
    AP-219, AP-223 as they come along
  Tom updating Modules 1050 and 1051 for AP-203e2.
  Max and ProSTEP team planning amendment for AP-214e2.
  Dave adding to AP-238 for DIS.

## Slide 3: Harmonization Results
Discussed and Resolved Incompatibilities
  Resolved AIM mapping differences on handling of all four value qualifications (range, plus/minus, etc)
  Agreed on common set of size dimensions
    New externally defined size, length, width, height
  Harmonized mapping of envelope principle
  Harmonized mapping of angular size full/half angle
  Extended directed flag to all location dimensions
  Adopted simplified angular location using axis placement.
  Added centered/adjoining flag to radial size dimension
Issues arising from AP-214 SEDS
  Added qualifying notes, including “auxiliary” and “theoretically exact” for dimensions (SEDS 888-891)
  Added way to specify dimensioning standard for a workpiece (SEDS 892)

## Slide 4: Harmonization Results
Discussed Big Picture Strategies for GD&T
  Linking of dimensions with the draughting presentation elements of the dimensions.
  Relationships with TC 10 and TC 213
  Developed response to TC-213 “expression of concern”
In Seattle, discussed some issues discovered on Geometric Tolerances
  Mapping path for affected_plane attribute (harmonization)
  Mapping for Compound_datum in AP-224 vs AP-214/1051 (harmonization)
  Distinction between Datum reference and Datum (usage)
  Link between datums and manufacturing features (usage)

## Slide 5: Resolution Details
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle, Angular Size Full/Half
  Centered vs Adjoining
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard
Geometric Tolerances
  Affected plane, common datum, and ARM clarification

## Slide 6: Position Statement For TC-213
In response to TC-213 “expression of concern”:
We are happy to use TC 213 terminology, and note that we are already referring to 5459:1981 for the definition of Datum.
We ask TC-213 to point out areas where we differ and we will be happy to adopt their terminology.
  Already using the “Common_Datum” term as AIM entity defined in AIC 519
  Will change uses of “Compound Datum” term to “Common Datum.”
  Welcome the chance to meet for a harmonization workshop on an as-needed basis.

## Slide 7: Resolution Details
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle, Angular Size Full/Half
  Centered vs Adjoining
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard
Geometric Tolerances
  Affected plane, common datum, and ARM clarification

## Slide 8: Summary of Resolutions
Value qualifications
  Limit, agreement to clarify mappings in AP-224
  Plus/minus, agreement on separate representations for use inside and outside of dimensions. AP-214 to correct mappings inside dimension to make proper use of dimensional_size, add new mapping for use outside of dimensions
  Limits and fits, as with plus/minus
  Value range, agreement on separate representations for use inside and outside of dimensions. Within dimensions the two rep item approach will be used, everywhere else value_range AIM entity will be used. AP 224 will also extend ARM to support ranges for normal properties.

## Slide 9: Value Limit Mapping
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
Dimension or property definition
on something
Adds qualified representation item to the
complex instance
type_qualifier
name = “maximum”
precision_qualifier
precision_value = 4
This approach is defined in both AP-214 and AP-224
Name of Limit
AP-214 specifies “maximum” or “minimum”
AP-224 does not specify string, but uses “MAX” and “MIN” in an example
Separate qualifier significant digits
Numeric value
for limit

## Slide 10: Value Limit Resolution
AP-224 will clarify ARM by creating subtype of Tolerance_limit for:
  Maximum limit: mapping will call out name=“maximum”
  Minimum limit: mapping will call out name=“minimum”
  Other limit: mapping will leave name unconstrained.

## Slide 11: Value Range
AP-224 has no mapping for use of value range outside of dimension.
  Willing to adopt AP-214 usage in those cases.
AP-214 has mappings for value range but no vendor implementation within dimension.
  There are vendor implementations of value range outside of dimension

## Slide 12: Value Range “Property” Mapping
representation
complex instance of
value_range
qualified_representation_item
name = “length”
For significant digits, a complex instance with qualified rep item is used, which points to a precision qualifier
complex instance of
measure_representation_item
length_measure_with_unit
name = “upper limit”
value = 100 mm
complex instance of
measure_representation_item
length_measure_with_unit
name = “lower limit”
value = 75 mm
Property definition
on product, feature, feature component, action, resource, or anything using a representation
precision_qualifier
precision_value = 4

## Slide 13: Value Range “Dimension” Mapping
shape dimension
representation
Significant digits are related to each value separately using a measure qualification
complex instance of
measure_representation_item
length_measure_with_unit
name = “upper range”
value = 100 mm
complex instance of
measure_representation_item
length_measure_with_unit
name = “lower range”
value = 75 mm
dimensional_size
dimensional characteristic
representation
shape_aspect
geometry and placement
instances
measure_qualification
measure_qualification
precision_qualifier
precision_value = 4

## Slide 14: Value Range Resolution
Agreed solution is to use
  “dimension” two rep item mapping inside of dimensions
  “property” value_range AIM mapping everywhere else
AP-214 to extend mappings for dimension as above.
AP-224 will extend ARM to support ranges for normal properties and map using compound item approach.

## Slide 15: Plus/Minus
AP-224 has implementation of both plus/minus mappings (in dimensions, in feature properties)
AP-214 has mappings for plus minus but no vendor implementation within dimension.
  No implementations outside of dimensions
  Mappings currently have an error that always requires the use of dimensional_size, even in a location dimension.
Module 1106 and 1050 mappings
  1106 has Plus/Minus for use outside of dimensions
    Adopt the qualified rep item mappings
  1050 has Plus/Minus for use inside dimensions
    Should have correct mappings, but derived from AP-214, so check to make sure that they do not have the same problem.

## Slide 16: Plus/Minus Resolution
Agreement on separate representations for use inside and outside of dimensions.
  See following slides for diagrams
AP-214 to correct mappings inside dimension to make proper use of dimensional_size, add new mapping for use outside of dimensions

## Slide 17: Plus/Minus “Property” Mapping (1/2)
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
All other property definitions
on product, feature, feature component, action, resource, or anything using a representation
Adds qualified representation item to the
complex instance
standard_uncertainty
measure_name = “upper limit”
uncertainty_value = 0.001
standard_uncertainty
measure_name = “lower limit”
uncertainty_value = - 0.001
precision_qualifier
precision_value = 4
Points to separate qualifiers for upper,
lower limits and significant digits
NOT FOR USE WITH A SIZE DIMENSION OR LOCATION DIMENSION
(which are mapped to Part 47 dimensional_size or
dimensional_location)
This is an example with length, could be used for angles, times, velocities, etc. as supported by the range of things representable by measure_with_unit

## Slide 18: Plus/Minus “Property” Mapping (2/2)
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
All other property definitions
on product, feature, feature component, action, resource, or anything using a representation
standard_uncertainty
measure_name = “upper limit”
uncertainty_value = 0.001
standard_uncertainty
measure_name = “lower limit”
uncertainty_value = - 0.001
precision_qualifier
precision_value = 4
This is current AP-224 representation.
AP-214 to add alternate mapping for use outside of dimensions when correcting mapping of plus/minus tolerance to dimensional_* entities
NOT FOR USE WITH A SIZE DIMENSION OR LOCATION DIMENSION
(which are mapped to Part 47 dimensional_size or
dimensional_location)

## Slide 19: Plus/Minus “Dimension” Mapping
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
value = 100 mm
precision_qualifier
precision_value = 4
dimensional_size
dimensional characteristic
representation
shape dimension
representation
shape_aspect
plus_minus_tolerance
tolerance_value
length_measure_with_unit
value = 0.001
length_measure_with_unit
value = - 0.001
lower_
bound
upper_bound
of_shape
Geometry and location
measure_qualification
measure_qualification
AP-214 current mapping always requires a dimensional_size, even if a location dimension
(need to fix mapping)

## Slide 20: Limits and Fits Resolution
AP-224 and AP-214 have mappings for limits and fits within dimension.
  AP_214 mappings currently have an error that always requires the use of dimensional_size, even in a location dimension.
AP-238 has requirement for use outside of dimension (as a property)
  Has developed mappings based on qualified rep item that follow the AP-224 plus / minus pattern.
Agreed to follow resolution adopted for plus minus
  Separate mappings for use inside and outside of dimension.
  Dave posted mapping paths to exploder and document repository.

## Slide 21: Limits and Fits “Property” Mapping
representation
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “diameter”
value = 100 mm
All other property definitions
on product, feature, feature component, action, resource, or anything using a representation
Adds qualified representation item to the complex instance
Uses qualitative_uncertainty for descriptors
qualitative_uncertainty
measure_name = “form variance”
uncertainty_value = “A”
qualitative_uncertainty
measure_name = “zone variance”
uncertainty_value = “H”
Follows the pattern established by the Plus/Minus mapping with qualifiers for each fit descriptor
qualitative_uncertainty
measure_name = “grade”
uncertainty_value = “IT01”
precision_qualifier
precision_value = 4
NOT FOR USE WITH A SIZE DIMENSION OR LOCATION DIMENSION
(which are mapped to Part 47 dimensional_size or
dimensional_location)

## Slide 22: Limits and Fits “Dimension” Mapping
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
value = 100 mm
precision_qualifier
precision_value = 4
dimensional_size
dimensional characteristic
representation
shape dimension
representation
shape_aspect
plus_minus_tolerance
limits_and_fits
form_variance = “A”
zone_variance = “H”
grade = “IT01”
of_shape
Geometry and location
AP-214 requires mapping fix already noted in plus/minus slide

## Slide 23: Resolution Details
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle, Angular Size Full/Half
  Centered vs Adjoining
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard
Geometric Tolerances
  Affected plane, common datum, and ARM clarification

## Slide 24: Summary of Resolutions
Types of Size Dimensions
  Update AP-214, AP-224, and Module 1050 as follows:
  Expand list of specific size dimensions to the union of types in 224, 214 and those “hiding” under general_size.
  Add a document reference to general_size that calls out where it is defined. Possibly rename to externally_defined_size.
    Upward compatible change to AP-214, 1050
Envelope Principle
  Update AP-214/Module 1050 mappings to AP-224 approach and relax ARM to allow envelope on any size dimension.
  Update AP-224 ARM to restrict usage of envelope to size only by moving attribute in the ARM to size_dimension
Angular Size Full/Half Angle
  Update AP-214/Module 1050 mappings to AP-224 approach.

## Slide 25: Common Set of Size Dimensions
Everyone will use the following sizes and AIM representations
  Note the string for Curved size is as used by AP-224, this will be a change for AP-214, which used “curved dimension”
  Curved size dimensional_size.name = 'curve length'
  Diameter size dimensional_size.name = 'diameter'
  Radial size dimensional_size.name = 'radius'
  Thickness size dimensional_size.name = 'thickness size'
  Length size dimensional_size.name = 'length'
  Width size dimensional_size.name = 'width'
  Height size dimensional_size.name = 'height‘
  External size externally_defined_dimension_definition

## Slide 26: Sizes with path
AP-224 defines radius, curve, and diameter size dimensions without path.
AP-214 defines them and length, width, height as part of general size, which has a path.
Agree to define the new size dimensions with an optional path.
  If no path, mapped as dimensional_size
  If present, mapped as dimensional_size_with_path

## Slide 27: External Size Suggested ARM
ENTITY externally_defined_size_dimension SUBTYPE OF (Size_dimension); external_source_id : STRING; external_source : assigned_document_select; used_path : OPTIONAL Measurement_path; END_ENTITY;
Aside from renaming in the ARM, upward compatible with existing general_size definition
In ARM, AP-214 and modules may do as a separate document_assignment + rule to require it.
In ARM, AP-224 may do as above.
In AIMs, will be mapped as document assignment

## Slide 28: Mapping for Externally Defined Size
Handled by AIM the new subtype below:
externally_defined_dimension_definition
  SUBTYPE OF (externally_defined_item, dimensional_size)
Mapping has two cases, depending on whether a path is specified
  If no path, mapped as externally_defined_dimension_definition
  If present, mapped as a complex instance of externally_defined_dimension_definition and dimensional_size_with_path
See next slide for agreements and strings.

## Slide 29: Mapping for Externally Defined Size
externally_defined_size_dimension
(possibly complex instance with
dimensional_size_with_path)
dimensional_size.name = “???”
externally_defined_item.item_id =
“external size dimension”
dimensional characteristic
representation
shape dimension
representation
shape_aspect
of_shape
Geometry and location
Numeric value
external_source
source_id = “external size
dimension specification”
Use the dimensional_size.name to describe the type of the dimension
(dimension_type/tolerance_class)
Mapping will use string constants shown in BLUE

## Slide 30: Size Dimension Resolutions
Change AP-214 general_size to externally defined size as described.
  Adds document reference, possible name change.
  Upward compatible change to AP-214, Module 1050
  New addition to AP-224
Move specific types out from general_size
  Radius, diameter, curved path become separate ARM objects in AP-214 and module 1050
  Others as below
Add missing size dimensions to AP-224
  Thickness
  Others as below
Add separate size dimensions for length, width and height to both APs.

## Slide 31: Envelope Principle
There were three different mappings for the envelope principle
  AP-224: name of the dimensional characteristic representation
  AP-214: classification assignment on plus_minus_tolerance
  Module 1050: classification assignment on dimensional_size
See diagram on next slide

## Slide 32: Envelope Principle
complex instance of
measure_representation_item
length_measure_with_unit
qualified_representation_item
name = “length”
value = 100 mm
dimensional_size
dimensional characteristic
representation
shape dimension
representation
name = “envelope tolerance”
shape_aspect
plus_minus_tolerance
tolerance_value
length_measure_with_unit
value = 0.001
length_measure_with_unit
value = - 0.001
lower_
bound
upper_bound
of_shape
Geometry and location
AP-224
applied_classification_assignment
classification_role
name=“further tolerance requirement”
group
name=“E”
description = “dimensioning principle”
AP-214
1050

## Slide 33: Envelope Principle Resolution
AP-214/Module 1050
  Change to dimensional_characteristic_representation.name approach in the AIM.
  AP-214 must change ARM to allow envelope on any size dimension. Move attribute envelope from value_limitation to size_dimension
AP-224
  Restrict usage of envelope to size only by moving attribute in the ARM to size_dimension

## Slide 34: Angular Size Full/Half Angle
Angular Size Full/Half mapping
  AP-224 maps as a rep_item name
    not clear exactly what the rep item should be
  AP-214 maps as a dimensional_size.name
Resolution
  Change to use a descriptive rep item named “angle type” with a description value of “full angle” or “half angle”
  Update AP-214 / Module 1050 mappings to use this approach.
  Update AP-224 mappings to use this approach.
  See diagram on next page.

## Slide 35: Angle Full/Half Mapping
shape dimension
representation
complex instance of
measure_representation_item
plane_angle_measure_with_unit
name = “upper range”
value = 22 deg
complex instance of
measure_representation_item
plane_angle_measure_with_unit
name = “lower range”
value = 19 deg
angular_size
dimensional characteristic
representation
descriptive_representation_item
name = “angle type”
desc = “full angle” / “half angle”

## Slide 36: SEDS on Radial Dimension
Radial Tolerances are not completely supported
  Curtis wants distinction between centered and “adjoining” radius tolerances
  ANSI Y14.5 does have two notions of radii, ISO 1101 may but is unknown.
  In practice, distinction between two types comes from how the feature is located.
    In STEP, we may not have a location dimension to get to it. Instead, may be located by the shape_rep geometry.
ACCEPT
  Add an optional ARM attribute to radial size dimension for centered vs adjoining
  Mapped as descriptive_representation_item
    name = “radius type”
    description either “centered” or “adjoining”

## Slide 37: Centered vs. Adjoining Radius
shape dimension
representation
complex instance of
measure_representation_item
length_measure_with_unit
name = “upper range”
value = 22 mm
complex instance of
measure_representation_item
length _measure_with_unit
name = “lower range”
value = 19 mm
dimensional_size
name = “radius”
dimensional characteristic
representation
descriptive_representation_item
name = “radius type”
desc = “centered” / “adjoining”

## Slide 38: SEDS on Radial Dimension
Radial Tolerances are not size tolerances
  Curtis cites confusion between feature-of-size and our notion of a size_dimension.
ACCEPT
  Some merit to risk of confusion, but do not want to reorganize the ARM
  Handle via informative notes to explain usage
    “NOTE Size_dimension as defined in this part of ISO 10303 describe an intrinsic length or angle characteristic of part shape. This includes characteristics of what are traditionally called “features-of-size”, but they are not limited to that usage alone. For example, the radial_size_dimension and curved_size_dimension application objects describe characteristics which may not be applied to “features-of-size”.

## Slide 39: Resolution Details
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle, Angular Size Full/Half
  Centered vs Adjoining
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard
Geometric Tolerances
  Affected plane, common datum, and ARM clarification

## Slide 40: Angular Location Issues
Much debate on the interpretation of Angular Location
  Source of many AP-214 SEDS (893-895)
  Proposal for a new, simplified angular location dimension with required orientation.
  All groups agreed to adopt.
  See following slide
Handling of directed dimension
  All supported for linear, but not angle (AP-214 SEDS 887)
  All groups agreed to move directed attribute in ARM up to the supertype of all location dimensions.

## Slide 41: Angular Location
Angular Location Interpretation Cases
  ARM and Mappings proposed by Tom, with some discussion on the exploder. Now acceptable to AP-224, AP-214, Modules.
  New orientation establishes X axis, angle extends in XY plane towards Y.
  Removed major angle, mirror origin, mirror target, and origin determination
  See diagram below and next page.
origin
(axis2_placement)
X
Y
Angle value
(from shape dimension representation)

## Slide 42: New Angular Location
shape dimension
representation
complex instance of
measure_representation_item
plane_angle_measure_with_unit
value = 20 deg
dimensional characteristic
representation
angular_location
Relating and related
shape_aspects
representation
property definition
property definition
representation
axis2_placement_2d/3d
name = “orientation”

## Slide 43: Resolution Details
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle, Angular Size Full/Half
  Centered vs Adjoining
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard
Geometric Tolerances
  Affected plane, common datum, and ARM clarification

## Slide 44: Qualifying Notes
Auxiliary/theoretically exact/notes on dimensions
  AP-214 SEDS 888-891
  Mapped as descriptive representation item in the shape dimension representation.
  There could be multiple notes. All will have the name rep_item.name “dimensional note”
  See diagram on next page.

## Slide 45: Auxiliary/Theoretically Exact/Notes
shape dimension
representation
complex instance of
measure_representation_item
plane_angle_measure_with_unit
value = 20 deg
angular_size
dimensional characteristic
representation
descriptive_representation_item
name = “dimensional note”
description = “auxiliary”
An auxiliary dimension.
Description could also be “theoretical” for theoretically exact.
Any other string indicates a qualifying note.

## Slide 46: Choice of Dimensioning Standard
No method to specify dimensioning standards
  AP-214 SEDS 892
  In discussion, agreed that this can be specified once for the entire product, NOT for individual tolerances.
Add ARM concept “part_dimensioning_standard”
  where in the ARM is up to each team, could be standalone or a subtype of an ARM concept for document assignment
Map to applied_document_reference
  Use the object_role to call out the type of assignment
    adr.object_role = "dimensioning standard“
  The associated part
    adr.items[] contains the product_definition of the part
  The document which identifies the governing standard.
    adr.assigned_document.id

## Slide 47: Resolution Details
Response to TC213 Concerns
Value Qualifications
  Value Limit / Value Range / Plus/Minus / Limits and Fits
Size Dimensions
  Common Set of Size Dimensions
  Envelope Principle, Angular Size Full/Half
  Centered vs Adjoining
Angular Location Dimension
AP-214 SEDS
  Qualifying notes
  Dimension standard
Geometric Tolerances
  Affected plane, common datum, and ARM clarification

## Slide 48: Affected Plane
AP-224 style allows more than one tolerance on a particular feature
  associates plane to tolerance through tolerance zone
AP-214 style allows only one plane for a particular feature
  associates plane to feature. If there is more than one tolerance, there is no way to give them different planes.
Recommend AP-224 usage
  Acceptable to AP-214, Modules. Need to update mappings.

## Slide 49: Affected Plane - AP-214 Mappings
property_definition_representation
property_definition
position_tolerance
representation
The Toleranced
Shape Aspect
shape_aspect_relationship
name = “affected plane association”
axis2_placement_3d
relating
related
shape_aspect
Only one plane can
be associated with a
given feature
toleranced_shape_aspect

## Slide 50: Affected Plane - AP-224 Mappings
property_definition_representation
property_definition
position_tolerance
representation
The Toleranced
Shape Aspect
shape_aspect_relationship
axis2_placement_3d
name = “affected plane”
relating
related
shape_aspect
desc = “affected plane”
tolerance_zone
Associated directly
with tolerance
toleranced_shape_aspect

## Slide 51: Compound Datum
AP-214/1051 maps to common_datum
  Datum elements are associated with a shape aspect relationship.
AP-224 maps to datum (in 224e2 document)
  Associates datum_feature not datums
  Shape aspect relationship in opposite direction.
  Why not map to common_datum?
  Undefined note in mapping table
  Need to change ARM name to Common_datum to satisfy the TC213 comments.
Recommend AP-214 mapping
  Common_datum is in AIC 519 for this purpose
  AP-224 agrees to adopt the mapping w/common_datum as documented in AP-214/1051 (flip SAR, and go to datum too)

## Slide 52: AIM Mappings
datum
shape_aspect_relationship
relating
related
datum_feature
Any type of Single_datum
common_datum
shape_aspect_relationship
relating
related
datum
AP-224 Mappings
AP-214/1051 Mappings

## Slide 53: Datum and Reference
ARM merges “datum” and “use of a datum”
Mappings seem to indicate that a Datum is a datum+datum_reference in the AIM
  Mapping paths currently not complete. Do not say how to get from a datum_reference to a datum in the AIM. (Ran into this when implementing for STIX & CAX-IF)
Precedence and modification are part of the reference, not the datum
  Forcing them into the datum ARM object means they can no longer be shared. Need to separate.
Things modeled as attributes in ARM mapped to complex instances in AIM.
  Awkward, can some be modeled as ARM subtypes?

## Slide 54: Datum References
geometric_tolerance_with_datum_reference
(actually, one of the AIC 519 subtypes)
datum_system
Geometric Tolerance
datum_reference
(or referenced_modified_datum)
datum
(possibly complex instance
with other things)
referenced_datum
AIM Representation
ARM Concept
Datum and Subtypes
This link is not in
the mapping table

## Slide 55: Datum References
datum_target
geometric_tolerance_with_datum_reference
(actually, one of the AIC 519 subtypes)
datum_system
Geometric Tolerance
datum_reference
(or referenced_modified_datum)
datum
referenced_datum
AIM Representation
ARM Concept
Datum Types
Datum Reference
datum_feature
shape_aspect_
relationship
datum
datum_target
shape_aspect_
relationship
-ED
-ING
complex instance
of datum and
derived_shape_-
aspect subtype
-ED
-ING
common_datum
-ING
-ED
Common Datum
Single Datum as
Derived Geometry
Single Datum as
Target Set
Single Datum as
Feature
shape_aspect_
relationship

## Slide 56: Refine ARM Concepts
Refine Datum ARM model
  Add Datum Usage
    Has precedence attribute (moved from datum)
    Change Geometric tolerances to refer to Datum_reference rather than Datum
  Replace the defined_by attribute on Single Datum with subtypes that handle each of the three defined cases
    Datum_defined_by_feature
    Datum_defined_by_ targets
    Datum_defined_by_ derived_shape
  Modified attribute remains in Single datum
  Is there TC213 terminology to consider?

## Slide 57: Changes To ARM
ENTITY Coaxiality_tolerance
SUBTYPE OF (Geometric_tolerance);
reference_datum : SET[1:2] OF Datum_reference;
END_ENTITY;
ENTITY Datum_reference
precedence : INTEGER;
referenced_datum: Datum;
END_ENTITY;
ENTITY Datum
ABSTRACT SUPERTYPE ;
END_ENTITY;
ENTITY Common_datum
SUBTYPE OF (Datum);
made_up_by : SET[2:?] OF Single_datum;
END_ENTITY;
ENTITY Single_datum
SUBTYPE OF (Datum);
datum_name : STRING;
modification : OPTIONAL Tolerance_condition;
END_ENTITY;
ENTITY Datum_defined_by_feature
SUBTYPE OF (Single_datum);
defined_by: Shape_element;
END_ENTITY;
ENTITY Datum_defined_by_targets
SUBTYPE OF (Single_datum);
defined_by: SET [1:?] Datum_target;
END_ENTITY;
ENTITY Datum_defined_by_derived_shape
SUBTYPE OF (Single_datum,Derived_geometry);
END_ENTITY;

## Slide 58: Using Features as Datums
What would it look like if one wanted to designate a manufacturing feature as a datum?
  Say, if two planar faces had to maintain a certain parallelism
parallelism_tolerance
datum_system
datum_reference
datum
referenced_datum
shape_aspect_relationship
-ED
-ING
“The Toleranced Face”
complex instance
of flat_face and
instanced_feature
“The Datum Face”
complex instance
of flat_face and
instanced_feature
and datum_feature
Must add datum_feature to types
toleranced_shape_aspect

## Slide 59
Some Background Slides

## Slide 60: Some Background on The Project
General Approach to Harmonization at Bath
  Reviewed ARM and AIM issues.
  Surveyed the room for technical and business priorities and constraints.
  Considered each issue to find options consistent with above priorities.

## Slide 61: Goals of Participants
Rank the following technical priorities so that we can evaluate our options
  Absolute minimal changes to existing standards
    May make standards more complex with alternate mappings. Benefits current implementations.
  Absolute minimal changes to existing implementations
    Standard may become more complex than above, even more benefits to current implementations. Minimize or eliminate change visible to implementers.
    Customers which would be disillusioned by any changes to the standard.
  Simplicity of resulting specification
    Consistent pattern so implementers know what to expect. Benefits adoption and future implementation.
    Also may encourage use in other contexts
    Minimize adoption time
  Accurate use of Integrated Resource semantics

## Slide 62: Goals of Participants
Person (Perspective) -- Prioritization of values
A - Min Change to STD, B- Min Change to Impl., C- Simplicity, D - IR accuracy
Bill Freeman (customer rep), Len Slovensky (224, 240, 223) - B, A, D, C
Sean Barker - D + Speed
Vanessa Lees (CTC) - D
Alan Crawford (224, customer rep)- Customer Impact (B), Credibility of STEP, Reuse of Existing Base
Martin Gibson - Customer Impact (B), Credibility of STEP
Max Ungerer (214, customer rep) - B (tolerances not implemented, but value ranges are implemented in other areas of the standard), A, speed, C, D
Tom Hendrix (203e2/modules) - D + Speed
King Yee (203e2/parametrics) - D + Speed, B
Chiakai Sakamoto (240) - B, A, D, C
Hiroyuki Hiraoka - C, Expandability
Vijay Srinivasan (TC213) - none of the above (IBM/Dassault) D + Speed
Friedrich Glantschnig (14649) - As with Alan Crawford above, push back any changes to IRs
Suk-Hwan Suh (14649) - C + Speed
Martin Hardwick (tool vendor) - Maximum new implementation => D, C, Speed
Ted Vorburger (219) - B, A, and to lesser extent D, C

## Slide 63: Analysis
B very important, D very important, Speed important
  A - Min Change to STD, B- Min Change to Impl., C- Simplicity, D - IR accuracy
AP-214 tolerances not implemented, but value ranges and limits are implemented in other areas of the standard
AP-224 tolerances implemented with all qualifications
  Plus/Minus most common
  range, limitation, limits and fits - how common?
AP-224 feature plus/minus widely used
  use of limitation outside of dimension - how common?
  does not support use of value range, limits and fits outside of dimensional tolerance