## Slide 1: Results of 14649/AP-238 Harmonization
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Seattle SC4 Meeting
October 2004

## Slide 2: Status of Work
At Bath joint meeting with WG12 discussed ways of clarifying the AP-238 AIM data.
  Add subtypes for AIM relationships make it more apparent how the relationships are used.
  Also look at the handling of project and setup in the AIM.
Circulated a draft of the new subclasses for review and comment on 2004-08-12
  Subclasses for all action method relationships.
  Eliminated product category for project and setup in favor of new product subtypes.

## Slide 3: Action Method Relationship Subtypes
Analyzed AP and found 18 distinct relationships
  some used in more than one place
  most distinguished by string, some also required existing subtypes (like sequential_method)
Create AMR subtypes and name them based on thing that is being referenced
  machining_adaptive_control_relationship
  machining_functions_relationship
  machining_operation_relationship
  machining_operator_instruction_relationship
  machining_process_model_relationship
  machining_strategy_relationship
  machining_technology_relationship
  machining_toolpath_sequence_relationship (actually a subtype of sequential_method)

## Slide 4: Action Method Relationship Subtypes
Further subtyping helpful for some relationships.
  multiple inheritance used when a different subtype is also needed for sequencing.
  machining_feature_relationship
    machining_feature_sequence_relationship (also inherits from sequential_method)
  machining_final_feature_relationship
  machining_process_body_relationship
    machining_process_sequence_relationship (also inherits from sequential_method)
    machining_process_concurrent_relationship (also inherits from concurrent_action_method)
    machining_process_branch_relationship

## Slide 5: Old Way: Milling Operation
The Operation
bottom_and_side_
milling_operation
desc = “rough”
To Workingstep
action_method_relationship
name = “machining strategy”
action_method_relationship
name = “approach strategy”
action_method_relationship
name = “machine functions”
action_method_relationship
name = “technology”
action_method_relationship
name = “operation”

## Slide 6: New Way: Milling Operation
The Operation
bottom_and_side_
milling_operation
desc = “rough”
To Workingstep
machining_strategy_relationship
name = “machining”
machining_strategy_relationship
name = “approach”
machining_functions_relationship
machining_operation_relationship
machining_technology_relationship

## Slide 7: Project and Setup Subtypes
Also added subtypes to clarify project and setup
  Added product subtypes to identify the project/setup
  Replaces the use of a product category classification.
    machining_project
    machining_setup
  Added product definition relationship subtypes to clarify the linkage between workpieces and the project or setup.
  Replaces the use of a plain PDR with a name string.
    machining_setup_workpiece_relationship
    machining_project_workpiece_relationship

## Slide 8: Old Way Project Example
product definition
product
name = “MAKE PARTS FAST”
product definition
formation
The Project
product_related_product_category
name = “machining project”
product definition
product
“widget”
product definition
formation
The Workpieces
product definition
product
“doohickey”
product definition
formation
product_related_product_category
name = “detail”
product definition relationship
name = “workpiece”
product definition relationship
name = “workpiece”

## Slide 9: New Way Project Example
product definition
machining_project
name = “MAKE PARTS FAST”
product definition
formation
The Project
product definition
product
“widget”
product definition
formation
The Workpieces
product definition
product
“doohickey”
product definition
formation
machining_project_
workpiece_relationship
machining_project_
workpiece_relationship

## Slide 10: Status of Work
AP-238 document has been updated as described
  New mappings in clause 5.1
  New AIM entity descriptions in clause 5.2
  Updated existing constraints in EXPRESS and clause 5.2
  Generated new short form and long form
    long form now using the latest AIC 522e2
    long form has updated assignments that eliminate unused AIM entities (a ballot comment)
  Updated XML and Part 21 examples for Example One circulated to step manufacturing list.