## Slide 1: ASME B5/TC56 Information Technology for Machine Tools
Notes: 1
1
1

## Slide 2: Information Technology for Machine tools
Goal:
Information models and electronic data formats for machine tool data
Why:
Enable efficient (distributed) access to unambiguous machine tool data
Applications:
  (E-)commerce (machine specification and comparison)
  Resource allocation (internal, external)
  Process planning / Machine programming
  Virtual machining
  Performance verification and tracking / process variability / quality control
  Plug-and-play machine installation, self-identification
  Machine intelligence (self-knowledge)
  Maintenance
  ….

## Slide 3: Example: Virtual machining
Virtual machine tool:
  A model that predicts an output of the machining process by simulating the actions of the machine tool in response to the part program and the environment.
Output:
  Verification part program
  Time required to make the part
  Tolerances part
  Tool life
  …...
Critical enabler is efficient access to relevant data:
  The part (geometry, tolerances, material)
  The process plan (part program, set-up and fixturing)
  The machine tool(s)
  The tool(s)
  The machine environment
Cutting Bits

## Slide 4
Example: Virtual machining
Cutting Bits
Virtual Machining
Design & Plan
Performance data in
standardized XML
format
The internet / intranet
Virtual Inspection
<XML>
<XML>
<XML>
*Courtesy
VulcanCraft/N-See
*
*
Notes: 3

## Slide 5: Related developments
Large machine tool users are building databases with
machine tool data, often with web access
  • Process planning • Performance tracking • Simulation
  • Maintenance • Programming • Resource allocation
Initiatives at NIST, B2B internet community, and others on information
models for manufacturing resource data, e.g.,
  Tooling data (e.g., ISO 13399)
  Machine tool properties and performance
B2B internet sites with machine tool specifications and search engines
Machine tool testing equipment with output in XML
New CAM applications, e.g., virtual machining, that require data on
machine tool performance

## Slide 6: ASME B5/TC56: Information Technology for Machine Tools
Scope:
  “Standardization of electronic data format for the exchange of machine tool definition and performance data encompassing machine description, test description, test data and derived results in accordance with established standards for machine tools, coordinate measuring machines, and their associated components.”
Members:
Agreements:
• Focus on data exchange
• XML adopted as language
• Presence of data elements not enforced, allow for user extensions
• Standardized unit system
Accomplishments
• Draft B5.59-1: “Data Specification for Machine Tool Performance Tests”
• Draft B5.59-2: “Data Specification for Properties of Machine Tools for Milling and Turning”
Est. April 5, 2000
Users of machine tools
Vendors of machine tools
Vendors of testing equipment
Testing services
CAM vendors
Academia

## Slide 7: Specification Process
Information model:
  Specification document with precise definitions of terms
  and relationships (draft standards)
  Computer-readable schema
  (XML Schema, EXPRESS)
Instances:
  XML data file
  “Part 21” data file
  SQL commands to generate database tables, views, and to store/retrieve data
Tools and infrastructure:
  XML Schema (format validation, style sheets, database)
  Style sheets
  Translators for current vendor formats (stand alone and web)
  Prototype web site to store, exchange, and analyze performance data
  (SQL database, style-sheets, scripts)
Standardization:
ASME B5/TC56
ASME B89 (CMMs)
ISO TC39/SC2 ?
ISO TC184/SC1 ?

## Slide 8
Example: Storage and analysis over the internet

## Slide 9: B5.59-1: Data Specification for Machine Tool Performance Tests
Specification properties and results of machine tool performance tests
    Measurement equipment and settings
    Measurement setup
    Raw measurement data
    Performance parameters (various standards)
Data can be used as both input and output to data acquisition
Focus on standardized tests (B5.54, B5.57, ISO 230 series)
Challenges:
    Many performance parameters
    Many tests/procedures for each class of parameters
    Results are affected by subtle test parameters
Thermal
Errors
Geometric
Errors
Machine
Dynamics
Stiffness &
Hysteresis
Contouring
Axis of
Rotation

## Slide 10: B5.59-2: Data Specification for Properties of Machine Tools for Milling and Turning
Standard specifies data elements for:
  Properties of a machine (“catalog” data):
  Summary machine performance (tables in B5.54 and B5.57)
  Error tables (currently limited to geometry)
    Compensation
    Capability analysis/simulation
Not included in current draft:
  Maintenance data
  Machine usage data (uptime, jobs, etc.)
  Machine programming data (e.g. available canned cycles only through URI)
  Detailed “controller” parameters
Tool handling (toolholder interface, turrets, .. )
Workpiece handling (table, pallet system, tailstock,..)
Sensors (tool setting, part probe, …)
Installation requirements
Environmental specification
Machine class
Machine configuration
Work zone
Machining and positioning axes
Work and tool spindles
Controller

## Slide 11: B5.59-2
XML

## Slide 12: B5.59-2
XML+
“Catalog”
Stylesheet

## Slide 13: International Standardization
ASME B5/TC56 endorsed submitting a New Work Item Proposal to ISO
(scheduled after B5 November meeting)
Possible approaches:
  ISO TC39 “Machine Tools” or TC39/SC2 “Test conditions…”
    WG would focus on definition of data elements and leave IT aspects to TC184
    Approach similar to that for the representation of tooling data
    (addressed by WG 34 of TC29 (small tools), liaison with TC184)
  ISO TC184/SC1
  Joint Working Group between ISO TC39/SC2 and TC184/SC1