## Slide 1: AP-238 Conformance Classes
CC1 – CNC Independent tool paths
  Tool path cutter location data (polylines and circular NOT SPLINES)
  Tool path is required
  Tool requirement data
  Project and one workplan (single set-up, linear list of workingstep)
  Set-up placement information
  PDM and Material identifier
  Operation data (technology, strategy, etc)
CC2 – Intelligent Set-up
  Everything from CC1 plus
  All Tool path types, described by any curve type
  Tool path is required
  Design geometry (stock and final part) (without features)
  Restricted area
  Multiple workplan (linear list of working step, nested workplan, and parallel workplan)

## Slide 2: AP-238 Conformance Classes
CC3 – Conditional Programming
  Everything in CC2 plus
  Tool path is optional
  Probing operation
  All programming constructs
  In-process (implicit) feature with parameter tolerance data
CC4 – Generative programming
  Everything in CC3 plus
  GD&T data sufficient to compute optimal speeds and feeds
  Final feature (AP-224) data with linkage to explicit geometry
  Anything else that we forgot