## Slide 1: AP-238 DIS Comment Resolution
STEP Tools, Inc.
14 First Street, Troy, NY 12180
(518) 687-2848 / (518) 687-4420 fax
http://www.steptools.com
Valencia SC4 Meeting
David Loffredo
loffredo@steptools.com

## Slide 2: AP-238 Testing Forums
Since Seattle, running AP-238 testing activities in conjunction with OMAC STEP-NC working group.
  Weekly conference calls w/CAD-CAM vendors, NC control vendors and several OEMs.
  January forum in Orlando focused on 5axis testing with cutter location paths, four data sources and two controls configured for different machine geometry
AP-238
AB Tool Tilt
BC Table Tilt

## Slide 3: AP-238 Testing Forums
5-axis machining tests at Boeing and NIST producing test articles using AP-238
  NAS 979 circle/diamond/square with inverted cone
  Representative aerospace part with 1-2degree inclines and tightly constrained positioning holes

## Slide 4: AP-238 Testing Forums
In May, focused on closed-loop machining testing cutter contact paths, probing operations
  Presented results at EASTEC 2005 in Springfield MA.
Testing forum is creating and processing AP-238:
  CC1 (toolpath only) and CC2 (toolpath + geometry) programs
  Cutter location paths described using a variety of 3axis and 5axis basis curves
  Cutter contact paths using surface normal vector
  Machining programs using english and metric units, geometry as well as speed, feed, and other process data
  Workpiece single point probing operation
  Driving Siemens 840D with TRAORI for 5axis, Fanuc 30i with TCP for 5axis, and initial work on Heidenhain
  Direct AP-238 export from UGS NX, MasterCAM, GibbsCAM, and AP-238 via APT from CATIA.

## Slide 5: AP-238 Testing Forums
Creating a large archive of AP-238 machining test data sets for distribution to future testers.
  Currently ~100 data sets spanning a variety of machining programs with STP files, screen dumps, reports and such.
  CC1 and CC2 files, simple 2.5D as well as multi-axis paths, surfacing and high-speed paths

## Slide 6: Reality Check: “ARM Savings”
Now that we have an large body of AIM test sets for reasonable parts, we can get hard numbers on the ARM implementation “savings”
Look at a realistic high-speed milling program
  Roughing and finishing program using a high-speed technique called trochoidal milling.
  Tool moves forward in loops to improve cooling, tool wear and accuracy.

## Slide 7: Reality Check: “ARM Savings”
The AP-238 CC1 file:
  One project, workpiece, and workplan.
  Two each of workingsteps, operations, technology, machine functions, toolpath features and tools (one each for roughing, finishing)
  26 cutter location toolpaths (23 roughing, 3 finishing)
  All of the associated AIM property and relationship objects necessary to describe the non-geometric parameters on them.
All the rest is Part 42 curve geometry, describing the toolpaths, which would be identical in an ISO 14649 ARM implementation.
  Strip all non-geometric information from the AP-238 file to find the minimum size of an equivalent ARM implementation.

## Slide 8: Reality Check: “ARM File Size Savings”
Manually strip everything but the curve geometry
  Complete file 25.8meg (25842485 bytes)
  Geometry only 25.8meg (25786744 bytes)
  ARM Savings: 0.2% (55741 bytes)
This is still too generous, because some of the savings were just /* */ comments in the file.
  17273 bytes were from comments, the savings attributable to entity data was just 38468 bytes (0.15%)
Assumes that ISO 14649 implementation uses zero bytes to describe:
  workplan, workingsteps, workpiece, features, technology and machine functions parameters.
  Actual savings would be less than 0.15%

## Slide 9: Reality Check: “ARM Instance Count Savings”
Response: Bytes are one thing, but what about the so-called AIM “explosion” in instance count?
  Complete File: 300200 instances (74 types)
    The geometry as below, plus:
    482 instances spread over 66 extra types
  Geometry Only: 299718 instances (8 types)
    1 plane (w/ 1 axis2_placement)
    12 composite curves (w/57258 composite curve segments)
    16748 polylines
    40524 trimmed curves
    40524 circles (w/ 40524 axis2_placements)
    104126 cartesian points
Even less savings by this metric, only 0.1%

## Slide 10: Reality Check: “ARM Processing Speed”
Response: Toolpath geometry is one thing, but a file that big is not usable.
  The file is good sized, but not unreasonable. 100meg+ files in common use on the CAD side.
Wall clock timing tests on Dave’s wimpy ~4 year old laptop with 800mhz PIII
  Time to parse P21 file and create objects in memory:
    26 sec
  Once in memory, time to process and convert the toolpaths to a form amenable to Siemens 840D or FANUC control:
    ~3 sec

## Slide 11: Reality Check: Other Files
Response: You picked some crazy special case to rig the statistics in your favor.
  I did start with the biggest file I had handy, but the results hold up for other realistic parts as well.
  About 100 CC1 test files that range from 15k to 8meg
  5-axis Airfoil Surfacing
    3.5meg, save 32874 bytes 0.9%
    38529 instances, save 300 0.7%
  3-axis Wheel Cover Surfacing
    816k, save 17222 bytes 2%
    8888 instances, save 221 2.5%

## Slide 12: Reality Check: Other Files
Did find a little more savings looking at small 2D files, with many small toolpaths.
  2.5D Pocketing
    443k, save 138k 31%
    4794 instances, save 1467 30%
    A bit more savings, but hardly overwhelming
Numbers still assume ARM implementation can use zero bytes / zero instances to describe:
  One project, workpiece, and workplan.
  Two each of workingsteps, operations, toolpath features and tools, 5 technologies, 1 machine functions
  106 cutter location toolpaths

## Slide 13: Reality Check: Conclusions
The numbers show ARM “efficiency” arguments just don’t hold any water.
  On real CC1 parts, only 0.2% to 2% savings at the cost of all integration and interoperability.
  Once you add workpiece BREP geometry to be able to view the part (CC2), these percentages will become even smaller!
  Only place with non-trivial savings are trivial files, which aren’t a performance concern anyway!

## Slide 14: AP-238 Status
DIS ballot ran six months ending 2005-05-31
  wg3n1534 AP-238 document
  wg3n1540 EXPRESS short form schema
  wg3n1541 EXPRESS long form schema
  wg3n1542 Comment log
  wg3n1538 AP validation report
DIS passed, 15 yes votes, no FDIS needed
  Swiss “no” vote later changed to abstention
  Ballot results available in sc4n1929
  119 comments from 7 countries, discussed in Valencia
    CH - 54 FR - 5
    JP - 11 KR - 16
    SE - 1 UK - 6
    US - 26

## Slide 15: Comment Summary
Comments can be grouped as follows:
  Relationship between AP-238, ISO 14649, others
  Harmonization of information requirements
  General document wording and structure
  Missing information requirements
  Usage clarifications needed
  Mapping and EXPRESS bugs
  Editorial bugs
The following slides walk through the discussion and handling of each.

## Slide 16: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 17: Relationship between 238/14649/others
CH 1-2,4-6,8
  Intent of these comments seems to be to rework our scope to forbid us from using AP-238 on a machine tool control.
  Reject, AP-238 is input to the machine tool control. AP-238 is the AIM encoding of the information requirements ISO 14649
  Work to make changes and clarify where we can, but we are under the following constraints
    SC4 boilerplate text cannot be changed without SC4 resolution
    The normative scope that was approved can not be changed without another DIS ballot cycle.

## Slide 18: Relationship between 238/14649/others
JP1-3
  Intent of these comments seems to be to clarify our scope to forbid AP-238 from intruding into non-machining processes defined by AP-240.
  Believe scope already prevents this.
  Wording carefully developed in Seoul with AP-240 editor to limit use to numerically controlled processes. AP-240 also handles non-NC processes and but was constrained against having sufficient information for automatic execution.
  Will add comment in clause one explaining position of AP-238 within the suite of step manufacturing aps.

## Slide 19: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 20: Harmonization of Information Requirements
CH 10-13,15-21, 23-30, 32-51
Philosophy for handling additional requirements.
  How can we handle integration with AP-224 features when necessary fields are missing from ISO 14649?
  How can we handle requirements discovered during testing and AP development when SC1 is no longer developing 14649?
  Reason for UOFs beyond what is in 14649. This integrated data must be present and does not preclude use on the control.
General approach
  Document information in AP-238 for publication in this edition, then submit a SEDS on ISO 14649 and send it to SC1/WG7.
  When added to future editions of ISO 14647, future editions of AP-238 can just reference instead of maintaining two copies of the definition (as we did with AIC522)

## Slide 21: Harmonization of Information Requirements
All comments discussed and resolutions developed
  CH 9,39,41,44,47 Remove multiple units
  CH 11-12, 21,29,33-35,38,40,42,43,45,51 Remove things added to AP-238 for feature harmonization with AP-224
  FR5 Handling of transition features
  UK1 Requirement for Final Features
  CH 18,27,28,30,46,50 GDT Data
  CH 19,23,24 PDM Data
  CH 14 Add 5-axis and free form operations
  CH 13,37 Remove nc_legacy_functions
  CH 15,25,26,49 Remove toolpath maximum deviation
  CH 15, 49 Remove relation on speed curve
  CH 16,32,KR1 Remove machine axis constraint
  CH 17,36 Remove tool holder profile

## Slide 22: Harmonization of Information Requirements
CH 9,39,41,44,47: Remove support for explicit units for geometry and process parameters
  All STEP APs supports multiple units in a file, a large number of existing designs have mixed units. Capability to explicitly state the natural units. Why shouldn’t STEP-NC.
  AP-238 testing activities encountered mixed units in every round, because data is developed by multiple people at multiple times so this is a common requirement.
  REJECT - Keep in AP-238 document, write up SEDS on ISO 14649 suggesting that units be added and send it to SC1/WG7.

## Slide 23: Harmonization of Information Requirements
CH 11-12, 21,29,33-35,38,40,42,43,45,51, UK1
  Remove various aspects of feature harmonization with AP-224, final featues, transition feature face/param, CH34 workingstep and final feature link, explicit representation.
  REJECT if comment says “remove”
  ACCEPT if comment just says “harmonize”
  Keep in AP-238 document, write up SEDS on ISO 14649 and send it to SC1/WG7. Note that AIC522 has been updated to add parametric description of transition features.
  For final and intermediate features, clarify descriptions and explain how they are used.
  UK1 Requirement for Final Features -- also handled by clarification.

## Slide 24: Harmonization of Information Requirements
FR5 Handling of transition features
  ACCEPT We do need to support these features but believe that the current edge round feature and fillet radius parameters can support this so no change is needed.

## Slide 25: Harmonization of Information Requirements
CH 19,23,24: PDM
  presented Poitiers October 2003, Bath July 2004, Review copy June 2004, CH23-24 says PDM not needed by ctl
  REJECT - AIM P41 data for PDM already referenced by 14649, but does not provide enough context for SC4 use. ARM definitions are needed to give context to the approvals, dates, person/org etc.
  Submit SEDS to 14649 to provide the additional context.

## Slide 26: Harmonization of Information Requirements
CH 18,27,28,30,46,50: GDT
  CH18 says add GDT to 14649, CH27 says GDT not needed by ctl, CH28,30,46 remove part of GDT definitions. CH50 is also an editorial
  CH18 ACCEPT - SC1 and SC4 agree that the GD&T definitions shared by AP-203/214/224/238/240 and 219 should also be in ISO-14649.
  CH27 REJECT - This is the opposite of CH18
  CH28,30,46 REJECT - The entire set of definitions should be used without modification as per CH18
  CH50 ACCEPT Add figure for total runout and other tolerances to clarify.

## Slide 27: Harmonization of Information Requirements (cont)
CH 15, 25, 26 Remove toolpath maximum deviation
  Technological rationale for this is clear.
  Came out of BCL (EIA494) definition, so we know that it is sufficient to convey the info.
  All agree that this should also be in ISO-14649-10
  Need to put in AP-238 because we need to reference a published version of ISO 14649 because of ISO rules.
    Could issue a TC on 14649-10
  REJECT - Keep in AP-238 document, write up SEDS on ISO 14649-10 and send it to SC1/WG7. Harmonize in future editions if necessary.

## Slide 28: Harmonization of Information Requirements (cont)
CH 15, 49 Remove relation on speed curve
  Relaxes constraint on curve to correct asymmetry in 14649-10
  SC4 believes this should also be in ISO-14649-10
  Need to put in AP-238 because we need to reference a published version of ISO 14649 because of ISO rules.
    Could issue a TC on 14649-10
  REJECT - Keep in AP-238 document, write up SEDS on ISO 14649-10 and send it to SC1/WG7. Harmonize in future editions if necessary

## Slide 29: Harmonization of Information Requirements (cont)
CH 16,32,KR1 Remove machine axis constraint
  SC4 believes this should also be in ISO-14649-11
  SC1 has agreed to discuss this for future editions
  Need to put in AP-238 because we need to reference a published version of ISO 14649 because of ISO rules.
  REJECT - Keep in AP-238 document, write up SEDS on ISO 14649-11 and send it to SC1/WG7. Harmonize in future editions if necessary

## Slide 30: Harmonization of Information Requirements (cont)
CH 17,36 Remove tool holder profile
  CH36 says tool holder not needed by ctl, only upstream at macro level (not true, as long as generative is present, need holder)
  P111 does not define complete volume for milling tool from gage line to tip.
  Within AP-238 clarify that the profile define the maximum envelope within which an actual tool holder must exist.
  All believe this should also be in ISO-14649-111
  REJECT - Keep in AP-238 document, write up SEDS on ISO 14649-111 and send it to SC1/WG7. Harmonize in future editions if necessary

## Slide 31: Harmonization of Information Requirements (cont)
CH 14 Add 5-axis and free form operations
  ACCEPT These definitions are present in the document, but in section 4.1.8. Add note to this section reminding the reader that the technology specific parts are in other clauses.

## Slide 32: Harmonization of Information Requirements (cont)
CH 13,37: Remove nc_legacy_functions
  The name “legacy” is highly objectionable.
  Rename extended_nc_function (externally defined?)
  extended_nc_function --> is a subtype of nc_function
    description string which identifies the function.
  ACCEPT - Replace nc_legacy_function with extended_nc_function defined as on next slide.
  Write up SEDS on ISO 14649-10 and send it to SC1/WG7, including the example of active clamping.

## Slide 33: Extended NC Function
Extended NC Function
  An extended_nc_function is a type of NC_function which specifies a manufacturing or handling operation which does not involve the interpolation of axes and for which no other more specific type of NC_function exists.
The data associated with an Extended NC Function are the following:
  description.
    description string which identifies the function

## Slide 34: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 35: General Wording and Structure
All comments discussed and resolutions developed
  FR1 General on interfacing non-SC4 parts.
  FR3 Reference to ISO 13399
  FR2 AAM
  JP4,5 Documentation of Imported AOs
  KR9 Synchronize with latest P111/P121
  CH 54,UK4 XML examples
  CH52,53, JP7: Conformance Classes

## Slide 36: Wording / Structure (1)
FR1: General on interfacing non-SC4 parts.
  ACCEPT all T24 projects are interfacing with the other groups as there are requirements. Note that we are harmonizing across the 10303 APs, ISO 14649, PLIB, 13399, and metrology groups DMIS/DML/TC213.
  Have stayed in liaison with MANDATE
FR3: Reference to ISO 13399
  ACCEPT
  Normative reference only possible if cited in normative text. Can cite it informatively in the bibliography.
  When we move to latest 14649-111/121, will add a normative or informative reference as needed.

## Slide 37: Wording / Structure (2)
FR2: AAM
  ACCEPT
  The activities of AP-238 are identical to those of ISO 14649
  Need to update the ISO 14649-1 AAM so that it refers to AP-238, AP-240, AP-219 and any other that fits (AP-224?)
  Would like to have a single AAM referenced by both.
  Issue to SC1 to update AAM to refer to APs as above.
JP4,5: Documentation of Imported AOs
  ACCEPT List of imported AOs present in Clause 4.1 UOF listings as well as Annex G ARM EXPRESS-G. All relationships documented in EXPRESS-G as well.

## Slide 38: Wording / Structure (3)
KR9: Synchronize with latest P111/P121
  ACCEPT need to update mappings to accommodate the changes in those parts.
CH 54 XML examples
  ACCEPT XML did not work out to be particularly helpful. Will withdraw Annex K
  Withdraw the XML examples, but keep the annex with annotated AIM examples for the 14649 examples as well as CC1 and CC2 examples.
UK4 XML examples
  REJECT turning workingstep is plural, milling is singular.

## Slide 39: Wording / Structure (4)
CH52,53, JP7: Conformance Classes
  SC4 CCs conform to business cases, if there are more business cases then we may need to add more CCs.
  The 14649 CCs are a matrix of technical permutations but not explicitly tied to business cases.
  Need documentation for any additional business cases that have been identified.
    Possibly divide CC3 into machining of 2.5D features and full features?
    Separate CCs for each technology (milling/turning?)
  Rather than split CCs, expand the granularity of the PICS proforma questionnaire to call out the different groups of technologies or features.

## Slide 40: Conformance Classes
Change to more appropriate names for the CCs
  CC1: CNC-independent tool paths
  CC2: Closed-Loop programming
    For non-linear machining programs. Will now include the probing, if/then/else and other types of advanced control flow entities.
  CC3: Feature-based programming
  CC4: Generative programming
Expand the granularity of the PICS proforma questionnaire to call out the different groups of technologies or features.
  milling / turning for all
  on CC3/CC4 (milling) 2.5d features, all features
  on CC3/CC4 (turning) all features
  CC2 and up, shape reps supported for workpiece

## Slide 41: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 42: Missing Information Requirements
All comments discussed and resolutions developed
  FR4 5-Axis Flank Milling
  JP8 Need surface finish, general properties
  US1 Toolpath ID
  US3 Boolean values not optional
  US4 Feature required when just doing toolpaths
  US11 Cutting component should not be required
  US14 Roughing and finishing for freeform milling
  US18 Geometric validation properties
  US21 Workpiece PDM fields
  US22 Inconsistent defs for toolaxis curves
  US19 Use of toolpaths in multiple locations
  US20 Full range of shape representations
  US26 Assumed machine tool characteristics.

## Slide 43: Missing Info (1)
FR4 5-Axis Flank Milling
  Applies to ruled surfaces, pockets where one side is a surface
  Can do today using explicit toolpaths
  5axis flank milling operation could be a new type of operation to call out generative machining for this thing
    What are the process parameters?
  Current features are process-free, there are a set of current features that could be machined using flank milling.
  Reluctance to add process-specific features
    Ruled surface feature instead?
  DEFER to Edition 2 of AP-238 and 14649-11 e2
    Can do today using explicit toolpaths.
    We would prefer it be added to ISO 14649-11 e2
    Could add to AP-238 if SC1 refuses, but need the extra time to discuss the process and feature parameters.

## Slide 44: Missing Info (2)
JP8 Need surface finish, general properties
  ACCEPT - Harmonization with AP-224, adopt existing ARM and mappings for part properties (surface finish, heat treat, etc.)
  Note that we are already using the AP-224 property for material, this is just bringing in the full description
  Suggest to SC1 that they should be added to ISO 14649-10 as well. Send back using SEDS as with others.

## Slide 45: Missing Info (3)
US1 Toolpath ID
  ACCEPT, add ID arm attribute mapped as per the other IDs.
US3 Boolean values not optional
  Would like to change ARM so they are optional with a well-defined default.
  Mainly with technology feed/spindle override and machine functions flood/mist/through spindle coolant on/off, and toolpath priority.
  Rationale is to reduce the coding effort for initial implementations
  ACCEPT do for three cases above, and any other for which a reasonable default exists.

## Slide 46: Missing Info (4)
US4 Feature required when just doing toolpaths
  REJECT feature is useful to get implementors thinking about the additional capabilities that can be added.
US11 Cutting component should not be required (may be moot)
  REJECT no longer in part 111
US14 Roughing and finishing for freeform milling
  An example of this is FANUC “Super G” mode, if you know that you are roughing, you can drive the machine much faster.
  ACCEPT - Add roughing and finishing subtypes as per other milling and turning operations. Send to SC1/WG7 as SEDS
US18 Volume and Area measures to support geometric validation properties
  ACCEPT make sure we pull in volume_measure_with_unit, area_measure_with_unit from P41 in AIM.

## Slide 47: Missing Info (5)
US21 Workpiece PDM fields
  Also helpful for traceability back to design
  ACCEPT, add as optional fields
US22 Inconsistent definitions for toolaxis curves in 14649
  cutter location trajectory interprets tool axis curve as IJK values
  cutter contact trajectory interprets tool axis curve as yaw and pitch angles (yet surface normal curve is IJK!)
  ACCEPT - use IJK for both in AP-238
    Strongly recommend to SC1 that the handling of toolaxis curves in 14649-10 be made consistent as well.
    Submit SEDS to SC1/WG7 as per other comments

## Slide 48: Missing Info (6)
US19 Use of toolpaths in multiple locations
  Workingstep, feature, operation
  Workingsteps may reuse operation + feature + toolpaths
    Associate an origin with workingstep?
    Path patterns that you repeat in many locations? (such as hole drilling patterns for thousands of holes)
  14649 has some verbage about locating toolpaths from features, but
    Not really workable in practice.
    axis2placement conventions different in 14649 and AIM (covered in fundamental concepts and assumptions)
    Unintuitive results if you start with a plain toolpath file and annotate with features later on (may have to numerically transform the toolpath geometry)

## Slide 49: Toolpaths in Multiple Locations
Discussion identified two different activities here
  Reuse a single toolpath in a different location
    Current ARM does not have any way to do.
    proposal for transformed toolpath addresses this
      axis placement + reference to another toolpath
    DEFER Should also be in 14649, propose addition
  Reuse all toolpaths from an operation in a different location
    ISO 14649 does by using origin from different features, but this doesn’t work for 238 because of feature harmonization constraints.
    Note that in 14649, features created specifically for the operation, so they can be given appropriate placement. AP238 may use feature from upstream with origin that was convenient for designer.
    Rather than implicitly handling through feature, make explicit as axis placement on workingstep. Would have same numeric value as ISO 14649 feature placement.
    ACCEPT Really only affects ap238, do it now.

## Slide 50: Operation/Toolpaths Origin ISO 14649
WS1
Operation
TPath
TPath
TPath
TPath
TPath
Feature 1
WS2
Feature 2
In 14649, feature
placement does
double duty as implict
origin for tpaths
In ap238 we have
harmonization constraints
that make this difficult
Placement

## Slide 51: Operation/Toolpaths Origin AP-238
WS1
Operation
TPath
TPath
TPath
TPath
TPath
Feature 1
WS2
Feature 2
Placement
Explicitly add placement to workingsteps
Placement

## Slide 52: Missing Info (7)
US20 Full range of shape representations
  ACCEPT with permitted usage as below
  Explicit shape on features only supported when shape reps with topology (faces) is present
  Only implicit shape for features can be used in other cases (which is how 14649 works today)
    AIC 512 faceted brep
    AIC 509 manifold surface (already present)
    AIC 501 edge-based wireframe
    AIC 502 shell-based wireframe
    AIC 507 geometrically-bounded surface (already present)
    AIC 510 geometrically-bounded wireframe
  This also harmonizes with AP-240/AP-223

## Slide 53: Missing Info (8)
US26 Assumed machine tool characteristics
  ACCEPT
    adopt machine_parameters ARM concept and mappings from AP-240
    Track progress of ASME B5.59-2 and enhance AP-238/240 when that becomes available.

## Slide 54: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 55: Usage Clarifications Needed
All comments discussed and resolutions developed
  US5 Spindle handling off/CW/CCW?
  US13 Complete circles in toolpaths
  US24 Interpretation of surface normal curve
  US25 Matching parameterization of curves.
  US23 Context for tool axis and normal vector curves
  KR10 Usage of length measure rep items
  US12 Usage of ratio measure
  US15 Units for counts, ratios and parameter value
  US2 Transition from tool requirements to actual tool

## Slide 56: Clarifications (1)
US5 Spindle handling off/CW/CCW?
  ACCEPT, document as follows in 5.2.1
  A speed of 0 means spindle off
  Positive is CCW
  Negative is CW
  That may work for rotational speed, but what if the spindle is specified as the surface speed (cutting speed)?
    Propose that we use the same sign convention as with the rotational speed (positive CCW / negative CW)
    Double check if Part 12 says something about this, use that convention if it does.
US13 Complete circles in toolpaths
  ACCEPT document trimmed_curve usage as in comment
    Recommend shared cartesian_point usage to avoid epsilon comparison.

## Slide 57: Clarifications (2)
US24 Interpretation of surface normal curve
  ACCEPT Implied that IJK, but put in an explicit statement that it is to be handled as IJK
US25 Matching parameterization of curves.
  ACCEPT adopt recommended algorithm from comment
US23 Context for tool axis and normal vector curves
  ACCEPT
    Explain representation context usage for the various cases of measures, curves, directions etc. in more detail in 5.2.1
    Add local rule to machining_toolpath requiring global unit context for basic curve, but not the IJK curves.
  If units are not needed, give geometric_representation_context but no global_unit_assigned_context is needed

## Slide 58: Clarifications (3)
KR10 Usage of length measure rep items
  ACCEPT It is difficult to understand this if your first exposure to it is from the mapping table. Explain usage of complex instances of measure_with_unit subtypes in 5.2.1 Include examples for length, angle, time
US12 Usage of ratio measure
  ACCEPT Add suggested explanation to 5.2.1
US15 Units for counts, ratios and parameter value
  ACCEPT add suggested usage explanation to 5.2.1

## Slide 59: Clarifications (4)
US2 Transition from tool requirements to actual tool
  ACCEPT
  Investigate adopting AP-240 approach. Tracking tool carousel id, could harmonize with that?
  Adopt AP-240 tool carousel definitions
  Look at tool_position from tool_placement_instruction
  tool_magazine_turret_carousel?
  C Sakamoto can provide guidance

## Slide 60: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 61: Mapping and EXPRESS Bugs
All comments discussed and resolutions developed
  KR2 turning_dwell_time_representation
  KR3 Feed_per_revolution
  US16 Use of count_measure/parameter_value
  US17 Unit on NUMERIC_PARAMETER
  KR4-8,UK2, US8,10 Mapping documentation bugs.
  JP9-11,UK3 EXPRESS-G
  KR12-14 Use of String in ARM EXPRESS-G
  KR15-16 turning_type_* in AIM EXPRESS-G
  US6,7 EXPRESS bugs

## Slide 62: Mapping Bugs (1)
KR2
  turning_dwell_time_representation ARM object? dwell_time type is mapped to machining_dwell_time_representation, was this added after P12v15?
  ACCEPT will update to latest Part 12 arm concepts as part of FDIS and will map this and any other things that have changed.
US16
  Mapping change for count_measure/parameter_value
  ACCEPT update mappings to use count_measure to be more consistent with AP-224 replicate feature handling of similar semantics.
US17
  Mapping for named/derived unit on NUMERIC_PARAMETER
  ACCEPT update mappings to permit both named and derived units to be used.

## Slide 63: Mapping Bugs (2)
KR4-8, US8,10 Mapping documentation bugs.
  ACCEPT fix text as indicated in comments.
  Also fix mapping table typos and such found by latest mapping table compilation software.
UK2,3 its_feature/its_features
  REJECT turning workingstep is plural, milling is singular.

## Slide 64: Mapping Bugs (3)
KR3
  Feed_per_revolution. Way of describing speed, but is actual measure a length or speed? Comment says it is a speed (len/time), existing document says length.
length/time
measure_with_unit
with unit (l/t)
length
measure_with_unit
with unit (l)
For lengths, we use the
special P41 subtype
length_measure_with unit

## Slide 65: Mapping Bugs (4)
Measure_with_unit has two attributes
  value_component ---> the REAL part, the numeric value
    This is the part 12
  unit_component ---> reference to the unit description instance
ACCEPT
  The quantity is not a length, it is a len/rev. So it should not be a length_measure_w_unit subtype and the unit should be a derived unit defined as len/rev
  The numeric value will, in fact, remain the same, but will appear in the value_component as a numeric_measure rather than a length_measure.
length/revolution
measure_with_unit
with unit (l/rev)

## Slide 66: EXPRESS Bugs (1)
JP9-11 EXPRESS-G
  ACCEPT will update diagrams to use consistent placement as much as can be done.
KR12-14 Use of String in ARM EXPRESS-G
  ACCEPT have the EXPRESS-G reference the “stubs” for the geometry rather than giving it as a string. See note at end of ARM diagrams. Treating as primitive type in ARM is common practice in the ARM diagrams of other APs.
KR15-16 turning_type_* in AIM EXPRESS-G
  ACCEPT The EXPRESS exists in the document but somehow were omitted from EXPRESS-G. Will add them to the diagram
US6,7 EXPRESS bugs
  (verify_rep_desc, AIC522 rules)
  ACCEPT, already corrected

## Slide 67: Comment Resolution
Relationship between AP-238, ISO 14649, others
Harmonization of information requirements
General document wording and structure
Missing information requirements
Usage clarifications needed
Mapping and EXPRESS bugs
Editorial bugs

## Slide 68: Editorial Bugs
All discussed and resolved as below
CH 7, 22,31,48,KR11, UK6, US9 General editorial
  ACCEPT fix the text where indicated
JP6 PDF problems?
  ACCEPT
  The referenced AIM definitions are there.
    5.2.3.1.44 machining process body relation
    5.2.3.1.50 machining process sequence relation
  Clarify comment, could not find in AIM EXPG. Does seem to be missing, will correct.
  Document workplan path as going through sequential method rather than the current process_body branch. It is clearer for the sequence characteristic that way.