## Slide 1
Traceability Approach
Julio Garrido Campos
Vigo University. Spain
jgarrido@aisa.uvigo.es
ISO TC 184/SC4 Technical Forum
June 12-17, 2005 Valencia
A traceability information model
for CNC manufacturing
Notes: Good afternoon.
…
I’m Julio Garrido
I’m from…
And I’m going to present a TRACEABILITY INFORMATION MODEL FOR AP238 MANUFACTURING.

## Slide 2
Traceability Approach
A traceability information model
for CNC manufacturing
This work is supported by
the Spanish Bureau of Science and Technology
MCYT (Ministerio de Ciencia Y Tecnología)
as project DPI2003-01967.

## Slide 3: Traceability Approach
1. Traceability & Product Characteristics.
  Traceability.
  Traceability principles & problems.
  Traceability in Complex Systems. e-Manufacturing (NC Systems).
  Product Characteristics.
2. Traceability Model.
  Traceability Data Model & Step-NC.
  WorkingSteps: Operations.
  Features & Tolerances: Characteristics.
3. Implementation.
  Demo Tool: NC-Explorer & Traceability.
  Future Work.
4. Conclusions.
  Solutions.
  The BIG QUESTION.
Notes: Presentation has 4 BLOKS.
1 Introduction to Traceability concept and product characteristics.
2 The traceability model proposal
3 The work done until now
4 Conclusions

## Slide 4: Traceability & Characteristics What is traceability? (1)
Is a set of practices to make avaliable all essential information about a product.
Achieved within each product, by registering characteristics & product manufacturing information like:
“the ability to trace the history, application or
location of what it is under consideration”
with what
(raw materials)
who
(employees, personel)
where
(handling, storage, transport)
when
(manufacturing timings)
other data
(additional data, resources )
how
machines & tools
ISO 8402:1994
ISO 9000:2000
How well
(characteristics)
Notes: ISO 9000 stadard DEFINES traceability AS ….
This means, in other words, that T is tracking, recording all relevant INF.
About a MANUF: process.
For instance ……
and also even HOW WELL, which means evaluat inf., or checking and OF COUSE, RECORDING, SPECIFIC FINAL PRODUCT CHARACT.

## Slide 5: Traceability & Characteristics STEP, Traceability & Characteristics (1)
SC4 Additional STEP requirements & traceability issues.
  Multiple Application support
    Conceptual Design & Product Planning
    Engineering Analysis
    ………….
    Logistics
    Packaging
    Manufacturing
    Quality
    Support & Maintenance
Traceability is about this, but is more than this.
Notes: All this DATA are essential to support others process such as
QUALITY
LOGISTICS
and even improve manufacturing process …
AND This PRODUCT LIVE Cicle processes lay INDEED into the scope of the STEP Standadr.

## Slide 6
Traceability & Characteristics What is traceability? (2)
Traceability Principles:
  Identification
  Data Capture & Recording
  Communication
  Links Management
Notes: BUT
HOW IS IMPLEMENTED A T SÝSTEM. A GENERAL ONE.
Well. BASICLYY, We FIRST need (USE) IDENTIFICATION Technologies to MARK SINGLE PRODUCTS AND PARTS.
THIS ID WILL BE THE LINK OF THE PHISICAL PRODUCT WITH TRACED/RECORDED DATA.

## Slide 7
Traceability & Characteristics What is traceability? (3)
Traceability Principles:
  Identification
  Data Capture & Recording
  Communication
  Links Management
with what
(raw materials)
who
(employees, personel)
where
(handling, storage, transport)
when
(manufacturing timings)
other data
(additional data, resources )
how
machines & tools
how well
(characteristics)
Notes: Second (Process) is the
RECORDING, AND SAVING OF DATA… Data about manufacturing process.
SO, previously, IT HAS TO BE DECIDED WICH DATA IS REQUIRED

## Slide 8
Traceability & Characteristics What is traceability? (4)
Traceability Principles:
  Identification
  Data Capture & Recording
  Communication
  Links Management
Traceability
database
Notes: AND ALSO ARE IMPORTANT ALL THIS DATA
Communication and managing,
specially when speaking about T In The extended enterprise.

## Slide 9
Traceability & Characteristics Problems (1)
Traceability in Dynamic, Complex & Heterogeneous systems.
Bill of Materials (list)
Product Structure
1. Traceability data
could be diffcult to understand
Notes: BUT & SPECIFICALY FOR THIS EXTENDED ENTERPRISE SITUATION:
- Many supply chain companies, WITH dynamic relations..
- ANd also when manufacturing COMPLEX PRODUCTS.
T. HAS TO FACE SOME IMPORTANT AND WELL KNOW PROBLEMS
ONE OF THESE PROBLES IS THE DATA SIGNIFICANCE ( OR DATA UNDERSTANDABILITY)
TO make the data SELF understandable, among common definition about traceb data, (whic means understand what a roww material lot means, for ex)
IT IS NEEDED ALSO A comon understandability of the manufacturing process. THIS IS ALREADY GEVEN, TODAY; BY STEP AP’s

## Slide 10
Traceability & Characteristics Problems (2)
Traceability in Dynamic, Complex & Heterogeneous systems.
Main Manufacturer
Supplier A1
Supplier A2
Supplier B
Supplier C1
1. Traceability data
could be diffcult to understand
2. Complex Supply Chain
different suppliers
or providers
Notes: OTHER problem comes from the complexity of the suuply chain, and its today flexibility

## Slide 11
Traceability & Characteristics Problems (2)
Traceability in Dynamic, Complex & Heterogeneous systems.
2. Complex Supply Chain
different suppliers
or providers
Main Manufacturer
Supplier A1
Supplier A2
Supplier C2
Supplier C1
Supplier B
(2) Supply Chain Change from Supplier C1 to C2
(1) Data Failure
(2) Data NOT AVALIABLE
2.2 Dynamic relations
supply chain is not static
2.1 Internal Traceability
data unlinked between
partners
1. Traceability data
could be diffcult to understand
Notes: TWO THINGS, for instance, may happen
  ONE.
  MAY Be A Local T Data is wrong or incomplete.
  SECOND
  One suply company may Dissapear or be change for other.
THEN, IF DATA IS NOT SENd (at the time the product) TO THE MAIN contractor company, IF in the FUTURE it needs this date, it may realices TOO LATE
-WETHER IT is wrong
- OR IT CAN’T REACH

## Slide 12
Product characteristic measurement is an important quality measurement process: Tolerances and many others …
  Each single failured characteristic, may have a big economic cost.
“traceability data” and “characteristic data”, share the same problems.
  Complex products may have thousands of characteristics defined.
  To manufacture complex products hundreds of suppliers may be involved.
Traceability & Characteristics Problems (4)
Notes: ABOUT TRACING “WHOW WELL” has somtninh dote (that is, when recordidng ptoduct characteristics)…
WE FIND THE SAME PROBLEMS COMEING from product complexity and supply chain complexity.
COMPLEX products may have defined thousand of CHARACTERISTIS
ALSO MANY COMPANIES MAY BE INVOLVED
AND ALL THIS MEASURES SHOULD BE CERTAINLY DONE AND VALIDATED…. EACH FAILURE ONE COULD BRING A BIG COST.

## Slide 13
Traceability & Characteristics Problems (3)
 characteristics must be set, defined, recorded, communicated, audited …
4. products can have 100s of different and heterogeneous characteristics defined.
3. traceability databases are not interconnected (internal traceability systems).
 traceability data is not always available for the main company.
2. multiple, and “eventual” contractor-subcontractor relationships.
 traceability data is difficult to “understand”.
1. the product or the manufacturing process is, itself complex:
traceability & characteristics common problems:
 traceability data is disaggregated, full traceability is difficult to achieve.




Traceability & Characteristics DATA
&
Product CAM Data
INTEGRATION

Notes: THEREFORE, AS CONCLÑUSIION, THERE ARE PROBLEMS OF
DAT UNDERTANDABITY
DATA ABAILABITY
DAT DIS-AGREGATION
THE NEED FOR PRODUCT CHAR AGREMENT Betwe partners.
FOR THEM, THE PROPOSITION IS THE INTEGRATION OF
HOW???? THROUGTH THE EMPLOYMENT OF A TRAZ. MODEL.

## Slide 14: Traceability Approach
1. Traceability & Product Characteristics.
  Traceability.
  Traceability principles & problems.
  Traceability in Complex Systems. e-Manufacturing (NC Systems).
  Product Characteristics.
2. Traceability Model.
  Traceability Data Model & Step-NC.
  WorkingSteps: Operations.
  Features & Tolerances: Characteristics.
3. Implementation.
  Demo Tool: NC-Explorer & Traceability.
  Future Work.
4. Conclusions.
  Solutions.
  The BIG QUESTION.
Notes: Second BOLK is TO PROPOSE AND Explain a T MODEl

## Slide 15: STEP NC & Traceability Model Step-NC + Traceability (1)
AP-238
File
Simple CNC machining Scenario
CAD/CAM Design
+ traceability configuration
1 File Per design
CNC Manufacturing
+ traceability recording
1 File Per Product
Manufactured
Traceability
Configuration
File (Part 21)
Trace
Data
Files P21
Trace
Data
Files P21
Trace
Data
Files P21
Inspection (Characteristics)
Manufacturing
Data Storage & Audit
Trace
Data
Files P21
Trace
Data
Files P21
Trace
Data
Files P21
Notes: THis is A EXAMPLE SCENAREO
.
We START FROM a CAM product desing. And WE MAKE a TRACE CONFIGURATION Linked to it.
BOTH ARE SEND TO THE MANUFACTRUNG PLACE
ON PRODUCTION, a DATA file is generated for each single manufactued piece.
Together with the products, theses files are sent back to the contractor side,
So it will be able so audit, check and save them.

## Slide 16
STEP NC & Traceability Model Step-NC + Traceability (2)
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
CNC
System
Customer
Shop
Machine Independent
CNC Control file
Manufacturing
+ traceability configuration
Traceability
Configuration
File (Pat 21)
Machine Independent
traceability configuration file
+ traceability
Finished Parts
+ traceability
Trace
Data
Files P21
Same traceability
structure
Common Objects
Reference
Notes: THE CONFIGURATION FILE IS A PART 21.
IT IS LINKED with the ap238 design and have internal references to objects in the CAM file. THESE GIVE STRUCURE AND MEANING TO THE T DATA.
From this conf file, the final T data files are generated.
With NOW the additional LINK to the final product identification (SERIAL NUMBER)…
AS These DATA Files come FROM configuration ONE,
it is possible to AUDIT to see if REQIREMNTS HAVE BEEN MET

## Slide 17: What is traced? The Traceability Model (1).
tr_Manufacturing
Operations_
relationship
Workpiece
product /
product definition
formation /
product definition
shape definition
representation
product definition
shape
The Trace
Project
Tr_project
(link to Ap238 file/document)
through
Document_Reference
tr_identification
_relationship
product
physical
product ref.
Ap238
WorkingStep
traceability data
tr_Characteristic
_relationship
Features &
tolerances data
traced_Operations L[0:?]
traced_Characteristics L[0:?]
Notes: THis is the general Structure of the model. WE CAN SEE
1- THE AP238 to link with
2- ALSO, the final physicial product manufactured.
3- QND THE MAIN Traceability MODEL ENTITIES

## Slide 18: What is traced? Traceability Model Header (1)
tr_Manufacturing
Operations_
relationship
Workpiece
product /
product definition
formation /
product definition
shape definition
representation
product definition
shape
The Trace
Project
Tr_project
(link to Ap238 file/document)
through
Document_Reference
tr_identification
_relationship
product
physical
product ref.
Ap238
WorkingStep
traceability data
tr_Characteristic
_relationship
Features &
tolerances data
traced_Operations L[0:?]
traced_Characteristics L[0:?]
Notes: LET HAVR A LOOK FIRST TO THE TRACE PROJECT ENTITY

## Slide 19: What is traced? Traceability Model Header (2)
Traceability Project Identification:
  Link between Step File & the Traceability File.
  Link between Product Design Data (WorkPiece) & Product Physical.
Traceability Project Data:
  Additional WorkPiece data to be defined & harmonized.
    Authorization, approval data, (STEP modules 10303-1015 & 1012… )
    Traceability Data Definitions.
  Traced Operations List(through traced_operations).
  Traced Characteristics List (through traced_characteristics).
The Trace
Project
Tr_project
(link to Ap238 file/document)
through
Document_Reference
tr_identification
_relationship
AP238 Data
physical
product ref.
Notes: THIS ENTITY IS THE HEAD ONE AND DEFINED THE DATA LINKS.
- ONE GENETRAL AP238 file
- ONE WITH THE physical piece identification
- SEVERAL External links to AP238 data objetcs (worpieces) REALTED with INTERNAL data bloks corresponding to MANUF OPERATIONS AND Characteristics.
-

## Slide 20: What is traced? WorkingSteps. Operations (1)
tr_Manufacturing
Operations_
relationship
Workpiece
product /
product definition
formation /
product definition
shape definition
representation
product definition
shape
The Trace
Project
Tr_project
(link to Ap238 file/document)
through
Document_Reference
tr_identification
_relationship
product
physical
product ref.
Ap238
WorkingStep
traceability data
tr_Caracteristic
_relationship
Features &
tolerances data
traced_Operations L[0:?]
traced_Characteristics L[0:?]
Notes: ABOUT T data for Manufacturing OPERATIONS

## Slide 21: What is traced? WorkingSteps. Operations (2)
At the heart of the STEP-NC model
  Workplans containing a sequence of Workingsteps.
  Each Workingstep associates an operation with a
  feature on the Workpiece.
feature:
round hole
Ap238 File
WorkingStep #975
WorkingStep #976
WorkingStep #977
WorkingStep #978
WorkingStep #979
trace _Manufacturing
Operation #976
Traceability data, associated with
each Workingstep executed within the physical manufacturing of any feature.
Traceability File
tr_Manufacturing
Operations_
Relationship
trace _Manufacturing
Operation #978
trace _Manufacturing
Operation #977
Notes: THE MODEL DEFInes a link between WORKINGSTEPS (in the AP238) and traceability data for them.

## Slide 22: What is traced? WorkingSteps. Operations (3).
tr_Manufacturing
Operations_
relationship
Trace_
Manufacturing
_ Operation
tr_identification
Product_identification
Tools data
used_tools L[0:?]
Selected Operation traceability data. STEP-NC model
  Tool usage, identification & timings
  Raw Materials identification + logistic data.
  Employees, Machine Operators …
  Model is Open to new Data
tr_Manufacturing_
Operation_Type
tr_Persons
tr_Raw_Materials
tr_Tools
Raw_Materials
data
Other
PDM Operation data
Operators L[0:?]
used_materials L[0:?]
Notes: A first common set of these trac. Data is considered. It includes data for
Persons
Raw materials
Machines involved.
Tools used
The data not only identifiy these resources but, VERY IMPORTAT, defines TIME STAMPS to RECORD WHEN HAS been started and ENDED IT USE.

## Slide 23: What is traced? GD&T. Characteristics (1)
tr_Manufacturing
Operations_
relationship
Workpiece
product /
product definition
formation /
product definition
shape definition
representation
product definition
shape
The Trace
Project
Tr_project
(link to Ap238 file/document)
through
Document_Reference
tr_identification
_relationship
product
physical
product ref.
Ap238
WorkingStep
traceability data
tr_Characteristic
_relationship
Features &
tolerances data
traced_Operations L[0:?]
traced_Characteristics L[0:?]
Notes: AND NOW, ABOUT T data for Manuacturing OPERATIONS

## Slide 24: What is traced? GD&T. Characteristics (2)
STEP-NC model supports GD&T. Tolerances
  Characteristics could be a wider concept.
  Each entity, can support or have, requirements
  specified by hundreds of different characteristics.
  Characteristics should be defined, registered, stored,
  audited, validated, authentified ..
feature:
round hole
Ap238 File
Tolerance (dim) #1175
Tolerance (size) #1256
Tolerance (pos) #1298
Tolerance (ang) #1417
trace _characteristic #1256
Traceability data, associated with
each characteristic traced
for any particular feature or tolerance requirement.
Traceability File
tr_Characteristic_
Relationship
trace _characteristic
#1417
trace _characteristic
#1298
Notes: THE MODEL DEFInes a link between TOLERANCE, FEAURES OR WORKINGSTEPS (in the AP238) and traceability data for them.

## Slide 25: What is traced? GD&T. Characteristics (6)
Trace_
Characteristic
tr_identification
Characteristic_identification
(id, name, desciption)
measure
Selected Characteristic traceability Data. STEP-NC model
  Characteristic Identification: Implicit or Explicit (Repository)
  Measure Rep. Item for Open Characteristics Data.
  Validation, Verification, Auditing, Comprobation, Control.
  Characterisitcs are heterogenous
  Model is Open to new Data or Redefinition
tr_Persons
tr_timeStamp
Measure_Representation_
Item
Timing
data
Operators L[0:?]
time
tr_Characteristic
_relationship
Notes: ALSO, A first common set of these trac. Data is considered. It includes data for
THE CHARCT KIND & VALUE
Persons
TIME STAMPS
Important here is that CHA may be predifined in a common repository or created and defined form scratch.

## Slide 26: Traceability Approach
1. Traceability & Product Characteristics.
  Traceability.
  Traceability principles & problems.
  Traceability in Complex Systems. e-Manufacturing (NC Systems).
  Product Characteristics.
2. Traceability Model.
  Traceability Data Model & Step-NC.
  WorkingSteps: Operations.
  Features & Tolerances: Characteristics.
3. Implementation.
  Demo Tool: NC-Explorer & Traceability.
  Future Work.
4. Conclusions.
  Solutions.
  The BIG QUESTION.
Notes: In GOING TO SKIP BOLK 3 to go fasTER but you can have a look later to SEE PRESENT WORK adn ..

## Slide 27
Traceability & Characteristics. Step-NC Approach + Traceability
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
CNC
System
Customer
Shop
Machine Independent
CNC Control file
Manufacturing
+ traceability configuration
Traceability
Configuration
File (Pat 21)
Machine Independent
traceability configuration file
+ traceability
Finished Parts
+ traceability
Trace
Data
Files P21
Same traceability
structure
Common Objects
Reference
Notes: Comming back to the general scenario, will have a lok at some of the applications.
FIRST, at CONFIGURATION Stage

## Slide 28: Traceability & Characteristics. Step-NC Explorer (1)
Setting Traceability requirements on a WorkingStep.
(tracing Operations)
Notes: We can see here a STEP TOOLS NC Explorer updated to work with the proposed T model in the CONFIGURATION mode.
We see a POP UP window configure T required for a Working step selected in the CAM model

## Slide 29: Traceability & Characteristics. Step-NC Explorer (2)
Setting Traceability requirements on a Tolerance.
(tracing Characteristics).
Notes: The same here but with the charateristic FOR a Tolerance selectection

## Slide 30
AP-238
File
Entity ID #31
Ap238 file & traceability File Link
Characteristic Requeriments Data Fields
Traceability File
Entity Links/Relations
(Entity ID 31  Tr_Characteristics #73)
Notes: Here is a squech of the T STEP 21 file result of the configuration.
IT shows, on GREEN, The external links for a defined characteristics with its related AP238 object.
On RED, it shows how T internal link (for a that characteristic) to its internal conf

## Slide 31
Traceability & Characteristics. Step-NC Approach + Traceability
CAD/CAM
System
CAD/CAM
Translator
AP-238
File
AP-203/224/240
CNC
System
Customer
Shop
Machine Independent
CNC Control file
Manufacturing
+ traceability configuration
Traceability
Configuration
File (Pat 21)
Machine Independent
traceability configuration file
+ traceability
Finished Parts
+ traceability
Trace
Data
Files P21
Same traceability
structure
Common Objects
Reference
Notes: Now, FOLLOWING THE CONF, A Tra, System at the manufacturing place , TRACK THE DATA CREATING A NEW Part 21 FILE

## Slide 32: Traceability & Characteristics. Step-NC Explorer. Traceability Data
Different Tool lots can be employed on the manufacturing process of identical pieces
LOT #TL12-01WF
LOT #TL14-25RK
Piece Nº 1
Piece Nº 2
This is recorded in the traceability files under tools identification.
The identifiaction, Item or Lot of the tool can be inspecting, when visualizing traceability data
Notes: For instance, if a TOOL LOT is required to be traced when making a piece.
BUT, to make one, may be we use a lot, and to make another (BUT IDENTICAL), we use other LOT.
THEn, We generate a part 21 Specifing ONE LOT or the other

## Slide 33: Traceability & Characteristics. Step-NC Explorer (3)
Inspecting Traceability data on a Feature. (NC-Explorer Update)
(Example of Visualization Options: traced characteristics & timings resume).
Notes: We can see here a STEP TOOLS NC Explorer updated to work with the proposed T model in the VISUALIZATIONG AND AUDITING mode.
We see some POP UP window showing diff alternatives.
Timming sequence.
Visualizing all data about one working step
….and many others.

## Slide 34
AP-238
File
Traceability File
Entity Links/Relations
Ap238 file & traceability File Link
WorkingStep ID #975
Notes: As we saw before with a CONFIGURATION FILE, we see Here a sketch of the T DATA STEP 21 file result of the previous configuration.
IT shows, on GREEN, The external links for a defined operation with its related AP238 object.
On RED, it shows how T internal link (for a that working step) to its recorded data

## Slide 35: Traceability & Characteristics. Step-NC Explorer (4).
Fast Auditing Traceability data over characteristics or WorkingSteps.
Tools for Visually Audting this data, and fast check with parts are or not traced and which ammoount of data has been completed is important.
Fast,& Easy to see which pieces, and which data has been correct registered at manufacturing.
Notes: Auditing permits, in complex products, check for the correctness and conpleteness of the data

## Slide 36: Related & Future Work. Ap 203 (1)
As an example of AP integration and compatibility, the Model has also been integrated into AP 203applications (StepTools Viewer).
  1. Samples of Configuration, Auditing & Visualization of trace requirements over StepViewer.
Notes: To Finish, i’d like to remark that the same model has also thoght to work in assembly manufacturing based on AP203 models.
Here we can see StepTools VIEWER updated to work with the proposed T model in CONF mode.

## Slide 37: Work Done & Future Work. Ap 203 (2)
Traceability Model in AP 203.
  2. Samples of Configuration, Auditing & Visualization of trace requirements over StepViewer
Traceability Model can be also linked to other Aps.
  Examples Ap240, and AP224.
Notes: Here in AUDITING AND REPORTING mode

## Slide 38: Traceability Approach
1. Traceability & Product Characteristics.
  Traceability.
  Traceability principles & problems.
  Traceability in Complex Systems. e-Manufacturing (NC Systems).
  Product Characteristics.
2. Traceability Model.
  Traceability Data Model & Step-NC.
  WorkingSteps: Operations.
  Features & Tolerances: Characteristics.
3. Implementation.
  Demo Tool: NC-Explorer & Traceability.
  Future Work.
4. Conclusions.
  Solutions.
  The BIG QUESTION.
Notes: Presentation has 3 BLOKS.
1 Introduction to Traceability concept ant product characteristics.
2 The traceability model proposal
3 The work done until now

## Slide 39
4. products can have 100s of different and heterogeneous characteristics defined.
2. multiple, and “eventual” contractor-subcontractor relationships.
1. the product or the manufacturing process is, itself complex :



 characteristics must be set, defined, recorded, communicated, audited …
 traceability data is not always available for the main company.
 traceability data is difficult to “understand”.
 traceability data is disaggregated, full traceability is difficult to achieve.
 traceability data as a standard part of PDE (product data exchange)
 generic definition of characteristics.
traceability in complex & highly dynamic environments (e-Manufacturing, CNC) solution & proposals :
Automation of traceability is an important task


Traceability & Characteristics Solutions (1)
3. traceability databases are not interconnected (internal traceability systems).
 traceability data delivered with the product.
 traceability data linked to CAD/CAM data.
STEP – EXPRESS (ISO 10303) information model for tracing manufacturing operations.



Notes: Then, CONCLUDING and coming back to the PRESented problems.
WITH
We get, for

## Slide 40: Traceability & Characteristics. The BIG QUESTION (1)
Feature
data Model
Operation
data Model
WorkingStep
data Model
Project
data Model
Traceability
data Model
WorkPlan
data Model
NC_parameters
data Model
Profile
data Model
WorkPlan
data Model
Core
STEP
Geometry
STEP NC Data Model
A new STEP Standard Information model for traceability ?
EXPRESS data model for traceability
Notes: AND, AS LAST SLID, I’ like to propose to you THE BIG CUESTION.
WICH IS