## Slide 1: AP229 - Forgings
Len Slovensky
Northrop Grumman/SCRA
slovensky@scra.org

## Slide 2: AP223 – Castings
Customer to metal caster
Metal caster to inspection
Metal caster to simulation
Metal caster to tooling shop
Metal caster to other operations
Customer to simulation
Casting process planning

## Slide 3: A STEP Manufacturing Suite
STEP
Product Data
Generation
Macro
Process
Planning
Micro
Process
Planning
AP240
AP203
AP240
and
AP238
Shop
Floor
Finished Part
(DESIGN)
(FACTORY)
(FACTORY)
(FACTORY)
STEP In, STEP Out,
STEP Throughout
Function
Standards
ISO 6983
M&G Codes
CMM
Inspection
Input from
Micro PP
NC programming
AP240
AP219
AP238
AP202, AP214 & AP203
AP223
AP224
ISO-13399
Cutting tools
ISO-13584
fasteners
AP214
AP214

## Slide 4: Common base manufacturing for AP’s
aic_advanced_brep – AIC514
aic_machining_feature – AIC522
aic_geometric_tolerances - AIC519
AP203
AP224
AP240
AP219
AP238
Dimensional tolerances
AP223
AP202
Major
Core
Components
harmonized
Implicit & Explicit base shape
AP214
Notes: Through the use of AICs and common mappings, all the manufacturing APs have a common base
Brep geometry
Tolerances
Features
PLIB reference
Etc.
Note – modules not used.

## Slide 5: AP229 – Forgings
1. ISO 10303-229 can be used to exchange product specification between a customer and a foundry bidding on a job. The Foundry then determines how best to produce the Forging.
2. Once the job is awarded to the foundry ISO 10303-229 is used to represent the design data
3. Once the mold, die, or tooling design is completed, ISO 10303-229 can be used to transfer the detailed design description between a foundry and a pattern, die, or tooling shop
4. Foundries are using forging simulation software to predict defects and reduce cost.
5. ISO 10303-229 can be used to transfer the simulation input and results between a process designer and a process modeler.ISO 10303-229 can be used to represent process plan data, such as instructions for melting, pouring, cooling, and forging. Also ISO 10303-229 can be used to represent the process data for quality control purposes.